## Slide 1: CS 211 Computer Architecture Lecture 12: RISC-V: Arithmetic and Load/Store instructions
Ravi Mittal
ravi.mittal@iitgoa.ac.in
Indian Institute of Technology, Goa

## Slide 2: Acknowledgements
Class Presentation, CS61C, Introduction to Assembly Language and RISC-V Instruction Set Architecture, University of Berkeley, Prof Krste Asanović & Randy H. Katz. http://inst.eecs.Berkeley.edu/~cs61c
Class Presentation, CS61C, Introduction to Machine Language, University of Berkeley, Branden Ghen, Fall 2019 http://inst.eecs.Berkeley.edu/~cs61c
Computer Organization and Design, The Hardware Software Interface, RISC-V edition, Patterson and Hennessey
Digital Design and Computer Architecture: RISC-V Edition, Harris & Harris Elsevier – Presentation.

## Slide 3: In today’s class, we will study
Introduction
Basic Arithmetic Instructions
  add, sub
Immediate Instructions
  addi
Data Transfer Instructions
  lw, sw
  lh, sh
  lb, sb

## Slide 4: Introduction

## Slide 5: RISC-V Instruction Set
RISC-V 32-bit integer instruction set (RV32I) version 2.2

## Slide 6: RISC-V Assembly Language
Assembly language is the human-readable representation of the computer’s native language
Each assembly language instruction specify
  Operations to be performed
  Operands to operate on
Instructions have an opcode and operands
add x1, x2, x3 # x1 = x2 + x3
Operation code (opcode)
Destination Operand
Second operand
First operand
# is assembly comment syntax

## Slide 7: Operands
Operand location: physical location in computer
  Registers
  Memory
  Constants (also called immediates)

## Slide 8: RISC-V Assembly Language Basic Arithmetic Instructions

## Slide 9: Addition and Subtraction of Integers
Addition in Assembly
Example: add x1,x2,x3 (in RISC-V)
Equivalent to: a = b + c (in C)
  where C variables ⇔ RISC-V registers are:
  a ⇔ x1, b ⇔ x2, c ⇔ x3
Subtraction in Assembly
Example: sub x3,x4,x5 (in RISC-V)
Equivalent to: d = e - f (in C)
  where C variables ⇔ RISC-V registers are: d ⇔ x3, e ⇔ x4, f ⇔ x5
Note that the format of sub is the same as that of add
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 10
Simplicity favors regularity
Consistent instruction format
Same number of operands (two sources and one destination)
Easier to encode and handle in hardware
Design Principle 1
Ref: Harris and Harris Book: Digital Design and Computer Architecture: RISC-V Edition

## Slide 11: Multiple Instructions
How to do the following C statement?
a = b + c + d - e;
Break into multiple instructions
  add x10, x1, x2 # a_temp = b + c
  add x10, x10, x3 # a_temp = a_temp + d
  sub x10, x10, x4 # a = a_temp - e
A single line of C may turn into several RISC-V instructions
Adapted form: Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 12: Design Principle 2
Make the common case fast
RISC-V includes only simple, commonly used instructions
Hardware to decode and execute instructions can be simple, small, and fast
More complex instructions (that are less common) performed using multiple simple instructions
RISC-V is a reduced instruction set computer (RISC), with a small number of simple instructions
Other architectures, such as Intel’s x86, are complex instruction set computers (CISC)
Ref: Harris and Harris Book: Digital Design and Computer Architecture: RISC-V Edition

## Slide 13: Immediate Instructions

## Slide 14: Immediates
Immediates are numerical constants
  They appear often in code, so there are special instructions for them
Instruction syntax for immediates:
opi dst, src, imm
  Operation names end with ‘i’, replace 2nd source register with an immediate
  Immediates can be up to 12-bits in size
  Interpreted as sign-extended two’s complement
  In assembly, immediate can be written in decimal, hexadecimal or binary
Example:
Add Immediate:
  addi x3,x4,-10 (in RISC-V)
  f = g - 10 (in C)
Adapted from: Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 15: Immediates
Suppose a → s0,b → s1. Convert the following C statement to RISC-V:
a = (5+b)-3;
addi t1, s1, 5
addi s0, t1, -3
Why no subi instruction?
Adapted from: Braden Ghena, Univ of California, Berkeley

## Slide 16: Data Transfer Instructions

## Slide 17: Data Transfer: Load from and Store to memory
Processor
Control
Datapath
PC
Registers
Arithmetic & Logic Unit
(ALU)
Memory
Input
Output
Bytes
Enable?
Read/Write
Address
Write Data = Store to memory
Read Data = Load from
memory
Processor-Memory Interface
I/O-Memory Interfaces
Program
Data
Much larger place
To hold values, but slower than registers!
Fast but limited place
To hold values
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 18: Memory Addresses are in Bytes
Data typically smaller than 32 bits, but rarely smaller than 8 bits (e.g., char type)–works fine if everything is a multiple of 8 bits
8 bit chunk is called a byte (1 word = 4 bytes)
Byte Addressable
Word addresses are 4 bytes apart
  Word address is same as address of rightmost byte – least-significant byte(i.e. Little-endian convention)
0x0000
0x0001
0x0002
0x0003
AB
67
45
23
01
Little Endian
F2
F1
AC
CD
EF
78
07
0x0004
0x0007
address
LSByte
MSByte
Word 0x78EFCDAB is stored as

## Slide 19: Byte-Addressable Memory (Revision)
The address of a memory word must now be multiplied by 4. For example,
  the address of memory word 2 is 2 × 4 = 8
  the address of memory word 10 is 10 × 4 = 40 (0x28)
RISC-V is byte-addressed, not word-addressed

## Slide 20: Data Transfer Instruction - syntax
Instruction syntax for data transfer:
memop reg, off(bAddr)
  memop = operation name (“operator”)
  reg = register for operation source or destination
  bAddr = register with pointer to memory (“base address”)
  off = address offset (immediate) in bytes (“offset”)
Accesses memory at address bAddr+off
Reminder: A register holds a word of raw data (no type) – make sure to use a register (and offset) that point to a valid memory address
Adapted from: Braden Ghena, Univ of California, Berkeley

## Slide 21: Load Word: lw instruction
lw <rd>, <offset>(<base register>)
Operation code (opcode)
Destination register
Offset
Base Register
Example: lw t1, 4(s0)
Address calculation:
  add offset (4) to the base address (s0)
  address = (s0 + 4)
Destination register (rd):
  t1 holds the value at address (s0 + 4)
Any register can be used to hold the base address

## Slide 22: Load Word: lw instruction - Example
RISC-V assembly code
lw x5, 4(x0) # read word at address 4 into x5
Result: x5 holds the value 0xF2F1AC07 after load
0x0000
0x0001
0x0002
0x0003
AB
67
45
23
01
Little Endian
07
AC
F1
CD
EF
78
F2
0x0004
0x0007
address
LSByte
MSByte

## Slide 23: lw: load word – Example 2
C code
int A[100];
g = h + A[3];
RISC-V assembly
lw x10,12(x13) # Reg x10 gets A[3]
add x11,x12,x10 # g = h + A[3]
Note: x13 – base register (pointer to A[0])
12 – offset in bytes
Offset must be a constant known at assembly time
Ref: Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 24: Store Word: sw instruction
sw <src1>, <offset>(<base register>)
Operation code (opcode)
Source register
Offset
Base Register
Result: stores the value held in t6 into memory address 0x2C (44)
RISC-V assembly code
sw t6, 44(zero) # write t6 into address 44

## Slide 25: sw: store word - Example 1
C code
int A[100];
A[10] = h + A[3];
Using Store Word (sw) in RISC-V:
lw x10,12(x13) # Temp reg x10 gets A[3]
add x10,x12,x10 # Temp reg x10 gets h + A[3]
sw x10,40(x13) # A[10] = h + A[3]
Note: x13 – base register (pointer)
12,40 – offsets in bytes
x13 + 12 and x13 + 40 must be multiples of 4
Notes: Note the change in notation ; Using register numbers instead of names.

## Slide 26: Memory and Variable Size
So Far:
  lw reg, off(bAddr)
  sw reg, off(bAddr)
What about characters (1 Byte) and shorts (sometimes 2 Bytes), etc? Want to be able to use interact with memory values smaller than a word.
Processor
Computer
Control
(“brain”)
Datapath
Registers
Memory
Devices
Input
Output
lw reg off(bAddr)
sw reg off(bAddr)
Notes: lb/sb have same syntax as lw/sw
Aside: also load/store halfword (lh/sh)

## Slide 27: Half-Word Instructions
lh reg, off(bAddr) “load half”
sh reg, off(bAddr) “store half”
  On sh, upper 16 bits are ignored
  On lh, upper 16 bits are filled by sign-extension

## Slide 28: Loading and Storing Bytes
In addition to word data transfers (lw, sw), RISC-V has byte data transfers:
  load byte: lb
  store byte: sb
Same format as lw, sw
E.g., lb x10,3(x11)
  contents of memory location with address = sum of “3” + contents of register x11 - is copied to the low byte position of register x10
byte loaded
zzz zzzz
x
…is copied to “sign-extend”
This bit
xxxx xxxx xxxx xxxx xxxx xxxx
x10:
Ref: Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 29: Unsigned Instructions (self reading)
  lhu reg, off(bAddr)“load half unsigned”
  lbu reg, off(bAddr)“load byte unsigned”
  On l(b/h)u, upper bits are filled by zero-extension
Why no s(h/b)u? Why no lwu?

## Slide 30: Lecture Summary
We have studied
  Basic arithmetic instruction: add
  Immediate type instructions: addi
  Load and store instructions: lw, sw, lh, sh, lb, sb

## Slide 31: Trivia
CS 305: Computer Architecture

## Slide 32: Who is She?
Andy Robert
Emmy Noether
Ada Lovelase
Maryam Mirzadhani
Rhea Chakraborty

## Slide 33
Wrote the first computer program
Her program calculated the Bernoulli numbers on Charles Babbage’s Analytical Engine
She was the daughter of the poet Lord Byron
Ada Lovelace, 1815-1852

## Slide 34: Backup

## Slide 35: Sign Extension
Decimal | Binary |  | 
 | 4-bit | 8-bit | 32-bit
3ten | 0011two | 0000 0011two | 0000 0000 0000 0011two
-3ten | 1101two | 1111 1101two | 1111 1111 1111 1101two
When is this relevant?
Any time you need a wider version of a narrower operand
  e.g., adding two integers of different widths
back

## Slide 36: RISC-V Instructions (1/2)
Instruction Syntax is rigid:
op dst, src1, src2
  1 operator, 3 operands
    op = operation name (“operator”)
    dst = register getting result (“destination”)
    src1 = first register for operation (“source 1”)
    src2 = second register for operation (“source 2”)
Keep hardware simple via regularity