## Slide 1: CS 211 Computer Architecture Lecture 15: RISC-V Instructions – Branching Instructions
Ravi Mittal
ravi.mittal@iitgoa.ac.in
Indian Institute of Technology, Goa

## Slide 2: Acknowledgements
Digital Design and Computer Architecture: RISC-V Edition, Harris & Harris Elsevier – Presentation.
Class Presentation, CS61C, Introduction to Assembly Language and RISC-V Instruction Set Architecture, University of Berkeley, Prof Krste Asanović & Randy H. Katz. http://inst.eecs.Berkeley.edu/~cs61c
Class Presentation, CS61C, Introduction to Machine Language, University of Berkeley, Branden Ghen, Fall 2019 http://inst.eecs.Berkeley.edu/~cs61c
Computer Organization and Design, The Hardware Software Interface, RISC-V edition, Patterson and Hennessey

## Slide 3: In today’s class we will study
How to generate constants?
Branching Instructions
  beq, bne, blt/bltu, bge/bgeu
Jumping instruction: j
Assembly level program for:
  if, if/else, while, for loops

## Slide 4: Overview
lw t0, 0(S2)
lw t1, 4(S2)
sw t1, 0(S2)
sw t0, 4(S2)
Higher-Level Language Program (e.g. C)
Assembly Language Program (e.g. RISC-V)
Machine Language Program (RISC-V)
Hardware Architecture Description (e.g. block diagrams)
Compiler
Assembler
Machine Interpretation
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
0000 1001 1100 0110 1010 1111 0101 1000
1010 1111 0101 1000 0000 1001 1100 0110
1100 0110 1010 1111 0101 1000 0000 1001
0101 1000 0000 1001 1100 0110 1010 1111
Logic Circuit Description (Circuit Schematic Diagrams)
Architecture Implementation
Today’s topic_

## Slide 5: Previous Classes
CS 211: Computer Architecture

## Slide 6: RISC-V Logical Instructions
Ref: Steven Ho, CS61C Su18 - Lecture 7 Univ of California, Berkeley
Notes: CS61C Su18 - Lecture 7

## Slide 7: So far we have studied
Arithmetic operations: add, sub, addi,
How to bring data from memory to register and vice versa?
  lw, sw, lb, sb, lbu
Bit-by-bit logical instructions
    and, or, xor
    andi, ori, xori
Logical Shift instructions
  sll, srl, sra
  slli, srli, srai

## Slide 8: Format for shift immediate type
I‐type encoding

## Slide 9: How to generate a constant?

## Slide 10: Generating Constant
12-bit signed constants using addi:
Any immediate that needs more than 12 bits cannot use this method.
addi rd, rs1, imm12 - format
C Code
// int is a 32-bit signed word
int a = -372;
RISC-V assembly code
# s0 = a
addi s0, x0, -372
Ref: Harris and Harris Book: Digital Design and Computer Architecture: RISC-V Edition

## Slide 11: Generating 32-bit constants
Use load upper immediate (lui) and addi:
lui: puts an immediate in the upper 20 bits of destination register, 0’s in lower 12 bits
C Code
int a = 0xFEDC8765;
RISC-V assembly code
# s0 = a
lui s0, 0xFEDC8
addi s0, s0, 0x765
Remember that addi sign-extends its 12-bit immediate
Ref: Harris and Harris Book: Digital Design and Computer Architecture: RISC-V Edition
lui instruction format

## Slide 12: Generating 32-bit constant (self reading)
If bit 11 of 32-bit constant is 1, increment upper 20 bits by 1 in lui
C Code
int a = 0xFEDC8EAB;
Note: -341 = 0xEAB
RISC-V assembly code
# s0 = a
lui s0, 0xFEDC9 # s0 = 0xFEDC9000
addi s0, s0, -341 # s0 = 0xFEDC9000 + 0xFFFFFEAB
# = 0xFEDC8EAB
Ref: Harris and Harris Book: Digital Design and Computer Architecture: RISC-V Edition

## Slide 13: RISC-V Branching Instructions

## Slide 14: Branching
Execute instructions out of sequence
Change of control flow
Types of branches:
  Conditional – change of control flow depending on outcome of comparison
    branch if equal (beq)
    branch if not equal (bne)
    branch if less than (blt/bltu)
    branch if greater than or equal to (bge/bgeu)
  Unconditional – always branch
    jump (j)
    jump register (jr)
    jump and link (jal)
    jump and link register (jalr)
Will talk about these when we discuss function calls
Ref: Harris and Harris Book: Digital Design and Computer Architecture: RISC-V Edition

## Slide 15: RISC-V Branching Instructions
 Conditional Branching

## Slide 16: Branch if equal: beq
Based on computation, do something different
In programming languages: if-statement
RISC-V: if-statement instruction is
beq register1,register2,L1
means: go to statement labeled L1 if (value in register1) == (value in register2)
….otherwise, go to next statement
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 17: Conditional Branching: beq
# RISC-V assembly
addi s0, zero, 4 # s0 = 0 + 4 = 4
addi s1, zero, 1 # s1 = 0 + 1 = 1
slli s1, s1, 2 # s1 = 1 << 2 = 4
beq s0, s1, target # branch is taken
addi s1, s1, 1 # not executed
sub s1, s1, s0 # not executed
target: # label
add s1, s1, s0 # s1 = 4 + 4 = 8
Labels indicate instruction location. They can’t be reserved words and must be followed by colon (:)
Ref: Harris and Harris Book: Digital Design and Computer Architecture: RISC-V Edition

## Slide 18: The Branch Not Taken: bne
# RISC-V assembly
addi s0, zero, 4 # s0 = 0 + 4 = 4
addi s1, zero, 1 # s1 = 0 + 1 = 1
slli s1, s1, 2 # s1 = 1 << 2 = 4
bne s0, s1, target # branch not taken
addi s1, s1, 1 # s1 = 4 + 1 = 5
sub s1, s1, s0 # s1 = 5 – 4 = 1
target:
add s1, s1, s0 # s1 = 1 + 4 = 5
Ref: Harris and Harris Book: Digital Design and Computer Architecture: RISC-V Edition

## Slide 19: Other Conditional Branches
Branch if less than (blt/bltu)
  blt s0, s1, target # branches if s0 < s1 (signed)
  bltu s0, s1, target # same as blt but interprets # s0 and s1 as unsigned
Branch if greater than or equal to (bge/bgeu)
  bge s0, s1, target # branches if s0 >= s1 (signed)
  bgeu s0, s1, target # branches if s0 >= s1 (unsigned)
Ref: Harris and Harris Book: Digital Design and Computer Architecture: RISC-V Edition

## Slide 20: RISC-V Branching Instructions
 Unconditional Branching: j

## Slide 21: Unconditional Branching: j
# RISC-V assembly
j target # jump to target
srai s1, s1, 2 # not executed
addi s1, s1, 1 # not executed
sub s1, s1, s0 # not executed
target:
add s1, s1, s0 # s1 = 1 + 4 = 5
Ref: Harris and Harris Book: Digital Design and Computer Architecture: RISC-V Edition
j is a pseudo instruction

## Slide 22: High-Level Code Constructs
if statements
if/else statements
while loops
for loops
Ref: Harris and Harris Book: Digital Design and Computer Architecture: RISC-V Edition

## Slide 23: if Statement
C Code
if (i == j)
f = g + h;
f = f – i;
RISC-V assembly code
# s0 = f, s1 = g, s2 = h
# s3 = i, s4 = j
bne s3, s4, L1
add s0, s1, s2
L1:
sub s0, s0, s3
Assembly tests opposite case (i != j) of high-level code (i == j)
Ref: Harris and Harris Book: Digital Design and Computer Architecture: RISC-V Edition

## Slide 24: if-else Statement
C Code
if (i == j)
f = g + h;
else
f = f – i;
RISC-V assembly code
# s0 = f, s1 = g, s2 = h
# s3 = i, s4 = j
bne s3, s4, L1
add s0, s1, s2
j done
L1:
sub s0, s0, s3
done:
Ref: Harris and Harris Book: Digital Design and Computer Architecture: RISC-V Edition

## Slide 25: while Loops
C Code
// determines the power
// of x such that 2x = 128
int pow = 1;
int x = 0;
while (pow != 128) {
pow = pow * 2;
x = x + 1;
}
RISC-V assembly code
# s0 = pow, s1 = x
addi s0, zero, 1
add s1, zero, zero
addi t0, zero, 128
while:
beq s0, t0, done
slli s0, s0, 1
addi s1, s1, 1
j while
done:
Assembly tests for the opposite case (pow == 128) of the C code (pow != 128).
Ref: Harris and Harris Book: Digital Design and Computer Architecture: RISC-V Edition

## Slide 26: for Loops
for (initialization; condition; loop operation)
statement
initialization: executes before the loop begins
condition: is tested at the beginning of each iteration
loop operation: executes at the end of each iteration
statement: executes each time the condition is met
Ref: Harris and Harris Book: Digital Design and Computer Architecture: RISC-V Edition

## Slide 27: for Loops
C Code
// add the numbers from 0 to 9
int sum = 0;
int i;
for (i=0; i!=10; i = i+1) {
sum = sum + i;
}
RISC-V assembly code
# s0 = i, s1 = sum
addi s1, zero, 0
add s0, zero, zero
addi t0, zero, 10
for:
beq s0, t0, done
add s1, s1, s0
addi s0, s0, 1
j for
done:
Ref: Harris and Harris Book: Digital Design and Computer Architecture: RISC-V Edition

## Slide 28: for Loop – Another example
C Code
// add the powers of 2 from 1
// to 100
int sum = 0;
int i;
for (i=1; i < 101; i = i*2) {
sum = sum + i;
}
RISC-V assembly code
# s0 = i, s1 = sum
addi s1, zero, 0
addi s0, zero, 1
addi t0, zero, 101
loop:
bge s0, t0, done
add s1, s1, s0
slli s0, s0, 1
j loop
done:
Ref: Harris and Harris Book: Digital Design and Computer Architecture: RISC-V Edition

## Slide 29: Class Summary
In this class we have studied use of the following instructions:
  bne, beq, blt, bge
We have also studied how we can develop assembly code for high level constructs
  if statements
  if/else statements
  while loops
  for loops
Do self reading of the following instructions:
  Multiplication instructions: mul, mulh, mulhu, mulhsu
  Division Instructions: div, divu

## Slide 30: Unconditional Branching (jr)
# RISC-V assembly
0x00000200 addi s0, zero, 0x210
0x00000204 jr s0
0x00000208 addi s1, zero, 1 # not executed
0x0000020C sra s1, s1, 2 # not executed
0x00000210 lw s3, 44(s1)
Ref: Harris and Harris Book: Digital Design and Computer Architecture: RISC-V Edition

## Slide 31: ASCII Code
American Standard Code for Information Interchange
Each text character has unique byte value
  For example, S = 0x53, a = 0x61, A = 0x41
  Lower-case and upper-case differ by 0x20 (32)

## Slide 32: Multiplication (Optional)
32 × 32 multiplication, 64-bit result
  mul s0, s1, s2
  s0 = lower 32 bits of result
  mulh s0, s1, s2
  s0 = upper 32 bits of result, treats operands as signed
  mulhu s0, s1, s2
  s0 = upper 32 bits of result, treats operands as
  unsigned
  mulhsu s0, s1, s2
  s0 = upper 32 bits of result, treats s1 as signed, s3
  as unsigned
Ref: Harris and Harris Book: Digital Design and Computer Architecture: RISC-V Edition

## Slide 33: Multiplication (Optional) : Example
32 × 32 multiplication, 64-bit result
For full 64-bit result:
    mulh s4, s1, s2
    mul s3, s1, s2
    {s4, s3} = s1 x s2
Could also use mulhu or mulhsu instead of mulh
Ref: Harris and Harris Book: Digital Design and Computer Architecture: RISC-V Edition

## Slide 34: Division
32-bit division, 32-bit quotient, remainder
  div s1, s2, s3 # s1 = s2/s3
    The contents of s2 is divided by the contents of s3 and the quotient is placed in s1
    Both operands and the result are signed values
  divu s1, s2, s3 # unsigned division
    The contents of s2 is divided by the contents of s3 and the quotient is placed in s1
    Both operands and the result are unsigned values