## Slide 1: CS 211 Computer Architecture Floating Point Numbers
Ravi Mittal
ravi.mittal@iitgoa.ac.in
Indian Institute of Technology, Goa

## Slide 2: Floating Point topics we will cover
Background: Fractional binary numbers
IEEE floating point standard: Definition
Example and properties
Rounding, addition, multiplication
Floating point in C
Summary

## Slide 3: Floating Point Quote
“95% of the folks out there are completely clueless about floating-point.”
  James Gosling Feb. 28, 1998
James Gosling
Sun Fellow
Java Inventor

## Slide 4: Towards Floating Point Number

## Slide 5: Reasoning about Fractions
Example 6-bit representation:
Big Idea: Why can’t we represent fractions? Because our bits all represent nonnegative powers of 2.
Example: 10 1010two = 1×25 + 1×23 + 1×21 = 42ten
The lowest power of 2 is 20, so the smallest difference between any two numbers is 20 = 1.
Example: 10 1011two = 42+1 = 43ten
0b xx xxxx
25
24
23
22
21
20

## Slide 6: Representation of Fractions
New Idea: Introduce a fixed “Binary Point” that signifies boundary between negative and nonnegative powers:
Example: 10.1010two = 1×21 + 1×2-1 + 1×2-3 = 2.625ten
Binary point numbers that match the 6-bit format above range from 0 (00.0000two) to 3.9375 (11.1111two)
0b xx.xxxx
21
20
2-1
2-2
2-3
2-4
Example 6-bit representation:

## Slide 7: Fractional Binary Numbers
2i
2i-1
4
2
1
1/2
1/4
1/8
2-j
bi | bi-1 | ••• | b2 | b1 | b0 | b-1 | b-2 | b-3 | ••• | b-j
• • •
Representation
  Bits to right of “binary point” represent fractional powers of 2
  Represents rational number:
• • •
Notes: Latex source for equation: \sum_{k=-j}^i b_k \times 2^k

## Slide 8: Fractional Binary Numbers: Examples
Value Representation
5 3/4 101.112
2 7/8 010.1112
63/64 001.01112
Observations
  Divide by 2 by shifting right
  Multiply by 2 by shifting left
  Numbers of form 0.111111…2 are just below 1.0
  1/2 + 1/4 + 1/8 + … + 1/2i + … ➙ 1.0
Notes: ε : Epsilon

## Slide 9: Representable Numbers
Limitation
  Can only exactly represent numbers of the form x/2k
  Other rational numbers have repeating bit representations
    Gives approximate number
Value Representation
  1/3 0.0101010101[01]…2
  1/5 0.001100110011[0011]…2
  1/10 0.0001100110011[0011]…2

## Slide 10: Number Representation Limitations
Given 32 bits (a word), what can we represent so far?
  Signed and Unsigned Integers
  4 Characters (ASCII)
  Instructions and Addresses
How do we encode the following:
  Real numbers (e.g. 3.14159)
  Very large numbers (e.g. 6.02×1023)
  Very small numbers (e.g. 6.626×10-34)
  Special numbers (e.g. ∞, NaN)
Floating
Point
Notes: We’re gonna be finishing up Number Representation.

## Slide 11: Scientific Notations

## Slide 12: Scientific Notation (Decimal)
Normalized form: exactly one digit (non-zero) to left of decimal point (the point “floats” to be in the standard position)
Alternatives to representing 1/1,000,000,000
  Normalized: 1.0×10-9
  Not normalized: 0.1×10-8, 10.0×10-10
2.625ten × 1023
radix (base)
decimal point
significand
exponent
Notes: Begin this slide by remembering to say that in order to keep track of where the point “floats” to, we store that info in the exponent number

## Slide 13: Scientific Notation (Binary)
Computer arithmetic that supports this called floating point due to the “floating” of the binary point
  Declare such variable in C as float
1.0101two × 21
radix (base)
binary point
exponent
significand

## Slide 14: Translating To and From Scientific Notation
Consider the number 1.011two×24
To convert to ordinary number, shift the decimal to the right by 4
  Result: 10110two = 22ten
For negative exponents, shift decimal to the left
  1.011two×2-2 => 0.01011two = 0.34375ten
Go from ordinary number to scientific notation by shifting until in normalized form
  1101.001two => 1.101001two×23
Notes: Put the point behind the first “significant” bit

## Slide 16: Floating Point Numbers

## Slide 17: Ariane 5
Ariane 5 - a heavy-lift space launch vehicle developed and operated by Arianespace for the European Space Agency. It was launched from the Centre Spatial Guyanais in French Guiana. It has been used to deliver payloads into geostationary transfer orbit or low Earth orbit.

## Slide 18: This is important!
Ariane 5 explodes on maiden voyage: $500 MILLION dollars lost
  64-bit floating point number assigned to 16-bit integer
  Causes rocket to get incorrect value of horizontal velocity and crash
Patriot Missile defense system misses scud – 28 people die
  System tracks time in tenths of second
  Converted from integer to floating point number
  Accumulated rounding error causes drift. 20% drift over 8 hours.
  Eventually (on 2/25/1991 system was on for 100 hours) causes range mis-estimation sufficiently large to miss incoming missiles.

## Slide 19: Goals of Floating Point
Support a wide range of values
  Both very small and very large
Keep as much precision as possible
Help programmer with errors in real arithmetic
  Support +∞, -∞, Not-A-Number (NaN), exponent overflow and underflow
Driven by numerical concerns
Positional notation is not effective in representing very large numbers
  Representation of 5 × 2100 would consist of the bit pattern 101 followed by 100 zeros
Notes: Want floating point to look more “”natural” in that small unsigned value -> small floating point value

## Slide 20: “Father” of Floating Point Standard
IEEE Standard 754 for Binary Floating-Point Arithmetic
www.cs.berkeley.edu/~wkahan/ieee754status/754story.html
Prof. Kahan
Prof. Emeritus
UC Berkeley
1989 ACM Turing Award Winner!
Notes: 1:30 in

## Slide 21: Floating Point Encoding
Use normalized, Base 2 scientific notation: +1.xxx…xtwo×2yyy…ytwo
Split a 32-bit word into 3 fields:
  S represents Sign (1 is negative, 0 positive)
  Exponent represents y’s
  Significand represents x’s
  Key Idea: More like Sign and Magnitude
S
Exponent
Significand
31 30
23 22
0
1 bit
8 bits
23 bits
Notes: Woah! We are splitting a 32 bit number into three fields. Does this look familiar? YES. Just like instructions formats!

## Slide 22: Comparison
Which is smaller? (i.e. closer to -∞)
  0 or 1 x 10-127 ?
  1 x 10-126 or 1 x 10-127 ?
  -1 x 10-127 or 0 ?
  -1 x 10-126 or -1 x 10-127 ?
Which is smaller? (i.e. closer to -∞)
  0 or 1 x 10-127 ?
  1 x 10-126 or 1 x 10-127 ?
  -1 x 10-127 or 0 ?
  -1 x 10-126 or -1 x 10-127 ?
Which is smaller? (i.e. closer to -∞)
  0 or 1 x 10-127 ?
  1 x 10-126 or 1 x 10-127 ?
  -1 x 10-127 or 0 ?
  -1 x 10-126 or -1 x 10-127 ?
Which is smaller? (i.e. closer to -∞)
  0 or 1 x 10-127 ?
  1 x 10-126 or 1 x 10-127 ?
  -1 x 10-127 or 0 ?
  -1 x 10-126 or -1 x 10-127 ?
Which is smaller? (i.e. closer to -∞)
  0 or 1 x 10-127 ?
  1 x 10-126 or 1 x 10-127 ?
  -1 x 10-127 or 0 ?
  -1 x 10-126 or -1 x 10-127 ?

## Slide 23: The Exponent Field
Use biased notation
  Read exponent as unsigned, but with bias of 127
  Exp field ranges from -127 (00000000two) to 128 (11111111two)
  Exponent 0 is represented as 01111111two = 127ten
To encode in biased notation, add the bias (add 127) then encode in unsigned:
  If we had 21, exp = 1 => 128 => 10000000two
  2127: exp = 127 => 254 => 11111110two

## Slide 24: The Exponent Field
Why use biased notation for the exponent?
  Remember that we want floating point numbers to look small when their actual value is small
    We don’t like how in 2’s complement, -1 looks bigger than 0. Bias notation preserves the linearity of value
Recall that only the first bit denotes sign
  Thus, floating point resembles sign and magnitude
S
Exponent
Significand
31 30
23 22
0
1 bit
8 bits
23 bits
magnitude

## Slide 25: Floating Point Encoding
What does this mean?
  Think of it as: (1 + Value of Significand)
  Since the Significand represents all the negative powers of 2, its total value is always < 1
  Example: 1.0101two = 1 + 2-2 + 2-4 = 1.3125
(-1)S x (1 . Significand) x 2(Exponent-127)
S
Exponent
Significand
31 30
23 22
0
1 bit
8 bits
23 bits
Notes: Why have the 1? Be sneaky and save a bit
Add animations

## Slide 26: Floating Point Encoding
Note the implicit 1 in front of the Significand
  Ex: 0011 1111 1100 0000 0000 0000 0000 0000two
    (-1)0 x (1 . 1two) x 2(127-127) = (1 . 1two) x 2(0)
    1.1two = 1.5ten, NOT 0.1two = 0.5ten
  Gives us an extra bit of precision
(-1)S x (1 . Significand) x 2(Exponent-127)
S
Exponent
Significand
31 30
23 22
0
1 bit
8 bits
23 bits
Notes: Tell them to remember the number 23!!!!

## Slide 27: Floating Point Encoding
Note the implicit 1 in front of the Significand
  Ex: 0011 1111 1100 0000 0000 0000 0000 0000two
    (-1)0 x (1 . 1two) x 2(127-127) = (1 . 1two) x 2(0)
    1.1two = 1.5ten, (NOT that 0.1two = 0.5ten )
  This gives us an extra bit of precision
(-1)S x (1 . Significand) x 2(Exponent-127)
S
Exponent
Significand
31 30
23 22
0
1 bit
8 bits
23 bits
Notes: Tell them to remember the number 23!!!!

## Slide 28: Precision options
Single precision: 32 bits
Double precision: 64 bits
Other formats: half precision, quad precision
s | exponent | Frac or Significand
1 | 8-bits | 23-bits
s | exponent | Frac pr Significand
1 | 11-bits | 52-bits

## Slide 29: Single Precision - Notationa
s | exponent | Fracrion or Significand
1 | 8-bits | 23-bits
S: sign bit (0  non-negative, 1  negative)
Normalize significand: 1.0 ≤ |significand| < 2.0
  Always has a leading pre-binary-point 1 bit, so no need to represent it explicitly (hidden bit)
  Significand is Fraction with the “1.” restored
Exponent: excess representation: actual exponent + Bias
  Ensures exponent is unsigned
  Single: Bias = 127; Double: Bias = 1203

## Slide 30: Single Precision
s | exp | frac
1 | 8-bits | 23-bits
S: sign bit (0  non-negative, 1  negative)
Normalize significand: 1.0 ≤ |significand| < 2.0
  Always has a leading pre-binary-point 1 bit, so no need to represent it explicitly (hidden bit)
  Significand is Fraction with the “1.” restored
Exponent: excess representation: actual exponent + Bias
  Ensures exponent is unsigned
  Single: Bias = 127; Double: Bias = 1203

## Slide 31: Precision and Accuracy
Precision is a count of the number of bits in a computer word used to represent a value
Accuracy is a measure of the difference between the actual value of a number and its computer representation
High precision permits high accuracy but doesn’t guarantee it. It is possible to have high precision but low accuracy.
Example: float pi = 3.14;
  pi will be represented using all 24 bits of the significand (highly precise), but is only an approximation (not accurate)
Don’t confuse these two terms!
Notes: Maybe cut out this slide. Not relevant

## Slide 32: Floating Point – Special Cases

## Slide 33: Floating Point Numbers - Special Cases
Exponent | Significand | Meaning
0x00 | ? | ?
0x00 | ? | ?
0x01 – 0xFE | anything | ± Num
0xFF | ? | ?
0xFF | ? | ?

## Slide 34: Representing Zero
Special case: Exp and Significand all zeros = 0
Two zeros! One for each sign bit +0 and -0
So, coded 0x00000000 = 0
But wait… what happened to zero?
  Using standard encoding 0x00000000 is 1.0×2-127≠0
    All because of implicit 1
Notes: Fix slides so looks pretty

## Slide 35: Floating Point Numbers - Special Cases
Exponent | Significand | Meaning
0x00 | 0 | ± 0
0x00 | ? | ?
0x01 – 0xFE | anything | ± Num
0xFF | ? | ?
0xFF | ? | ?

## Slide 36: Representing Very Small Numbers
What are the normal numbers closest to 0? (here, normal means the exponent is nonzero)
  a = 1.0…00two×21-127 = (1+ 0 ) x 2-126 = 2-126
  b = 1.0…01two×21-127 = (1+2-23) x 2-126 = 2-126 + 2-149
b
a
0
+∞
-∞
Gaps!
  The gap between 0 and a is 2-126
  The gap between a and b is 2-149
  We want to represent numbers between 0 and a
    How? The implicit 1 forces the 2-126 term to stay :(
    Solution: Take out the implicit 1!
  Special case: Exp = 0, Significand ≠ 0 are denorm numbers

## Slide 37: Denorm Numbers
Short for “denormalized numbers”
  No leading 1
  Careful! Denorm exponent bias is now 126 when Exp = 0x00
Now what do the gaps look like?
  Smallest denorm: ± 0.0…01two×2-126 = ± 2-149
  Largest denorm: ± 0.1…1two×2-126 = ± (2-126 – 2-149)
  Smallest norm: ± 1.0…0two×2-126 = ± 2-126
No uneven gap! Increments by 2-149
So much closer to 0
Notes: Here’s another exercise: reason about why the denorm bias is 126 by trying to evaluate the two floating point number that surround a in the previous slide

## Slide 38: Floating Point Representation
Numerical Form: (–1)s M 2E
  Sign bit s determines whether number is negative or positive
  Significand M normally a fractional value in range [1.0,2.0).
    Ranges between 1 and 2 – ε ; or between 0 and 1 – ε
  Exponent E weights value by power of two
Encoding
  MSB s is sign bit s
  exp field encodes E
  frac field encodes M
s | exp | frac
  Example: 1521310 = (-1)0 x 1.11011011011012 x 213

## Slide 39: Floating Point Numbers - Special Cases
Exponent | Significand | Meaning
0x00 | 0 | ± 0
0x00 | non-zero | ± Denorm Num
0x01 – 0xFE | anything | ± Num
0xFF | ? | ?
0xFF | ? | ?

## Slide 40: Other Special Cases
Exp = 0xFF, Significand = 0: ± ∞
  e.g. division by 0
  Still work in comparisons
Exp = 0xFF, Significand ≠ 0: Not a Number (NaN)
  e.g. square root of negative number, 0/0, ∞–∞
  NaN propagates through computations
  In theory: Significand can be useful for debugging
Largest value (besides ∞)?
  Exp = 0xFF has now been taken! Exp = 0xFE has largest: 1.1…1two×2127 = 2128 – 2104
Notes: Remind students that there are different types of NaNs but they won’t be tested on them,they just needa know what the range of all NaNs are

## Slide 41: Floating Point Numbers - Special Cases
Exponent | Significand | Meaning
0x00 | 0 | ± 0
0x00 | non-zero | ± Denorm Num
0x01 – 0xFE | anything | ± Num
0xFF | 0 | ± ∞
0xFF | non-zero | NaN

## Slide 42: Limitations of Floating Point Numbers

## Slide 43: Floating Point Limitations (1/2)
What if result x is too large? (abs(x)> 2128)
  Overflow: Exponent is larger than what can be represented
What if result x too small? (0 < abs(x)< 2-149)
  Underflow: Negative exponent is larger than can be represented
What if result runs off the end of the Significand?
  Rounding occurs and can lead to unexpected results
  FP has different rounding modes
0
2-149
2128
1
-1
-2-149
-2128
underflow
overflow
overflow
Notes: Have another slide explaining about the gaps that come about when the exponent field changes
Remember that we can only represent 232 distinct things. Just bc we have a bigger range doesnt mean we get more numbers. We lose precision as we have higher exponents

## Slide 44: Trivia …

## Slide 45: Floating Point Gaps
Does adding 0x00000001 always add the same value to the floating point number?
NO—it’s value depends on the exponent field
ex: 1.0two x 22 = 4 1.0two x 23 = 8 1.1two x 22 = 6 1.1two x 23 = 12
Thus floating points are quite different from the number representations you’ve learned so far
+2
+4
Notes: Have another slide explaining about the gaps that come about when the exponent field changes
Remember that we can only represent 232 distinct things. Just bc we have a bigger range doesnt mean we get more numbers. We lose precision as we have higher exponents

## Slide 46: Big Data, this is just the Beginning
2010
2015
1023
World's Data (Bytes)
You are here
The number of stars in the universe
Sensors & Devices
VoIP
Enterprise Data
Social Media
Notes: “The Internet of [Things] could raise the level of U.S. gross domestic product by 2%-5% by 2025.
This gain… if realized, would boost the annual U.S. GDP growth rate by 0.2%-0.4% points over this period, bringing growth closer to 3% per year.”

## Slide 47: Computing Needs are continuously changing… more and more computing power is required… at lower cost

## Slide 48: No free lunch for software engineers… Moore’s law is reducing … Transistor count is not doubling every two years… Power wall issue.. Memory wall issue..

## Slide 49: Cost of making Chips is increasing…

## Slide 50: Why can’t we copy the success from software?

## Slide 52
How did Instagram turn into USD 1Billion acquisition with only 13 employees?

## Slide 53: Power of Open Source

## Slide 54: A Success Story
He led a life full of hardships as his family struggled hard to meet ends meet. His house did not even have electricity, says Forbes
He and his mother migrated to Mountain View and managed to get a two-bedroom apartment with the help of government support
He used to do menial jobs like cleaning and mopping at a grocery store while his mother took up a baby sitting job. Life took a tragic turn when his mother was diagnosed with cancer
By 18, he learnt computer networking all by himself with the help of manuals from a used book store
Finally, he enrolled at San Jose State University worked at Ernst & Young as a security tester

## Slide 55: A Success Story .. continues
Joined Yahoo and left it ..
Along with a friend, he developed a software ..a messaging application
He released this application.. Active users went up to 250K
By 2011, the app was in the top 20 apps
By 2013, the app had active user base of 200 million
Today, it’s user base is over 450 million
Now, it has just 32 engineers
Facebook acquired this application for USD 16 Billion
What is this application?

## Slide 56: What is this application?
Instagram
Zoom
Messenger
WhatsApp
Snapchat
Youtube

## Slide 57: What is this application?
Instagram
Zoom
Messenger
WhatsApp
Snapchat
Youtube

## Slide 58: Who is this person?
Jan Koum

## Slide 59: Learning…
You too can innovate…
You need to learn to be creative…
Ready to dirty your hands..
Power of open source software…
You can create amazing applications with open source software..
  Linux
  GNU compiler collection
  Python
  PHP
  Blender

## Slide 60: Why hardware in not opensource..
Some companies monopolized the market..
Intel’s ISA is known.. But not micro-code
You can’t design your own chip unless you invest millions..
Implementation details of ARM, MIPS, Intel, etc are not open-sourced..
  You don’t have access to code and design libraries
It’s changing now … with RISC V
  Open source Hardware
  Developed to support many applications
    Desktop, Mobiles, GPUs, Special purpose processors

## Slide 61: We will study RISC V

## Slide 62: Towards Two’s complement number

## Slide 63: Negative number..concept
Computers cant do subtraction easily if we use sign and magnitude representation
CS 305: Computer Architecture

## Slide 64: Binary Modular Arithmetic
If we use a fixed number of bits, addition and other operations may produce results outside the range that the output can represent (up to 1 extra bit for addition)
  This is known as an overflow
Common approach: Ignore the extra bit
  Gives rise to modular arithmetic: With N-bit numbers, equivalent to following all operations with mod 2N
  Visually, numbers “wrap around”:

## Slide 65: Representing negative numbers
We can simply relabel some of the digits to represent negative numbers while representing the nice properties of modular arithmetic
This is called 2’s
Complement Encoding

## Slide 66: 2’s complement encoding
In two’s complement encoding, the high-order bit of the N-bit representation has negative weight:
Negative numbers have “1” in the high-order bit
Most negative number? 10...0000 -2N-1
Most positive number? 01...1111 +2N-1 - 1
If all bits are 1? 11...1111 - 1

## Slide 67: Two’s Complement and Arithmetic
To negate a number (i.e., compute –A given A), we invert all the bits and add one
  Why does this work?

## Slide 68: Two’s Complement and Arithmetic
To compute A-B, we can simply use addition and compute A+(-B)
  Result: Same circuit can add and subtract
Example:

## Slide 69: Two-complement Encoding Example (Cont.)
x = 15213: 00111011 01101101
y = -15213: 11000100 10010011