## Slide 1: CS 211 Computer Architecture Lecture 18 - 19: Floating Point Numbers
Ravi Mittal
ravi.mittal@iitgoa.ac.in
Indian Institute of Technology, Goa

## Slide 2: Floating Point topics we will cover
Towards Floating Point Numbers
Scientific Notations
Floating Point Numbers
Floating Point – Special Cases
Limitations of Floating Point Numbers
Extra Slides - Backup

## Slide 3: Reading and References
Computer System: A programmer’s Perspective, by Bryant and O’Hallaron, Chapter 2.4.2 on Floating Point Represenation
Prof Krste Asanović & Randy Katz, CS 61C: Computer Architecture, University of Berkeley, California
Nick Riasanovsky, CS 61C: Computer Architecture, University of Berkeley, California

## Slide 4: Floating Point Quote
“95% of the folks out there are completely clueless about floating-point.”
  James Gosling Feb. 28, 1998
James Gosling
Sun Fellow
Java Inventor
Ref: CS61-C –Univ of Berkeley, California

## Slide 5
“According to my calculation,
you should float now ... I think ...”
“It’s an inexact science.”

## Slide 6: Towards Floating Point Number

## Slide 7: Reasoning about Fractions
Example 6-bit representation:
Big Idea: Why can’t we represent fractions? Because our bits all represent nonnegative powers of 2.
Example: 10 1010two = 1×25 + 1×23 + 1×21 = 42ten
The lowest power of 2 is 20, so the smallest difference between any two numbers is 20 = 1.
Example: 10 1011two = 42+1 = 43ten
0b xx xxxx
25
24
23
22
21
20
Ref: CS61-C –Univ of California, Berkeley

## Slide 8: Representation of Fractions
New Idea: Introduce a fixed “Binary Point” that signifies boundary between negative and nonnegative powers:
Example: 10.1010two = 1×21 + 1×2-1 + 1×2-3 = 2.625ten
Binary point numbers that match the 6-bit format above range from 0 (00.0000two) to 3.9375 (11.1111two)
0b xx.xxxx
21
20
2-1
2-2
2-3
2-4
Example 6-bit representation:
Ref: CS61-C –Univ of California, Berkeley

## Slide 9: Fractional Binary Numbers
2i
2i-1
4
2
1
1/2
1/4
1/8
2-j
bi | bi-1 | ••• | b2 | b1 | b0 | b-1 | b-2 | b-3 | ••• | b-j
• • •
Representation
  Bits to right of “binary point” represent fractional powers of 2
  Represents rational number:
• • •
Notes: Latex source for equation: \sum_{k=-j}^i b_k \times 2^k

## Slide 10: Fractional Binary Numbers: Examples
Value Representation
5 3/4 101.112
2 7/8 010.1112
Observations
  Divide by 2 by shifting right
  Multiply by 2 by shifting left
  Numbers of form 0.111111…2 are just below 1.0
  1/2 + 1/4 + 1/8 + … + 1/2i + … ➙ 1.0
Notes: ε : Epsilon

## Slide 11: Representable Numbers
Limitation
  Can only exactly represent numbers of the form x/2k
  Other rational numbers have repeating bit representations
    Gives approximate number
Value Representation
  1/3 0.0101010101[01]…2
  1/5 0.001100110011[0011]…2
  1/10 0.0001100110011[0011]…2

## Slide 12: Number Representation Limitations
Given 32 bits (a word), what can we represent so far?
  Signed and Unsigned Integers
  4 Characters (ASCII)
  Instructions and Addresses
How do we encode the following:
  Real numbers (e.g. 3.14159)
  Very large numbers (e.g. 6.02×1023)
  Very small numbers (e.g. 6.626×10-34)
  Special numbers (e.g. ∞, NaN)
Floating
Point
Ref: CS61-C –Univ of California, Berkeley
Notes: We’re gonna be finishing up Number Representation.

## Slide 13: Scientific Notations

## Slide 14: Scientific Notation (Decimal)
Normalized form: exactly one digit (non-zero) to left of decimal point (the point “floats” to be in the standard position)
Alternatives to representing 1/1,000,000,000
  Normalized: 1.0×10-9
  Not normalized: 0.1×10-8, 10.0×10-10
2.625ten × 1023
radix (base)
decimal point
significand
exponent
Ref: CS61-C –Univ of California, Berkeley
Notes: Begin this slide by remembering to say that in order to keep track of where the point “floats” to, we store that info in the exponent number

## Slide 15: Scientific Notation (Binary)
Computer arithmetic that supports this called floating point due to the “floating” of the binary point
  Declare such variable in C as float
1.0101two × 21
radix (base)
binary point
exponent
significand
Ref: CS61-C –Univ of California, Berkeley

## Slide 16: Translating To and From Scientific Notation
Consider the number 1.011two×24
To convert to ordinary number, shift the decimal to the right by 4
  Result: 10110two = 22ten
For negative exponents, shift decimal to the left
  1.011two×2-2 => 0.01011two = 0.34375ten
Go from ordinary number to scientific notation by shifting until in normalized form
  1101.001two => 1.101001two×23
Ref: CS61-C –Univ of California, Berkeley
Notes: Put the point behind the first “significant” bit

## Slide 17: Floating Point Numbers

## Slide 18: Ariane 5
Ariane 5 - a heavy-lift space launch vehicle developed and operated by Arianespace for the European Space Agency. It was launched from the Centre Spatial Guyanais in French Guiana. It has been used to deliver payloads into geostationary transfer orbit or low Earth orbit.

## Slide 19: This is important!
Ariane 5 explodes on maiden voyage: $500 MILLION dollars lost
  64-bit floating point number assigned to 16-bit integer
  Causes rocket to get incorrect value of horizontal velocity and crash
Patriot Missile defense system misses scud – 28 people die
  System tracks time in tenths of second
  Converted from integer to floating point number
  Accumulated rounding error causes drift. 20% drift over 8 hours.
  Eventually (on 2/25/1991 system was on for 100 hours) causes range mis-estimation sufficiently large to miss incoming missiles.

## Slide 20: Goals of Floating Point
Support a wide range of values
  Both very small and very large
Keep as much precision as possible
Help programmer with errors in real arithmetic
  Support +∞, -∞, Not-A-Number (NaN), exponent overflow and underflow
Driven by numerical concerns
Positional notation is not effective in representing very large numbers
  Representation of 5 × 2100 would consist of the bit pattern 101 followed by 100 zeros
Ref: CS61-C –Univ of California, Berkeley
Notes: Want floating point to look more “”natural” in that small unsigned value -> small floating point value

## Slide 21: “Father” of Floating Point Standard
IEEE Standard 754 for Binary Floating-Point Arithmetic
www.cs.berkeley.edu/~wkahan/ieee754status/754story.html
Prof. Kahan
Prof. Emeritus
UC Berkeley
1989 ACM Turing Award Winner!
Ref: CS61-C –Univ of California, Berkeley
Notes: 1:30 in

## Slide 22: Floating Point Encoding
Use normalized, Base 2 scientific notation: +1.xxx…xtwo×2yyy…ytwo
Split a 32-bit word into 3 fields:
  S represents Sign (1 is negative, 0 positive)
  Exponent represents y’s
  Significand represents x’s
  Key Idea: More like Sign and Magnitude
S
Exponent
Significand
31 30
23 22
0
1 bit
8 bits
23 bits
Ref: CS61-C –Univ of California, Berkeley
Notes: Woah! We are splitting a 32 bit number into three fields. Does this look familiar? YES. Just like instructions formats!

## Slide 23: Comparisons
Which is smaller? (i.e. closer to -∞)
  0 or 1 x 10-127 ?
  1 x 10-126 or 1 x 10-127 ?
  -1 x 10-127 or 0 ?
  -1 x 10-126 or -1 x 10-127 ?
Which is smaller? (i.e. closer to -∞)
  0 or 1 x 10-127 ?
  1 x 10-126 or 1 x 10-127 ?
  -1 x 10-127 or 0 ?
  -1 x 10-126 or -1 x 10-127 ?
Which is smaller? (i.e. closer to -∞)
  0 or 1 x 10-127 ?
  1 x 10-126 or 1 x 10-127 ?
  -1 x 10-127 or 0 ?
  -1 x 10-126 or -1 x 10-127 ?
Which is smaller? (i.e. closer to -∞)
  0 or 1 x 10-127 ?
  1 x 10-126 or 1 x 10-127 ?
  -1 x 10-127 or 0 ?
  -1 x 10-126 or -1 x 10-127 ?
Which is smaller? (i.e. closer to -∞)
  0 or 1 x 10-127 ?
  1 x 10-126 or 1 x 10-127 ?
  -1 x 10-127 or 0 ?
  -1 x 10-126 or -1 x 10-127 ?
Ref: CS61-C –Univ of California, Berkeley

## Slide 24: The Exponent Field
Use biased notation
  Read exponent as unsigned, but with bias of 127
  Exp field ranges from -127 (00000000two) to 128 (11111111two)
  Exponent 0 is represented as 01111111two = 127ten
To encode in biased notation, add the bias (add 127) then encode in unsigned:
  If we had 21, exp = 1 => 128 => 10000000two
  2127: exp = 127 => 254 => 11111110two
Ref: CS61-C –Univ of California, Berkeley

## Slide 25: The Exponent Field
Why use biased notation for the exponent?
  Remember that we want floating point numbers to look small when their actual value is small
    We don’t like how in 2’s complement, -1 looks bigger than 0. Bias notation preserves the linearity of value
Recall that only the first bit denotes sign
  Thus, floating point resembles sign and magnitude
S
Exponent
Significand
31 30
23 22
0
1 bit
8 bits
23 bits
magnitude
Ref: CS61-C –Univ of California, Berkeley

## Slide 26: Floating Point Encoding
What does this mean?
  Think of it as: (1 + Value of Significand)
  Since the Significand represents all the negative powers of 2, its total value is always < 1
  Example: 1.0101two = 1 + 2-2 + 2-4 = 1.3125
(-1)S x (1 . Significand) x 2(Exponent-127)
S
Exponent
Significand
31 30
23 22
0
1 bit
8 bits
23 bits
Ref: CS61-C –Univ of California, Berkeley
Notes: Why have the 1? Be sneaky and save a bit
Add animations

## Slide 27: Floating Point Encoding
Note the implicit 1 in front of the Significand
  Ex: 0011 1111 1100 0000 0000 0000 0000 0000two
    (-1)0 x (1 . 1two) x 2(127-127) = (1 . 1two) x 2(0)
    1.1two = 1.5ten
  Gives us an extra bit of precision
(-1)S x (1 . Significand) x 2(Exponent-127)
S
Exponent
Significand
31 30
23 22
0
1 bit
8 bits
23 bits
Ref: CS61-C –Univ of California, Berkeley
Notes: Tell them to remember the number 23!!!!

## Slide 28: Precision options
Single precision: 32 bits
Double precision: 64 bits
Other formats: half precision, quad precision
s | exponent | Frac or Significand
1 | 8-bits | 23-bits
s | exponent | Frac pr Significand
1 | 11-bits | 52-bits

## Slide 29: Single Precision - Notation
s | Exponent | Fraction or Significand
1 | 8-bits | 23-bits
S: sign bit (0  non-negative, 1  negative)
Normalize significand: 1.0 ≤ |significand| < 2.0
  Always has a leading pre-binary-point 1 bit, so no need to represent it explicitly (hidden bit)
  Significand is Fraction with the “1.” restored
Exponent: excess representation: actual exponent + Bias
  Ensures exponent is unsigned
  Single: Bias = 127; Double: Bias = 1203

## Slide 30: Precision and Accuracy
Precision is a count of the number of bits in a computer word used to represent a value
Accuracy is a measure of the difference between the actual value of a number and its computer representation
High precision permits high accuracy but doesn’t guarantee it. It is possible to have high precision but low accuracy.
Example: float pi = 3.14;
  pi will be represented using all 24 bits of the significand (highly precise), but is only an approximation (not accurate)
Don’t confuse these two terms!
Ref: CS61-C –Univ of California, Berkeley
Notes: Maybe cut out this slide. Not relevant

## Slide 31: Floating Point – Special Cases

## Slide 32: Floating Point Numbers - Special Cases
Exponent | Significand | Meaning
0x00 | ? | ?
0x00 | ? | ?
0x01 – 0xFE | anything | ± Num
0xFF | ? | ?
0xFF | ? | ?
Ref: CS61-C –Univ of California, Berkeley

## Slide 33: Representing Zero
Special case: Exp and Significand all zeros = 0
Two zeros! One for each sign bit +0 and -0
So, coded 0x00000000 = 0
But wait… what happened to zero?
  Using standard encoding 0x00000000 is 1.0×2-127≠0
    This is because of implicit 1
Ref: CS61-C –Univ of California, Berkeley
Notes: Fix slides so looks pretty

## Slide 34: Floating Point Numbers - Special Cases
Exponent | Significand | Meaning
0x00 | 0 | ± 0
0x00 | ? | ?
0x01 – 0xFE | anything | ± Num
0xFF | ? | ?
0xFF | ? | ?
Ref: CS61-C –Univ of California, Berkeley

## Slide 35: Representing Very Small Numbers
What are the normal numbers closest to 0? (here, normal means the exponent is nonzero)
  a = 1.0…00two×21-127 = (1+ 0 ) x 2-126 = 2-126
  b = 1.0…01two×21-127 = (1+2-23) x 2-126 = 2-126 + 2-149
b
a
0
+∞
-∞
Gaps!
  The gap between 0 and a is 2-126
  The gap between a and b is 2-149
  We want to represent numbers between 0 and a
    How? The implicit 1 forces the 2-126 term to stay
    Solution: Take out the implicit 1 (becomes denorm)
  Special case: Exp = 0, Significand ≠ 0 are denorm numbers
Ref: CS61-C –Univ of California, Berkeley

## Slide 36: Denorm Numbers
Short for “denormalized numbers”
  No leading 1
  Careful! Denorm exponent bias is now 126 when Exp = 0x00
Now what do the gaps look like?
  Smallest denorm: ± 0.0…01two×2-126 = ± 2-149
  Largest denorm: ± 0.1…1two×2-126 = ± (2-126 – 2-149)
  Smallest norm: ± 1.0…0two×2-126 = ± 2-126
No uneven gap! Increments by 2-149
So much closer to 0
Ref: CS61-C –Univ of California, Berkeley
Notes: Here’s another exercise: reason about why the denorm bias is 126 by trying to evaluate the two floating point number that surround a in the previous slide

## Slide 37: Floating Point Numbers - Special Cases
Exponent | Significand | Meaning
0x00 | 0 | ± 0
0x00 | non-zero | ± Denorm Num
0x01 – 0xFE | anything | ± Num
0xFF | ? | ?
0xFF | ? | ?
Ref: CS61-C –Univ of California, Berkeley

## Slide 38: Other Special Cases
Exp = 0xFF, Significand = 0: ± ∞
  e.g. division by 0
  Still work in comparisons
Exp = 0xFF, Significand ≠ 0: Not a Number (NaN)
  e.g. square root of negative number, 0/0, ∞–∞
  NaN propagates through computations
  In theory: Significand can be useful for debugging
Largest value (besides ∞)?
  Exp = 0xFF has now been taken! Exp = 0xFE has largest: 1.1…1two×2127 = 2128 – 2104
Ref: CS61-C –Univ of California, Berkeley
Notes: Remind students that there are different types of NaNs but they won’t be tested on them,they just needa know what the range of all NaNs are

## Slide 39: Floating Point Numbers - Special Cases
Exponent | Significand | Meaning
0x00 | 0 | ± 0
0x00 | non-zero | ± Denorm Num
0x01 – 0xFE | anything | ± Num
0xFF | 0 | ± ∞
0xFF | non-zero | NaN
Ref: CS61-C –Univ of California, Berkeley

## Slide 40: Limitations of Floating Point Numbers

## Slide 41: Floating Point Limitations (1/2)
What if result x is too large? (abs(x)> 2128)
  Overflow: Exponent is larger than what can be represented
What if result x too small? (0 < abs(x)< 2-149)
  Underflow: Negative exponent is larger than can be represented
What if result runs off the end of the Significand?
  Rounding occurs and can lead to unexpected results
  FP has different rounding modes
0
2-149
2128
1
-1
-2-149
-2128
underflow
overflow
overflow
Ref: CS61-C –Univ of California, Berkeley
Notes: Have another slide explaining about the gaps that come about when the exponent field changes
Remember that we can only represent 232 distinct things. Just bc we have a bigger range doesnt mean we get more numbers. We lose precision as we have higher exponents

## Slide 42: Floating Point Limitations (2/2)
FP addition is NOT associative!
  You can find Big and Small numbers such that: Small + Big + Small ≠ Small + Small + Big
  This is due to rounding errors: FP approximates results because it only has 23 bits for Significand
Despite being seemingly “more accurate,” FP cannot represent all integers
  e.g. 224 + 223 + 1 = 25165825 (try it!)
  Be careful when casting between int and float
Ref: CS61-C –Univ of California, Berkeley
Notes: Information can get lost when casting between int and float (in both directions!)
Some optimizations change the ordering of FP operations, which can lead to errors.

## Slide 43: Normalized Encoding Example
Value: float F = 15213.0;
  1521310 = 111011011011012
  = 1.11011011011012 x 213
Significand
  M = 1.11011011011012
  frac = 110110110110100000000002
Exponent
  E = 13
  Bias = 127
  exp = 140 = 100011002
Result: 0 10001100 11011011011010000000000
s
exp
frac
v = (–1)s M 2E
E = exp – Bias

## Slide 44: C float Decoding Example 1
float: 0xC0A00000
binary:
1 | 8-bits | 23-bits
E = 129
S = 1 -> negative number
M = 1.010 0000 0000 0000 0000 0000
M = 1 + 1/4 = 1.25
v = (–1)s M 2E
E = exp – Bias
v = (–1)s M 2E =
  Bias = 2k-1 – 1 = 127

## Slide 45: C float Decoding Example #1
E = 129
S = 1 -> negative number
M = 1.010 0000 0000 0000 0000 0000
M = 1 + 1/4 = 1.25
v = (–1)s M 2E
E = exp – Bias
v = (–1)s M 2E =
float: 0xC0A00000
binary: 1100 0000 1010 0000 0000 0000 0000 0000
1 | 1000 0001 | 010 0000 0000 0000 0000 0000
1 | 8-bits | 23-bits

## Slide 46: C float Decoding Example #2
float: 0xC0A00000
binary: 1100 0000 1010 0000 0000 0000 0000 0000
1 | 1000 0001 | 010 0000 0000 0000 0000 0000
1 | 8-bits | 23-bits
E = exp – Bias = 129 – 127 = 2 (decimal)
S = 1 -> negative number
M = 1.010 0000 0000 0000 0000 0000
M = 1 + 1/4 = 1.25
v = (–1)s M 2E
E = exp – Bias
v = (–1)s M 2E = (-1)1 * 1.25 * 22 = -5
  Bias = 2k-1 – 1 = 127

## Slide 47: C float Decoding Example #3
E = 129
S = 1 -> negative number
M = 0.010 0000 0000 0000 0000 0000
M = 1 + 1/4 = 1.25
v = (–1)s M 2E
E = 1 – Bias
v = (–1)s M 2E =
float: 0x001C0000
binary: 0000 0000 0001 1100 0000 0000 0000 0000
0 | 0000 0000 | 001 1100 0000 0000 0000 0000
1 | 8-bits | 23-bits

## Slide 48: C float Decoding Example #2
float: 0x001C0000
E = 1 – Bias = 1 – 127 = –126 (decimal)
S = 0 -> positive number
M = 0.001 1100 0000 0000 0000 0000
M = 1/8 + 1/16 + 1/32 = 7/32 = 7*2–5
v = (–1)s M 2E
E = 1 – Bias
v = (–1)s M 2E = (-1)0 * 7*2–5 * 2–126 = 7*2–131
  Bias = 2k-1 – 1 = 127
binary: 0000 0000 0001 1100 0000 0000 0000 0000
0 | 0000 0000 | 001 1100 0000 0000 0000 0000
1 | 8-bits | 23-bits
v ≈ 2.571393892 X 10–39

## Slide 49: Backup

## Slide 50: Floating Point Representation
Numerical Form: (–1)s M 2E
  Sign bit s determines whether number is negative or positive
  Significand M normally a fractional value in range [1.0,2.0).
    Ranges between 1 and 2 – ε ; or between 0 and 1 – ε
  Exponent E weights value by power of two
Encoding
  MSB s is sign bit s
  exp field encodes E
  frac field encodes M
s | exp | frac
  Example: 1521310 = (-1)0 x 1.11011011011012 x 213

## Slide 51: Precision options
Single precision: 32 bits
Double precision: 64 bits
Other formats: half precision, quad precision
s | exp | frac
1 | 8-bits | 23-bits
s | exp | frac
1 | 11-bits | 52-bits

## Slide 52: Single Precision
s | exp | frac
1 | 8-bits | 23-bits
S: sign bit (0  non-negative, 1  negative)
Normalize significand: 1.0 ≤ |significand| < 2.0
  Always has a leading pre-binary-point 1 bit, so no need to represent it explicitly (hidden bit)
  Significand is Fraction with the “1.” restored
Exponent: excess representation: actual exponent + Bias
  Ensures exponent is unsigned
  Single: Bias = 127; Double: Bias = 1203

## Slide 53: Three “kinds” of floating point numbers
s | exp | frac
1 | e-bits | f-bits
00…00
exp ≠ 0 and exp ≠ 11…11
11…11
denormalized
normalized
special
v = (–1)s M 2E

## Slide 54: “Normalized” Values
When: exp ≠ 000…0 and exp ≠ 111…1
Exponent coded as a biased value: E = exp – Bias
  exp: unsigned value of exp field
  Bias = 2k-1 - 1, where k is number of exponent bits
    Single precision: 127 (exp: 1…254, E: -126…127)
    Double precision: 1023 (exp: 1…2046, E: -1022…1023)
Significand coded with implied leading 1: M = 1.xxx…x2
  xxx…x: bits of frac field
  Minimum when frac=000…0 (M = 1.0)
  Maximum when frac=111…1 (M = 2.0 – ε)
  Get extra leading bit for “free”
v = (–1)s M 2E

## Slide 55: “Normalized” Values
When: exp ≠ 000…0 and exp ≠ 111…1
Exponent coded as a biased value: E = exp – Bias
  exp: unsigned value of exp field
  Bias = 2k-1 - 1, where k is number of exponent bits
    Single precision: 127 (exp: 1…254, E: -126…127)
    Double precision: 1023 (exp: 1…2046, E: -1022…1023)
Significand coded with implied leading 1: M = 1.xxx…x2
  xxx…x: bits of frac field
  Minimum when frac=000…0 (M = 1.0)
  Maximum when frac=111…1 (M = 2.0 – ε)
  Get extra leading bit for “free”
v = (–1)s M 2E

## Slide 56: Single-Precision Range
Smallest value
  Exponent: 00000001  exponent E = 1 – 127 = –126
  Fraction: 000…00  significand = 1.0
  ±1.0 × 2–126 ≈ ±1.2 × 10–38
Largest value
  exponent: 11111110  actual exponent E = 254 – 127 = +127
  Fraction: 111…11  significand ≈ 2.0
  ±2.0 × 2+127 ≈ ±3.4 × 10+38
v = (–1)s M 2E
E = exp – Bias

## Slide 57: Categories of Floating Point numbers

## Slide 58: Denormalized Values
Condition: exp = 000…0
Exponent value: E = 1 – Bias (instead of exp – Bias) (why?)
Significand coded with implied leading 0: M = 0.xxx…x2
  xxx…x: bits of frac
Cases
  exp = 000…0, frac = 000…0
    Represents zero value
    Note distinct values: +0 and –0 (why?)
  exp = 000…0, frac ≠ 000…0
    Numbers closest to 0.0
    Equispaced
    Gradual underflow
v = (–1)s M 2E
E = 1 – Bias
Notes: Denormalized numbers serve two purposes. First, they provide a way to represent numeric value 0, since with a normalized number we must always have M ≥ 1, and hence we cannot represent 0.
In fact, the floating-point representation of +0.0 has a bit pattern of all zeros: the sign bit is 0, the exponent field is all zeros (indicating a denormalized value), and the fraction field is all zeros, giving M = f = 0
Curiously, when the sign bit is 1, but the other fields are all zeros, we get the value −0.0. With IEEE floating-point format, the values −0.0 and +0.0 are considered different in some ways and the same in others.
A second function of denormalized numbers is to represent numbers that are very close to 0.0. They provide a property known as gradual underflow in which possible numeric values are spaced evenly near 0.0.

## Slide 59: Special Values
Condition: exp = 111…1
Case: exp = 111…1, frac = 000…0
  Represents value  (infinity)
  Operation that overflows- when we multiply two very large numbers or we divide by zero
  Both positive and negative
  E.g., 1.0/0.0 = −1.0/−0.0 = +, 1.0/−0.0 = −
Case: exp = 111…1, frac ≠ 000…0
  Not-a-Number (NaN)
  Represents case when no numeric value can be determined
  E.g., sqrt(–1),  − ,   0
  Sometimes one can represent uninitialized data with NaaN

## Slide 60: Dynamic Range (s=0 only)
s exp frac E Value
0 0000 000 -6 0
0 0000 001 -6 1/8*1/64 = 1/512
0 0000 010 -6 2/8*1/64 = 2/512
…
0 0000 110 -6 6/8*1/64 = 6/512
0 0000 111 -6 7/8*1/64 = 7/512
0 0001 000 -6 8/8*1/64 = 8/512
0 0001 001 -6 9/8*1/64 = 9/512
…
0 0110 110 -1 14/8*1/2 = 14/16
0 0110 111 -1 15/8*1/2 = 15/16
0 0111 000 0 8/8*1 = 1
0 0111 001 0 9/8*1 = 9/8
0 0111 010 0 10/8*1 = 10/8
…
0 1110 110 7 14/8*128 = 224
0 1110 111 7 15/8*128 = 240
0 1111 000 n/a inf
closest to zero
largest denorm
smallest norm
closest to 1 below
closest to 1 above
largest norm
Denormalized
numbers
Normalized
numbers
v = (–1)s M 2E
norm: E = exp – Bias
denorm: E = 1 – Bias
(-1)0(0+1/4)*2-6
(-1)0(1+1/8)*2-6

## Slide 61: Floating Point Gaps
Does adding 0x00000001 always add the same value to the floating point number?
NO—it’s value depends on the exponent field
ex: 1.0two x 22 = 4 1.0two x 23 = 8 1.1two x 22 = 6 1.1two x 23 = 12
Thus floating points are quite different from the number representations you’ve learned so far
+2
+4
Notes: Have another slide explaining about the gaps that come about when the exponent field changes
Remember that we can only represent 232 distinct things. Just bc we have a bigger range doesnt mean we get more numbers. We lose precision as we have higher exponents

## Slide 62: Floating Point Representation
Numerical Form: (–1)s M 2E
  Sign bit s determines whether number is negative or positive
  Significand M normally a fractional value in range [1.0,2.0).
    Ranges between 1 and 2 – ε ; or between 0 and 1 – ε
  Exponent E weights value by power of two
Encoding
  MSB s is sign bit s
  exp field encodes E
  frac field encodes M
s | exp | frac
  Example: 1521310 = (-1)0 x 1.11011011011012 x 213