## Slide 1: CS 211 Computer Architecture Lecture 20: RISC-V – Machine Language - 1
Ravi Mittal
ravi.mittal@iitgoa.ac.in
Indian Institute of Technology, Goa

## Slide 2: Acknowledgements
Class Presentation, CS61C, Introduction to Assembly Language and RISC-V Instruction Set Architecture, University of Berkeley, Prof Krste Asanović & Randy H. Katz. http://inst.eecs.Berkeley.edu/~cs61c
Book: Digital Design and Computer Architecture: RISC-V Edition, Harris & Harris Elsevier – Presentation.
Computer Organization and Design, The Hardware Software Interface, RISC-V edition, Patterson and Hennessey

## Slide 3: RISC-V: So far we have studied
Arithmetic operations: add, sub, addi,
How to bring data from memory to register and vice versa?
  lw, sw, lb, sb, lbu
Bit-by-bit logical instructions
  and, or, xor
  andi, ori, xori
Logical Shift instructions
  sll, srl, sra, slli, srli, srai
Generating Constants
Branching Instructions: beq, bne, blt/bltu, bge/bgeu
Jumping instruction: j
Assembly level program for: if, if/else, while, for loops
Function Calls
  Basics
  Input arguments and Return Value
The Stack
  Basics
  How functions use a stack
  Stack use in non-leaf function calls
  Recursive Functions
Floating Point Operations

## Slide 4: In today’s class we will study
Instruction Formats – Design aspects
Instruction Types
R-Format Instructions

## Slide 5: Instruction Format – Design Aspects

## Slide 6: Instructions as Numbers
Most data we work with is in words (32-bit chunks):
  Each register is a word
  lw and sw both access memory one word at a time
So how do we represent instructions?
  Remember: Computer only understands 1s and 0s, so assembler string “add x10,x11,x0” is meaningless to hardware
  RISC-V seeks simplicity: since data is in words, make instructions be fixed-size 32-bit words also
    Same 32-bit instructions used for RV32, RV64, RV128
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 7: Levels of Representation/Interpretation
We__
were__
here._
lw t0, 0(x2)
lw t1, 4(x2)
sw t1, 0(x2)
sw t0, 4(x2)
Higher-Level Language Program (e.g. C)
Assembly Language Program (e.g. RISCV)
Machine Language Program (RISCV)
Hardware Architecture Description (e.g. block diagrams)
Compiler
Assembler
Machine Interpretation
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
0000 1001 1100 0110 1010 1111 0101 1000
1010 1111 0101 1000 0000 1001 1100 0110
1100 0110 1010 1111 0101 1000 0000 1001
0101 1000 0000 1001 1100 0110 1010 1111
Logic Circuit Description (Circuit Schematic Diagrams)
Architecture Implementation
We__
are__
here._
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 8: The Assembler
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 9: Instruction Types

## Slide 10: Instructions as Numbers
Divide the 32 bits of an instruction into “fields”
  Regular field sizes → simpler hardware
  Each field tells processor something about instruction
Define 6 types of instruction formats:
  R-Format I-Format S-Format U-Format
  SB-Format UJ-Format
31
0
By convention, RISC-V instructions are each 1 word = 4 bytes = 32 bits
Notes: 6 formats to memorize, but 4 formats to internalize (R with three registers, I with two registers and an immediate, S with two registers and an address, U with a big immediate/address)

## Slide 11: Instructions Types
We could define different fields for each instruction, but RISC-V seeks simplicity, so define six basic types of instruction formats:
  R-format for register-register arithmetic logical operations – Instructions using 3 register inputs
    add, xor, mul
  I-format for register-immediate arithmetic operations and loads
    addi, lw, jalr, slli
  S-format for stores - sw, sb
  B-format (also called SB - format) for branches - beq, bge
  U-format for 20-bit upper immediate instructions
    lui, auipc —upper immediate is 20-bits
  J-format (also called UJ) for jumps (minor variant of U-format)
    The jump instruction: jal
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 12: Summary of RISC-V Instruction Formats
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 13: R-Format Instructions

## Slide 14: R-Format Instructions (1/3)
Define “fields” of the following number of bits each: 7 + 5 + 5 + 3 + 5 + 7 = 32
Each field has a name:
Each field is viewed as its own unsigned int
  5-bit fields can represent any number 0-31, while 7-bit fields can represent any number 0-127, etc.
31
0
7
7
5
5
3
5
funct7
opcode
rs2
rs1
funct3
rd
31
0
Ref: CS61C, Univ of California, Berkeley

## Slide 15: R-Format Instructions (2/3)
opcode (7): partially specifies operation
  e.g. R-types have opcode = 0b0110011, SB (branch) types have opcode = 0b1100011
funct7+funct3 (10): combined with opcode, these two fields describe what operation to perform
How many R-format instructions can we encode?
  with opcode fixed at 0b0110011, just funct varies: (27) x (23)= (210) = 1024
Question: Why aren’t opcode and funct7 and funct3 a single 17-bit field?
funct7
opcode
rs2
rs1
funct3
rd
31
0
Ref: CS61C, Univ of California, Berkeley

## Slide 16: R-Format Instructions register specifier
  rs1 (Source Register #1): specifies register containing first operand
  rs2 : specifies second register operand
  rd (Destination Register): specifies register which will receive result of computation
  Each register field holds a 5-bit unsigned integer (0-31) corresponding to a register number (x0-x31)
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 17: R-Format Example
RISCV Instruction: add x5,x6,x7
  Field representation (hexadecimal):
  Field representation (binary):
two
0x0
0x33
0x7
0x6
0x0
0x5
31
0
0000000
0110011
00111
00110
000
00101
31
0
  hex representation: 0x 0073 02B3
  decimal representation: 7,537,331
  Called a Machine Language Instruction
Ref: CS61C, Univ of California, Berkeley
Notes: x5 = t0, x6 = t1, x7 = t2

## Slide 18: R-Format Example
Note the order of registers in the assembly code:
add rd, rs1, rs2
Ref: Harris and Harris Book: Digital Design and Computer Architecture: RISC-V Edition

## Slide 19: More R-type Examples
Note immediate shift instructions (like srai t1, t2, 29) are R-type instructions. They encode the shift amount in the rs2 field.
Ref: Harris and Harris Book: Digital Design and Computer Architecture: RISC-V Edition

## Slide 20: All RV32 R-format instructions
Different encoding in funct7 + funct3 selects different operations

## Slide 21: Class Summary
Instructions can be designed in multiple ways based on
  Legacy constraints
  Application type
  Simple and uniform instruction format
    All instructions have fields of certain type of fixed length
RISC-V instructions are
  Simple, Regular, complete and elegant
  Uniform
  Easy to understand
  Easy to implement
We have studied machine instruction (instruction format) for R-type instructions