## Slide 1: CS 211 Computer Architecture Lecture 21: RISC-V Machine Instructions - 2
Ravi Mittal
ravi.mittal@iitgoa.ac.in
Indian Institute of Technology, Goa

## Slide 2: Acknowledgements
Class Presentation, CS61C, Introduction to Assembly Language and RISC-V Instruction Set Architecture, University of Berkeley, Prof Krste Asanović & Randy H. Katz. http://inst.eecs.Berkeley.edu/~cs61c
Book: Digital Design and Computer Architecture: RISC-V Edition, Harris & Harris Elsevier – Presentation.
Computer Organization and Design, The Hardware Software Interface, RISC-V edition, Patterson and Hennessey

## Slide 3: RISC-V: So far we have studied
Arithmetic operations: add, sub, addi,
How to bring data from memory to register and vice versa?
  lw, sw, lb, sb, lbu
Bit-by-bit logical instructions
  and, or, xor
  andi, ori, xori
Logical Shift instructions
  sll, srl, sra, slli, srli, srai
Generating Constants
Branching Instructions: beq, bne, blt/bltu, bge/bgeu
Jumping instruction: j
Assembly level program for: if, if/else, while, for loops
Function Calls
  Basics
  Input arguments and Return Value
The Stack
  Basics
  How functions use a stack
  Stack use in non-leaf function calls
  Recursive Functions
Floating Point Numbers
Instruction Formats
R-Format Instructions

## Slide 4: In this class we will study
Instruction Formats
I-format
S-format
B-format
U-format

## Slide 5: RISC-V Instruction Formats Introduction (Revision)

## Slide 6: Instructions Format
One word is 32 bits, so divide instruction word into “fields”
Each field tells processor something about instruction
We could define different fields for each instruction, but RISC-V seeks simplicity, so define six basic types of instruction formats:
  R-format for register-register arithmetic operations
  I-format for register-immediate arithmetic operations and loads
  S-format for stores
  B-format for branches (minor variant of S-format, called SB before)
  U-format for 20-bit upper immediate instructions
  J-format for jumps (minor variant of U-format, called UJ before)
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 7: Summary of RISC-V Instruction Formats
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 8: I-Format

## Slide 9: I-Format Instructions
What about instructions with immediates?
  5-bit field only represents numbers up to the value 31 – too small= immediates must be larger than this
Ideally, RISC-V would have only one instruction format (for simplicity): unfortunately, we need to compromise
Define new instruction format that is mostly consistent with R-format
  Notice if instruction has immediate, then uses at most 2 registers (one source, one destination)
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 10: I-Format Instruction Layout
  Only one field is different from R-format, rs2 and funct7 replaced by 12-bit signed immediate, imm[11:0]
  Remaining fields (rs1, funct3, rd, opcode) same as before
  imm[11:0] can hold values in range [-2048ten , +2047ten ]
    12-bit two’s compliment immediate
  Immediate is always sign-extended to 32-bits before use in an arithmetic operation
  We’ll later see how to handle immediates > 12 bits
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 11: I-Format Example
RISC-V Assembly Instruction:
  addi x15,x1,-50
111111001110
00001
000
01111
0010011
OPCODE-Imm
rd=15
ADD
imm=-50
rs1=1
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley
  hex representation: 0x FCE0 8793

## Slide 12: All RV32 I-format Arithmetic Instructions
“Shift-by-immediate” instructions only use lower 5 bits of the immediate value for shift amount (can only shift by 0-31 bit positions)
One of the higher-order immediate bits is used to distinguish “shift right logical” (SRLI) from “shift right arithmetic” (SRAI)
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 13: Load Instructions are also I-Type
The 12-bit signed immediate is added to the base address in register rs1 to form the memory address
  This is very similar to the add-immediate operation but used to create address not to create final result
The value loaded from memory is stored in register rd
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 14: I-Format Load Example
RISC-V Assembly Instruction:
  lw x14, 8(x2)
000000001000
00010
010
01110
0000011
LOAD
rd=14
LW
imm=+8
rs1=2
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 15: I-Format More Example
Note the differing order of operands in assembly and machine codes:
addi rd, rs1, imm
lw rd, imm(rs1)
Ref: Harris and Harris Book: Digital Design and Computer Architecture: RISC-V Edition

## Slide 16: All RV32 Load Instructions
LBU is “load unsigned byte”
LH is “load halfword”, which loads 16 bits (2 bytes) and sign-extends to fill destination 32-bit register
LHU is “load unsigned halfword”, which zero-extends 16 bits to fill destination 32-bit register
There is no LWU in RV32, because there is no sign/zero extension needed when copying 32 bits from a memory location into a 32-bit register
funct3 field encodes size and signedness of load data
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 17: S-Format

## Slide 18: S-Format Used for Stores
  Store needs to read two registers, rs1 for base memory address, and rs2 for data to be stored, as well as need immediate offset
  Note that stores don’t write a value to the register file, unlike rd!
  RISC-V design decision is move low 5 bits of immediate to where rd field was in other instructions – keep rs1/rs2 fields in same place
    register names more critical than immediate bits in hardware design
  imm: 12-bit two’s complement immediate
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 19: S-Format Example
RISC-V Assembly Instruction:
  sw x14, 8(x2)
0000000
01110
00010
010
01000
0100011
STORE
offset[4:0]
=8
SW
offset[11:5]
=0
rs2=14
rs1=2
combined 12-bit offset = 8
0000000
01000
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 20: S-Format: More examples
Note the differing order of operands in assembly and machine codes:
sw rs2, imm(rs1)
Ref: Harris and Harris Book: Digital Design and Computer Architecture: RISC-V Edition

## Slide 21: All RV32 Store Instructions
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 22: Conditional Branches B-Format

## Slide 23: Branching Instructions
beq, bne, bge, blt
  Need to specify an address to go to
  Also take two registers to compare
How to encode label, i.e., where to branch to?
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 24: Branching Instruction Usage
Branches typically used for loops
  if-else, while, for
  Loops are generally small (< 50 instructions)
  Function calls and unconditional jumps handled with jump instructions (J-Format)
Recall: Instructions stored in a localized area of memory (Code/Text)
  Largest branch distance limited by size of code
  Address of current instruction stored in the program counter (PC)
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley
code
static data
heap
stack
∞
0

## Slide 25: RISC-V B-Format for Branches
B-format is mostly same as S-Format
3 operands
  rs1: register source 1
  rs2: register source 2
  imm12:1: 12-bit two’s complement immediate – address offset
But now immediate represents values -4096 to +4094 in 2-byte increments
The 12 immediate bits encode even 13-bit signed byte offsets (lowest bit of offset is always zero, so no need to store it)
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 26: RISC-V Conditional Branches
Example: BEQ x1, x2, Label
Branches read two registers but don’t write a register (similar to stores)
How to encode label, i.e., where to branch to?
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 27: PC-Relative Addressing
PC-Relative Addressing: Use the immediate field as a two’s complement word offset to PC
  Branches generally change the PC by a small amount
  Can specify ± 212 addresses from the PC
Why not use byte address offset from PC as the immediate?

## Slide 28: Branching Reach
Recall: RISCV uses 32-bit addresses, and memory is byte-addressed
Instructions are “word-aligned”: Address is always a multiple of 4 (in bytes)
  PC ALWAYS points to an instruction
Let immediate specify #words instead of #bytes
  Instead of specifying ± 211 bytes from the PC, we will now specify ± 211 words = ± 213 byte addresses around PC
As the last two bits of word address are always 0,
we don’t need to encode them.
However, we use total 13 bits instead of possible 14 bits.
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley
Notes: Locker room analogy

## Slide 29: Branch Calculation
If we don’t take the branch:
PC = PC+4 = next instruction
If we do take the branch:
PC = PC + (immediate*4)
Observations:
  immediate is number of instructions to move (remember, specifies words) either forward (+) or backwards (–)
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 30: RISC-V Feature, n×16-bit instructions
Extensions to RISC-V base ISA support 16-bit compressed instructions and also variable-length instructions that are multiples of 16-bits in length
16-bit = half-word
To enable this, RISC-V scales the branch offset to be half-words even when there are no 16-bit instructions
Reduces branch reach by half and means that ½ of possible targets will be errors on RISC-V processors that only support 32-bit instructions
RISC-V conditional branches can only reach ± 210 × 32-bit instructions either side of PC
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 31: Example Instruction Compression
Code taken from Tock embedded operating system

## Slide 32: RISC-V B-Format for Branches
B-format is mostly same as S-Format, with two register sources (rs1/rs2) and a 12-bit immediate
But now immediate represents values -212 to +212-2 in 2-byte increments
The 12 immediate bits encode even 13-bit signed byte offsets (lowest bit of offset is always zero, so no need to store it)
imm[12|10:5]
opcode
rs2
rs1
func3
imm[4:1|11]
31
0
7
7
5
5
3
5
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 33: Branch Example (1/2)
RISCV Code:
  Loop: beq x19,x10,End add x18,x18,x10 addi x19,x19,-1 j Loop End: <target instr>
Branch offset =
(Branch with offset of 0, branches to itself)
Start counting from instruction AFTER the branch
1
2
3
4
4×32-bit instructions = 16 bytes
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 34: Branch Example (1/2)
RISCV Code:
  Loop: beq x19,x10,End add x18,x18,x10 addi x19,x19,-1 j Loop End: <target instr>
Start counting from instruction AFTER the branch
1
2
3
4
???????
1100011
01010
10011
000
?????
31
0
7
7
5
5
3
5
BRANCH
rs2=10
rs1=19
BEQ
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 35: Branch Example (1/2)
  beq x19,x10,offset = 16 bytes
  13-bit immediate, imm[12:0], with value 16 0000000010000
0 000000
1100011
01010
10011
000
1000 0
31
0
imm[12|10:5]
imm[4:1|11]
imm[0] discarded, always zero
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 36: All RISC-V Branch Instructions
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 37: U-type

## Slide 38: U-Type for Upper Immediate Instruction
Upper Immediate Type
2 operands:
  rd: destination register
  imm31:12:upper 20 bits of a 32-bit immediate
Used for two instructions
  LUI – Load Upper Immediate
  AUIPC – Add Upper Immediate to PC
Ref: Harris and Harris Book: Digital Design and Computer Architecture: RISC-V Edition

## Slide 39: lui Example
Ref: Harris and Harris Book: Digital Design and Computer Architecture: RISC-V Edition

## Slide 40: lui to create long immediates (Revise)
LUI writes the upper 20 bits of the destination with the immediate value, and clears the lower 12 bits
Together with an ADDI to set low 12 bits, can create any 32-bit value in a register using two instructions (LUI/ADDI)
lui x10, 0x87654 # x10 = 0x87654000
addi x10, x10, 0x321 # x10 = 0x87654321
Ref: Harris and Harris Book: Digital Design and Computer Architecture: RISC-V Edition
Remember the corner case – discussed earlier

## Slide 41: AUIPC: Add Upper Immediate to pc
It is used to build pc-relative addresses using U-type format
Form a 32-bit offset
  Offset = 20-bit U-immediate + filling in the lowest 12 bits with zeros,
PC + Offset  Destination Register
Used for PC-relative addressing
Label: AUIPC x10, 0 # Puts address of label in x10
Ref: Harris and Harris Book: Digital Design and Computer Architecture: RISC-V Edition

## Slide 42: Summary of RISC-V instruction Formats

## Slide 43: Class Summary
In this class we have studied RISC-V instructions
  R-Format
  I-Format
  S-Format
  B-Format
  U-Format

## Slide 44: Backup Slides

## Slide 45: B-Type Example (1/2)
The 13-bit immediate encodes where to branch (relative to the branch instruction)
Immediate encoding is strange
Example:
Ref: Harris and Harris Book: Digital Design and Computer Architecture: RISC-V Edition

## Slide 46: B-Type Example (2/2)
Note the differing order of operands in assembly and machine codes:
beq rs1, rs2, imm12:1
Ref: Harris and Harris Book: Digital Design and Computer Architecture: RISC-V Edition

## Slide 47: PC-Relative Addressing
In the Branch Instruction, we have used PC-relative addressing
PC-Relative Addressing: Use the immediate field as a two’s-complement offset to PC
  Branches generally change the PC by a small amount
  Can specify ± 212 addresses from the PC in two byte increment
We will study Addressing methods in the next class
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley