## Slide 1: CS 211 Computer Architecture Lecture 22 : RISC-V Machine Instructions – Part 3 J-Type Instructions, Addressing Modes (for self study)
Ravi Mittal
ravi.mittal@iitgoa.ac.in
Indian Institute of Technology, Goa

## Slide 2: Acknowledgements
Class Presentation, CS61C, Introduction to Assembly Language and RISC-V Instruction Set Architecture, University of Berkeley, Prof Krste Asanović & Randy H. Katz. http://inst.eecs.Berkeley.edu/~cs61c
Book: Digital Design and Computer Architecture: RISC-V Edition, Harris & Harris Elsevier – Presentation.
Computer Organization and Design, The Hardware Software Interface, RISC-V edition, Patterson and Hennessey

## Slide 3: RISC-V: So far we have studied
Arithmetic operations: add, sub, addi,
How to bring data from memory to register and vice versa?
  lw, sw, lb, sb, lbu
Bit-by-bit logical instructions
  and, or, xor
  andi, ori, xori
Logical Shift instructions
  sll, srl, sra, slli, srli, srai
Generating Constants
Branching Instructions: beq, bne, blt/bltu, bge/bgeu
Jumping instruction: j
Assembly level program for: if, if/else, while, for loops
Function Calls
  Basics
  Input arguments and Return Value
The Stack
  Basics
  How functions use a stack
  Stack use in non-leaf function calls
  Recursive Functions
Instruction Formats
  R-Type
  I-Type
  S-Type
  B-Type

## Slide 4: In today’s class we will study
J-type Instruction
Addressing Modes

## Slide 5: J-type Instructions

## Slide 6: J-Format for Jump Instructions
Used for jump-and-link instruction (jal)
2 operands:
  rd: destination register
  imm20,10:1,11,19:12: 20 bits (20:1) of a 21-bit immediate

## Slide 7: jal Instructions
jal rd immediate
It does the following:
  saves return address: PC + 4  register rd
  PC relative jump: PC + sign extended (2*immediate)  PC
    Target somewhere in the range of -220 to 220 relative to PC
In words, the offset is sign-extended, multiplied by 2, and added to the value of the PC (address of jal instruction)
imm[20]
imm[10:1]
rd
imm[19:12]
imm[11]
opcode
1
10
1
8
5
7

## Slide 8: Uses of jal
Assembler “j” jump is pseudo-instruction, uses JAL but sets rd=x0 to discard return address
# j pseudo-instruction
j Label = jal x0, Label #Discard return address
# Call function within 218 instructions of PC
jal ra, FuncName
Assembler Shorthand:
  By convention, x1 is generally used as the “link register”. If the register is not mentioned, then x1 is implied.
  jal FuncName # Call FuncName

## Slide 9: jal example
#address RISC-V Assembly
0x0000540C jal ra, func1
0x00005410 add s1, s2, s3
…. …
…. …
0x0000541C func1: add s4, s5, s8
note that func1 is 1610 bytes away from jal (from 0..540C)
Offset = 0000 0000 0000 0001 0000
Immediate = 0 0000 0000 0000 0001 0100
Note that offset is of 21 bits (last bit i.e. least significant bit is always zero and hence it is not coded

## Slide 10: jal example
Assembly Machine code
jal ra, func1
note that func1 is 1610 bytes away from jal
Offset = 0000 0000 0000 0001 0000
Immediate = 0 0000 0000 0000 0001 0000
0
000 0001000
00001
00000000
0
1100111
1
10
1
8
5
7

## Slide 11: jalr
jalr is an I-type instruction.
It writes (return address) PC+4 to rd and jumps to rs1+imm (12 bit sign extended)
Example:
lui s7, 0x801FA # s7 = 0x801FA000
jalr s2, s7, 0x7BC # s2 = PC + 4
# PC = s7 + 0x7BC
# = 0x801FA7BC
In this case, rd = s2, rs1 = s7, imm = 0x7BC

## Slide 12: Summary of RISC-V instruction Formats

## Slide 13: Addressing Modes

## Slide 14: Addressing Modes
How do we address the operands?
An addressing mode defines how an instruction specifies its operands
RISC-V addressing modes
Register Only
Immediate
Base Addressing
PC-Relative
Ref: Harris and Harris Book: Digital Design and Computer Architecture: RISC-V Edition

## Slide 15: Addressing Modes
Register Only
Operands found in registers
  Example: add s0, t2, t3
  Example: sub t6, s1, s0
Immediate
12-bit signed immediate used as an operand
  Example: addi s4, t5, -73
  Example: ori t3, t7, 0xFF
Ref: Harris and Harris Book: Digital Design and Computer Architecture: RISC-V Edition

## Slide 16: Addressing Modes
Base Addressing
Loads and Stores
Address of operand is:
  base address + immediate
  Example: lw s4, 72(zero)
    address = 0 + 72
  Example: sw t2, -25(t1)
    address = t1 - 25
Ref: Harris and Harris Book: Digital Design and Computer Architecture: RISC-V Edition

## Slide 17: Addressing Modes
PC-Relative Addressing: branches and jal
The signed offset encoded in the immediate field is added to the PC to obtain the target address
  New PC value
Target address is relative to the current PC

## Slide 18: Addressing Modes
PC-Relative Addressing: branches and jal
Address Instruction
0x354 L1: addi s1, s1, 1
0x358 sub t0, t1, s7
... ...
0xEB0 bne s8, s9, L1
  The label is (0xEB0-0x354) = 0xB5C (2908) instructions before bne
Ref: Harris and Harris Book: Digital Design and Computer Architecture: RISC-V Edition

## Slide 19: Backup

## Slide 20: Constants/Immediates
lw and sw use constants or immediates
immediately available from instruction
12-bit two’s complement number
addi: add immediate
Subtract immediate (subi) necessary?
C Code
a = a + 4;
b = a – 12;
RISC-V assembly code
# s0 = a, s1 = b
addi s0, s0, 4
addi s1, s0, -12
Ref: Harris and Harris Book: Digital Design and Computer Architecture: RISC-V Edition

## Slide 21: Immediate Encoding
Immediate bits mostly occupy consistent instruction bits
Sign bit of signed immediate is in msb of instruction
Recall that rs2 of R-type can encode immediate shift amount
Instruction Bits
Ref: Harris and Harris Book: Digital Design and Computer Architecture: RISC-V Edition