## Slide 1: CS 211 Computer Architecture Lecture 23: RISC-V Instructions – Additional Pseudo Instructions, Integer Multiplication and Division Floating Point Instructions
Ravi Mittal
ravi.mittal@iitgoa.ac.in
Indian Institute of Technology, Goa

## Slide 2: Acknowledgements
Book: Digital Design and Computer Architecture: RISC-V Edition, Harris & Harris Elsevier – Presentation.
Class Presentation, CS61C, Introduction to Assembly Language and RISC-V Instruction Set Architecture, University of Berkeley, Prof Krste Asanović & Randy H. Katz. http://inst.eecs.Berkeley.edu/~cs61c
Computer Organization and Design, The Hardware Software Interface, RISC-V edition, Patterson and Hennessey

## Slide 3: Contents
Pseudo Instructions
Integer Multiplication and Division
Floating Point Instructions

## Slide 4: Pseudo Instructions
CS 305: Computer Architecture

## Slide 5: pseudoinstructions
Pseudoinstruction | Corresponding RISC-V Instructions | Description
j label | jal zero, label | Jump to label; do not write return address
jr ra | jalr zero, ra, 0 | Jump to address in ra
mv t5, s3 | addi t5, s3, 0 | t5 = s3
not s7, t2 | xori s7, t2, -1 | s7 = the bit-wise inversion of t2
nop | addi zero, zero, 0 | “no operation” – do nothing
li s8, 0x56789DEF | lui s8, 0x5678A addi s8, s8, 0xDEF | s8 = 32-bit immediate
li s8, 0x7EF | addi s8, zero, 0x7EF | s8 = 12-bit signed immediate
bgt s1, t3, L3 | blt t3, s1, L3 | if s1 > t3, branch to L3
bgez t2, L7 | bge t2, zero, L7 | if t2 ≥ zero, branch to L7
call L1 | jal L1 | call nearby function
call L5 | auipc ra, imm31:12 jalr ra, ra, imm11:0 | call far away function
ret | jalr zero, ra, 0 | return from function

## Slide 6: Pseudo Instructions
Valid in assembly language but not in machine language
(i.e., maps to multiple machine language instructions)
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley
Notes: auipc: add upper immediate to PC R[rd] = PC + {imm, 12’b0}
Lui: load upper immediate R[rd] = imm + 12’b0
Ori: inclusive OR immediate R[rd] = R[rs1] ^ imm

## Slide 7: Signed and Unsigned Instructions
Multiplication and division
Set less than
Loads
Ref: Harris and Harris Book: Digital Design and Computer Architecture: RISC-V Edition

## Slide 8: Integer Multiplication and Division

## Slide 9: Multiplication and Division
Signed: multh, div
Unsigned: multhu, multhsu, divu
Ref: Harris and Harris Book: Digital Design and Computer Architecture: RISC-V Edition

## Slide 10: Integer Multiplication
Paper and pencil example (unsigned):
  Multiplicand 1000 8
  Multiplier x 1001 9 72
m bits x n bits = m + n bit product
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 11: Integer Multiplication
Paper and pencil example (unsigned):
  Multiplicand 1000 8
  Multiplier x 1001 9 1000 0000 0000 + 1000 01001000 72
m bits x n bits = m + n bit product
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 12: Integer Multiplication
In RISC-V, we multiply registers, so:
  32-bit value x 32-bit value = 64-bit value
Syntax of Multiplication (signed):
  MUL performs an 32-bit×32-bit multiplication and places the lower 32 bits in the destination register
  MULH performs the same multiplication but returns the upper 32 bits of the full 2×32-bit product
  If 64-bit product is required, then the recommended code sequence is:
  MULH rdh, rs1, rs2 MUL rdl, rs1, rs2 (source register specifiers must be in same order and rdh cannot be the same as rs1 or rs2)
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 13: Integer Multiplication
Example:
  in C: a = b * c; # a should be declared long long
  in RISC-V:
    Let b be t2; let c be t3; and let a be t0 and t1 (since it may be up to 64 bits)
  mulh t0,t2,t3 # upper half of # product into t0 mul t1,t2,t3 # lower half of # product into t1
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 14: Integer Division
Paper and pencil example (unsigned):
  1001 Quotient Divisor 1000|1001010 Dividend -1000 10 101 1010 -1000 10 Remainder (or Modulo result)
Dividend = Quotient x Divisor + Remainder
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 15: Integer Division
Syntax of Division (signed):
  DIV performs signed integer division of 32 bits by 32 bits. REM provides the remainder of the corresponding division operation
  If the quotient and remainder are required from the same division, the recommended code sequence is: DIV rdq, rs1, rs2 REM rdr, rs1, rs2 (rdq cannot be the same as rs1 or rs2)
Implements C division (/) and modulo (%)
Example in C: a = c / d; b = c % d;
In RISC-V: a↔t0; b↔t1; c↔t2; d↔t3
  div t0,t2,t3 # a=c/d
  rem t1,t2,t3 # b=c%d
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 16: Addition and Subtraction
RISC-V does not provide unsigned addition or instructions for detecting overflow because it can be done with existing instructions:
Example: detecting unsigned overflow:
  add t0, t1, t2
  bltu t0, t1, overflow
Example: detecting signed overflow:
  add t0, t1, t2
  slti t3, t2, 0 # t3=1 if t2 neg.
  slt t4, t0, t1 # t4=1 if result < t1
  bne t3, t4, overflow # overflow if:
  # t2 neg & result>=t1 or
  # t2 pos & result<t1
Ref: Harris and Harris Book: Digital Design and Computer Architecture: RISC-V Edition

## Slide 17: Floating Point Operations

## Slide 18: Floating Point Operations
RISC-V offers three floating point extensions:
  RVF: single-precision (32-bit)
  RVD: double-precision (64-bit)
  RVQ: quad-precision (128-bit)
Ref: Harris and Harris Book: Digital Design and Computer Architecture: RISC-V Edition

## Slide 19: Floating Point Registers
32 Floating point registers
Width is highest precision – for example, if RVQ is implemented, registers are 128 bits wide
When multiple floating point extensions are implemented, the lower-precision values occupy the lower bits of the register
Ref: Harris and Harris Book: Digital Design and Computer Architecture: RISC-V Edition

## Slide 20: Floating Point Registers
Name | Register Number | Usage
ft0-7 | f0-7 | Temporary variables
fs0-1 | f8-9 | Saved variables
fa0-1 | f10-11 | Function arguments/Return values
fa2-7 | f12-17 | Function arguments
fs2-11 | f18-27 | Saved variables
ft8-11 | f28-31 | Temporary variables
Ref: Harris and Harris Book: Digital Design and Computer Architecture: RISC-V Edition

## Slide 21: Floating Point Instructions
Append .s (single), .d (double), .q (quad) for precision
    add.s, add.d, and add.q
Arithmetic operations:
  fadd, fsub, fdiv, fsqrt, fmin, fmax,
  multiply-add : fmadd, fmsub, fnmadd, fnmsub
Load and Store
  flw, fld
  fsw, fsd
Branch on FP condition code true or false
  B.cond
Other instructions:
move (fmv.x.w, fmv.w.x)
convert (fcvt.w.s, fcvt.s.w, etc.)
comparison (feq, flt, fle)
classify (fclass)
sign injection (fsgnj, fsgnjn, fsgnjx)
Ref: Harris and Harris Book: Digital Design and Computer Architecture: RISC-V Edition

## Slide 22: Floating Point Instruction Formats
Use R-, I-, and S-type formats
Introduce another format for multiply-add instructions that have 4 register operands: R4-type
Ref: Harris and Harris Book: Digital Design and Computer Architecture: RISC-V Edition

## Slide 23: FP Example: °F to °C
C code:
float f2c (float fahr) { return ((5.0/9.0)*(fahr - 32.0)); }
  fahr in f10, result in f10, literals in global memory space
Compiled RISC-V code
f2c:
flw f0,const5(x3) // f0 = 5.0f
flw f1,const9(x3) // f1 = 9.0f
fdiv.s f0, f0, f1 // f0 = 5.0f / 9.0f
flw f1,const32(x3) // f1 = 32.0f
fsub.s f10,f10,f1 // f10 = fahr – 32.0
fmul.s f10,f0,f10 // f10 = (5.0f/9.0f)*(fahr–32.0f)
jalr x0,0(x1) // return

## Slide 24: Who Cares About FP Accuracy?
Important for scientific code
  But for everyday consumer use?
    “My bank balance is out by 0.0002¢!” 
The Intel Pentium FDIV bug
  The market expects accuracy
  See Colwell, The Pentium Chronicles

## Slide 25: Concluding Remarks
ISAs support arithmetic
  Signed and unsigned integers
  Floating-point approximation to reals
Bounded range and precision
  Operations can overflow and underflow