## Slide 1: CS 211 Computer Architecture Lecture 24 : Microarchitecture - Datapath Design – 1 Processor Components Sequential Logic Circuit, Registers, Clock
Ravi Mittal
ravi.mittal@iitgoa.ac.in
Indian Institute of Technology, Goa

## Slide 2: In this lecture we will study
Microarchitecture – Top level view
Logic Circuits
  Basics
  Circuits that can store information
  RS Latch
  Gated D latch
  The Clock
  FSM

## Slide 3: Overview
lw $t0, 0($2)
lw $t1, 4($2)
sw $t1, 0($2)
sw $t0, 4($2)
Higher-Level Language Program (e.g. C)
Assembly Language Program (e.g. RISC-V)
Machine Language Program (RISC-V)
Hardware Architecture Description (e.g. block diagrams)
Compiler
Assembler
Machine Interpretation
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
0000 1001 1100 0110 1010 1111 0101 1000
1010 1111 0101 1000 0000 1001 1100 0110
1100 0110 1010 1111 0101 1000 0000 1001
0101 1000 0000 1001 1100 0110 1010 1111
Logic Circuit Description (Circuit Schematic Diagrams)
Architecture Implementation
We are here
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 4: Why is this important to study Hardware Design?
Computer scientists should have an answer to the question “How does a computer work?”
So you can understand how code is actually executed on a computer
Why do we care about how code executes?
  Reliability
  Performance
  Security
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 5: Hardware Design
Example of the power of layered abstractions
  Transistors -> Combinational Logic
  Combinational Logic -> Sequential Logic
  Sequential Logic -> Processors
  Processors -> Machine Language
  Machine Language -> Assembly
  Assembly -> High-level Programming Languages
  High-level Programming Languages -> Word, Facebook, Twitter
At each step we can “abstract away” the lower steps and (mostly) forget they exist

## Slide 6: Hardware Design
  Transistors
  Combinational Logic
  Sequential Logic
  Processors
  Machine Language
  Assembly
  High-level Programming Languages
Covered in Digital Logic Course
We will briefly discuss these today
Next 12 lectures
Covered in lectures so far

## Slide 7: Microarchitecture
Defines the specific arrangement of
  Registers
  ALU
  FSM
  Memories
  Other logic building blocks
RISC-V architectures - can be designed in many ways – based on requirements of
  Performance
  Cost
  Complexity
Let’s go bottom up when discussing Microarchitecture
  Logic Circuits, Components, Datapath, Control logic

## Slide 8: Logic Circuits Basics

## Slide 9: Synchronous Digital Systems (SDS)
Synchronous:
  All operations coordinated by a central clock
    “Heartbeat” of the system! (processor frequency)
Hardware of a processor, such as a RISC-V processor, is an example of a Synchronous Digital System

## Slide 10: Types of Logic Circuits
Synchronous Digital Systems consist of two basic types of circuits:
  Combinational Logic (CL) circuits
    Output is a function of the inputs only, not the history of its execution
    E.g., circuits to add A, B (ALUs)
  Sequential Logic (SL)
    Circuits that “remember” or store information
    State Elements
    E.g., memories and registers (Registers)

## Slide 11: Circuits that can store Information

## Slide 12: Sequential Circuits: Introduction
Combinational circuit output depends only on current input
We want circuits that produce output depending on current and past input values – circuits with memory
Sequential Circuit gives sequence to events; Use feedback
Sequential Circuit
Combinational
Circuit
inputs
outputs
Storage
Element
From Prof Onur Mutlu’s presentation

## Slide 13: State Elements
State of the system
  Sequential logic might explicitly remember certain previous inputs, or it might distil the prior inputs into a smaller amount of information called the state of the system
  The state of a digital sequential circuit is a set of bits called state variables that contain all the information about the past necessary to explain the future behaviour of the circuit
  The state of a circuit influences its future behavior
State elements store state
  Bistable circuit
  RS Latch
  D Latch
  D Flip-flop
State Elements used in a
Processor:
Registers, PC, Memory

## Slide 14: Uses of State Elements
Place to store values for later use:
  Register files (like x0-x31 on the RISC-V)
  Memory (caches and main memory)
Help control flow of information between combinational logic blocks
  State elements hold up the movement of information at input to combinational logic blocks to allow for orderly passage

## Slide 15: Basic Storage Element The RS Latch

## Slide 16: The RS (Reset-Set) Latch
The simplest implementation of the R-S Latch
  Two NAND gates with outputs feeding into each other’s input
  Data is stored at Q (inverse at Q’)
  S and R inputs are held at 1 then Q =Qprev Memory!
  S (set): drive S to 0 (keeping R at 1) to change Q to 1
  R (reset): drive R to 0 (keeping S at 1) to change Q to 0
S and R should never both be 0 at the same time
S
R
Q’
Q
Input |  | Output
R | S | Q
1 | 1 | Qprev
1 | 0 | 1
0 | 1 | 0
0 | 0 | Invalid
From Prof Onur Mutlu’s presentation

## Slide 17: Why not R=S=0?
1
0
If R=S=0, Q and Q’ will both settle to 1, which breaks our invariant that Q = !Q’
If S and R transition back to 1 at the same time, Q and Q’ begin to oscillate between 1 and 0 because their final values depend on each other (metastability)
S
R
Q’
Q
Input |  | Output
R | S | Q
1 | 1 | Qprev
1 | 0 | 1
0 | 1 | 0
0 | 0 | Invalid
1
0
0
0
1
1
From Prof Onur Mutlu’s presentation

## Slide 18: The Gated D Latch

## Slide 19: The Gated D Latch
How do we guarantee correct operation of an RS Latch?
S
R
Q’
Q
From Prof Onur Mutlu’s presentation

## Slide 20: The Gated D Latch
How do we guarantee correct operation of an R-S Latch?
  Add two more NAND gates!
  Q takes the value of D, when write enable (WE) is set to 1
  S and R can never be 0 at the same time!
S
R
Q’
Q
Write
Enable
D
From Prof Onur Mutlu’s presentation

## Slide 21: The Gated D Latch
S
R
Q’
Q
Write
Enable
D
Input |  | Output
WE | D | Q
0 | 0 | Qprev
0 | 1 | Qprev
1 | 0 | 0
1 | 1 | 1
Note that the circuit is un-clocked
From Prof Onur Mutlu’s presentation

## Slide 22: The Clock

## Slide 23: The Clock
A microprocessor is composed of many different circuits that are operating simultaneously – if each circuit X takes in inputs at time TIX, takes time TEX to execute the logic, and produces outputs at time TOX, imagine the complications in co-ordinating the tasks of every circuit
All circuits on the chip share a clock signal (a square wave) that tells every circuit when to accept inputs, how much time they have to execute the logic, and when they must produce outputs

## Slide 24
Clock Terminology
Cycle time
Rising clock edge
Falling clock edge
4 GHz = clock speed = 1 = 1 .
cycle time 250 ps

## Slide 25: The Clock
Clock frequency fs | Period tcycle = 1/fs
CPU 2.5 GHz | 400 ps
Drum/heartbeat, 1Hz | 1 s
fs = 1/ tcycle
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley
Notes: Faster processors enabled
digital audio ~ 1980
digital video 199x
… now enables entirely new functions (e.g. search engines) that did not even exist with analog processing.
But: many physical signals are inherently analog. E.g. my voice: I cannot speak ”digital”, and you could not understand me anyway.
{signal: [ {name: 'clk', wave: 'P....'}, {name: 'instr', wave: '34534', data: 'instr_1 instr_2 instr_3 instr_4 instr_5'}, {node: 'abcdef'}], edge: ['a<->b t<sub>cycle', 'c<->b t<sub>cycle', 'c<->d t<sub>cycle', 'd<->e t<sub>cycle', 'e<->f t<sub>cycle', ], config: { hscale: 3 }}

## Slide 26: Changing State: The Notion of Clock (I)
We need a clock to dictate when to change state
  Clock signal alternates between 0 & 1
At the start of a clock cycle ( ), system state changes
  During a clock cycle, the state stays constant
Edge-triggered clocking: all state changes occur on a clock edge
In an edge-triggered methodology, either the rising edge or the falling edge of the clock is active and causes state changes to occur
CLK:
0
1
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 27: Changing State: The Notion of Clock (II)
Clock is a general mechanism that triggers transition from one state to another in a sequential circuit
Clock synchronizes state changes across many sequential circuit elements
Combinational logic evaluates for the length of the clock cycle
Clock cycle should be chosen to accommodate maximum combinational circuit delay
The clock edge acts as a sampling signal, causing the value of the data input to a state element to be sampled and stored in the state element
  The sampling process is essentially instantaneous
  eliminates problems that could occur if signals were sampled at slightly different times

## Slide 28: Relationship between state elements and combinational logic
The signals that are written into state elements must be valid when the active clock edge occurs
State element’s output changes after clock’s active edge
  Provides valid inputs to combinational logic block
Clock must have a long enough period so that all the signals in the combinational logic block stabilize
The clock edge samples those values for storage in the state elements
In this course (CS211), we consider rising edge triggered state changes
Notes: The write signal must still be gated with the clock so that the update occurs only on the clock edge if the write signal is active.

## Slide 29: Finite State Machines

## Slide 30: Finite State Machines
What is a Finite State Machine (FSM)?
  A discrete-time model of a stateful system
  Each state represents a snapshot of the system at a given time
An FSM pictorially shows
  1. the set of all possible states that a system can be in
  2. how the system transitions from one state to another
An FSM can model
  A traffic light, an elevator, fan speed, a microprocessor, etc.
An FSM enables us to pictorially think of a stateful system using simple diagrams

## Slide 31: Finite State Machines (FSMs)
FSM consists of Five elements:
  A finite number of states
    State: snapshot of all relevant elements of the system at the time of the snapshot
  A finite number of external inputs
  A finite number of external outputs
  An explicit specification of all state transitions
    How to get from one state to another
  An explicit specification of what determines each external output value
From Prof Onur Mutlu’s presentation

## Slide 32: Finite State Machines (FSMs)
Each FSM consists of three separate parts:
  next state logic
  state register
  output logic
state register
At the beginning of the clock cycle, next state is latched into the state register
From Prof Onur Mutlu’s presentation

## Slide 33: Finite State Machines (FSMs) Consist of:
Sequential circuits
  State register(s)
    Store the current state and
    Load the next state at the clock edge
Combinational Circuits
  Next state logic
    Determines what the next state will be
Output logic
    Generates the outputs
From Prof Onur Mutlu’s presentation
Notes: discuss DFlipFlop here. Latch doesn't do this, so we need sequential circuit that stores state and loads next state at the clock edge. next state is available for the full clock cycle
now lets take a look at this.

## Slide 34: State Register Implementation with D type Flipflop

## Slide 35: State Register Implementation
How can we implement a state register? Two properties:
  1. We need to store data at the beginning of every clock cycle
  2. The data must be available during the entire clock cycle
CLK:
0
1
Register
Input:
Register
Output:
Desired behavior
Notes: Introduce clock much earlier maybe.
input data is sampled once.

## Slide 36: The Problem with Latches
Currently, we cannot simply wire a clock to WE of a latch
  Whenever the clock is high, the latch propagates D to Q
  The latch is transparent
D
Q
CLK = WE
CLK:
0
1
Register
Input:
Register
Output:
Recall the
Gated D Latch
From Prof Onur Mutlu’s presentation

## Slide 37: The Problem with Latches
Currently, we cannot simply wire a clock to WE of a latch
  Whenever the clock is high, the latch propagates D to Q
  The latch is transparent
D
Q
CLK = WE
CLK:
0
1
Register
Input:
Register
Output:
Recall the
Gated D Latch
Undesirable!
From Prof Onur Mutlu’s presentation

## Slide 38: The Problem with Latches
Currently, we cannot simply wire a clock to WE of a latch
  When the clock is high Q will not take on D’s value AND
  When the clock is low the latch will propagate D to Q
D
Q
CLK = WE
CLK:
0
1
Input:
Output:
Recall the
Gated D Latch
How can we change the latch, so that
1) D (input) is observable at Q (output)
only at the beginning of next clock cycle?
2) Q is available for the full clock cycle

## Slide 39: The Need for a New Storage Element
To design viable FSMs
We need storage elements that allow us
  to read the current state throughout the current clock cycle
  AND
  not write the next state values into the storage elements until the beginning of the next clock cycle.
From Prof Onur Mutlu’s presentation

## Slide 40: The D Flip-Flop
1) state change on clock edge, 2) data available for full cycle
D Latch (Slave)
D Latch (Master)
D
Q
CLK
When the clock is low, master propagates D to the input of slave (Q unchanged)
Only when the clock is high, slave latches D (Q stores D)
  At the rising edge of clock (clock going from 0->1), Q gets assigned D
CLK:
0
1

## Slide 41: The D Flip-Flop
1) state change on clock edge, 2) data available for full cycle
At the rising edge of clock (clock going from 0->1), Q gets assigned D
At all other times, Q is unchanged
CLK:
0
1
CLK
D
Q
Q
__
D Flip-Flop
From Prof Onur Mutlu’s presentation

## Slide 42: The D Flip-Flop
How do we implement this?
At the rising edge of clock (clock going from 0->1), Q gets assigned D
At all other times, Q is unchanged
CLK:
0
1
CLK
D
Q
Q
__
D Flip-Flop
We can use these Flip-Flops
to implement the state register!

## Slide 43: Rising-Clock-Edge Triggered Flip-Flop
Two inputs: CLK, D
Function
  The flip-flop “samples” D on the rising edge of CLK (positive edge)
  When CLK rises from 0 to 1, D passes through to Q
  Otherwise, Q holds its previous value
  Q changes only on the rising edge of CLK
A flip-flop is called an edge-triggered state element because it captures data on the clock edge
  Note that a latch is a level-triggered state element
CLK
From Prof Onur Mutlu’s presentation
RS latch operates on input levels
D FF operates on (clock) edges

## Slide 44: (Positive) Edge Triggered Flip-Flop
D
Q
CLK
Time
Clock “CLK”
Notes: {signal: [ {name: 'clk', wave: '0H..l..H...', node: '.a.....b'}, {name: 'D', wave: '1....0.....'}, {name: 'Q', wave: '0..1.....0.', node: '...c.....d'},], edge: [ 'a~->c', 'b~->d',]}

## Slide 45: Register
Multiple parallel flip-flops, each of which storing 1 bit
This register stores 4 bits
This line represents 4 wires
Condensed
From Prof Onur Mutlu’s presentation

## Slide 46: A 4-Bit D-Flip-Flop-Based Register (Internally)
Image source: Patt and Patel, “Introduction to Computing Systems”, 3rd ed., tentative page 95.

## Slide 47: Class Summary
Processor design requires design of FSM
FSM consists of Sequential logic Circuits that can store state of the system
We have looked at functioning of
  RS latch
  Gated D latch
    Problems of unstable output with Gated D latch
  Use of clock – Edge triggering concept
  The D Flipflop
    They are the basic component of register file