## Slide 1: CS 211 Computer Architecture Lecture 25: Microarchitecture Design - Datapath – Part 1 Processor components – PC, FSM, Muxes, Adder, Subtractor
Ravi Mittal
ravi.mittal@iitgoa.ac.in
Indian Institute of Technology, Goa

## Slide 2: Acknowledgements
Book: Harris and Harris, Digital Design and Computer Architecture – RISC-V
Class Presentation, CS61C, Introduction to Assembly Language and RISC-V Instruction Set Architecture, University of Berkeley, Prof Krste Asanović & Randy H. Katz. http://inst.eecs.Berkeley.edu/~cs61c
Lecture slides of Prof Onur Mutlu, ETH Zurich, Spring 2018,
Book: Pratt and Patel, Introduction to Computing Systems: From Bits & Gates to C/C++ & Beyond

## Slide 3: RISC-V: So far we have studied
Arithmetic operations: add, sub, addi,
How to bring data from memory to register and vice versa?
  lw, sw, lb, sb, lbu
Bit-by-bit logical instructions
  and, or, xor
  andi, ori, xori
Logical Shift instructions
  sll, srl, sra, slli, srli, srai
Generating Constants
Branching Instructions: beq, bne, blt/bltu, bge/bgeu
Jumping instruction: j
Assembly level program for: if, if/else, while, for loops
Function Calls
  Basics
  Input arguments and Return Value
The Stack
  Basics
  How functions use a stack
  Stack use in non-leaf function calls
  Recursive Functions
Floating Point Numbers
Instruction Formats
Machine Instructions
Microarchitecture
  Combinational and Sequential logic
  Clock
  Registers

## Slide 4: Computer Architecture
lw t0, 0(x2)
lw t1, 4(x2)
sw t1, 0(x2)
sw t0, 4(x2)
Higher-Level Language Program (e.g. C)
Assembly Language Program (e.g. RISCV)
Machine Language Program (RISCV)
Hardware Architecture Description (e.g. block diagrams)
Compiler
Assembler
Machine Interpretation
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
0000 1001 1100 0110 1010 1111 0101 1000
1010 1111 0101 1000 0000 1001 1100 0110
1100 0110 1010 1111 0101 1000 0000 1001
0101 1000 0000 1001 1100 0110 1010 1111
Logic Circuit Description (Circuit Schematic Diagrams)
Architecture Implementation
We are here
Notes: Great Ideas:
Levels of Representation & Interpretation
Technology Trends
Principle of Locality & the Memory Hierarchy
Parallelism
Performance Measurement & Improvement
Dependability via Redundancy

## Slide 5: Microarchitecture Components
Microarchitecture has two interacting components
  The datapath
  The control unit
Datapath operate on words of data
Datapath contains structures such as
  Registers
  Memories
  ALU, Adder, Subtractor, Comparator
  Multiplexer
  Buses
Control unit
  Receives instruction from datapath
  It tells datapath how to execute the instructions
  It produces control signals for muxes, ALU, registers, Memories

## Slide 6: In this class we will study
Muxes, Adder, Subtractor, Comparator
ALU
Sequential logic Circuits – Signal and Waveforms
Registers

## Slide 7: Muxes, Adder, Subtractor, Comparator

## Slide 8: Conceptual RISC-V Datapath
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 9: Data Multiplexer(e.g., 2-to-1 x n-bit-wide)
“mux”
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley
Hardware is hard – permanent – It does what you want it to do
Use Muxes to pick from among inputs
  S input selects on one of 2S inputs
Represents that this wire has n bits
Notes: Go to Logisim and do design from mux

## Slide 10: N Instances of 1-bit-Wide Mux
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 11: 1-bit 4-to-1 Multiplexer
How many rows in Truth Table?
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 12: 1-Bit Adder (self study)
1-Bit Adders

## Slide 13: Multibit Adder
Types of carry-propagate adders (CPAs):
  Ripple-carry (slow)
  Carry-lookahead (fast)
  Prefix (faster)
Carry-lookahead and prefix adders are fast for large adders but require more hardware
Symbol
Ref: Harris and Harris Book: Digital Design and Computer Architecture: RISC-V Edition

## Slide 14: Subtractor
Cin = 1
Ref: Harris and Harris Book: Digital Design and Computer Architecture: RISC-V Edition
Notes: To compute Y = A − B, first create the two’s complement of B: Invert the bits of B to obtain B and add 1 to get −B=B+1. Add this quantity to A to get Y=A+B+1=A−B. This sum can be performed with a single CPA by adding A + B with Cin = 1

## Slide 15: Comparator
A comparator determines whether two binary numbers are equal or if one is greater or less than the other.
Two types
  Equality Comparator
  Magnitude comparator (less than)
Ref: Harris and Harris Book: Digital Design and Computer Architecture: RISC-V Edition

## Slide 16
Comparator: Equality
Ref: Harris and Harris Book: Digital Design and Computer Architecture: RISC-V Edition

## Slide 17: Arithmetic and Logic Unit (ALU)

## Slide 18: Conceptual RISC-V Datapath - ALU
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 19: ALU: Arithmetic Logic Unit
Most processors contain a special logic block called “Arithmetic and Logic Unit” (ALU)
Let’s consider a very simple ALU
ALU should perform:
  Addition
  Subtraction
  AND
  OR
Ref: Harris and Harris Book: Digital Design and Computer Architecture: RISC-V Edition

## Slide 20: ALU: Arithmetic Logic Unit
ALUControl1:0 | Function
00 | Add
01 | Subtract
10 | AND
11 | OR
Example: Perform A + B
ALUControl = 00
Result = A + B
Ref: Harris and Harris Book: Digital Design and Computer Architecture: RISC-V Edition

## Slide 21: ALU: Arithmetic Logic Unit
ALU: Arithmetic Logic Unit
ALUControl1:0 | Function
00 | Add
01 | Subtract
10 | AND
11 | OR
Example: Perform A OR B
Ref: Harris and Harris Book: Digital Design and Computer Architecture: RISC-V Edition

## Slide 22: ALU: Arithmetic Logic Unit
ALU: Arithmetic Logic Unit
ALUControl1:0 | Function
00 | Add
01 | Subtract
10 | AND
11 | OR
Example: Perform A OR B
ALUControl1:0 = 11
Mux selects output of OR gate as Result, so
Result = A OR B
Ref: Harris and Harris Book: Digital Design and Computer Architecture: RISC-V Edition

## Slide 23: ALU: Arithmetic Logic Unit
ALU: Arithmetic Logic Unit
ALUControl1:0 | Function
00 | Add
01 | Subtract
10 | AND
11 | OR
Example: Perform A + B
ALUControl1:0 = 00
ALUControl0 = 0, so:
Cin to adder = 0
2nd input to adder is B
Mux selects Sum as Result, so
Result = A + B

## Slide 24: ALU with Status Flag
Flag | Description
N | Result is Negative
Z | Result is Zero
C | Adder produces Carry out
V | Adder oVerflowed
ALU with Status Flags
Some ALUs are designed with extra outputs called flags
Ref: Harris and Harris Book: Digital Design and Computer Architecture: RISC-V Edition

## Slide 25: Sequential Logic Components - Basics

## Slide 26: Type of Circuits
Digital Systems consist of two basic types of circuits:
  Combinational Logic (CL)
    Output is a function of the inputs only, not the history of its execution
    e.g. circuits to add A, B (ALUs)
  Sequential Logic (SL)
    Circuits that “remember” or store information
    a.k.a. “State Elements”
    e.g. memory and registers (Registers)

## Slide 27: Accumulator Example
Want: S=0;
for X1,X2,X3 over time...
S = S + Xi
An example of why we would need sequential logic
Assume:
  Each X value is applied in succession, one per cycle
  The sum since time 1 (cycle) is present on S
SUM
Xi
S
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 28: First Try: Does this work?
No!
How to control the next iteration of the ‘for’ loop?
How do we say: S = 0?
Feedback
X
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 29: Second Try: How About This?
A Register is the state element that is used here to hold up the transfer of data to the adder
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 30: Uses for State Elements
Place to store values for some amount of time:
  Register files (like in RISC-V)
  Memory (caches and main memory)
Help control flow of information between combinational logic blocks
  State elements are used to hold up the movement of information at the inputs to combinational logic blocks and allow for orderly passage
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 31: Signals and Waveforms: Clocks
Signals transmitted over wires continuously
Transmission is effectively instantaneous
  Implies that any wire only contains one value at any given time
Rising Edge
Falling Edge
Clock period (CPU cycle time)
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 32: Signals and Waveforms
  All signals change after clock “triggers”
Stack signals on top of each other
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 33: Signals and Waveforms: Grouping
A group of wires when interpreted as a bit field is called a bus
X
Time
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 34: Dealing with Waveform Diagrams
When does a signal update?
  A state element updates based on CLK triggers
  A combinational element updates ANY time ANY of its inputs changes

## Slide 35: Second Try: How About This?
Rough timing …
Time
Delay through Adder
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 36: Registers - Basics

## Slide 37: Registers
Small memory storage locations
Clock input (inputs active only on a clock “tick”)
Data input (can be various bit widths)
Data output (can be various bit widths)
Reset (sets value to zero)
Write Enable (can it be written to)
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 38: Register Internals (revision)
n number of Flip-Flops
  Output flips and flops between 0 and 1
Specifically this is a “D-type Flip-Flop”
  D is “data input”, Q is “data output”
  In reality, has 2 outputs (Q and Q), but we only care about 1
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley
Notes: Can see Wikipedia page for gate internals and other types of flip-flops.

## Slide 39: Lecture Summary
Datapath consists of many combinational logic components including Multiplexers, Adders, Subtractors, Comparators etc
We have studied sequential logic component basics