## Slide 1: CS 211 Computer Architecture Lecture 26: Microarchitecture Design - Datapath – Part 2
Ravi Mittal
ravi.mittal@iitgoa.ac.in
Indian Institute of Technology, Goa

## Slide 2: Acknowledgements
Book: Harris and Harris, Digital Design and Computer Architecture – RISC-V
Class Presentation, CS61C, Introduction to Assembly Language and RISC-V Instruction Set Architecture, University of Berkeley, Prof Krste Asanović & Randy H. Katz. http://inst.eecs.Berkeley.edu/~cs61c
Lecture slides of Prof Onur Mutlu, ETH Zurich, Spring 2018,
Book: Pratt and Patel, Introduction to Computing Systems: From Bits & Gates to C/C++ & Beyond

## Slide 3: Computer Architecture
lw t0, 0(x2)
lw t1, 4(x2)
sw t1, 0(x2)
sw t0, 4(x2)
Higher-Level Language Program (e.g. C)
Assembly Language Program (e.g. RISCV)
Machine Language Program (RISCV)
Hardware Architecture Description (e.g. block diagrams)
Compiler
Assembler
Machine Interpretation
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
0000 1001 1100 0110 1010 1111 0101 1000
1010 1111 0101 1000 0000 1001 1100 0110
1100 0110 1010 1111 0101 1000 0000 1001
0101 1000 0000 1001 1100 0110 1010 1111
Logic Circuit Description (Circuit Schematic Diagrams)
Architecture Implementation
We are here
Notes: Great Ideas:
Levels of Representation & Interpretation
Technology Trends
Principle of Locality & the Memory Hierarchy
Parallelism
Performance Measurement & Improvement
Dependability via Redundancy

## Slide 4: In the class we will study
Flip-Flop Timing behavior
Program Counter – Max Frequency
Register File
Storage Elements for RISC-V machine
Single Cycle, Multicycle, Pipeline Machines

## Slide 5: Datapath Components
Microarchitecture has two interacting components
  The datapath
  The control unit
Datapath operate on words of data
Datapath contains structures such as
  Registers
  Memories
  ALU
  Multiplexer
  Buses
Control unit
  Receives instruction from datapath
  It tells datapath how to execute the instructions
  It produces control signals for muxes, ALU, registers, Memories

## Slide 6: Flip-Flop Timing Behavior

## Slide 7: Flip-Flop Timing Terminology (1/2)
Edge-triggered D-type flip-flop
  This one is “rising edge-triggered”
On the rising edge of the clock, input d is sampled and transferred to the output. At other times, the input d is ignored and the previously sampled value is retained
Example waveforms:

## Slide 8: Flip-Flop Timing Terminology (2/3)
Camera Analogy: Taking a photo
  Setup time: don’t move since about to take picture (open camera shutter)
  Hold time: need to hold still after shutter opens until camera shutter closes
  Time to data: time from open shutter until image appears on the output (viewfinder)

## Slide 9: Flip-Flop Timing Terminology (3/3)
Now applied to hardware:
  Setup Time: how long the input must be stable before the clock trigger for proper input read
  Hold Time: how long the input must be stable after the clock trigger for proper input read
  “Clock-to-Q” Delay: how long it takes the output to change, measured from the clock trigger

## Slide 10: Flip-Flop Timing Behavior

## Slide 11: Flip-Flop Timing Behavior
Setup Time

## Slide 12: Flip-Flop Timing Behavior
Hold Time

## Slide 13: Flip-Flop Timing Behavior
Clock-to-Q

## Slide 14: Accumulator Revisited Proper Timing
reset signal shown
In practice Xi might not arrive to the adder at the same time as Si-1
Si temporarily is wrong, but register always captures correct value
In good circuits, instability never happens around rising edge of CLK
“Undefined” (unknown) signal

## Slide 15: Review of Timing Terms
Clock: steady square wave that synchronizes system
Flip-flop: one bit of state that samples every rising edge of Clock (positive edge-triggered)
Register: several bits of state that samples on rising edge of Clock (positive edge-triggered); also has RESET
Setup Time: when input must be stable before Clock trigger
Hold Time: when input must be stable after Clock trigger
Clock-to-Q Delay: how long it takes output to change from Clock trigger
Notes: STOP HERE

## Slide 16: Flip-Flop Timing
Notes: {signal: [ {name: 'clk', wave: '0.H..', node: '..a'}, { node: '.bc'}, { node: '..de'}, {name: 'D', wave: 'x4.x.', node: '.k.l', data: 'Data'}, { node: '..f.g'}, {name: 'Q', wave: 'x...4', node: '....h', data:'Data'},], edge: [ 'b<->c t<sub>setup', 'k-b', 'a-f', 'd<->e t<sub>hold', 'e-l', 'f<->g t<sub>clk-to-Q', 'g-h' ], config: { hscale: 1.5 }}

## Slide 17: Flip-Flop Timing
Time | Description
tsetup | time during which D must not change before positive clock edge
thold | time during which D must not change after positive clock edge
tclk-to-Q | delay after positive clock edge after which D appears at Q output

## Slide 18: Model for Synchronous Systems
Combinational logic blocks separated by registers
  Clock signal connects only to sequential logic elements
  Feedback is optional depending on application
How do we ensure proper behavior?
  How fast can we run our clock?

## Slide 19: Maximum Clock Frequency
Combinatorial
Logic
(CL)
Register
(flip-flops)
Optional Feedback
Output
Input
Clock
CL
tCL

## Slide 20: Maximum Clock Frequency
What is the maximum frequency of the circuit?
  Limited by how much time is needed to get correct next state to the register
Max Delay =
Min Period = Max Delay
Max Freq = 1/Min Period
CLK-to-Q Delay
+ CL Delay
+ Setup Time
Notes: Hold time is included in CLK-to-Q delay.
Make sure to shift thinking for setup time for next clock trigger (one clock cycle).

## Slide 21: Program Counter – Max Frequency

## Slide 22: Program Counter (PC)
Next PC
Current PC

## Slide 23: Maximum PC Clock Speed
Minimum cycle time:
Maximum clock rate:
Example: tsetup ≥ 15ps, tadd = 75ps, tclk-toQ ≥ 10ps
tmin ≥ 100ps
fclk-max ≤ 10GHz

## Slide 24: The Critical Path
+
Reg
Reg
The critical path is the longest delay between any two registers in a circuit
The clock period must be longer than this critical path, or the signal will not propagate properly to that next register
Critical Path =
CLK-to-Q Delay
+ CL Delay 1
+ CL Delay 2
+ CL Delay 3
+ Adder Delay
+ Setup Time

## Slide 25: The Critical Path
When setting clock period in synchronous systems, must allow for worst case
Path through combinational logic that is worst case called “critical path”
  Can be estimated by number of “gate delays”: Number of gates must go through in worst case
Idea: Doesn’t matter if speedup other paths if don’t improve the critical path

## Slide 26: How do we go faster?
Pipelining!
Split operation into smaller parts and add a register between each one
  We will study pipelining later in the course

## Slide 27: Register File

## Slide 28: Register File
A register file with two read ports and one write port
Write Enable
Ref: Harris and Harris Book: Digital Design and Computer Architecture: RISC-V Edition

## Slide 29: Register File
The implementation of two read ports for a register file with n registers can be done with a pair of n-to-1 multiplexors
Ref: Harris and Harris Book: Digital Design and Computer Architecture: RISC-V Edition

## Slide 30: Register File
The write port for a register file is implemented with a decoder that is used with the write signal to generate the C input to the registers
Ref: Harris and Harris Book: Digital Design and Computer Architecture: RISC-V Edition

## Slide 31: Finite State Machine (FSM) (Self Reading) - See backup slides

## Slide 32: FSM
How do we represent sequential logic?
  Truth tables could account for history
  We could do boolean logic with prior state as a variable
We can also use a new representation: Finite State Machines

## Slide 33: Finite State Machines (FSMs)
A convenient way to conceptualize computation over time
Function can be represented with a state transition diagram
With combinational logic and registers, any FSM can be implemented in hardware!
States: S0, S1, S2
Initial State: S0
Transitions of form:
input/output

## Slide 34: Hardware Implementation of FSM
Register holds a representation of the FSM’s state
  Must assign a unique bit pattern for each state
  Output is present/current state (PS/CS)
  Input is next state (NS)
Combinational Logic implements transition function (state transitions + output)
+
=

## Slide 35: Hardware Implementation of FSM
clock
Notes: A finite-state machine can be implemented with a register to hold the current state and a block of combinational logic that computes the next-state function and the output function
Figure shows how a finite-state machine with 4 bits of state, and thus up to 16 states, might look.
The combinational logic block is often implemented using structured logic, such as a PLA. A PLA can be constructed automatically from the next-state and output function tables.

## Slide 36: Storage Elements

## Slide 37: Storage Element: Idealized Memory
Memory (idealized)
  One input bus: Data In
  One output bus: Data Out
Memory word is found by:
  Address selects the word to put on Data Out
  Write Enable = 1: address selects the memory word to be written via the Data In bus
Clock input (CLK)
  CLK input is a factor ONLY during write operation
  During read operation, behaves as a combinational logic block: Address valid  Data Out valid after “access time”
Clk
Data In
Write Enable
32
32
DataOut
Address
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley
Notes: The last storage element you will need for the datapath is the idealized memory to store your data and instructions.
This idealized memory block has just one input bus (Data In) and one output bus (Data Out).
When Write Enable is 0, the address selects the memory word to put on the Data Out bus.
When Write Enable is 1, the address selects the memory word to be written via the DataIn bus at the next clock tick.
Once again, the clock input is a factor ONLY during the write operation.
During read operation, it behaves as a combinational logic block.
That is if you put a valid value on the address lines, the output bus DataOut will become valid after the access time of the memory.

## Slide 38: Storage Element: Register (Building Block)
Similar to D Flip Flop except
  N-bit input and output
  Write Enable input
Write Enable:
  Negated (or deasserted) (0): Data Out will not change
  Asserted (1): Data Out will become Data In on rising edge of clock
clk
Data In
Write Enable
N
N
Data Out
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley
Notes: As far as storage elements are concerned, we will need a N-bit register
The significant difference here is that the register will have a Write Enable input.
That is the content of the register will NOT be updated if Write Enable is not asserted (0).
The content is updated at the clock tick ONLY if the Write Enable signal is asserted (1).

## Slide 39: Storage Element: Register File
Register File consists of 32 registers:
  Two 32-bit output busses:
  busA and busB
  One 32-bit input bus: busW
Register is selected by:
  RA (number) selects the register to put on busA (data)
  RB (number) selects the register to put on busB (data)
  RW (number) selects the register to be written via busW (data) when Write Enable is 1
Clock input (clk)
  Clk input is a factor ONLY during write operation
  During read operation, behaves as a combinational logic block:
    RA or RB valid  busA or busB valid after “access time.”
Clk
busW
Write Enable
32
32
busA
32
busB
5
5
5
RW
RA
RB
32 x 32-bit
Registers
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley
Notes: We will also need a register file that consists of 32 32-bit registers with two output busses (busA and busB) and one input bus.
The register specifiers RA and RB select the registers to put on busA and busB respectively.
When Write Enable is 1, the register specifier Rw selects the register to be written via busW.
In our simplified version of the register file, the write operation will occurs at the clock tick.
Keep in mind that the clock input is a factor ONLY during the write operation.
During read operation, the register file behaves as a combinational logic block.
That is if you put a valid value on Ra, then bus A will become valid after the register file’s access time.
Similarly if you put a valid value on Rb, bus B will become valid after the register file’s access time. In both cases (Ra and Rb), the clock input is not a factor.

## Slide 40: State Required by RV32I ISA
Each instruction reads and updates this state during execution:
Registers (x0..x31)
  Register file (or regfile) Reg holds 32 registers x 32 bits/register: Reg[0].. Reg[31]
  First register read specified by rs1 field in instruction
  Second register read specified by rs2 field in instruction
  Write register (destination) specified by rd field in instruction
  x0 is always 0 (writes to Reg[0]are ignored)
Program Counter (PC)
  Holds address of current instruction
Memory (MEM)
  Holds both instructions and data, in one 32-bit byte-addressed memory space
  We’ll use separate memories for instructions (IMEM) and data (DMEM)
    Later we’ll replace these with instruction and data caches
  Instructions are read (fetched) from instruction memory (assume IMEM read-only)
  Load/store instructions access data memory

## Slide 41: Single Cycle Vs Multicycle Machines

## Slide 42: Single-cycle Machine
Executes an entire instruction in one cycle
The cycle time is limited by the slowest instruction
It doesn’t require any non-architecture state (note that the state elements are: PC, Instruction Memory, Register File, and Data Memory)
Cycle time limited by longest instruction – load word (lw)
Requires separate instruction and data memories
Single-cycle
Multicycle

## Slide 43: Multi-cycle Machine
Higher clock speed
Simpler instructions run faster
Control signals needed in the next cycle can be generated in the current cycle
Reuse of functional unit in multiple cycles within an instruction – eg. Adder
Single memory
  Fetching instruction in one cycle
  Writing data in another cycle
Less hardware requirement
Not in use now
Single-cycle
Multicycle

## Slide 44: Pipelined Machines
Applies pipelining to single cycle machine
Executes several instructions simultaneously
  High throughput
Must add logic to handle dependencies between simultaneously executing instructions
Requires nonarchitectural pipeline registers
Pipelined processors must access instructions and data in the same cycle  use of separate instruction and data memories
All commercial high-performance processors use pipelining today
Will study this architecture later in the course

## Slide 45: Lecture Summary
In logic circuits, the maximum clock frequency depends on
  Setup time, Click-to-Q time, and Combinational Circuit delay
One clock cycle should be big enough to accommodate summation of setup time, Click-to-q time, and combinational circuit delay
Synchronous digital circuits use clock signals
  Flip-flop / Registers are required for timing synchronization and control instability due to timing mismatch of input signals
Storage elements for RISC-V machine: Register file, Memory
Single cycle designs are simpler – but hardly in use
  We will first study single cycle architecture for RISC-V machine

## Slide 46: Backup

## Slide 47: FSM
Consists of:
  State register
    Stores current state
    Loads next state at clock edge
  Combinational logic
    Computes the next state
    Computes the outputs

## Slide 48: Using Hardware Description Language
Hardware Description Language (HDL)
  A programming language for describing hardware, used for generating simulations of a hardware design and also as input to synthesis tools that can generate actual hardware
It serves two purposes
  It provides an abstract description of the hardware to simulate and debug the design
  Hardware implementation using logic synthesis and hardware compilation tools
Two popular HDLs
  Verilog is somewhat more heavily used in industry and is based on C
  VHDL, which is based on Ada

## Slide 49: Comparator: less than
N-bit signed comparator
Ref: Harris and Harris Book: Digital Design and Computer Architecture: RISC-V Edition

## Slide 50: Example: Serial Communication
Wifi sends data “1 bit at a time”
How do we know where a byte “starts”?
Send “preamble …”
  E.g. 3 one’s in a row

## Slide 51: FSM* to Detect 3 One’s
FSM to detect the occurrence of 3 consecutive 1’s in the input.
* FSM = Finite State Machine
State transition diagram:
State transitions are controlled by
the clock: on each clock cycle the FSM
  checks the inputs,
  transitions to a new state, and
  produces a new output …
Notes: {signal: [ {name: 'clk', wave: 'l.H.l.H.l.H.l.H.l.H.l.H.l'}, {name: 'in', wave: '1...0...1...........0....'}, {name: 'out', wave: '0..................1...0.'}, {name: 'state', wave: '3..4...3...4...5...3...3.', data:['S0', 'S0', 'S1', 'S0', 'S1', 'S2', 'S0']},]}

## Slide 52: FSM to Detect 3 One’s
FSM to detect the occurrence of 3 consecutive 1’s in the input.
State transition diagram:
Notes: {signal: [ {name: 'clk', wave: 'l.H.l.H.l.H.l.H.l.H.l.H.l'}, {name: 'in', wave: '1...0...1...........0....'}, {name: 'out', wave: '0..................1...0.'}, {name: 'state', wave: '3..4...3...4...5...3...3.', data:['S0', 'S0', 'S1', 'S0', 'S1', 'S2', 'S0']},]}

## Slide 53: FSM to Detect 3 One’s
FSM to detect the occurrence of 3 consecutive 1’s in the input.
State transition diagram:
State transitions are controlled by
the clock: on each clock cycle the FSM
  checks the inputs,
  transitions to a new state, and
  produces a new output …
Notes: {signal: [ {name: 'clk', wave: 'l.H.l.H.l.H.l.H.l.H.l.H.l'}, {name: 'in', wave: '1...0...1...........0....'}, {name: 'out', wave: '0..................1...0.'}, {name: 'state', wave: '3..4...3...4...5...3...3.', data:['S0', 'S0', 'S1', 'S0', 'S1', 'S2', 'S0']},]}

## Slide 54: FSM Combinatorial Logic
Truth Table
Current State | Input | Next State | Output
State | Code
State Encoding

## Slide 55: FSM Combinatorial Logic
Truth Table
State | Code
State Encoding
State | Code
S0 | 00
S1 | 01
S2 | 10
unused | 11
PS | Input | NS | Output
XX | 0 | 00 | 0
00 | 1 | 01 | 0
01 | 1 | 10 | 0
10 | 1 | 00 | 1
11 | X | 00 | 0

## Slide 56: Finite State Machines (FSM) - Summary
Describe computation over time
Represent FSM with “state transition diagram”
Start at given state and input, follow some edge to next (or same) state
With combinational logic and registers, any FSM can be implemented in hardware
state transition diagram

## Slide 57: Conceptual RISC-V Datapath
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley