## Slide 1: CS 211 Computer Architecture Lecture 27 : Datapath Design – 3 Single Cycle Datapath (R-Type Instructions)
Ravi Mittal
ravi.mittal@iitgoa.ac.in
Indian Institute of Technology, Goa

## Slide 2: Just be here !
If it goes out ... Bring it back

## Slide 3: Acknowledgements
Class Presentation, CS61C, Introduction to Assembly Language and RISC-V Instruction Set Architecture, University of Berkeley, Prof Krste Asanović & Randy H. Katz. http://inst.eecs.Berkeley.edu/~cs61c
Class presentation CS61C Sequential Logic and Finite State Machines, Instructor: Nick Riasanovsky
Computer Organization and Design, The Hardware Software Interface, RISC-V edition, Patterson and Hennessey
Digital Design and Computer Architecture: RISC-V Edition, Harris & Harris, Elsevier – Presentation.

## Slide 4: RISC-V: So far we have studied
Arithmetic operations: add, sub, addi,
How to bring data from memory to register and vice versa?
  lw, sw, lb, sb, lbu
Bit-by-bit logical instructions
  and, or, xor, andi, ori, xori
Logical Shift instructions
  sll, srl, sra, slli, srli, srai
Generating Constants
Branching Instructions: beq, bne, blt/bltu, bge/bgeu
Jumping instruction: j
Assembly level program for: if, if/else,
Function Calls
  Basics, Input arguments and Return Value
  while, for loops
The Stack
  Basics, How functions use a stack
  Stack use in non-leaf function calls
  Recursive Functions
Floating Point Numbers
Instruction Formats
Machine Instructions
Microarchitecture
  Combinational and Sequential logic
  Clock, Registers, Muxes, Adder, Subtractor, Comparator, Buses, Register file, Idealized Memory
  Timing considerations
  Maximum frequency
  Single Cycle Vs Multicycle vs Pipeline

## Slide 5: In this class we will study
Requirements of Instruction Set
Single Cycle (one instruction per cycle) Datapath
Assembling datapath for add/sub, addi instructions

## Slide 6: Requirements of Instruction Set

## Slide 7: Requirements of the Instruction Set
Memory (MEM)
  Instructions Memory and data Memory
Registers (x0 - x31)
PC
Sign Extender
Add/Sub/OR unit for operation on register(s) or sign extended immediate
Add 4 (or maybe sign extended immediate) to PC
Compare if registers equal?
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 8: Components of the Datapath
Combinational Elements
State Elements + Clocking Methodology
Building Blocks
32
32
A
B
32
Sum
CarryOut
CarryIn
Adder
32
A
B
32
Y
32
Select
MUX
Multiplexer
32
32
A
B
32
Result
OP
ALU
ALU
Adder
Zero
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 9: One Instruction Per Cycle Datapath

## Slide 10: Register Transfer Language (RTL)
RTL gives the meaning of the instructions
Inst Register Transfers
ADD R[rd]  R[rs1] + R[rs2]; PC  PC + 4
SUB R[rd]  R[rs1] – R[rs2]; PC  PC + 4
ORI R[rd]  R[rs1] | sign_ext(Imm12); PC  PC + 4
LW R[rd]  MEM[ R[rs1] + sign_ext(Imm12)]; PC  PC + 4
SW MEM[ R[rs1] + sign_ext(Imm12) ]  R[rs2]; PC  PC + 4
BEQ if ( R[rs] == R[rt] ) then PC  PC + (sign_ext(Imm12) || 0) else PC  PC + 4
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 11: Designing our Datapath: Where to start?
6 different formats: R, I , S, B, U, J
  Arithmetic, Immediate, Store, Branch, Upper-immediate, JAL
Instructions are classified into these formats based on their behaviors, meaning each type does something a little different

## Slide 12: The RISC-V Lite Subset
ADD and SUB
  add rd,rs1,rs2
  sub rd,rs1,rs2
OR Immediate:
  ori rd,rs1,imm12
LOAD and STORE Word
  lw rd,rs1,imm12
  sw rs2,rs1,imm12
BRANCH:
  beq rs1,rs2,imm12
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley
Notes: In today’s lecture, I will show you how to implement the following subset of RISC-V instructions: add, subtract, or immediate, load, store, branch, and the jump instruction.
The Add and Subtract instructions use the R format. The Op together with the Func fields together specified all the different kinds of add and subtract instructions.
Rs and Rt specifies the source registers. And the Rd field specifies the destination register.
The Or immediate instruction uses the I format. It only uses one source register, Rs. The other operand comes from the immediate field. The Rt field is used to specified the destination register. (Note that dest is the Rt field!)
Both the load and store instructions use the I format and both add the Rs and the immediate filed together to from the memory address.
The difference is that the load instruction will load the data from memory into Rt while the store instruction will store the data in Rt into the memory.
The branch on equal instruction also uses the I format. Here Rs and Rt are used to specified the registers we need to compare.
If these two registers are equal, we will branch to a location offset by the immediate field.
Finally, the jump instruction uses the J format and always causes the program to jump to a memory location specified in the address field.
I know I went over this rather quickly and you may have missed something. But don’t worry, this is just an overview. You will keep seeing these (point to the format) all day today.

## Slide 13: One instruction per cycle machine
Single-cycle machine
Sequential
Logic
(State)
Combinational
Logic
Knick Riasanovsky, Univ of California, Berkeley

## Slide 14: One-Instruction-Per-Cycle RISC-V Machine
On every tick of the clock, the computer executes one instruction
Current state outputs drive the inputs to the combinational logic, whose outputs settles at the values of the state before the next clock edge
At the rising clock edge, all the state elements are updated with the combinational logic outputs, and execution moves to the next clock cycle
Reg[]
pc
IMEM
DMEM
Combinational Logic
clock
IMEM: Instruction Memory
DMEM: Data Memory
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 15: Basic Phases of Instruction Execution
IMEM
+4
rs2
rs1
rd
Reg[]
ALU
DMEM
imm
1. Instruction
Fetch
2. Decode/
Register
Read
3. Execute
4. Memory
5. Register
Write
PC
mux
Clock
time
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 16: Why Five Stages?
Could we have a different number of stages?
  Yes. Many other architectures do
So why does RISC-V have five stages if instructions tend to idle for at least one stage?
  The five stages are the union of all the operations needed by all the instructions
  There is one instruction, load (lw/lb) that uses all five stages
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 17: Assembling the Datapath for add/sub instruction

## Slide 18: Implementing R type instruction
add rd, rs1, rs2
Instruction makes two changes to machine’s state:
  Reg[rd] = Reg[rs1] + Reg[rs2]
  PC = PC + 4
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 19: Implementing R type instruction
What needs to be done to execute R type instruction
  (1) Get the instruction
  (2) Parse instruction fields (rd, rs1, rs2, operation…)
  (3) Read data based on parsed operands
  (4) Perform operation
  (5) Write result to our destination register
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 20: Implementing R type instruction
(1) Get the instruction
  add x1 x2 x3
(2) Parse instruction fields (rd, rs1, rs2, operation…)
  rd = x1 rs1 = x2 rs2 = x3
(3) Read data based on parsed operands
  R[x2] R[x3]
(4) Perform operation
  R[x2] + R[x3]
(5) Write result to our destination register
  R[x1] = R[x2] + R[x3]

## Slide 21: Implementing R-Types
IMEM
+4
pc
Control
(1) Get the instruction
PC holds the address of our current instruction
Get instruction from IMEM

## Slide 22: Implementing R-Types
IMEM
+4
pc
inst[11:7]
inst[19:15]
inst[24:20]
Control
(2) Parse instruction fields (rd, rs1, rs2, operation…)
What registers are we operating on?
Where do they lie in our instruction format?
How big is each field?

## Slide 23: Implementing R-Types
IMEM
+4
pc
inst[11:7]
inst[19:15]
inst[24:20]
Control
(3) Read data based on parsed operands
New hardware: Register File
Simultaneous read R[rs1] and R[rs2]
Note that reading can be done anytime
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
R[rs1]
R[rs2]

## Slide 24: Implementing R-Types
IMEM
+4
ALU
pc
inst[11:7]
inst[19:15]
inst[24:20]
Control
(4) Perform operation
New hardware: ALU (Arithmetic Logic Unit)
  Abstraction for adders, multipliers, dividers, etc.
How does ALU know what operation to execute?
  Our first control bit! ALUSel(ect)
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
R[rs1]
R[rs2]
ALUSel
inst[31:0]

## Slide 25: There are many R-Type operations!
ALUSel is a control bit which encodes the operation to be performed on operands
The value of ALUSel is a mapping from func3 and func7 values to operations
“if func3 == 000 and func7 == 0000000, perform an add”

## Slide 26: Implementing R-Types
IMEM
+4
ALU
pc
inst[11:7]
inst[19:15]
inst[24:20]
Control
(5) Write result to our destination register
The data we want to write is the result of computing operation on operands, ie. the output from our ALU
Send it back to the regfile for writing
RegWEn control signal
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
wb
R[rs1]
R[rs2]
ALUSel
inst[31:0]
RegWriteEnable
(RegWEn)

## Slide 27: Timing Diagram for add
1000
1004
PC
1004
1008
PC+4
add x1,x2,x3
add x6,x7,x9
inst[31:0]
Clock
time
+4
pc
pc+4
inst[11:7]
inst[19:15]
inst[24:20]
IMEM
inst[31:0]
+
RegWEn
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Reg[rs1]
Reg[rs2]
clock
alu
Reg[2]
Reg[7]
Reg[rs1]
Reg[2]+Reg[3]
alu
Reg[7]+Reg[9]
Reg[3]
Reg[9]
Reg[rs2]
???
Reg[1]
Reg[2]+Reg[3]
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 28: Implementing sub instruction
Almost the same as add, except now have to subtract operands instead of adding them
Instruction bit 30 selects between add and subtract
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 29: Datapath for add/sub
Control Logic
+4
pc
pc+4
inst[11:7]
inst[19:15]
inst[24:20]
IMEM
inst[31:0]
RegWEn
(1=write, 0=no write)
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Reg[rs1]
Reg[rs2]
alu
ALU
ALUSel
(Add=0/Sub=1)
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 30: Implementing other R-Format instructions
All implemented by decoding funct3 and funct7 fields and selecting appropriate ALU function
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 31: Datapath for addi

## Slide 32: Implementing the addi instruction
RISC-V Assembly Instruction:
  addi x15,x1,-50
111111001110
00001
000
01111
0010011
OP-Imm
rd=15
ADD
imm=-50
rs1=1
CS61C Prof Dan Garcia and Miki Lustig, Univ of California, Berkeley

## Slide 33: Datapath for add/sub
+4
Add
clk
addr
inst
IMEM
PC
pc+4
Inst[24:20]
ALU
+
clk
Reg [ ]
Inst[19:15]
Inst[11:7]
AddrB
AddrA
DataA
DataB
AddrD
DataD
alu
Reg[rs1]
Reg[rs2]
Control logic
RegWEn
(1=Write, 0=NoWrite)
ALUSel
Inst[31:0]
CS61C Prof Dan Garcia and Miki Lustig, Univ of California, Berkeley

## Slide 34: Datapath for add/sub
+4
Add
clk
addr
inst
IMEM
PC
pc+4
Inst[24:20]
ALU
+
clk
Reg [ ]
Inst[19:15]
Inst[11:7]
AddrB
AddrA
DataA
DataB
AddrD
DataD
alu
Reg[rs1]
Reg[rs2]
Inst[31:0]
Control logic
RegWEn
(1=Write, 0=NoWrite)
ALUSel
Immediate should
be here
CS61C Prof Dan Garcia and Miki Lustig, Univ of California, Berkeley

## Slide 35: Adding addi to Datapath
+4
Add
clk
addr
inst
IMEM
PC
pc+4
Inst[24:20]
ALU
+
clk
Reg [ ]
Inst[19:15]
Inst[11:7]
AddrB
AddrA
DataA
DataB
AddrD
DataD
alu
Reg[rs1]
Reg[rs2]
Inst[31:0]
Control logic
RegWEn
(1=Write, 0=NoWrite)
ALUSel
(add=0/ sub=1)
BSel
(rs2=0/ Imm=1)
0
1
Imm[31:0]
CS61C Prof Dan Garcia and Miki Lustig, Univ of California, Berkeley

## Slide 36: Adding addi to Datapath
+4
Add
clk
addr
inst
IMEM
PC
pc+4
Inst[24:20]
ALU
+
clk
Reg [ ]
Inst[19:15]
Inst[11:7]
AddrB
AddrA
DataA
DataB
AddrD
DataD
alu
Reg[rs1]
Reg[rs2]
Inst[31:0]
Control logic
RegWEn=1
ALUSel= add
BSel
(rs2=0/ Imm=1)
Bsel = 1
ImmSel=I
0
1
Imm[31:0]
Imm.
Gen
+4
Add
clk
addr
inst
IMEM
PC
pc+4
Inst [31:20]
CS61C Prof Dan Garcia and Miki Lustig, Univ of California, Berkeley

## Slide 37: Adding addi to Datapath
+4
Add
clk
addr
inst
IMEM
PC
pc+4
Inst[24:20]
ALU
+
clk
Reg [ ]
Inst[19:15]
Inst[11:7]
AddrB
AddrA
DataA
DataB
AddrD
DataD
alu
Reg[rs1]
Reg[rs2]
Inst[31:0]
Control logic
RegWEn=1
ALUSel= add
BSel
(rs2=0/ Imm=1)
Bsel = 1
ImmSel=I
0
1
Imm[31:0]
Imm.
Gen
+4
Add
clk
addr
inst
IMEM
PC
pc+4
Inst [31:20]
(1) Get the instruction
(2) Parse instruction fields (rd, rs1, rs2, operation, imm…)
(3) Read data based on parsed operands
(4) Perform operation
(5) Write result to our destination register
CS61C Prof Dan Garcia and Miki Lustig, Univ of California, Berkeley

## Slide 38: I-Format immediates
inst[31:0]
------inst[31]-(sign-extension)-------
inst[30:20]
imm[31:0]
Imm.
Gen
inst[31:20]
imm[31:0]
ImmSel=I
High 12 bits of instruction (inst[31:20]) copied to low 12 bits of immediate (imm[11:0])
Immediate is sign-extended by copying value of inst[31] to fill the upper 20 bits of the immediate value (imm[31:12])
31 30
20
15
7
12
19
14
11
6
0
rs1
funct3
rd
opcode
imm[11:0]
12
CS61C Prof Dan Garcia and Miki Lustig, Univ of California, Berkeley

## Slide 39: R+I Datapath
+4
Add
clk
addr
inst
IMEM
PC
pc+4
Inst[24:20]
ALU
+
clk
Reg [ ]
Inst[19:15]
Inst[11:7]
AddrB
AddrA
DataA
DataB
AddrD
DataD
alu
Reg[rs1]
Reg[rs2]
Inst<31:0>
Control logic
RegWEn
ALUSel
BSel
0
1
Imm[31:0]
Imm.
Gen
+4
Add
clk
addr
inst
IMEM
PC
pc+4
Inst [31:20]
Works for all other I-format arithmetic instructions (slti,sltiu,andi, ori,xori,slli,srli, srai) just by changing ALUSel
ImmSel
CS61C Prof Dan Garcia and Miki Lustig, Univ of California, Berkeley

## Slide 40: A few notes on our new datapath...
Control signals:
  ALUSel: What operation are we performing?
  RWEn: Should we write to our destination register?
  BSel: (R[rs1] and R[rs2]) or (R[rs1] and imm)?
  ImmSel: How should we reassemble the immediate?
  MemRW: Should we read from memory or write to it?
  WBSel: Do we want to write back to our destination register the ALU output or DMEM output?
Often these values are encoded as binary values, but we may represent some (ie. ImmSel, ALUSel) with words instead (add, I-type, etc.)

## Slide 41: Class Summary
We have studied single cycle Datapath design for
  add, sub, addi instructions