## Slide 1: CS 211 Computer Architecture Lecture 28: RISC-V – Datapath Design Part 4 Single Cycle Data Path Implementation for Instructions: load, store, branching
Ravi Mittal
ravi.mittal@iitgoa.ac.in
Indian Institute of Technology, Goa

## Slide 2: Acknowledgements
Class Presentation, CS61C, RISC-V Datapath II, University of California, Berkeley, Prof Dan Garcia and Miki Lustig. http://inst.eecs.Berkeley.edu/~cs61c
Class presentation CS61C RISC-V CPU Control, Pipelining, Instructor: Morgan Rae Reschenberg, University of California, Berkeley
Harris and Harris Book: Digital Design and Computer Architecture: RISC-V Edition
Computer Organization and Design, The Hardware Software Interface, RISC-V edition, Patterson and Hennessey

## Slide 3: RISC-V: So far we have studied
Arithmetic operations: add, sub, addi,
How to bring data from memory to register and vice versa?
  lw, sw, lb, sb, lbu
Bit-by-bit logical instructions
  and, or, xor, andi, ori, xori
Logical Shift instructions
  sll, srl, sra, slli, srli, srai
Generating Constants
Branching Instructions: beq, bne, blt/bltu, bge/bgeu
Jumping instruction: j
Assembly level program for: if, if/else,
Function Calls
  Basics, Input arguments and Return Value
  while, for loops
The Stack
  Basics, How functions use a stack
  Stack use in non-leaf function calls
  Recursive Functions
Floating Point Numbers
Instruction Formats
Machine Instructions
Microarchitecture
  Combinational and Sequential logic
  Clock, Registers, Muxes, Adder, Subtractor, Comparator, Buses, Register file, Idealized Memory
  Timing considerations
  Maximum frequency
  Single Cycle Vs Multicycle vs Pipeline
  Datapath design for R-type, and I-type Instructions: add, sub, addi

## Slide 4: Last Class

## Slide 5: Basic Phases of Instruction Execution
IMEM
+4
rs2
rs1
rd
Reg[]
ALU
DMEM
imm
1. Instruction
Fetch
2. Decode/
Register
Read
3. Execute
4. Memory
5. Register
Write
PC
mux
Clock
time

## Slide 6: Implementing R-Types
IMEM
+4
ALU
pc
inst[11:7]
inst[19:15]
inst[24:20]
Control
(5) Write result to our destination register
  The data we want to write is the result of computing operation on operands, ie. the output from our ALU
  Send it back to the regfile for writing
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
wb
R[rs1]
R[rs2]
ALUSel = add
inst[31:0]

## Slide 7: Adding addi to Datapath
+4
Add
clk
addr
inst
IMEM
PC
pc+4
Inst[24:20]
ALU
+
clk
Reg [ ]
Inst[19:15]
Inst[11:7]
AddrB
AddrA
DataA
DataB
AddrD
DataD
alu
Reg[rs1]
Reg[rs2]
Inst[31:0]
Control logic
RegWEn=1
ALUSel= add
BSel
(rs2=0/ Imm=1)
Bsel = 1
ImmSel=I
0
1
Imm[31:0]
Imm.
Gen
+4
Add
clk
addr
inst
IMEM
PC
pc+4
Inst [31:20]
CS61C Prof Dan Garcia and Miki Lustig, Univ of California, Berkeley

## Slide 8: Adding addi to Datapath
+4
Add
clk
addr
inst
IMEM
PC
pc+4
Inst[24:20]
ALU
+
clk
Reg [ ]
Inst[19:15]
Inst[11:7]
AddrB
AddrA
DataA
DataB
AddrD
DataD
alu
Reg[rs1]
Reg[rs2]
Inst[31:0]
Control logic
RegWEn=1
ALUSel= add
BSel
(rs2=0/ Imm=1)
Bsel = 1
ImmSel=I
0
1
Imm[31:0]
Imm.
Gen
+4
Add
clk
addr
inst
IMEM
PC
pc+4
Inst [31:20]
(1) Get the instruction
(2) Parse instruction fields (rd, rs1, rs2, operation, imm…)
(3) Read data based on parsed operands
(4) Perform operation
(5) Write result to our destination register
CS61C Prof Dan Garcia and Miki Lustig, Univ of California, Berkeley

## Slide 9: R+I Datapath
+4
Add
clk
addr
inst
IMEM
PC
pc+4
Inst[24:20]
ALU
+
clk
Reg [ ]
Inst[19:15]
Inst[11:7]
AddrB
AddrA
DataA
DataB
AddrD
DataD
alu
Reg[rs1]
Reg[rs2]
Inst<31:0>
Control logic
RegWEn
ALUSel
BSel
0
1
Imm[31:0]
Imm.
Gen
+4
Add
clk
addr
inst
IMEM
PC
pc+4
Inst [31:20]
Works for all other I-format arithmetic instructions (slti,sltiu,andi, ori,xori,slli,srli, srai) just by changing ALUSel
ImmSel
CS61C Prof Dan Garcia and Miki Lustig, Univ of California, Berkeley

## Slide 10: In this class, we will study
Datapath for lw
Datapath for sw
Datapath for branch instructions

## Slide 11: I-Type Instruction: lw Datapath for lw

## Slide 12: Loads are also of I-type : lw
RISC-V Assembly Instruction (I-type):
  lw x14, 8(x2)
5
3
7
5
31
20
15
7
12
19
14
11
6
0
rs1
funct3
rd
opcode
imm[11:0]
12
offset[11:0]
base
width
dest
LOAD
31
20
15
7
12
19
14
11
6
0
00010
010
01110
0000011
000000001000
imm= +8
rs1=2
LW
rd=14
LOAD
The 12-bit signed immediate is added to the base address in register rs1 to form the memory address
  This is very similar to the add-immediate operation but used to create address not to create final result
The value loaded from memory is stored in register rd
CS61C Prof Dan Garcia and Miki Lustig, Univ of California, Berkeley

## Slide 13: Adding lw to Datapath
+4
Add
clk
addr
inst
IMEM
PC
pc+4
Inst[24:20]
ALU
+
clk
Reg [ ]
Inst[19:15]
Inst[11:7]
AddrB
AddrA
DataA
DataB
AddrD
DataD
alu
Reg[rs1]
Reg[rs2]
Inst[31:0]
Control logic
RegWEn
=1
ALUSel
=Add
Bsel
=1
WBSel
=0
MemRW
=Read
0
1
Imm[31:0]
Imm.
Gen
+4
Add
clk
addr
inst
IMEM
DMEM
addr
DataR
PC
pc+4
Inst [31:20]
1
0
clk
ImmSel
=I
mem
wb
pc
CS61C Prof Dan Garcia and Miki Lustig, Univ of California, Berkeley
5
3
7
5
31
20
15
7
12
19
14
11
6
0
rs1
funct3
rd
opcode
imm[11:0]

## Slide 14: All RV32 Load Instructions
Supporting the narrower loads requires additional logic to extract the correct byte/halfword from the value loaded from memory, and sign- or zero-extend the result to 32 bits before writing back to register file
funct3 field encodes size and ‘signedness’ of load data
imm[11:0]
rs1
000
rd
0000011
imm[11:0]
rs1
001
rd
0000011
imm[11:0]
rs1
010
rd
0000011
lb
lh
lw
imm[11:0]
rs1
100
rd
0000011
lbu
imm[11:0]
rs1
101
rd
0000011
lhu

## Slide 15: Immediate Encoding (repeat)
Immediate bits mostly occupy consistent instruction bits
Sign bit of signed immediate is in msb of instruction
Recall that rs2 of R-type can encode immediate shift amount
Instruction Bits
Ref: Harris and Harris Book: Digital Design and Computer Architecture: RISC-V Edition

## Slide 16: Datapath for S-type Instructions

## Slide 17: All RV32 Store Instructions
Prof Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 18: Adding sw Instruction
sw: Reads two registers, rs1 for base memory address, and rs2 for data to be stored, as well immediate offset!
  sw x14, 8(x2)
0000000
01110
00010
010
01000
0100011
combined 12-bit offset = 8
0000000
01000
7
5
5
3
7
5
31
25
20
15
7
12
24
19
14
11
6
0
Imm[11:5]
rs2
rs1
funct3
imm[4:0]
opcode
offset[11:5]
base
width
src
STORE
offset[4:0]
STORE
offset[4:0]
=8
SW
offset[11:5]
=0
rs2=14
rs1=2
CS61C Prof Dan Garcia and Miki Lustig, Univ of California, Berkeley

## Slide 19: Datapath with lw
+4
Add
clk
addr
inst
IMEM
PC
pc+4
Inst[24:20]
ALU
+
clk
Reg [ ]
Inst[19:15]
Inst[11:7]
AddrB
AddrA
DataA
DataB
AddrD
DataD
alu
Reg[rs1]
Reg[rs2]
Inst[31:0]
Control logic
RegWEn
ALUSel
BSel
MemRW
0
1
Imm[31:0]
Imm.
Gen
+4
Add
clk
addr
inst
IMEM
DMEM
addr
DataR
PC
pc+4
Inst [31:20]
1
0
clk
WBSel
ImmSel
mem
wb
pc
CS61C Prof Dan Garcia and Miki Lustig, Univ of California, Berkeley

## Slide 20: Adding sw to Datapath
+4
Add
clk
addr
inst
IMEM
PC
pc+4
Inst[24:20]
ALU
+
clk
Reg [ ]
Inst[19:15]
Inst[11:7]
AddrB
AddrA
DataA
DataB
AddrD
DataD
alu
Reg[rs1]
Reg[rs2]
Inst[31:0]
Control logic
RegWEn =0
ALUSel
=Add
Bsel
=1
MemRW
=Write
0
1
Imm[31:0]
Imm.
Gen
+4
Add
clk
addr
inst
IMEM
DMEM
addr
DataR
DataW
PC
pc+4
Inst [31:7]
1
0
clk
WBSel =*
(*=Don’t care)
ImmSel
=S
mem
wb
pc
+4
Add
clk
addr
inst
IMEM
DMEM
addr
DataR
DataW
PC
pc+4
CS61C Prof Dan Garcia and Miki Lustig, Univ of California, Berkeley

## Slide 21: I+S Immediate Generation
inst[31:0]
S
I
1
6
5
5
Just need a 5-bit mux to select between two positions where low five bits of immediate can reside in instruction
Other bits in immediate are wired to fixed positions in instruction
imm[11:5]
rs2
rs1
funct3
imm[4:0]
S-opcode
25
24
31
20
15
7
12
19
14
11
6
0
rs1
funct3
rd
I-opcode
imm[11:0]
S
I
inst[24:20]
inst[31] (sign extension)
I
inst[30:25]
inst[11:7]
inst[31] (sign extension)
inst[30:25]
S
31
5
11
10
4
0
I/S
imm[31:0]
Imm.
Gen
I/S
ImmSel =
CS61C Prof Dan Garcia and Miki Lustig, Univ of California, Berkeley

## Slide 22: Datapath for Branches

## Slide 23: Modifying Program Execution - branching, jumping
So far we’ve been working with instructions that modify the contents of registers in our reg file or instructions that modify memory
We also have instructions which modify how the program executes
  These change the value of our PC register to an instruction at a label or register address
    These instructions are either PC-relative (add an immediate to PC) or absolute (encode an actual address that PC is to change to)
Let’s start with branching!
Ref: CS61C Morgan Reschenberg, Univ of California, Berkeley

## Slide 24: Types of Branches
Conditional – change of control flow depending on outcome of comparison
  branch if equal (beq)
  branch if not equal (bne)
  branch if less than (blt/bltu)
  branch if greater than or equal to (bge/bgeu)
Unconditional – always branch
  jump (j)
  jump register (jr)
  jump and link (jal)
  jump and link register (jalr)
Ref: Harris and Harris Book: Digital Design and Computer Architecture: RISC-V Edition

## Slide 25: Implementing Branches
B-format is mostly same as S-Format, with two register sources (rs1/rs2) and a 12-bit immediate
But now immediate represents values -4096 to +4094 in 2-byte increments
The 12 immediate bits encode even 13-bit signed byte offsets (lowest bit of offset is always zero, so no need to store it)
Assembly Inst Example: BEQ x1, x2, Label
Label is encoded in machine instruction using PC relative addressing

## Slide 26: Implementing Branches
Branching involves two operations:
  Comparison (R[rs1] == R[rs2], possibly <, >, etc.)
  Addition (PC = PC + Imm)
Different change to the state:
  PC = PC + 4, branch not taken PC + immediate, branch taken
Our ALU can do comparison or addition, but not both! We need an additional hardware!
Ref: CS61C Morgan Reschenberg, Univ of California, Berkeley

## Slide 27: Branch Comparator
BrEq = 1, if A=B
BrLT = 1, if A < B
BrUn = 1 selects unsigned comparison for BrLT, 0 = signed
BGE branch: A >= B, if !(A<B)
“Output” control signals are used to set other controls! (ex. we only want to write to PC if our branch succeeded)
Branch Comp.
A (R[rs1])
B
(R[rs2])
BrUn
BrEq
BrLT

## Slide 28: Adding Branches
+4
Add
addr
inst
IMEM
pc+4
Inst[24:20]
ALU
+
clk
Reg [ ]
Inst[19:15]
Inst[11:7]
AddrB
AddrA
DataA
DataB
AddrD
DataD
alu
Reg[rs1]
Reg[rs2]
Inst[31:0]
Control logic
RegWEn =0
ALUSel
=Add
Bsel
=1
MemRW
=Read
Asel
=1
0
1
Imm[31:0]
Imm.
Gen
Add
clk
addr
inst
IMEM
DMEM
addr
DataR
DataW
PC
Inst [31:7]
1
0
clk
WBSel =*
(*=Don’t care)
Branch
Comp
1
0
ImmSel
=B
1
0
PCSel= taken/not taken
BrUn
BrEq
BrLT
mem
wb
pc

## Slide 29: Adding Branches
+4
Add
addr
inst
IMEM
pc+4
Inst[24:20]
ALU
+
clk
Reg [ ]
Inst[19:15]
Inst[11:7]
AddrB
AddrA
DataA
DataB
AddrD
DataD
alu
Reg[rs1]
Reg[rs2]
Inst[31:0]
Control logic
RegWEn =0
ALUSel
=Add
Bsel
=1
MemRW
=Read
Asel
=1
0
1
Imm[31:0]
Imm.
Gen
Add
clk
addr
inst
IMEM
DMEM
addr
DataR
DataW
PC
Inst [31:7]
1
0
clk
WBSel =*
(*=Don’t care)
Branch
Comp
1
0
ImmSel
=B
1
0
PCSel= taken/not taken
BrUn
BrEq
BrLT
mem
wb
pc

## Slide 30: RISC-V Immediate Encoding
Instruction Encodings, inst[31:0]
32-bit immediates produced, imm[31:0]
Only bit 7 of instruction changes role in immediate between S and B
Upper bits sign-extended from
inst[31] always

## Slide 31: Class Summary
CPU design involves datapath and control logic
Typical five stages of execution
  Fetch, Decode, Execute, Memory access, Write back
We have studied datapath design for
  load instructions: lw
  store instructions: sw
  Branch instructions: sw