## Slide 1: CS 211 Computer Architecture Lecture 31: RISC-V Single Cycle Design – Performance, Multicycle design, Pipeline Datapath
Ravi Mittal
ravi.mittal@iitgoa.ac.in
Indian Institute of Technology, Goa

## Slide 2: Acknowledgements
Class Presentation, RISC-V CPU Control, Pipelinging, CS61C, Great Ideas in Computer Architecture, University of Berkeley, Morgan Rae Rechenberg
Class Presentation, CS61C, Machine Structures, University of Berkeley, Dan Garcia and Miki Lustig, 2019
Class Presentation, CS61C, Introduction to Assembly Language and RISC-V Instruction Set Architecture, University of Berkeley, Prof Krste Asanović & Randy H. Katz. http://inst.eecs.Berkeley.edu/~cs61c
Computer Organization and Design, The Hardware Software Interface, RISC-V edition, Patterson and Hennessey
Digital Design and Computer Architecture: RISC-V Edition, Harris & Harris Elsevier – Presentation.

## Slide 3: RISC-V: So far we have studied
Arithmetic operations: add, sub, addi,
How to bring data from memory to register and vice versa?
  lw, sw, lb, sb, lbu
Bit-by-bit logical instructions
  and, or, xor, andi, ori, xori
Logical Shift instructions
  sll, srl, sra, slli, srli, srai
Generating Constants
Branching Instructions: beq, bne, blt/bltu, bge/bgeu
Jumping instruction: j
Assembly level program for: if, if/else,
Function Calls
  Basics, Input arguments and Return Value
  while, for loops
The Stack
  Basics, How functions use a stack
  Stack use in non-leaf function calls
  Recursive Functions
Floating Point Numbers
Instruction Formats
Machine Instructions
Microarchitecture
  Combinational and Sequential logic
  Clock, Registers, Muxes, Adder, Subtractor, Comparator, Buses, Register file, Idealized Memory
  Timing considerations, Maximum frequency
  Single Cycle Vs Multicycle vs Pipeline
  Datapath design for R-type, and I-type Instructions: add, sub, addi, lw, sw, branch instructions
  Control Logic design for Single Cycle Datapath

## Slide 4: In this lecture, we will study
Performance of Single Cycle Datapath
Multicycle Datapath
Pipeline Concept

## Slide 5: Performance of Single Cycle Datapath

## Slide 6: Instruction Timing
IF | ID | EX | MEM | WB | Total
IMEM | Reg Read | ALU | DMEM | Reg W | 
200 ps | 100 ps | 200 ps | 200 ps | 100 ps | 800 ps
CS61C Prof Dan Garcia and Miki Lustig, Univ of California, Berkeley

## Slide 7: Instruction Timing
Maximum clock frequency
  fmax = 1/800ps = 1.25 GHz
Most blocks idle most of the time! ex. “IF” active after every 600ps
Instr | IF = 200ps | ID = 100ps | ALU = 200ps | MEM=200ps | WB = 100ps | Total
add | X | X | X |  | X | 600ps
beq | X | X | X |  |  | 500ps
jal | X | X | X |  | X | 600ps
lw | X | X | X | X | X | 800ps
sw | X | X | X | X |  | 700ps
Instruction 1
Instruction 2
ID
MEM
WB
ALU
IF
ID
MEM
WB
ALU
IF
Clk
CS61C Prof Dan Garcia and Miki Lustig, Univ of California, Berkeley

## Slide 8: Performance Measures
In our example, CPU executes instructions at 1.25 GHz
  1 instruction every 800 ps
Can we improve its performance?
  What do we mean with this statement?
  At what level?
  At task level:
    Quicker response time, so one job finishes faster?
    More jobs per unit time (e.g. web server returning pages)?
    Longer battery life?
At datapath level for Single Cycle ?
CS61C Prof Dan Garcia and Miki Lustig, Univ of California, Berkeley

## Slide 9: “Iron Law” of Processor Performance
Time = Instructions Cycles Time
Program Program * Instruction * Cycle
CS61C Prof Dan Garcia and Miki Lustig, Univ of California, Berkeley

## Slide 10: Instructions per Program
Determined by
  Task
  Algorithm, e.g. O(N2) vs O(N)
  Programming language
  Compiler
  Instruction Set Architecture (ISA)
Time = Instructions Cycles Time
Program Program * Instruction * Cycle
CS61C Prof Dan Garcia and Miki Lustig, Univ of California, Berkeley

## Slide 11: (Average) Clock cycles per Instruction, or CPI
Determined by
  ISA and processor implementation (or microarchitecture)
    E.g. for “our” single-cycle RISC-V design, CPI = 1
  Complex instructions (e.g. strcpy), CPI >> 1
    True for most CISC languages
  Superscalar processors, CPI < 1 (Will study later)
Time = Instructions Cycles Time
Program Program * Instruction * Cycle

## Slide 12: Time per Cycle (1/Frequency)
Determined by
  Processor microarchitecture (processor critical path)
  Technology (e.g. transistor size)
  Power budget (lower voltages reduce transistor speed)
Time = Instructions Cycles Time
Program Program * Instruction * Cycle

## Slide 13: Speed Trade-off Example
For some task (e.g. image compression) …
 | Processor A | Processor B
# Instructions | 1 Million | 1.5 Million
Average CPI | 2.5 | 1
Clock rate f | 2.5 GHz | 2 GHz
Execution time | 1 ms | 0.75 ms
Processor B is faster for this task, despite executing more instructions and having a lower clock rate! Why? Each instruction is less complex! (~2.5 B instructions = 1 A instruction)

## Slide 14: Trivia
If we reduce the time a program takes to execute by pipelining our CPU, which factor is likely to shrink?
Instructions per program
Cycles per instruction
Time per cycle
Time = Instructions Cycles Time
Program Program * Instruction * Cycle

## Slide 15: Trivia
If we reduce the time a program takes to execute by pipelining our CPU, which factor is likely to shrink?
Instructions per program
Cycles per instruction (This will increase!)
Time per cycle
Time = Instructions Cycles Time
Program Program * Instruction * Cycle
CS61C Prof Dan Garcia and Miki Lustig, Univ of California, Berkeley

## Slide 16: Multicycle Datapath

## Slide 17: Ways of Datapath and Control Design
There are many ways of designing the data path and control logic
Single-cycle, multi-cycle, pipelined datapath
Hardwired/combinational vs. microcoded/microprogrammed control
  Control signals generated by combinational logic versus
  Control signals stored in a memory structure
Control signals and structure depend on the datapath design

## Slide 18: Single-cycle vs. Multi-cycle: Control and Data
Single-cycle machine:
  Everything related to an instruction happens in one clock cycle
  Simple
  Cycle time limited by longest instruction (lw)
Multi-cycle machine:
  Higher clock speed
  Simpler instructions run faster
  Control signals needed in the next cycle can be generated in the current cycle
  Motivation: avoid making all instructions take as long as the slowest one
Single-cycle
Multicycle

## Slide 19: Multicycle Processor
Only one stage of instruction per clock cycle
  The clock is made as long as the slowest stage
Advantage over single cycle execution:
  Unused stages in a particular instruction can be skipped
CS61C Prof Dan Garcia and Miki Lustig, Univ of California, Berkeley

## Slide 20: Multicycle Approach
Breakup the instructions into steps,
  Each step takes a cycle
  Balance the amount of work to be done
  Restrict each cycle to use only one major functional unit
At the end of a cycle
  Store values for use in later cycles (easiest thing to do)
  Introduce additional (internal) registers

## Slide 21: Multicycle RISC-V Processor
Ref: Digital Design and Computer Architecture: RISC-V Edition, Harris & Harris Elsevier

## Slide 22: Multicycle Datapath Approach
Replace Instruction and Data memories with a single unified memory – more realistic
  In the single-cycle design, we used separate instruction and data memories because we needed to read the instruction memory and read or write the data memory all in one cycle
Use of new non-architectural state elements
  Instruction Register
  Registers to store output from Register File, ALU output
Now we can reuse functional units
  ALU used to compute address and to increment PC
  Memory used for instruction and data

## Slide 23: Multicycle RISC-V Processor – Note use of Registers
Ref: Digital Design and Computer Architecture: RISC-V Edition, Harris & Harris Elsevier

## Slide 24: Reasons for not using Multicycle Design
Benchmark - SPECINT2000 – contains approximately
25% loads, 10% stores, 11% branches, 2% jumps, and 52% R-type instructions
Average CPI = 4.14  Not much benefit
Cycle time is not exactly equal to one fifth of single cycle design
  Due to fact that not all steps are of the same length
Additional complexity compared to single cycle design
Not in use

## Slide 25: Pipeline Concept

## Slide 26: Pipeline Analogy: Doing Laundry
Mira, Nidhi, Bobby, and Ayush each have one load of clothes to wash, dry, fold, and Iron(Press)
  Washer takes 30 minutes
  Dryer takes 30 minutes
  “Folder” takes 30 minutes
  “Ironing” takes 30 minutes to iron clothes
M
N
B
A
Ref: CS61C Morgan Reschenberg, Univ of California, Berkeley
Notes: lol wash the MIPS green shirts

## Slide 27: Sequential Laundry (in Covid times)
Sequential laundry takes 8 hours for 4 loads
1 load finishes every 2 hours, and Ayush is up til 2 AM...
T
a
s
k
O
r
d
e
r
B
N
A
M
30
Time
30
30
30
30
30
30
30
30
30
30
30
30
30
30
30
6 PM
7
8
9
10
11
12
1
2 AM
Ref: CS61C Morgan Reschenberg, Univ of California, Berkeley

## Slide 28: Pipelined Laundry
T
a
s
k
O
r
d
e
r
B
N
A
M
12
2 AM
6 PM
7
8
9
10
11
1
Time
30
30
30
30
30
30
30
Pipelined laundry takes 3.5 hours for 4 loads!
1 load finishes every half hour (after the first load, which takes 2 hours)

## Slide 29: Pipelining Lessons (1/2)
Pipelining doesn’t decrease latency of single task; it increases throughput of entire workload
Multiple tasks operating simultaneously using different resources
Potential speedup ~ number of pipeline stages
Speedup reduced by time to fill and drain the pipeline: 8 hours/3.5 hours which gives 2.3X speedup vs. potential 4X in this example
6 PM
7
8
9
Time
30
30
30
30
30
30
30
B
N
A
M
T
a
s
k
O
r
d
e
r
Ref: CS61C Morgan Reschenberg, Univ of California, Berkeley

## Slide 30: Pipelining Lessons (2/2)
6 PM
7
8
9
Time
20
20
30
20
30
30
30
B
N
A
M
T
a
s
k
O
r
d
e
r
Suppose new Washer takes 20 minutes, new Iron takes 20 minutes. How much faster is pipeline?
  Pipeline rate limited by slowest pipeline stage
  Unbalanced lengths of pipeline stages reduces speedup
Ref: CS61C Morgan Reschenberg, Univ of California, Berkeley

## Slide 31: Pipelined Datapath

## Slide 32: Quick review: Circuit pipelining!
When we calculate cycle time, or critical path, we do so between state elements, inputs, and outputs.
Adding registers between circuit components decreases our critical path and increases our frequency
Ref: CS61C Morgan Reschenberg, Univ of California, Berkeley

## Slide 33: Pipelining with RISC-V
Phase | Pictogram | tstep Serial
Instruction Fetch |  | 200 ps
Reg Read |  | 100 ps
ALU |  | 200 ps
Memory |  | 200 ps
Register Write |  | 100 ps
tinstruction |  | 800 ps
add t0, t1, t2
or t3, t4, t5
sll t6, t0, t3
tcycle
instruction sequence
tinstruction
tcycle Pipelined
200 ps
200 ps
200 ps
200 ps
200 ps
1000 ps
Ref: CS61C Morgan Reschenberg, Univ of California, Berkeley
Notes: Tc = “Time between completion of instructions”

## Slide 34: Pipeline Performance
Tc - time between completion of instructions
  to measure speedup
Speedup is due to increased throughput
  Latency for each instruction does not decrease, in fact it may increase if our stages are uneven!
It takes longer for the first instruction to finish, but every instruction after finishes faster!
Ref: CS61C Morgan Reschenberg, Univ of California, Berkeley

## Slide 35: Pipeline Performance
Assume time for stages is
  100ps for register read or write
  200ps for other stages
Compare pipelined datapath with single-cycle datapath
Instr | Instr fetch | Register read | ALU op | Memory access | Register write | Total time
ld (lw) | 200ps | 100 ps | 200ps | 200ps | 100 ps | 800ps
sd (sw) | 200ps | 100 ps | 200ps | 200ps |  | 700ps
R-format | 200ps | 100 ps | 200ps |  | 100 ps | 600ps
beq | 200ps | 100 ps | 200ps |  |  | 500ps
Ref: CS61C Morgan Reschenberg, Univ of California, Berkeley

## Slide 36: Pipeline Performance
Single-cycle (Tc= 800ps)
Pipelined (Tc= 200ps)
Ref: CS61C Morgan Reschenberg, Univ of California, Berkeley

## Slide 37: Pipeline Speedup
If all stages are balanced
  i.e., all take the same time
  Time between instructionspipelined = Time between instructionsnonpipelined Number of stages
  Spedup = Number of stages in the pipeline
If not balanced, speedup is less
Speedup due to increased throughput
  Latency (time for each instruction) does not decrease
Ref: CS61C Morgan Reschenberg, Univ of California, Berkeley

## Slide 38: Lecture Summary
Multicycle Datapath – Not in use
Single cycle Datapath – Too inefficient - Not in use
Pipelining improves performance by exploiting Instruction Level Parallelism
  5-stage pipeline for RV32I: IF, ID, EX, MEM, WB
  Executes multiple instructions in parallel
  Each instruction has the same latency, but there’s better throughput
  Think: what problems does pipelining introduce?