## Slide 1: CS 211 Computer Architecture Lecture 32: Multicycle Datapath: Pipelining – 2 Pipelined Datapath, Structural Hazard
Ravi Mittal
ravi.mittal@iitgoa.ac.in
Indian Institute of Technology, Goa

## Slide 2: Acknowledgements
Class Presentation, RISC-V CPU Control, Pipelinging, CS61C, Great Ideas in Computer Architecture, University of Berkeley, Morgan Rae Rechenberg
Class Presentation, CS61C, Machine Structures, University of Berkeley, Dan Garcia and Miki Lustig, 2019
Class Presentation, CS61C, Introduction to Assembly Language and RISC-V Instruction Set Architecture, University of Berkeley, Prof Krste Asanović & Randy H. Katz. http://inst.eecs.Berkeley.edu/~cs61c
Computer Organization and Design, The Hardware Software Interface, RISC-V edition, Patterson and Hennessey
Digital Design and Computer Architecture: RISC-V Edition, Harris & Harris Elsevier – Presentation.

## Slide 3: In this lecture we will study
RISC-V Pipeline
Hazard
Structural Hazard

## Slide 4: In the last class, we studied Pipelined Datapath – Concept

## Slide 5: Quick review: Circuit pipelining!
When we calculate cycle time, or critical path, we do so between state elements, inputs, and outputs.
Adding registers between circuit components decreases our critical path and increases our frequency
Ref: CS61C Morgan Reschenberg, Univ of California, Berkeley

## Slide 6: Pipelining with RISC-V
Phase | Pictogram | tstep Serial
Instruction Fetch |  | 200 ps
Reg Read |  | 100 ps
ALU |  | 200 ps
Memory |  | 200 ps
Register Write |  | 100 ps
tinstruction |  | 800 ps
add t0, t1, t2
or t3, t4, t5
sll t6, t0, t3
tcycle
instruction sequence
tinstruction
tcycle Pipelined
200 ps
200 ps
200 ps
200 ps
200 ps
1000 ps
Ref: CS61C Morgan Reschenberg, Univ of California, Berkeley
Notes: Tc = “Time between completion of instructions”

## Slide 7: Pipeline Performance
Tc - time between completion of instructions
  to measure speedup
Speedup is due to increased throughput
  Latency for each instruction does not decrease, in fact it may increase if our stages are uneven!
It takes longer for the first instruction to finish, but every instruction after finishes faster!
Ref: CS61C Morgan Reschenberg, Univ of California, Berkeley

## Slide 8: Pipeline Performance
Assume time for stages is
  100ps for register read or write
  200ps for other stages
Compare pipelined datapath with single-cycle datapath
Instr | Instr fetch | Register read | ALU op | Memory access | Register write | Total time
ld (lw) | 200ps | 100 ps | 200ps | 200ps | 100 ps | 800ps
sd (sw) | 200ps | 100 ps | 200ps | 200ps |  | 700ps
R-format | 200ps | 100 ps | 200ps |  | 100 ps | 600ps
beq | 200ps | 100 ps | 200ps |  |  | 500ps
Ref: CS61C Morgan Reschenberg, Univ of California, Berkeley

## Slide 9: Pipeline Performance
Single-cycle (Tc= 800ps)
Pipelined (Tc= 200ps)
Ref: CS61C Morgan Reschenberg, Univ of California, Berkeley

## Slide 10: Pipeline Speedup
If all stages are balanced
  i.e., all take the same time
  Time between instructionspipelined = Time between instructionsnonpipelined Number of stages
If not balanced, speedup is less
Speedup due to increased throughput
  Latency (time for each instruction) does not decrease
Ref: CS61C Morgan Reschenberg, Univ of California, Berkeley

## Slide 11: RISC-V Pipeline

## Slide 12: Pipelining with RISC-V
add t0, t1, t2
or t3, t4, t5
sll t6, t0, t3
tcycle
instruction sequence
tinstruction
 | Single Cycle | Pipelining
Timing | tstep = 100 … 200 ps | tcycle = 200 ps
 | Register access only 100 ps | All cycles same length
Instruction time, tinstruction | = tcycle = 800 ps | 1000 ps
Clock rate, fs | 1/800 ps = 1.25 GHz | 1/200 ps = 5 GHz
Relative speed | 1 x | 4 x
Ref: CS61C Morgan Reschenberg, Univ of California, Berkeley
Notes: Tc = “Time between completion of instructions”

## Slide 13: Sequential vs Simultaneous
add t0, t1, t2
or t3, t4, t5
sll t6, t0, t3
tcycle
= 200 ps
instruction sequence
tinstruction = 1000 ps
sw t0, 4(t3)
lw t0, 8(t3)
addi t2, t2, 1
What happens sequentially, what happens simultaneously?
Ref: CS61C Morgan Reschenberg, Univ of California, Berkeley
Notes: Tc = “Time between completion of instructions”

## Slide 14: Instruction Level Parallelism (ILP)
Pipelining allows us to execute parts of multiple instructions at the same time using the same hardware!
  This is known as instruction level parallelism
Ref: CS61C Morgan Reschenberg, Univ of California, Berkeley

## Slide 15: Sequential vs Simultaneous
add t0, t1, t2
or t3, t4, t5
sll t6, t0, t3
tcycle
= 200 ps
instruction sequence
tinstruction = 1000 ps
sw t0, 4(t3)
lw t0, 8(t3)
addi t2, t2, 1
What happens sequentially, what happens simultaneously?
Notes: Tc = “Time between completion of instructions”

## Slide 16: RISC-V Pipeline
add t0, t1, t2
or t3, t4, t5
slt t6, t0, t3
tcycle
= 200 ps
instruction sequence
tinstruction = 1000 ps
sw t0, 4(t3)
lw t0, 8(t3)
addi t2, t2, 1
Resource use by instruction over time
Resource use in a particular time slot
Ref: CS61C Morgan Reschenberg, Univ of California, Berkeley

## Slide 17: Single-Cycle RISC-V RV32I Datapath
IMEM
ALU
Imm.
Gen
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
0
1
2
1
0
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
pc+4
alu
mem
wb
alu
pc+4
Reg[rs1]
pc
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel
RegWEn
BrUn
BrEq
BrLT
ASel
BSel
ALUSel
MemRW
WBSel
PCSel
wb
Ref: CS61C Morgan Reschenberg, Univ of California, Berkeley

## Slide 18: Single-Cycle RISC-V RV32I Datapath
Ref: CS61C Morgan Reschenberg, Univ of California, Berkeley

## Slide 19: Pipeline Registers
Need registers between stages
  To hold information produced in the previous cycle
Ref: CS61C Morgan Reschenberg, Univ of California, Berkeley

## Slide 20: Pipelining RISC-V RV32I Datapath
IMEM
ALU
Imm.
Gen
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
0
1
2
1
0
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
pc+4
alu
mem
wb
alu
pc+4
Reg[rs1]
pc
imm[31:0]
Reg[rs2]
wb
Instruction Fetch
(F)
Instruction Decode/Register Read
(D)
ALU Execute
(X)
Memory Access
(M)
Write Back
(W)
NOTE: Control signals are also pipelined!
Ref: CS61C Morgan Reschenberg, Univ of California, Berkeley

## Slide 21: Pipelined RISC-V RV32I Datapath
IMEM
ALU
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
aluX
pcF+4
+4
pcD
pcF
pcX
pcM
instD
instX
rs1X
rs2X
aluM
rs2M
immX
Imm.
Recalculate PC+4 in M stage to avoid sending both PC and PC+4 down pipeline
instM
instW
Must pipeline instruction along with data, so control operates correctly in each stage
Ref: CS61C Morgan Reschenberg, Univ of California, Berkeley
Recall that PC+4 value is required in jal, jalr instructions

## Slide 22: Each stage operates on different instruction
IMEM
ALU
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
aluX
pcF+4
+4
pcD
pcF
pcX
pcM
instD
instX
rs1X
rs2X
aluM
rs2M
immX
Imm.
instM
instW
add t0, t1, t2
or t3, t4, t5
slt t6, t0, t3
sw t0, 4(t3)
lw t0, 8(t3)
Pipeline registers separate stages, hold data for each instruction in flight
Ref: CS61C Morgan Reschenberg, Univ of California, Berkeley

## Slide 23: Pipelined Control
Control signals derived from instruction (as in single cycle implementation)
  Information is stored in pipeline registers for use by later stages
Ref: CS61C Morgan Reschenberg, Univ of California, Berkeley

## Slide 24: Trivia
Assume the stage times shown below. Suppose we remove loads and stores from our ISA. Consider going from a single-cycle implementation to a 4-stage pipelined
Instr Fetch | Reg Read | ALU Op | Mem Access | Reg Write
200ps | 100 ps | 200ps | 200ps | 100 ps
What is throughput speedup?
What is the latency (instruction level)?
Ref: CS61C Morgan Reschenberg, Univ of California, Berkeley

## Slide 25: Trivia
Assume the stage times shown below. Suppose we remove loads and stores from our ISA. Consider going from a single-cycle implementation to a 4-stage pipelined
Instr Fetch | Reg Read | ALU Op | Mem Access | Reg Write
200ps | 100 ps | 200ps | 200ps | 100 ps
  Note that there is no memory access
  Throughput Speedup:
    Single Cycle: (IF+ID+EX+WB) = 600 ps
    Pipeline: (4*max_stage)/4 = 200 ps
    old/new = 600/200 = 3x faster
Ref: CS61C Morgan Reschenberg, Univ of California, Berkeley

## Slide 26: Trivia
Assume the stage times shown below. Suppose we remove loads and stores from our ISA. Consider going from a single-cycle implementation to a 4-stage pipelined
Instr Fetch | Reg Read | ALU Op | Mem Access | Reg Write
200ps | 100 ps | 200ps | 200ps | 100 ps
Single Cycle Instruction latency:
  IF+ID+EX+WB = 600 ps
Pipelined Instruction latency:
  4*max_stage = 800ps
Latency speedup = 800/600 = 1.33 x slower
Ref: CS61C Morgan Reschenberg, Univ of California, Berkeley

## Slide 27: Hazards

## Slide 28: Pipelining Hazards
A hazard is a situation that prevents starting the next instruction in the next clock cycle
Structural hazard
  A required resource is busy (e.g. needed in multiple stages)
Data hazard
  Data dependency between instructions
  Need to wait for previous instruction to complete its data read/write
Control hazard
  Flow of execution depends on previous instruction
Ref: CS61C Morgan Reschenberg, Univ of California, Berkeley

## Slide 29: Structural Hazard

## Slide 30: Structural Hazard
Problem: Two or more instructions in the pipeline compete for access to a single physical resource
Solution 1: Instructions take it in turns to use resource, some instructions have to stall
Solution 2: Add more hardware to machine
Can always solve a structural hazard by adding more hardware
Ref: CS61C Morgan Reschenberg, Univ of California, Berkeley

## Slide 31: Structural Hazard: Regfile!
I
n
s
t
r
O
r
d
e
r
Load
Add
Store
Sub
Or
Time (clock cycles)
RegFile: Used in ID and WB!
Ref: CS61C Morgan Reschenberg, Univ of California, Berkeley

## Slide 32: Regfile Structural Hazards
Each instruction:
  can read up to two operands in decode stage
  can write one value in writeback stage
Avoid structural hazard by having separate “ports”
  two independent read ports and one independent write port
Three accesses per cycle can happen simultaneously
Clk
portW
Write Enable
32
32
portA
32
portB
5
5
5
RW
RA
RB
32 x 32-bit
Registers
Ref: CS61C Morgan Reschenberg, Univ of California, Berkeley

## Slide 33: Structural Hazard: Memory Access
add t0, t1, t2
lw t0, 8(t3)
slt t6, t0, t3
instruction sequence
sw t0, 4(t3)
add t0, t1, t2
Instruction and data memory used simultaneously
  Use two separate memories
Single memory module would have caused Structural Hazard
Ref: CS61C Morgan Reschenberg, Univ of California, Berkeley

## Slide 34: Instruction and Data Caches
Processor
Control
Datapath
PC
Registers
Arithmetic & Logic Unit
(ALU)
Memory (DRAM)
Bytes
Program
Data
Instruction Cache
Data
Cache
Caches: small and fast “buffer” memories
Ref: CS61C Morgan Reschenberg, Univ of California, Berkeley
Fast on-chip memory, separate for Instructions and Data

## Slide 35: Structural Hazards – Summary
Conflict for use of a resource
In RISC-V pipeline with a single memory
  Load/store requires data access
  Without separate memories, instruction fetch would have to stall for that cycle
    All other operations in pipeline would have to wait
Pipelined datapaths require separate instruction/data memories
  Or separate instruction/data caches
RISC-V is designed to avoid structural hazards
  e.g. at most one memory access/instruction

## Slide 36: Lecture Summary
Pipelining is very useful concept
  It increases throughput
  Significant speedup is achieved compared to Single Cycle Design
  Each component in Datapath is efficiently utilized
Designing pipeline datapath is not straightforward – just by putting registers between stages
Instructions may use a component in a stage at the same time – resulting in structural hazard
In complex architectures, Structural hazards can be resolved by
  Stalling instructions
  Using extra hardware – Preferred method