## Slide 1: CS211 Computer Architecture Lecture 33: Pipeline Datapath- Data Hazard
Ravi Mittal
ravi.mittal@iitgoa.ac.in
Indian Institute of Technology, Goa

## Slide 2: Acknowledgements
Class Presentation, RISC-V CPU Control, Pipelining, CS61C, Great Ideas in Computer Architecture, University of Berkeley, Morgan Rae Rechenberg
Book: Digital Design and Computer Architecture: RISC-V Edition, Harris & Harris Elsevier
Class Presentation, CS61C, Machine Structures, University of Berkeley, Dan Garcia and Miki Lustig, 2019
Class Presentation, CS61C, Introduction to Assembly Language and RISC-V Instruction Set Architecture, University of Berkeley, Prof Krste Asanović & Randy H. Katz. http://inst.eecs.Berkeley.edu/~cs61c
Computer Organization and Design, The Hardware Software Interface, RISC-V edition, Patterson and Hennessey

## Slide 3: Last Class

## Slide 4: Pipelining Hazards
A hazard is a situation that prevents starting the next instruction in the next clock cycle
Structural hazard (Resource Dependence)
  A required resource is busy (e.g. needed in multiple stages)
Data hazard (Data Dependence)
  Data dependency between instructions
  Need to wait for previous instruction to complete its data read/write
Control hazard
  Flow of execution depends on previous instruction

## Slide 5: Structural Hazard: Regfile!
I
n
s
t
r
O
r
d
e
r
Load
Add
Store
Sub
Or
Time (clock cycles)
RegFile: Used in ID and WB!

## Slide 6: Regfile Structural Hazards
Each instruction:
  can read up to two operands in decode stage
  can write one value in writeback stage
Avoid structural hazard by having separate “ports”
  two independent read ports and one independent write port
Three accesses per cycle can happen simultaneously
Clk
portW
Write Enable
32
32
portA
32
portB
5
5
5
RW
RA
RB
32 x 32-bit
Registers
Ref: CS61C Morgan Reschenberg, Univ of California, Berkeley

## Slide 7: Instruction and Data Caches
Processor
Control
Datapath
PC
Registers
Arithmetic & Logic Unit
(ALU)
Memory (DRAM)
Bytes
Program
Data
Instruction Cache
Data
Cache
Caches: small and fast “buffer” memories
Ref: CS61C Morgan Reschenberg, Univ of California, Berkeley

## Slide 8: Structural Hazards – Summary
Conflict for use of a resource
In RISC-V pipeline with a single memory
  Load/store requires data access
  Without separate memories, instruction fetch would have to stall for that cycle
    All other operations in pipeline would have to wait
Pipelined datapaths require separate instruction/data memories
  Or separate instruction/data caches
RISC-V is designed to avoid structural hazards
  e.g. at most one memory access/instruction
Ref: CS61C Morgan Reschenberg, Univ of California, Berkeley

## Slide 9: In this class we will study
Data Hazard in R-type Instructions
  Data Hazard Solutions: Nop, Forwarding
Data Hazard in Loads
  Data Hazard Solutions: Stalling Pipeline, Rearranging instructions

## Slide 10: Data Hazard in R-type Instructions

## Slide 11: Data Hazards
Consider the following sequence of instructions:
add t0, t1, t2
sub t4, t0, t3
and t5, t0, t6
or t7, t0, t8
xor t9, t0, t10
Stored
during WB
Read during ID
Ref: CS61C Morgan Reschenberg, Univ of California, Berkeley

## Slide 12: Data Hazards
sub t4, t0, t3
and t5, t0, t6
or t7, t0, t8
xor t9, t0, t10
add t0, t1, t2
Time (clock cycles)
Only an issue if no double pumping – Write during the first half and read during the second half
Identifying data hazards:
Where is data WRITTEN?
Where is data READ?
Does the WRITE happen AFTER the READ?
Ref: CS61C Morgan Reschenberg, Univ of California, Berkeley

## Slide 13: Data Hazards
sub t4, t0, t3
and t5, t0, t6
or t7, t0, t8
xor t9, t0, t10
add t0, t1, t2
Time (clock cycles)
Only an issue if no double pumping – Write during the first half and read during the second half
Without some fix, sub and and will calculate wrong result!
Ref: CS61C Morgan Reschenberg, Univ of California, Berkeley

## Slide 14: Solution 1: Stalling
Problem: Instruction depends on result from previous instruction
  add t0, t1, t2 sub t4, t0, t3
Bubble:
  effectively NOP: affected pipeline stages do “nothing” (add x0 x0 x0)
  Insert NOP at compile time  compilers need to know about pipeline
Ref: CS61C Morgan Reschenberg, Univ of California, Berkeley

## Slide 15: Nops and Performance
A software solution would be to require the programmer or compiler to insert nop instructions between instructions
The software interlocks, nops, complicates programming and degrades performance
Not an ideal solution

## Slide 16: Data Hazard Solution 2: Forwarding
Forward result as soon as it is available, even though it’s not stored in RegFile yet
sub t4, t0, t3
and t5, t0, t6
or t7, t0, t8
xor t9, t0, t10
add t0, t1, t2
Forwarding: grab operand from pipeline stage, rather than register file
Ref: CS61C Morgan Reschenberg, Univ of California, Berkeley

## Slide 17: Forwarding (aka Bypassing)
Use result when it is computed
  Don’t wait for it to be stored in a register
  Requires extra hardware in the datapath (and extra control!)
Ref: CS61C Morgan Reschenberg, Univ of California, Berkeley

## Slide 18: Detect Need for Forwarding (example)
add t0, t1, t2
or t3, t0, t5
sub t6, t0, t3
X
M
W
D
instX.rd
instD.rs1
Compare destination of older instructions in pipeline with sources of new instruction in decode stage.
Must ignore writes to x0
Ref: CS61C Morgan Reschenberg, Univ of California, Berkeley

## Slide 19: Forwarding Path
IMEM
ALU
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
aluX
pcF+4
+4
pcD
pcF
pcX
pcM
instD
instX
rs1X
rs2X
aluM
rs2M
immX
Imm.
instM
instW
Forwarding Control Logic
Ref: CS61C Morgan Reschenberg, Univ of California, Berkeley

## Slide 20: Data Hazard in Loads

## Slide 21: Data Hazard: Loads
Recall: Dataflow backwards in time are hazards
Can’t solve all cases with forwarding
  Must stall instruction dependent on load (sub), then forward after the load is done (more hardware)
sub t3, t0, t2
lw t0, 0(t1)
Ref: CS61C Morgan Reschenberg, Univ of California, Berkeley

## Slide 22: Data Hazard: Loads – Sol 1: Stalling
Hardware stalls pipeline
  Called “hardware interlock”
  Holding up the operation until data is available
This is what happens in hardware in a “hardware interlock”
sub t3, t0, t2
and t5, t0, t4
or t7, t0, t6
lw t0, 0(t1)
bubble
bubble
bubble
Ref: CS61C Morgan Reschenberg, Univ of California, Berkeley

## Slide 23: Data Hazard: Loads
Stalling the sub instruction after Decoding operation (before register read). Instruction add should remain in Fetch stage during both cycles.. And so on
Use forwarding
Double pumping
sub t3, t0, t2
and t5, t0, t4
or t7, t0, t6
lw t0, 0(t1)
bubble
bubble
bubble
Ref: CS61C Morgan Reschenberg, Univ of California, Berkeley

## Slide 24: Stalling Hardware
Book: Harris and Harris

## Slide 25: Stalling – Another example (self reading)
Book: Harris and Harris

## Slide 26: Stalling – Another example (self reading)
Book: Harris and Harris

## Slide 27: Data Hazard Loads: Soln 2 Rearrange Instructions
Move independent useful instructions forward
If there are instructions that are not data dependent on the current instruction, these can be moved up next to the current instruction
This will insure that there is no stalls
The number of independent instructions to be inserted (moved up) depends on when the data is becoming available (due to dependency)
Care must be taken in moving instruction forward (moving up).
Ref: CS61C Morgan Reschenberg, Univ of California, Berkeley

## Slide 28: Code Scheduling to Avoid Stalls
Reorder code to avoid use of load result in the next instruction!
RISC-V code for D=A+B; E=A+C;
Original Order:
lw t1, 0(t0)
lw t2, 4(t0)
add t3, t1, t2
sw t3, 12(t0)
lw t4, 8(t0)
add t5, t1, t4
sw t5, 16(t0)
Alternative:
lw t1, 0(t0)
lw t2, 4(t0)
lw t4, 8(t0)
add t3, t1, t2
sw t3, 12(t0)
add t5, t1, t4
sw t5, 16(t0)
Stall!
Stall!
13 cycles
11 cycles
Ref: CS61C Morgan Reschenberg, Univ of California, Berkeley
Uses forwarding also

## Slide 29: Quiz 1
For the code sequences below, choose one of the statements below:
  addi $t1,$t0,1
  addi $t2,$t0,2
  addi $t3,$t0,2
  addi $t3,$t0,4
  addi $t5,$t1,5
No stalls as is
No stalls with forwarding
Must Stall
Ref: CS61C Morgan Reschenberg, Univ of California, Berkeley

## Slide 30: Quiz 1
For the code sequences below, choose one of the statements below:
  addi $t1,$t0,1
  addi $t2,$t0,2
  addi $t3,$t0,2
  addi $t3,$t0,4
  addi $t5,$t1,5
No stalls as is
No stalls with forwarding
Must Stall
Ref: CS61C Morgan Reschenberg, Univ of California, Berkeley

## Slide 31: Quiz 2
For the code sequences below, choose one of the statements below:
  add $t1,$t0,$t0
  addi $t2,$t0,5
  addi $t4,$t1,5
No stalls as is
No stalls with forwarding
Must Stall
Ref: CS61C Morgan Reschenberg, Univ of California, Berkeley

## Slide 32: Quiz 2
For the code sequences below, choose one of the statements below:
  add $t1,$t0,$t0
  addi $t2,$t0,5
  addi $t4,$t1,5
No stalls as is
No stalls with forwarding
Must Stall
Ref: CS61C Morgan Reschenberg, Univ of California, Berkeley

## Slide 33: Quiz 3
For the code sequences below, choose one of the statements below:
  lw $t0,0($t0)
  add $t1,$t0,$t0
No stalls as is
No stalls with forwarding
Must Stall
Ref: CS61C Morgan Reschenberg, Univ of California, Berkeley

## Slide 34: Quiz 3
For the code sequences below, choose one of the statements below:
  lw $t0,0($t0)
  add $t1,$t0,$t0
No stalls as is
No stalls with forwarding
Must Stall
Ref: CS61C Morgan Reschenberg, Univ of California, Berkeley

## Slide 35: Class Summary
Hazards potentially limit performance
Data Hazard are due to data dependency
There are multiple ways to handle data dependency
  Insert NOPS – Software driven – complicated
  Data Forwarding
  Stall the pipeline – when data dependency can’t be resolved by compiler and other methods – Hardware driven
  Rearrange Instructions (forward independent instructions – that have no data dependency) – Compiler driven