## Slide 1: CS 211 Computer Architecture Lecture 34: RISC-V Pipeline Control Hazard; How to exploit parallelism?
Ravi Mittal
ravi.mittal@iitgoa.ac.in
Indian Institute of Technology, Goa

## Slide 2: Acknowledgements
Class Presentation, RISC-V CPU Control, Pipelining, CS61C, Great Ideas in Computer Architecture, University of Berkeley, Morgan Rae Rechenberg
Book: Digital Design and Computer Architecture: RISC-V Edition, Harris & Harris Elsevier
Prof Mutlu’s class presentation, ETH, Spring 2121

## Slide 3: Last Class

## Slide 4: An Ideal Pipeline
Repetition of identical operations
  The same operation is repeated on a large number of different inputs (e.g., all laundry loads go through the same steps)
Repetition of independent operations
  No dependencies between repeated operations
Uniformly partitionable suboperations that don’t share resources
Fitting examples: automobile assembly line, doing laundry, Buffet line where each counter-server takes the same time
  What about the instruction processing “cycle”?
Ref: Prof Mutlu’s Class Presentation

## Slide 5: Instruction Pipeline: Not An Ideal Pipeline
Identical operations ... NOT!
 different instructions  not all need the same stages
    Forcing different instructions to go through the same pipe stages
     external fragmentation (some pipe stages idle for some instructions)
Uniform suboperations ... NOT!
 different pipeline stages  not the same latency
Need to force each stage to be controlled by the same clock
     internal fragmentation (some pipe stages are too fast but all take the same clock cycle time)
Independent operations ... NOT!
 instructions are not independent of each other
    Need to detect and resolve inter-instruction dependencies to ensure the pipeline provides correct results
     pipeline stalls (pipeline is not always moving)
Ref: Prof Mutlu’s Class Presentation

## Slide 6: Pipelining Hazards
A hazard is a situation that prevents starting the next instruction in the next clock cycle
Structural hazard
  A required resource is busy (e.g. needed in multiple stages)
Data hazard
  Data dependency between instructions
  Need to wait for previous instruction to complete its data read/write
Control hazard
  Flow of execution depends on previous instruction

## Slide 7: Handling Data Hazard
How do we ensure that our programs run correctly?
Insert nops in code at compile time
Rearrange code at compile time
Forward data at run time
Stall the processor at run time
Hardware stalling requires all stages before stalled stage to be stalled and stages after stalled stage to work normal
  In Buffet line, suddenly a person stops you (as some dishes are running low), but people ahead of you keep on moving

## Slide 8: In this class we will study
Control Hazard – Introduction
Control Hazard – Branch Prediction
Superscalar processors
How to exploit parallelism?

## Slide 9: Control Hazard – Branch Instruction

## Slide 10: Control Dependence
Question: What should the fetch PC be in the next cycle?
Answer: The address of the next instruction
If the fetched instruction is a non-control-flow instruction:
  Next Fetch PC is the address of the next-sequential instruction
  Easy to determine if we know the size of the fetched instruction
If the instruction that is fetched is a control-flow instruction (branch instructions):
  How do we determine the next Fetch PC?

## Slide 11: Control Hazards
Branch (beq, bne,...) determines flow of control
  Fetching next instruction depends on branch outcome
  Pipeline can’t always fetch correct instruction
    Result isn’t known until end of execute
Simple Solution: Stall on every branch instruction until we have the new PC value
  How long must we stall?
Ref: CS61C Morgan Reschenberg, Univ of California, Berkeley

## Slide 12: Quiz 1
How many instructions after beq are affected by the control hazard?
1
2
3
4
5
beq
Instr 1
Instr 2
Instr 3
Instr 4
Ref: CS61C Morgan Reschenberg, Univ of California, Berkeley

## Slide 13: Quiz 1
How many instructions after beq are affected by the control hazard?
1
2
3
4
5
beq
Instr 1
Instr 2
Instr 3
Instr 4

## Slide 14: Quiz 2: Branch Stall
How many bubbles required for branch?
1
2
3
4
5
beq
Instr 1
Instr 2
Instr 3
Instr 4
Time (clock cycles)
Ref: CS61C Morgan Reschenberg, Univ of California, Berkeley

## Slide 15: Quiz 2: Branch Stall
How many bubbles required for branch?
1
2
3
4
5
beq
Instr 1
Instr 2
Instr 3
Instr 4
Time (clock cycles)
Ref: CS61C Morgan Reschenberg, Univ of California, Berkeley

## Slide 16: Control Hazard – Branch Prediction

## Slide 17: Control Hazard: Branch Prediction
Guess the outcome of a branch, fix afterwards if necessary
  Must cancel (flush) all instructions in pipeline that depended on guess that was wrong
  How many instructions do we end up flushing?
Backward branches are usually taken (loops)
Consider the history of whether the branch was previously taken – to improve the prediction
Good prediction reduces fraction of branches requiring a flush
Modern branch predictors have high accuracy
  > 95%
  It can reduce branch penalties significantly

## Slide 18: Kill Instructions after Branch if Taken
beq t0, t1, label
sub t2, s0, t5
or t6, s0, t3
label: xxxxxx
PC updated reflecting branch outcome
Taken branch
Flush out this instruction
Flush out this instruction
Two instructions are affected by an incorrect branch.
Extra hardware is needed to incorporate “Flushing out” logic
Ref: CS61C Morgan Reschenberg, Univ of California, Berkeley

## Slide 19: Branch Prediction
beq t0, t1, label
label: …..
…..
Taken branch
Guess next PC!
Check guess correct
In the correct case, we don’t have any stalls/NOP’s at all!
Prediction, if done correctly, is better on average than stalling
Ref: CS61C Morgan Reschenberg, Univ of California, Berkeley

## Slide 20: Branch Prediction
Ideal pipelined processor: CPI = 1
Branch mis-prediction increases CPI
Static branch prediction:
  Check direction of branch (forward or backward)
  If backward, predict taken
  Else, predict not taken
Dynamic branch prediction:
  Keep history of last several hundred (or thousand) branches in branch table
    Branch destination
    Whether branch was taken
  To execute a branch
    Check table and predict the same outcome for next fetch
    If wrong, flush pipeline and flip prediction

## Slide 21: Static Branch Prediction
Compiler determines whether branch is likely to be taken or likely to be not taken
Decision is based on analysis or profile information
  90% of backward-going branches are taken
  50% of forward-going branches are not taken
How does the compiler inform this decision ?

## Slide 22: Dynamic Branch Prediction
Monitor branch behavior and learn
  Key assumption: past behavior indicative of future behavior
Learning based on past behavior (learned history)
Predict
  Outcome: taken or not taken
  Target: address of instruction to branch to
Check actual outcome and update the history
Squash incorrectly fetched instructions
Temporal correlation (Time)
  If I tell you that a certain branch was taken last time, does this help?
  The way a branch resolves may be a good predictor of the way it will resolve at the next execution

## Slide 23: One bit branch predictor
Remembers whether branch was taken the last time and does the same thing

## Slide 24: 2-Bit Predictor
Only change prediction on two successive mispredictions

## Slide 25: Superscalar Processors

## Slide 26: Increasing Processor Performance
Clock rate
  Limited by technology and power dissipation
Pipelining
  “Overlap” instruction execution
  Deeper pipeline: 5 => 10 => 15 stages
    Less work per stage → shorter clock cycle
    But more potential for hazards (CPI > 1)
Multi-issue ”super-scalar” processor
  Multiple execution units (ALUs)
    Several instructions executed simultaneously
    CPI < 1 (ideally)
Ref: CS61C Morgan Reschenberg, Univ of California, Berkeley

## Slide 27: Superscalar Execution
Idea: Fetch, decode, execute, retire multiple instructions per cycle
  N-wide superscalar  N instructions per cycle
A superscalar processor issues several instructions at a time each of which operates on a single piece of data
Need to add the hardware resources for doing so
Hardware performs the dependence checking between concurrently-fetched instructions
Ref: Prof Mutulu’s lecture

## Slide 28: Superscalar Architecture
Multiple copies of datapath: Can fetch/decode/execute multiple instructions per cycle
Two way superscalar processor fetches and executes two instructions per cycle
Book: Harris and Harris

## Slide 29: In-Order Superscalar Performance Example
Ideal IPC = 2
Actual IPC = 2 (6 instructions issued in 3 cycles)
Book: Harris and Harris

## Slide 30: Superscalar performance with dependencies
Ideal IPC = 2
Actual IPC = 1.2 (6 instructions issued in 5 cycles)

## Slide 31: Superscalar Execution Tradeoffs
Advantages
  Higher IPC (instructions per cycle)
Disadvantages
  Higher complexity for dependency checking
    Require checking within a pipeline stage
    Renaming becomes more complex in an Out of Order processor
  More hardware resources needed
Commercial processors may be three-, four-, or even six-way superscalar
They must handle control hazards such as branches as well as data hazards
real programs have many dependencies, so wide superscalar processors rarely fully utilize all of the execution units
Book: Harris and Harris

## Slide 32: Exploit Parallelism

## Slide 33: But what if we want to improve general computing?
Exploit Parallelism!

## Slide 34: Parallelism Analogy
I want to peel 100 potatoes as fast as possible:
I can learn to peel potatoes faster
OR
I can get 99 friends to help me
Any time one result doesn’t depend on another, doing the task in parallel can be a big win

## Slide 35: Types of Parallelism
Instruction-Level Parallelism (ILP)  Already studied
  Execute independent instructions from one instruction stream in parallel (pipelining, superscalar, VLIW)
Thread-Level Parallelism (TLP)
  Execute independent instruction streams in parallel (multithreading, multiple cores)
Data-Level Parallelism (DLP)
  Execute multiple operations of the same type in parallel (vector/SIMD execution)

## Slide 36: Lecture Summary
Hazards reduce effectiveness of pipelining
Control Hazards
  Address of next instruction uncertain/unknown
Control Hazards are handled effectively by dynamic branch prediction
Superscalar processors use multiple execution units for additional instruction level parallelism
  Performance benefit highly code dependent