## Slide 1: CS 211 Computer Architecture Lecture 35: Memory Hierarchy and Cache Memory
Ravi Mittal
ravi.mittal@iitgoa.ac.in
Indian Institute of Technology, Goa

## Slide 2: References and Acknowledgements
Krste Asanović & Randy H. Katz, CS 61C: Great Ideas in Computer Architecture (Machine Structures), http://inst.eecs.berkeley.edu/~cs61c/
Chapter 6, Memory Hierarchy, Book: Computer Systems: A programmer’s perspective, Randal E. Bryant and David R. O’Hallaron
MIT Course 6.004 Computation Structures, Spring 2020, Lecture on Cache
Book: Digital Design and Computer Architecture: RISC-V Edition, Harris & Harris Elsevier

## Slide 3: Review

## Slide 4
Ref: Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 5: Great Idea: Principle of Locality/Memory Hierarchy
Ref: Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 6: In this class we will study
Cache Memory Concept
Principle of Locality
Memory Hierarchy to Exploit locality
Memory Access using Cache

## Slide 7: Kilo, Mega, Giga, Tera, Peta, Exa, Zetta, Yotta
Common use prefixes (all SI, except K [= k in SI])
Confusing! Common usage of “kilobyte” means 1024 bytes, but the “correct” SI value is 1000 bytes
Hard Disk manufacturers & Telecommunications are the only computing groups that use SI factors
What is advertised as a 1 TB drive actually holds about 90% of what you expect
A 1 Mbit/s connection transfers 106 bits per second

## Slide 8: Kilo, Mega, Giga, Tera, Peta, Exa, Zetta, Yotta

## Slide 9: Kilo, Mega, Giga, Tera, Peta, Exa, Zetta, Yotta
International Electrotechnical Commission (IEC) in 1999 introduced these to specify binary quantities
Names come from shortened versions of the original SI prefixes (same pronunciation) and bi is short for “binary”, but pronounced “bee” :-(
Now SI prefixes only have their base-10 meaning and never have a base-2 meaning

## Slide 10: Cache Memory - Concept

## Slide 11: Memory Performance
Memory Speed ?
  Latency
  Throughput
Latency
  Latency is the time to access the first byte of information
Throughput
  The number of bytes per second that can be delivered
Ideally memories should have low latency and high throughput

## Slide 12: Storage in a Computer
Processor
  Holds data in register files (~ 100 Bytes)
  Registers accessed on sub-nanosecond timescale
Memory (“main memory”)
  Significantly more capacity than registers (~ GiB) – say 8 GiB
  Access time ~ 50-100 ns
  DRAM memory is 10-100 times slower than processor – in terms of speed (execution time for processor vs access time for the Main Memory)
  DRAM throughput is good: 30
Hundreds of clock cycles per memory access
  Would CPU wait for so long (say 500 cycles) to get data from memory?
  It will be very slow computation

## Slide 13: Processor-Memory Speed Gap
“Moore’s Law”
Processor-Memory
Performance Gap (grows 50%/year)
1989 first Intel CPU with cache on chip
1998 Pentium III has two cache levels on chip
µProc
55%/year
(2X/1.5yr)
DRAM Speed
7%/year
(2X/10yrs)
Ref: Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 14: Processor-Memory Speed
DRAM could keep up with processors in the 1970s
By early 80’s memories become way too slow compared to processors
2005 -2010: Multicore systems further worsen the gap between processor and memory speeds

## Slide 15
Ref: Krste Asanović & Randy H. Katz, Univ of California, Berkeley
DRAM

## Slide 16: Library Analogy
Writing a report on a specific topic
  e.g. history of the computer (your internet is out)
While at library, take books from shelves and put them on shelf above your desk
If need more, go get them and bring back to shelf
  Don’t return earlier books since might still need them
  Limited space on shelf; which books do we keep?
You hope these ~10 books on shelf enough to write report
  Only 0.00001% of the books in a big library
Ref: Krste Asanović & Randy H. Katz, Univ of California, Berkeley
Notes: main stax -> shelf -> desk
Some text explaining
change pix

## Slide 17
Ref: Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 18: Introducing Cache Memory
Ref: Book – Harris and Harris

## Slide 19: Principle of Locality

## Slide 20: Principle of Locality (1/3)
Principle of Locality:
Programs access only a small portion of the full address space at any instant of time (spatial locality) and repeatedly access that portion (temporal locality)
Address space holds both code and data
A “typical” program has a lot of locality in memory references
  Typical programs are composed of “loops”
  Loops and sequential instruction execution mean generally localized code access
Ref: Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 21: Principle of Locality (2/3)
Temporal Locality (locality in time)
  Go back to the same book on desk multiple times
  If a memory location is referenced then it will tend to be referenced again soon
Spatial Locality (locality in space)
  When go to shelves, grab many books on computers since related books are stored together
  If a memory location is referenced, the locations with nearby addresses will tend to be referenced soon
  Most notable examples:
    Instruction memory references
    Array/data structure references
Ref: Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 22: Memory Locality
Temporal:
Spatial:
Bryant and O’Hallaron, Computer Systems: A Programmer’s Perspective, Third Edition

## Slide 23: Memory Reference Patterns
Ref: Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 24: Memory Reference Patterns
Ref: Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 25: Locality Example
Data references
  Reference array elements in succession (stride-1 reference pattern).
  Reference variable sum each iteration.
Instruction references
  Reference instructions in sequence.
  Cycle through loop repeatedly.
sum = 0;
for (i = 0; i < n; i++)
sum += a[i];
return sum;
Spatial or Temporal
Locality?
temporal
spatial
temporal
spatial
Bryant and O’Hallaron, Computer Systems: A Programmer’s Perspective, Third Edition

## Slide 26: Principle of Locality (3/3)
We exploit the principle of locality in hardware via a memory hierarchy where:
  Levels closer to processor are faster (and more expensive per bit - hence smaller)
  Levels farther from processor are larger (and less expensive per bit - hence slower)
Goal: Create the illusion of memory being almost as fast as fastest memory and almost as large as biggest memory of the hierarchy
Ref: Krste Asanović & Randy H. Katz, Univ of California, Berkeley
Notes: Mention that making fast and efficient small hardware is more expensive than bigger, slower hardware

## Slide 27: Memory Hierarchy to Exploit Locality

## Slide 28: Memory Hierarchy Schematic
Smaller,
Faster, More expensive
Bigger,
Slower, Cheaper
Processor
Level 1
Level 2
Level n
Level 3
. . .
Lower Higher
Ref: Krste Asanović & Randy H. Katz, Univ of California, Berkeley
Notes: The Processor accesses data out of the highest levels.
Lowest level (usually disk) contains all available data.

## Slide 29: Memory Cache Concept
Cache holds a copy of a subset of main memory
  We often use $ (“cash”) to abbreviate cache (e.g. D$ = Data Cache, L1$ = Level 1 Cache)
Keep recently accessed data in automatically managed fast memory
  Anticipation: the data will be accessed again soon
Cache is
  SRAM
  Implemented with same IC processing technology as CPU
  Integrated on-chip
    On-chip memory eliminates lengthy delays caused by traveling to and from a separate chip
  The cache speed is comparable to the processor speed
  It is faster but more expensive than main memory (DRAM)
Ref: Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 30: Memory Transfer in the Hierarchy
Inclusive: data in L1$ ⊂ data in L2$ ⊂ data in MM ⊂ data in SM
Processor
L1$
L2$
Secondary Memory
Main Memory
Block: Unit of transfer between main memory and cache; Also between Caches
4-8 bytes (word)
16-128 bytes (block)
4,096+ bytes (page)
8-32 bytes (block)
Ref: Krste Asanović & Randy H. Katz, Univ of California, Berkeley
Notes: Symbol ⊂ means “is a subset of”

## Slide 31: The Problem
Bigger is slower
  SRAM, 1 MB-16MB, 0.5 nanosec
  DRAM, 1 GB – 16 GB 10- 50 nanosec
  Hard Disk, Terabyte, ~5000000 nanosec
Faster is more expensive (dollars and chip area)
  SRAM, < 100$ per Giga Byte
  DRAM, < 10$ per Giga Byte
  Hard Disk < 0.05 per Giga Byte
    These sample values (circa ~2020) scale with time
Other technologies are evolving, too
  Flash memory (mature)

## Slide 32: Memory Hierarchy Technologies
Caches use static RAM (SRAM)
  Fast (typical access times of 0.5 ns)
  Higher power, expensive
  Static: content will last as long as power is on
Main memory uses dynamic RAM (DRAM)
  Lower power, cheaper
  Slower (typical access times of 10- 50 ns)
  Dynamic: needs to be “refreshed” regularly (~ every 8 ms)
Ref: Krste Asanović & Randy H. Katz, Univ of California, Berkeley
Notes: In case you didn’t know, RAM stands for Random Access Memory.
Size comparison: DRAM/SRAM is 4 to 8 times
Cost/cycle time comparison SRAM/DRAM is 8 to 16 times
http://parts.digikey.com/1/parts/1211303-ic-sram-1mbit-10ns-32soj-cy7c109d-10vxi.html
Quantity discount 10ns 1MBit SRAM $2.24, $17/Mbyte, $1700/100 Mbyte, $17000/GByte
http://www.frys.com/template/harddrives
DRAM: 4GB @ $70 or $17.50 per GB
24GB@$800 = $33/Gbyte
http://www.frys.com/category/Outpost/Hard+Drives+&+Memory/Memory/Notebook+Memory/Apple+-+Mac++Memory/
DDR2 1GB @ $25 per
DDR3 1 GB @ $37.5 per
FLASH Media
Approx. $2 per Gbyte

## Slide 33: A Typical Memory Hierarchy (1/2)
On-Chip Components
Second
Level
Cache
(SRAM)
Control
Datapath
Secondary
Memory
(Disk
or Flash)
RegFile
Main
Memory
(DRAM)
Data
Cache
Instr
Cache
Cost/bit: highest
Speed: ½’s 1’s 10’s 100’s 1,000,000’s
(cycles)
Size: 100’s 10K’s M’s G’s T’s
(bytes)
lowest
Ref: Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 34: A Typical Memory Hierarchy (2/2)
Ref: MIT Course 6.004 Computation Structures

## Slide 35: So, what is the difference between 3 levels of Caches?
Capacity: L1: 32KB L2: 256KB L3: 10 MB
Speed: L1: 2-4 Cycles L2: 10 Cycles L3: 40 Cycles
What else? Why different speeds (access time)?
  Technology is different !
  Size is different. Small memory is faster
L1 is made from larger transistors and wider metal tracks
   Higher speed, but more space and power

## Slide 36: Example Memory Hierarchy
Regs
L1 cache
(SRAM)
Main memory
(DRAM)
Local secondary storage
(local disks)
Larger,
slower,
and
cheaper
(per byte)
storage
devices
Remote secondary storage
(e.g., Web servers)
Local disks hold files retrieved from disks
on remote servers.
L2 cache
(SRAM)
L1 cache holds cache lines (blocks) retrieved from the L2 cache.
CPU registers hold words retrieved from the L1 cache.
L2 cache holds cache lines
retrieved from L3 cache.
L0:
L1:
L2:
L3:
L4:
L5:
Smaller,
faster,
and
costlier
(per byte)
storage
devices
L3 cache
(SRAM)
L3 cache holds cache lines
retrieved from main memory.
L6:
Main memory holds disk blocks retrieved from local disks.

## Slide 37: Memory Access using Cache

## Slide 38: Who manages transfers?
Registers ↔ Memory
  By compiler (or assembly level programmer)
Cache ↔ Main memory
  By the cache controller hardware
Main memory ↔ Disks (secondary storage)
  By the OS (virtual memory, which is a later topic)
  Virtual to physical address mapping assisted by the hardware (TLB)
  By the programmer (files)
We are here
Ref: Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 39: Cache Philosophy (1/2)
Programmer-invisible hardware mechanism to give illusion of speed of fastest memory with size of largest memory
  Works fine (mostly) even if programmer has no idea what a cache is
A small, interim storage component that transparently retains (caches) data from recently accessed locations
Ref: MIT Course 6.004 Computation Structures
Programmer visible Cache?

## Slide 40: Cache Philosophy (2/2)
Processor sends accesses to cache
  Cache hit: Data for this address in cache, returned quickly
  Cache miss: Data not in cache
    Fetch data from memory, send it back to processor
    Retain this data in the cache (replacing some other data)
Processor must deal with variable memory access time
Ref: MIT Course 6.004 Computation Structures

## Slide 41: Memory Access without Cache
Load word instruction: lw t0, 0(t1) t1 contains 0x12F0 Memory[0x12F0] = 99
  Processor issues address 0x12F0 to Memory
  Memory reads word at address 0x12F0 (99)
  Memory sends 99 to Processor
  Processor loads 99 into register t0
Ref: Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 42: Adding Cache to Computer
Ref: Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 43: Memory Access with Cache
Load word instruction: lw t0,0(t1)
t1 contains 0x12F0, Memory[0x12F0] = 99
With cache:
Processor issues address 0x12F0 to Cache
  Cache checks to see if has copy of data at address 0x12F0
  If finds a match (Hit): cache reads 99, sends to processor
  No match (Miss): cache sends address 0x12F0 to Memory
    Memory reads 99 at address 0x12F0
    Memory sends 99 to Cache
    Cache replaces word which can store 0x12F0 with new 99
    Cache sends 99 to processor
  Processor loads 99 into register t0
Ref: Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 44: Cache Memory – Invisible to Programmers

## Slide 45: Memory Hierarchy Interface
Programming model: Single memory, single address space
Machine transparently stores data in fast or slow memory, depending on usage patterns
Ref: MIT Course 6.004 Computation Structures

## Slide 46: Caches Concept (revision)
Cache: A smaller, faster storage device that acts as a staging area for a subset of the data in a larger, slower device.
Fundamental idea of a memory hierarchy:
  For each k, the faster, smaller device at level k serves as a cache for the larger, slower device at level k+1.
Why do memory hierarchies work?
  Because of locality, programs tend to access the data at level k more often than they access the data at level k+1.
  Thus, the storage at level k+1 can be slower, and thus larger and cheaper per bit.
Big Idea (Ideal): The memory hierarchy creates a large pool of storage that costs as much as the cheap storage near the bottom, but that serves data to programs at the rate of the fast storage near the top.
Bryant and O’Hallaron, Computer Systems: A Programmer’s Perspective, Third Edition

## Slide 47: Quiz
Instructions generally have spacial and temporal locality.
Which of the following statement is not true?
  The first time a function with no loops executes the processor can take advantage of spacial locality
  The first time a function with no loops executes the processor can take advantage of temporal locality
  The first time a function with loops executes the processor can take advantage of spacial locality
  The first time a function with loops executes the processor can take advantage of temporal locality
Ref: Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 48: Quiz
Instructions generally have spacial and temporal locality.
Which of the following statement is not true?
  The first time a function with no loops executes the processor can take advantage of spacial locality
  The first time a function with no loops executes the processor can take advantage of temporal locality
  The first time a function with loops executes the processor can take advantage of spacial locality
  The first time a function with loops executes the processor can take advantage of temporal locality
Ref: Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 49: Class Summary
Present to the programmer as much memory as the largest memory at the speed of the fastest memory
Approach: Memory Hierarchy
  Successively higher levels contain “most used” data from lower levels
  Exploits temporal and spatial locality
Cache is Programmer-invisible hardware mechanism to give illusion of speed of fastest memory with size of largest memory

## Slide 50: Backup Slides

## Slide 51: Cache Philosophy - Interface
Programming model: Single memory, single address space
Ref: MIT Course 6.004 Computation Structures

## Slide 52: Cache Philosophy - Interface
Approach 1: Expose Hierarchy
  Registers, SRAM, DRAM, Flash, Hard Disk
  Tell programmer to “use them cleverly”
Approach 2: Hide Hierarchy
  Programming model: Single memory, single address space
  Machine transparently stores data in fast or slow memories depending on usage patterns
Ref: MIT Course 6.004 Computation Structures

## Slide 53
Modern processors have separate caches for instructions and data, as well as several levels of caches implemented in different sizes

## Slide 54: Qualitative Estimates of Locality
Claim: Being able to look at code and get a qualitative sense of its locality is a key skill for a professional programmer.
Question: Does this function have good locality with respect to array a?
int sum_array_rows(int a[M][N])
{
int i, j, sum = 0;
for (i = 0; i < M; i++)
for (j = 0; j < N; j++)
sum += a[i][j];
return sum;
}
Answer: yes
Hint: array layout is row-major order
• • •
a
[0]
[0]
a
[0]
[N-1]
• • •
a
[1]
[0]
a
[1]
[N-1]
• • •
a
[M-1]
[0]
a
[M-1]
[N-1]
• • •
Bryant and O’Hallaron, Computer Systems: A Programmer’s Perspective, Third Edition

## Slide 55: Locality Example
Question: Does this function have good locality with respect to array a?
int sum_array_cols(int a[M][N])
{
int i, j, sum = 0;
for (j = 0; j < N; j++)
for (i = 0; i < M; i++)
sum += a[i][j];
return sum;
}
Answer: no, unless…
M is very small
• • •
a
[0]
[0]
a
[0]
[N-1]
• • •
a
[1]
[0]
a
[1]
[N-1]
• • •
a
[M-1]
[0]
a
[M-1]
[N-1]
• • •
Bryant and O’Hallaron, Computer Systems: A Programmer’s Perspective, Third Edition