## Slide 1: Happy Ramanavami

## Slide 2: Your behavior
Did you ever look into your behavior?
Why do you behave in a particular way?
  Is it appropriate behavior?
How can you change your behavior, if you think so?
Most of the people who fail in their career
it’s due to their behavior
Not due to their competence !
So, the first thing is to watch your behavior

## Slide 3: CS 211 Computer Architecture Lecture 36: Cache Memory organization – Set Associative Caches
Ravi Mittal
ravi.mittal@iitgoa.ac.in
Indian Institute of Technology, Goa

## Slide 4: Acknowledgements
Krste Asanović & Randy H. Katz, CS 61C: Great Ideas in Computer Architecture (Machine Structures), http://inst.eecs.berkeley.edu/~cs61c/
Chapter 6, Memory Hierarchy, Book: Computer Systems: A programmer’s perspective, Randal E. Bryant and David R. O’Hallaron
Prof Onur Mutlu’s Class Presentation, ETH Zürich, Lecture 21b: Memory Hierarchy and Caches, Sprint 2020
Patterson and Hennessy, Book: Computer Organization and Design, Hardware/Software Interface, RISC-V Edition
MIT 6.004 Spring 2020, Class on Caches
Digital Design and Computer Architecture: RISC-V Edition, Harris & Harris Elsevier

## Slide 5: In this class we will study
Review of Cache concepts
Direct Mapped Cache
Set Associative Cache
Fully Associative Cache
Cache and Associativity

## Slide 6: Last Class

## Slide 7: Great Idea: Principle of Locality/Memory Hierarchy
Ref: Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 8: Cache Memory
Ref: MIT Course 6.004 Computation Structures

## Slide 9: Memory Hierarchy Interface
Programming model: Single memory, single address space
Machine transparently stores data in fast or slow memory, depending on usage patterns
Ref: MIT Course 6.004 Computation Structures

## Slide 10: Cache – Main Memory Interaction
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Larger, slower, cheaper memory
viewed as partitioned into “blocks”
Data is copied in block-sized transfer units
Smaller, faster, more expensive
memory caches a subset of
the blocks
4
4
4
10
10
10
Bryant and O’Hallaron, Computer Systems: A Programmer’s Perspective, Third Edition

## Slide 11: Cache : Hit
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Data in block b is needed
Request: 14
14
Block b is in cache:
Hit!
Bryant and O’Hallaron, Computer Systems: A Programmer’s Perspective, Third Edition

## Slide 12: Cache: Miss
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Data in block b is needed
Request: 12
Block b is not in cache:
Miss!
Block b is fetched from
memory
Request: 12
12
12
12
Block b is stored in cache
Placement policy: determines where b goes
Replacement policy: determines which block gets evicted (victim)
Bryant and O’Hallaron, Computer Systems: A Programmer’s Perspective, Third Edition

## Slide 13: Direct Mapped Cache

## Slide 14: Direct Mapped Cache
Each memory location is mapped to exactly one location in the cache
  Hence called Direct Mapped Cache
  Therefore, we only need to look in a single location in the cache for the data if it exists in the cache
Block is the unit of transfer between cache and memory
  Word Block and Line are used interchangeably
    Though some authors define line as block + Tag + valid bit

## Slide 15: Direct Mapped Cache: Block Size 1 byte
Ref: Dan Garcia Univ of California, Berkeley

## Slide 16: Direct Mapped Cache: Block Size 2 bytes
Ref: Dan Garcia Univ of California, Berkeley
16 blocks  4 blocks

## Slide 17: Direct Mapped Cache: Use Tag
8
2
14
1E
Ref: Dan Garcia Univ of California, Berkeley

## Slide 18: Direct Mapped Cache: Block Size 2 bytes
1
0
2
3
Ref: Dan Garcia Univ of California, Berkeley

## Slide 19: Direct Mapped Caches – address parts
Since multiple memory addresses map to the same cache index, how do we know which one is there?
What if the block size is > 1 ?
Answer: divide memory address into three fields
Ref: Dan Garcia Univ of California, Berkeley

## Slide 20: Direct-Mapped Cache Terminology
All fields are read as unsigned integers.
Index
  specifies the cache index (which “row”/”set” of the cache we should look in)
  Which colour we must look into – in previous example
Tag
  These are used to distinguish between all the memory addresses that map to the same location (all the same color blocks in MM that map to one block in Cache
  Tag – Higher order bits
Offset
  once we’ve found correct block, specifies which byte within the block we want

## Slide 21: Direct Mapped Cache – Example 1
Main Memory: 32 words (bytes) that maps to 8 words (bytes) of cache
Cache: 8-blocks that uses the three lowest bits (8=23) of the block address
  Each block consists of one word (one byte)
What if there is no data in a location?
  Valid bit (V): 1 = present, 0 = not present
  Initially 0
Ref: Patterson and Hennessey: Computer Organization and Design
2 bits
3 bits
0 bits
Address of word:
tag
Index
or set
block
offset

## Slide 22: Direct Mapped Cache: Example 1
Cache: 8-blocks, 1 word/block, direct mapped
MM: 32 blocks  Cache 8 blocks mapping
Initial state
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | N |  | 
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | N |  | 
111 | N |  | 
Ref: Patterson and Hennessey: Computer Organization and Design

## Slide 23: Direct Mapped Cache: Example 1
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | N |  | 
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
22 | 10 110 | Miss | 110
Ref: Patterson and Hennessey: Computer Organization and Design

## Slide 24: Direct Mapped Cache: Example 1
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | Y | 11 | Mem[11010]
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
26 | 11 010 | Miss | 010
Ref: Patterson and Hennessey: Computer Organization and Design

## Slide 25: Direct Mapped Cache: Example 1
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | Y | 11 | Mem[11010]
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
22 | 10 110 | Hit | 110
26 | 11 010 | Hit | 010
Ref: Patterson and Hennessey: Computer Organization and Design

## Slide 26: Direct Mapped Cache: Example 1
Index | V | Tag | Data
000 | Y | 10 | Mem[10000]
001 | N |  | 
010 | Y | 11 | Mem[11010]
011 | Y | 00 | Mem[00011]
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
16 | 10 000 | Miss | 000
3 | 00 011 | Miss | 011
16 | 10 000 | Hit | 000
Ref: Patterson and Hennessey: Computer Organization and Design

## Slide 27: Direct Mapped Cache: Example 1
Index | V | Tag | Data
000 | Y | 10 | Mem[10000]
001 | N |  | 
010 | Y | 10 | Mem[10010]
011 | Y | 00 | Mem[00011]
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
18 | 10 010 | Miss | 010
Ref: Patterson and Hennessey: Computer Organization and Design

## Slide 28: Blocks and Addressing the Cache
Each block maps to a location in the cache, determined by the index bits in the address
  used to index into the tag and data
Cache access:
  1) index into the tag and data entry (stores) with index bits in address
  2) check valid bit
  3) compare tag bits in address with the stored tag in tag store
If a block is in the cache (cache hit), the stored tag should be valid and match the tag of the block
8-bit address
tag
index
byte in block
3 bits
3 bits
2b
Ref: Prof Onur Mutlu’s Presentation

## Slide 29: Direct-Mapped Cache: Example 2
byte-addressable main memory: 256 bytes, 8-byte per block  32 blocks
  Note that we have shown block numbers in the diagram
Assume cache: 64 bytes, 8 blocks
  Direct-mapped: A block can go to only one location
  Addresses with same index contend for the same location - Cause conflict misses
Tag
Data
Address
tag
index
offset
3 bits
3 bits
2b
V
tag
=?
MUX
byte in block:
offset
Hit?
Data
Main Memory
Block: 00000
Block: 00001
Block: 00010
Block: 00011
Block: 00100
Block: 00101
Block: 00110
Block: 00111
Block: 01000
Block: 01001
Block: 01010
Block: 01011
Block: 01100
Block: 01101
Block: 01110
Block: 01111
Block: 10000
Block: 10001
Block: 10010
Block: 10011
Block: 10100
Block: 10101
Block: 10110
Block: 10111
Block: 11000
Block: 11001
Block: 11010
Block: 11011
Block: 11100
Block: 11101
Block: 11110
Block: 11111

## Slide 30: Direct-Mapped Cache: 1-way
Block: 00000
Block: 00001
Block: 00010
Block: 00011
Block: 00100
Block: 00101
Block: 00110
Block: 00111
Block: 01000
Block: 01001
Block: 01010
Block: 01011
Block: 01100
Block: 01101
Block: 01110
Block: 01111
Block: 10000
Block: 10001
Block: 10010
Block: 10011
Block: 10100
Block: 10101
Block: 10110
Block: 10111
Block: 11000
Block: 11001
Block: 11010
Block: 11011
Block: 11100
Block: 11101
Block: 11110
Block: 11111
Main Memory
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
Cache Memory
Index
000
001
111
tag
index
offset
3 bits
3 bits
2b

## Slide 31: Direct-Mapped Caches - Observations
Two blocks in memory that map to the same index in the cache cannot be present in the cache at the same time
  One index  one entry
Can lead to 0% hit rate if more than one block accessed in an interleaved manner map to the same index
  Assume addresses A and B have the same index bits but different tag bits
  A, B, A, B, A, B, A, B, …  conflict in the cache index
  All accesses are conflict misses
Ref: Prof Onur Mutlu’s Presentation

## Slide 32: Set Associative Caches

## Slide 33: Set Associativity
In previous example, Addresses 0 and 8 always conflict in direct mapped cache
Instead of having one column of 8, have 2 columns of 4 blocks
2 blocks represent one set
Set: Set is indexed by index bits; Here each set has two blocks
  Each block in a set has it’s own tag
Key idea: Associative memory within the set
+ Accommodates conflicts better (fewer conflict misses)
-- More complex, slower access, larger tag store
Ref: Prof Onur Mutlu’s Presentation

## Slide 34: Set Associative Cache: 2-way
Block: 00000
Block: 00001
Block: 00010
Block: 00011
Block: 00100
Block: 00101
Block: 00110
Block: 00111
Block: 01000
Block: 01001
Block: 01010
Block: 01011
Block: 01100
Block: 01101
Block: 01110
Block: 01111
Block: 10000
Block: 10001
Block: 10010
Block: 10011
Block: 10100
Block: 10101
Block: 10110
Block: 10111
Block: 11000
Block: 11001
Block: 11010
Block: 11011
Block: 11100
Block: 11101
Block: 11110
Block: 11111
Main Memory
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
Cache Memory
Index : 2 bits
Tag: 3 bits
4 colored blocks  2 index bits
8 blocks of the same color in MM are mapped
to 2 blocks in Cache  3 tag bits
SET 0
SET 1
SET 2
SET 3
Index

## Slide 35: Set Associative Cache: 2- way
Way 1
Way 0
V
tag
=?
V
tag
=?
Logic
MUX
MUX
byte offset
SET 0
Hit
Ref: Prof Onur Mutlu’s Presentation
tag
index
byte Offset
3 bits
2 bits
3b
Logic
Logic
Hit1
Hit0
Hit1
tag
V
tag
V
block
block
SET 1
SET 2
SET 3

## Slide 36: Set Associative Cache: 4-way
Block: 00000
Block: 00001
Block: 00010
Block: 00011
Block: 00100
Block: 00101
Block: 00110
Block: 00111
Block: 01000
Block: 01001
Block: 01010
Block: 01011
Block: 01100
Block: 01101
Block: 01110
Block: 01111
Block: 10000
Block: 10001
Block: 10010
Block: 10011
Block: 10100
Block: 10101
Block: 10110
Block: 10111
Block: 11000
Block: 11001
Block: 11010
Block: 11011
Block: 11100
Block: 11101
Block: 11110
Block: 11111
Main Memory
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
Index : 1 bit
Tag: 4 bits
Cache Memory
2 colored blocks  1 index bit
16 blocks (of same color) in MM are mapped to
4 blocks (of a set) in Cache  4 tag bits
SET0
SET1
tag
index
byte Offset
3 bits
1 bit
4b

## Slide 37: Set Associative Cache: 4 - way
Two sets
Each set has 4 blocks (Lines)
Way 1
Way 0
V
tag
SET0
Ref: Prof Onur Mutlu’s Presentation
tag
index
byte Offset
3 bits
1 bit
4b
V
tag
V
tag
V
tag
Way 2
Way 3
SET1

## Slide 38: Fully Associative Cache

## Slide 39: Set Associative Cache: 8-way (Fully Associative)
Block: 00000
Block: 00001
Block: 00010
Block: 00011
Block: 00100
Block: 00101
Block: 00110
Block: 00111
Block: 01000
Block: 01001
Block: 01010
Block: 01011
Block: 01100
Block: 01101
Block: 01110
Block: 01111
Block: 10000
Block: 10001
Block: 10010
Block: 10011
Block: 10100
Block: 10101
Block: 10110
Block: 10111
Block: 11000
Block: 11001
Block: 11010
Block: 11011
Block: 11100
Block: 11101
Block: 11110
Block: 11111
Main Memory
Index : 0 bit
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
Tag: 5 bits : To find out the blocks that are present in
cache
tag
index
byte Offset
3 bits
0 bit
5b

## Slide 40: Fully Associative
One set
Each set has 8 blocks (Lines)
SET
Ref: Prof Onur Mutlu’s Presentation
tag
index
byte Offset
3 bits
0 bit
5b
V
tag
V
tag
V
tag
V
tag
Way 1
Way 0
Way 2
Way 3
V
tag
V
tag
V
tag
V
tag
Way 5
Way 4
Way 6
Way 7

## Slide 41: Cache and Associativity

## Slide 42: Range of Set-Associative Caches
For a fixed-size cache, and a given block size, each increase by a factor of two in associativity doubles the number of blocks per set (i.e., the number of “ways”) and halves the number of sets
  Decreases the size of the index by 1 bit and increases the size of the tag by 1 bit
Block offset
Index
Tag
More Associativity (more ways)
What if we can also change the block size?
Ref: Krste Asanović & Randy H. Katz, Univ of California, Berkeley
Notes: For class handout

## Slide 43: Set Associate Caches: 1-way to 8-way
Direct Mapped: 8 blocks, 1 way, 1 tag comparator, 8 sets (1 block / set), index 3 bits
2 Way Set Associative: 8 blocks, 2 ways, 2 tag comparators, 4 sets (2 blocks/set), index 2 bits
4 Way Set Associative: 8 blocks, 4 ways, 4 tag comparators, 2 sets (4 blocks/set), index 1 bit,
Fully Associative: 8 blocks, 8 ways, 8 tag comparators, 1 set (8 blocks / set), index 0 bit
0
1
2
3
DM: 8 sets
1 way
4
5
6
7
0
1
2
3
FA: 1 set
8 ways
4
5
6
7
0
1
2
3
2 Way SA: 4 sets
Set 0
Set 1
Set 2
Set 3
4
5
6
7
0
1
2
3
4 Way SA: 2 sets
Set 0
Set 1
4
5
6
7
Ref: Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 44: Associative Caches: Another view
32 blocks mapped to 8 blocks in cache
Block 12 placed in 8 block cache:
  Fully associative, direct mapped, 2-way set associative
  S.A. Mapping = Block Number Modulo Number Sets
0 1 2 3 4 5 6 7
Block
no.
Fully associative:
block 12 can go anywhere
0 1 2 3 4 5 6 7
Block
no.
Direct mapped:
block 12 can go only into block 4 (12 mod 8)
0 1 2 3 4 5 6 7
Block
no.
Set associative:
block 12 can go anywhere in set 0 (12 mod 4)
Set
0
Set
1
Set
2
Set
3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
Block-frame address
1 1 1 1 1 1 1 1 1 1 2 2 2 2 2 2 2 2 2 2 3 3
Block
no.
8 Sets
1 Set

## Slide 45: Lecture Summary
Memory hierarchy exploits principle of locality to deliver lots of memory at fast speeds
Caches can be organized as
  Direct mapped – A block in MM can be mapped only to one specific block in Cache
  Two-way Associative – A block in MM can be mapped to any one of the two blocks in a specific set in Cache
  N-way Associative – A block in MM can be mapped to any one of the N-blocks in a specific set in Cache
  Fully Associative – A block in MM can be mapped to any block in the Cache
Set associativity must be properly chosen for optimal performance

## Slide 46: Associativity (and Tradeoffs)
Degree of associativity: How many blocks can map to the same index (or set)?
Higher associativity
  ++ Higher hit rate
  -- Slower cache access time (hit latency and data access latency)
  -- More expensive hardware (more comparators)
Diminishing returns from higher
  associativity
associativity
hit rate
Ref: Prof Onur Mutlu’s Presentation

## Slide 47: Block Size Consideration
Larger blocks should reduce miss rate
  Due to spatial locality
But in a fixed-sized cache
  Larger blocks  fewer of them
    More competition  increased miss rate
    As a result, a block will be bumped out of the cache before many of its words are accessed
Each line represents a cache of different size.
Ref: Patterson and Hennessey: Computer Organization and Design

## Slide 48: Backup

## Slide 49: General Cache Organization (S, E, B)
E = 2e lines per set
S = 2s sets
set
line
0
1
2
B-1
tag
v
B = 2b bytes per cache block (the data)
Cache size
= S x E x B data bytes
valid bit
Bryant and O’Hallaron, Computer Systems: A Programmer’s Perspective, Third Edition

## Slide 50: Cache Read
E = 2e lines per set
S = 2s sets
0
1
2
B-1
tag
v
valid bit
B = 2b bytes per cache block (the data)
t bits
s bits
b bits
Address of word:
tag
set
index
block
offset
data begins at this offset
Locate set
Check if any line in set has matching tag
Yes + line valid: hit
Locate data starting at offset
Bryant and O’Hallaron, Computer Systems: A Programmer’s Perspective, Third Edition

## Slide 51: Example: Direct Mapped Cache (E = 1)
S = 2s sets
Direct mapped: One line per set
Assume: cache block size B=8 bytes
t bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
find set
Bryant and O’Hallaron, Computer Systems: A Programmer’s Perspective, Third Edition

## Slide 52: Example: Direct Mapped Cache (E = 1)
Direct mapped: One line per set
Assume: cache block size B=8 bytes
t bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
match: assume yes (= hit)
valid? +
block offset
tag
Bryant and O’Hallaron, Computer Systems: A Programmer’s Perspective, Third Edition

## Slide 53: Example: Direct Mapped Cache (E = 1)
Direct mapped: One line (block) per set
Assume: cache block size B=8 bytes
t bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
match: assume yes (= hit)
valid? +
int (4 Bytes) is here
block offset
If tag doesn’t match (= miss): old line is evicted and replaced
Bryant and O’Hallaron, Computer Systems: A Programmer’s Perspective, Third Edition

## Slide 54: E-way Set Associative Cache (Here: E = 2)
E = 2: Two lines per set
Assume: cache block size B=8 bytes
t bits
0…01
3 bits
Address
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
find set
2 lines per set
sets
Bryant and O’Hallaron, Computer Systems: A Programmer’s Perspective, Third Edition

## Slide 55: E-way Set Associative Cache (Here: E = 2)
E = 2: Two lines per set
Assume: cache block size B=8 bytes
t bits
0…01
100
Address of short int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
compare both
valid? +
match: yes (= hit)
block offset
tag
Bryant and O’Hallaron, Computer Systems: A Programmer’s Perspective, Third Edition

## Slide 56: E-way Set Associative Cache (Here: E = 2)
E = 2: Two lines per set
Assume: cache block size B=8 bytes
t bits
0…01
100
Address of short int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
compare both
valid? +
match: yes (= hit)
block offset
tag
5
4
short int (2 Bytes) is here
No match or not valid (= miss):
One line in set is selected for eviction and replacement
Replacement policies: random, least recently used (LRU), …
Bryant and O’Hallaron, Computer Systems: A Programmer’s Perspective, Third Edition

## Slide 57: Cache Philosophy - Interface
Programming model: Single memory, single address space
Ref: MIT Course 6.004 Computation Structures

## Slide 58: Cache Philosophy - Interface
Approach 1: Expose Hierarchy
  Registers, SRAM, DRAM, Flash, Hard Disk
  Tell programmer to “use them cleverly”
Approach 2: Hide Hierarchy
  Programming model: Single memory, single address space
  Machine transparently stores data in fast or slow memories depending on usage patterns
Ref: MIT Course 6.004 Computation Structures

## Slide 59: General Notes on Caches (1/3)
Recall: Memory is byte-addressed
We haven’t specified the size of our “blocks,” but will usually be multiple of word size (32-bits)
  How do we access individual words or bytes within a block?
Cache is smaller than memory
  Can’t fit all blocks at once, so multiple blocks in memory must map to the same slot in cache
  Need some way of identifying which memory block is currently in each cache slot
OFFSET
INDEX
TAG
Ref: Krste Asanović & Randy H. Katz, Univ of California, Berkeley
Notes: “slot” or “cubby” or “locker” or “location”
Add cache block partitioned to words

## Slide 60: General Notes on Caches (2/3)
What does cache initially hold?
  Garbage! Cache considered “cold”
  Keep track with Valid bit
Effect of block size (K Bytes):
  Spatial locality dictates our blocks consist of adjacent bytes, which differ in address by 1
  Offset field: Low bits of memory address can be used to index to specific bytes within a block
    Block size needs to be a power of two (in bytes)

## Slide 61: General Notes on Caches (3/3)
Effect of cache size (C Bytes):
  “Cache Size” refers to total stored data
  Determines number of blocks the cache can hold (C/K blocks)
  Tag field: Leftover upper bits of memory address determine which portion of memory the block came from (identifier)
Notes: Can also call tag field the “block number” (only works for fully associative).

## Slide 62: Cache Abstraction and Metrics
Cache hit rate = (# hits) / (# hits + # misses) = (# hits) / (# accesses)
Average memory access time (AMAT)
= ( hit-rate * hit-latency ) + ( miss-rate * miss-latency )
Address
Tag Store
(is the address
in the cache?
+ bookkeeping)
Data Store
(stores
memory
blocks)
Hit/miss?
Data
Ref: Prof Onur Mutlu’s Presentation

## Slide 63: Set Associativity
Addresses 0 and 8 always conflict in direct mapped cache
Instead of having one column of 8, have 2 columns of 4 blocks
Tag store
Data store
V
tag
=?
V
tag
=?
Address
tag
index
byte in block
3 bits
2 bits
3b
Logic
MUX
MUX
byte in block
Key idea: Associative memory within the set
+ Accommodates conflicts better (fewer conflict misses)
-- More complex, slower access, larger tag store
SET
Hit?
Ref: Prof Onur Mutlu’s Presentation