## Slide 1: CS211 Computer Architecture Lecture 38: Cache – 4 : Cache Memory Performance
Ravi Mittal
ravi.mittal@iitgoa.ac.in
Indian Institute of Technology, Goa

## Slide 2: Acknowledgements
Krste Asanović & Randy H. Katz, CS 61C: Great Ideas in Computer Architecture (Machine Structures), http://inst.eecs.berkeley.edu/~cs61c/
Chapter 6, Memory Hierarchy, Book: Computer Systems: A programmer’s perspective, Randal E. Bryant and David R. O’Hallaron
Prof Onur Mutlu’s Class Presentation, ETH Zürich, Lecture 21b: Memory Hierarchy and Caches, Sprint 2020
Patterson and Hennessy, Book: Computer Organization and Design, Hardware/Software Interface, RISC-V Edition
MIT 6.004 Spring 2020, Class on Caches
Digital Design and Computer Architecture: RISC-V Edition, Harris & Harris Elsevier

## Slide 3: In this class we will study
Cache Memory – Performance
Understanding Cache Misses
Average Memory Access Time (AMAT)
Pipelined Datapath with Cache Memory

## Slide 4: Cache Memory: Performance

## Slide 5: Cache Performance Metrics
Hit Rate
  Percentage of memory accesses in a program or set of instructions that result in a cache hit
  In cache, which is almost million times smaller than MM, the hit rate is 90%-95% (eg 4KiB cache vs 4 GiB Main Memory)
  Hit Rate = No of hits / No of memory accesses
  = 1 – Miss Rate
Miss Rate
  Fraction of memory references that are not found in cache (misses / accesses) = 1 – hit rate
  Typical numbers (in percentages):
    3-10% for L1
    Can be quite small (e.g., < 1%) for L2, depending on size, etc.
Miss Penalty
  Time it takes to service a miss
  Additional time required because of a miss (to replace a block in the cache from lower level)
    Typically 1000 cycles for main memory

## Slide 6: Cache Performance Metrics
Hit Time
  Time to deliver a line (block) in the cache to the processor
    Includes time to determine whether the line is in the cache (tag comparison)
Note that cache is a circuit structure that sits inside core of the processor. It’s critical path component for the processor
Cache has to be properly chosen so that it doesn’t impact the cycle time of the processor
Hit time of the cash is in nano seconds – usually one fourth of a cycle

## Slide 7: Understanding Cache Misses

## Slide 8: Types of Cache Misses
Cold (compulsory) miss
  Cold misses occur because the cache starts empty and this is the first reference to the block
  Cold fact of life: not a whole lot you can do about it
  If you are going to run “billions” of instruction, Compulsory Misses are insignificant
Capacity miss
  Occurs when the set of active cache blocks (working set) is larger than the cache
  Solution: increase cache size
Bryant and O’Hallaron, Computer Systems: A Programmer’s Perspective, Third Edition

## Slide 9: Types of Cache Misses
Conflict (Collision) miss
Multiple memory locations mapped to the same cache location
Block i at level k+1 must be placed in block (i mod 4) at level k
Conflict misses occur when the level k cache is large enough, but multiple data objects all map to the same level k block.
  E.g. Referencing blocks 0, 8, 0, 8, 0, 8, ... would miss every time
Solution 1: increase cache size
Solution 2: increase associativity

## Slide 10: Miss Rate vs. Cache Size on the Integer Portion of SPECCPU2000

## Slide 11: 3Cs Analysis
Three sources of misses (SPEC2000 integer and floating-point benchmarks)
  Compulsory misses 0.006%; not visible
  Capacity misses, function of cache size
  Conflict portion depends on associativity and cache size

## Slide 12: Average Memory Access Time (AMAT)

## Slide 13: Memory Performance
Average memory access time (AMAT): average time for processor to access memory considering both hits and misses
How to reduce AMAT?
Memory Performance
AMAT = Time for a hit + Miss rate × Miss penalty

## Slide 14: How to reduce AMAT?
Reduce the time to hit in the cache
  Reduce cache size  hit time decreases
  Decrease associativity  decrease in the number of sets  less time due to less tag-matching
  Direct mapped Cache has low hit time
Reduce the miss rate: Miss rate depends on access patterns
  Larger cache, Larger block sizes, more associativity
Reduce the miss penalty
  Example: Use multiple cache levels

## Slide 15: Reducing Miss Rate: 3Cs
Reducing Compulsory Misses
  Difficult to avoid
  One technique: Prefetching
Reducing Capacity Misses
  Increase cache size
  It may increase Hit Time
Reducing Conflict Misses
  Increase associativity
    Fully associative cache has low miss rate
  However it may increase Hit Time

## Slide 16: Reducing Miss Penalty
“Cost” (usually in cycles, or fractions of a second of a miss)
  Going to the next level of cache
Contributing factors:
  How “big” is your memory hierarchy?
    Good probability of finding things at a level
  Smaller block size → lower MP
There are many smart techniques to reduce miss penalty
  Use of Write buffers
  Sub-block placement
  Early restart and critical word first
  Multilevel cache

## Slide 17: AMAT Example
Processor specs: 200 ps clock, Miss Penalty of 50 clock cycles, Miss Rate of 0.02 misses/instruction, and Hit Time of 1 clock cycle
  AMAT = 1 + 0.02 * 50 = 2 clock cycles = 400 ps
Which improvement would be best?
  190 ps clock
    2 cycles = 2*190 = 380
  Miss Penalty of 40 clock cycles
    1 + 0.02 * 40 = 360
  Miss Rate of 0.015 misses/instruction
    1 + .15 * 50 = 350

## Slide 18: Multilevel Cache Design Considerations
L1 cache focuses on low hit time (fast access)
  minimize Hit Time to achieve shorter clock cycle
  L1 Miss Penalty significantly reduced by presence of L2 cache
     L1 Cache can be smaller/faster even with higher miss rate
  smaller cache has fewer rows
L2, L3 caches focus on low miss rate
  As much as possible avoid reaching to main memory (heavy penalty)
  larger caches with larger block sizes (same # rows)

## Slide 19: Multilevel Cache AMAT
AMAT = L1 HT + L1 MR × L1 MP
  Now L1 MP depends on other cache levels
    Must trace ENTIRE path to memory
L1 MP = L2 HT + L2 MR × L2 MP
  If more levels, then continue this chain (i.e. MPi = HTi+1 + MRi+1 × MPi+1)
  Final MP is main memory access time
For two levels:
  AMAT = L1 HT + L1 MR × (L2 HT + L2 MR × L2 MP)

## Slide 20: Cache Design Space
Several interacting dimensions
  Cache size
  Block size
  Associativity
  Replacement policy
  Write-through vs. write-back
  Write allocation
Optimal choice is a compromise
  Depends on access characteristics
    Workload
    Use (I-cache, D-cache)
  Depends on technology / cost
Simplicity often wins
Associativity
Cache Size
Block Size
Bad
Good
Less
More
Factor A
Factor B
Computer architects expend considerable effort optimizing organization of cache hierarchy – big impact on performance and power!
Notes: No fancy replacement policy is needed for the direct mapped cache.
As a matter of fact, that is what cause direct mapped trouble to begin with: only one place to go in the cache--causes conflict misses.
No fancy replacement policy is needed for the direct mapped cache.
As a matter of fact, that is what cause direct mapped trouble to begin with: only one place to go in the cache--causes conflict misses.
Besides working at Sun, I also teach people how to fly whenever I have time.
Statistic have shown that if a pilot crashed after an engine failure, he or she is more likely to get killed in a multi-engine light airplane than a single engine airplane.
The joke among us flight instructors is that: sure, when the engine quit in a single engine stops, you have one option: sooner or later, you land. Probably sooner.
But in a multi-engine airplane with one engine stops, you have a lot of options. It is the need to make a decision that kills those people.

## Slide 21: Effect of Block and Cache Sizes on Miss Rate
Cache Size
Miss rate goes up if the block size becomes a significant fraction of the cache size because the number of blocks that can be held in the same size cache is smaller
Notes: Increasing the block size usually decreases the miss rate.
A more serious problem is that the miss penalty goes up since it is primarily determined by the time to fetch the block from the next lower level of the hierarchy and load it into the cache.

## Slide 22: Benefits of Set-Associative Caches
Consider cost of a miss vs. cost of implementation
Largest gains are in going from direct mapped to 2-way (20%+ reduction in miss rate)
As cache size grows the relative improvement from associativity increases slightly
Notes: As cache sizes grow, the relative improvement from associativity increases only slightly; since the overall miss rate of a larger cache is lower, the opportunity for improving the miss rate decreases and the absolute improvement in miss rate from associativity shrinks significantly.

## Slide 23: Impact of Larger Cache on AMAT?
Reduces misses
Longer Access time (Hit time): smaller is faster
  Increase in hit time will likely add another stage to the pipeline
At some point, increase in hit time for a larger cache may overcome improvement in hit rate, yielding a decrease in performance
Computer architects expend considerable effort optimizing organization of cache hierarchy – big impact on performance and power!
Notes: AMAT = 1 + 0.02x50 = 2

## Slide 24: Increasing Block Size (self reading)
Hit time remains unchanged as block size increases
  There might be slight hit-time reduction as number of tags is reduced, so faster to access memory holding tags
Miss rate goes down first due to increase in spatial locality, then it increases due to increased conflict misses as a fewer blocks are in cache
Miss penalty rises as block size increases

## Slide 25: Increasing Associativity? (self reading)
Increases Hit time increases as associativity increases
  Increases, with large step from direct-mapped to >=2 ways
  Use of mux – increase hit time
Miss rate goes down as associativity increases
  Goes down due to reduced conflict misses, but most gain is from 1->2->4-way with limited benefit from higher associativities
Miss penalty remains unchanged associativity increases
  replacement policy runs in parallel with fetching missing line from memory

## Slide 26: Pipelined datapath with Cache Memory

## Slide 27: Pipelined RISC-V RV32I Datapath (with Instruction and Data Caches)
IMEM
ALU
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
aluX
pcF+4
+4
pcD
pcF
pcX
pcM
instD
instX
rs1X
rs2X
aluM
rs2M
immX
Imm.
Recalculate PC+4 in M stage to avoid sending both PC and PC+4 down pipeline
instM
instW
Must pipeline instruction along with data, so control operates correctly in each stage
Primary I$
Hit?
Addr Instr
pcF
instD
“Bubble”
PCen
To Memory Controller
Refill $ Data from Lower Levels of Memory Hierarchy
Primary D$
Hit?
Addr DataR
DataW
Refill D$ data from Lower Levels of Memory Hierarchy
Memory Controller & Stall entire CPU on D$ miss
Write Back/Thru to Memory

## Slide 28: Summary
Cache performance depends heavily on cache design
Parameters that effect Cache performance
  Cache Size
  Block Size
  Associativity
  Replacement policies
  Cache organization – Write through vs Write back, Write allocate vs Write no allocate
Cache performance vs cost

## Slide 29: Multilevel Cache Diagram
Return
L1$
L2$
Main Memory
.
.
.
CPU
Memory
Access
Path of data back to CPU
Miss
Miss
Hit
Hit
Legend:
Request for data
Return of data
Store
Store
If Write Allocate
Write Miss
Write Miss
Notes: The stores back in higher-level caches depends on your write-miss policy (write allocate or no-write allocate).