## Slide 1: CS 211 Computer Architecture Lecture 39: Virtual Memory - 1
Ravi Mittal
ravi.mittal@iitgoa.ac.in
Indian Institute of Technology, Goa

## Slide 2: We will study today ..
Motivation for Virtual Memory
Physical Address, Virtual Address and Address Space
Address Translation
Address Translation and Virtual Memory Organization
Memory Protection
Summary

## Slide 3: Reading for this lecture
Memory Organization
Chapter 8, Digital Design and Computer Architecture, Harris and Harris
Lecture 25b: Virtual Memory, Prof Onur Mutulu, ETH Zurich, https://safari.ethz.ch/digitaltechnik/spring2018/doku.php?id=schedule
Chapter 6, Memory Hierarchy, Book: Computer Systems: A programmer’s perspective, Randal E. Bryant and David R. O’Hallaron

## Slide 4: Memory Organization: What we have studied so far

## Slide 5: Recall: Memory Locality
A “typical” program has a lot of locality in memory references
  typical programs are composed of “loops”
Temporal: A program tends to reference the same memory location many times and all within a small window of time
Spatial: A program tends to reference a cluster of memory locations at a time
  most notable examples:
    Instruction memory references
    Array/data structure references

## Slide 6: Example Memory Hierarchy
Regs
L1 cache
(SRAM)
Main memory
(DRAM)
Local secondary storage
(local disks)
Larger,
slower,
and
cheaper
(per byte)
storage
devices
Remote secondary storage
(e.g., Web servers)
Local disks hold files retrieved from disks
on remote servers.
L2 cache
(SRAM)
L1 cache holds cache lines retrieved from the L2 cache.
CPU registers hold words retrieved from the L1 cache.
L2 cache holds cache lines
retrieved from L3 cache.
L0:
L1:
L2:
L3:
L4:
L5:
Smaller,
faster,
and
costlier
(per byte)
storage
devices
L3 cache
(SRAM)
L3 cache holds cache lines
retrieved from main memory.
L6:
Main memory holds disk blocks retrieved from local disks.

## Slide 7: Recall: Caches
Cache: A smaller, faster storage device that acts as a staging area for a subset of the data in a larger, slower device.
Fundamental idea of a memory hierarchy:
  For each k, the faster, smaller device at level k serves as a cache for the larger, slower device at level k+1.
Why do memory hierarchies work?
  Because of locality, programs tend to access the data at level k more often than they access the data at level k+1.
  Thus, the storage at level k+1 can be slower, and thus larger and cheaper per bit.
Big Idea (Ideal): The memory hierarchy creates a large pool of storage that costs as much as the cheap storage near the bottom, but that serves data to programs at the rate of the fast storage near the top.
Bryant and O’Hallaron, Computer Systems: A Programmer’s Perspective, Third Edition

## Slide 8: Recall: General Cache Concepts
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Larger, slower, cheaper memory
viewed as partitioned into “blocks”
Data is copied in block-sized transfer units
Smaller, faster, more expensive
memory caches a subset of
the blocks
4
4
4
10
10
10
Bryant and O’Hallaron, Computer Systems: A Programmer’s Perspective, Third Edition

## Slide 9: General Cache Organization (S, E, B)
E = 2e lines per set
S = 2s sets
set
line
0
1
2
B-1
tag
v
B = 2b bytes per cache block (the data)
Cache size
= S x E x B data bytes
valid bit
Bryant and O’Hallaron, Computer Systems: A Programmer’s Perspective, Third Edition

## Slide 10: N-Way Set Associative Cache

## Slide 11: What is Virtualization?

## Slide 12: Virtual World
Virtual Memory
Virtual Machine
Virtual LAN
Virtual Private Network
Server Virtualization
Link Virtualization
Platform Virtualization
Resource Virtualization
Virtual Desktop

## Slide 13: Virtualization ?
Virtualization is the process of creating software based or virtual, representation of something
  Virtual Applications
  Servers
  Storage
  Networks
The abstraction of computer resources
Virtualization is the process of creating a software-based, or virtual, representation of something, such as virtual applications, servers, storage and networks.
The access request for the resource is intercepted and different view of the resource is presented

## Slide 14: So far we looked at Cache and MM… How to make it virtual and why?

## Slide 15: A System Using Physical Addressing
Used in “simple” systems like embedded microcontrollers in devices like cars, elevators, and digital picture frames
This is not the way most systems work: Desktop, Mobile etc
0:
1:
M-1:
Physical (Main) memory
CPU
2:
3:
4:
5:
6:
7:
Physical address
(PA)
Data word
8:
...
4
Notes: The main memory of a computer system is organized as an array of M contiguous byte-size cells. Each byte has a unique physical address (PA).

## Slide 16: A System with Physical Memory Only
Examples:
  Most Cray machines
  Early PCs
  Nearly all embedded systems
CPU’s load or store addresses used
directly to access memory
CPU
0:
1:
N-1:
Memory
Physical
Addresses
Notes: Potential Problem?

## Slide 17: How about when we run multiple programs (processes)?

## Slide 18: Multiprogramming
OS runs multiple applications simultaneously
  Strictly one process at a time but context switch
OS switches between processes very quickly
  Context switching
Deciding what process to run is called scheduling
  Programs can be scheduled in a variety of ways!

## Slide 19: User mode: multiple applications
CPU
RAM
Process A
Process B

## Slide 20: User mode: multiple applications
CPU
RAM
Process A
Process B

## Slide 21: User mode: multiple applications
CPU
RAM
Process A
Process B
Process A

## Slide 22: User mode: multiple applications
CPU
RAM
Process A
Process B
Process A
SWITCH

## Slide 23: User mode: multiple applications
CPU
RAM
Process A
Process B
Process A
Process B
Wait… that shouldn’t happen!

## Slide 24: User mode: multiple applications
CPU
RAM
Process A
Process B
Process A
Process B
Please give me Process A’s data! I am evil!

## Slide 25: User mode: multiple applications
CPU
RAM
Process A
Process B
Process A
Process B
Process C
Process C

## Slide 26: User mode: multiple applications
CPU
RAM
Process A
Process A
Process C
Process C
Process D
Process D
Hmm… There’s enough space, but not all together!

## Slide 27: User mode: multiple applications
CPU
RAM
Process A
Process A
Process C
Process C
Process D
Process D
There we go!

## Slide 28: User mode: multiple applications
CPU
RAM
Process A
Process A
Process C
Process C
Process D
Process D
Wait… This isn’t my data?

## Slide 29: Protection Required
Application could overwrite another application’s memory
Applications may want to address more memory than that is available in MM
Solution: Virtual Memory. Give each process the illusion of a full memory address space that it has completely to itself

## Slide 30: Virtual: The Illusion!
CPU
RAM
Process A
I am the ONLY PROCESS accessing memory, and I don’t have to share it with anyone!

## Slide 31: Physical: The Reality!
CPU
RAM
Process A
Process B
Process A
Process B
Process C
Process C
DISK

## Slide 32: Memory Hierarchy
Regs
L2 Cache
Memory
Disk
Tape
Instr Operands
Blocks
Pages
Files
Upper Level
Lower Level
Faster
Larger
L1 Cache
Blocks
Now:
Virtual Memory
Earlier: Caches

## Slide 33: “Bare” 5-Stage Pipeline
In a bare machine, the only kind of address is a physical address
PC
Inst. Cache
D
Decode
E
M
Data Cache
W
+
Main Memory (DRAM)
Memory Controller
Physical Address
Physical Address
Physical Address
Physical Address
Physical Address

## Slide 34: Virtual address and Physical Address
PC
Inst. Cache
D
Decode
E
M
Data Cache
W
+
Main Memory (DRAM)
Memory Controller
Physical Address
Physical Address
Physical Address
Physical Address
Physical Address
Logical Address

## Slide 35: Address Spaces
Linear address space: Ordered set of contiguous non-negative integer addresses: {0, 1, 2, 3 … }
Virtual address space: Set of N = 2n virtual addresses {0, 1, 2, 3, …, N-1}
  N-bit address space: a virtual address space with N = 2n addresses
  Modern systems typically support either 32-bit or 64-bit virtual address spaces.
Physical address space: Set of M = 2m physical addresses {0, 1, 2, 3, …, M-1}
Notes: Virtual Address Space is usually much larger than Physical Address Space
Physical Address space is that of DRAM – the main memory.
Virtual address space is the same for all processes.

## Slide 36: Why Virtual Memory?
When you execute a program, do you bother about main memory?
Don’t you assume that all the memory is for your program?
Do you even know what location in Main Memory your program resides?
Do you also know if the full program resides in the Main Memory?
What is your view about the addresses used in your program or process?
  BTW, you know that a process is an instance of executing program

## Slide 37: Why Virtual Memory (VM)?
Uses main memory efficiently
  Use DRAM as a cache for parts of a virtual address space
Simplifies memory management
  Each process gets the same uniform linear address space
Isolates address spaces
  One process can’t interfere with another’s memory
  User program cannot access privileged kernel information and code

## Slide 38: Each process has it’s own (virtual) address space
Process 1
Process 2
Process n

## Slide 39: Address Space, Virtual Address, Physical Address

## Slide 40: Address Spaces
Virtual address space: Set of N = 2n virtual addresses {0, 1, 2, 3, …, N-1}
  Set of addresses that the user program knows about
  N-bit address space: a virtual address space with N = 2n addresses
  Modern systems typically support either 32-bit or 64-bit virtual address spaces.
Physical address space: Set of M = 2m physical addresses {0, 1, 2, 3, …, M-1}
  Set of addresses that map to actual physical locations in memory
  Hidden from user applications
Notes: Virtual Address Space is usually much larger than Physical Address Space
Physical Address space is that of DRAM – the main memory.
Virtual address space is the same for all processes.

## Slide 41: Virtual vs. Physical Addresses
Each Process uses it’s own address space
Processes use virtual addresses, e.g., 0 … 0xffff,ffff
  Many processes, all using same (conflicting) addresses
Memory uses physical addresses (also, e.g., 0 ... 0xffff,ffff)
Memory manager maps virtual to physical addresses
Processor (& Caches)
Control
Datapath
PC
Registers
(ALU)
Memory (DRAM)
Bytes
?
Virtual Address
Physical Address
Many of these (software & hardware cores)
One main memory
Memory manager
Ref: Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 42: VM as a tool for caching

## Slide 43: VM as a Tool for Caching
Conceptually, virtual memory is an array of N contiguous bytes stored on disk. Virtual Memory (on disk) has pages.
  Pages are bigger (say 4KB) thank Blocks (typically 64 bytes)
The contents of the array on disk are cached in physical memory (DRAM cache)
  These cache blocks are called pages (size is P = 2p bytes)
PP 2m-p-1
Physical memory
Empty
Empty
Uncached
VP 0
VP 1
VP 2n-p-1
Virtual memory
Unallocated
Cached
Uncached
Unallocated
Cached
Uncached
PP 0
PP 1
Empty
Cached
0
N-1
M-1
0
Virtual pages (VPs)
stored on disk
Physical pages (PPs)
cached in DRAM
Notes: Virtual Pages are numbered VP0, VP1, … VP 2n-p - 1

## Slide 44: Note
At any point in time, the set of virtual pages is partitioned into three disjoint subsets:
  Unallocated: Pages that have not yet been allocated (or created) by the VM system. Unallocated blocks do not have any data associated with them, and thus do not occupy any space on disk.
  Cached: Allocated pages that are currently cached in physical memory.
  Uncached: Allocated pages that are not cached in physical memory.

## Slide 45: DRAM Cache Organization
DRAM cache organization driven by the enormous miss penalty
  DRAM is about 10x slower than SRAM
  Disk is about 10,000x slower than DRAM
  Time to load block from disk > 1ms (> 1 million clock cycles)
    CPU can do a lot of computation during that time
Consequences
  Large page (block) size: typically 4 KB
    Linux “huge pages” are 2 MB (default) to 1 GB
  Fully associative
    Any VP can be placed in any PP
    Requires a “large” mapping function – different from cache memories
  Highly sophisticated, expensive replacement algorithms
    Too complicated and open-ended to be implemented in hardware
  Write-back rather than write-through

## Slide 46: Enabling Data Structure: Page Table
A page table is an array of page table entries (PTEs) that maps virtual pages to physical pages.
  Per-process kernel data structure in DRAM
null
null
Memory resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 4
Virtual memory
(disk)
Valid
0
1
0
1
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3

## Slide 47: Note
Each page in the virtual address space has a PTE at a fixed offset in the page table
Each PTE consists of a valid bit and an n-bit address field
The valid bit indicates whether the virtual page is currently cached in DRAM
If the valid bit is set, the address field indicates the start of the corresponding physical page in DRAM where the virtual page is cached
Valid bit is not set:
  Null address indicates that the virtual page has not been allocated
  Non-null address points to the start of virtual page on disk
Any physical page can contain any virtual page (fully associative)

## Slide 48: Page Hit
Page hit: reference to VM word that is in physical memory (DRAM cache hit)
null
null
Memory resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 4
Virtual memory
(disk)
Valid
0
1
0
1
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
Virtual address

## Slide 49: Page Fault
Page fault: reference to VM word that is not in physical memory (DRAM cache miss)
null
null
Memory resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 4
Virtual memory
(disk)
Valid
0
1
0
1
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
Virtual address

## Slide 50: Triggering a Page Fault
User writes to memory location
That portion (page) of user’s memory is currently on disk
MMU triggers page fault exception
  Raise privilege level to supervisor mode
  Causes procedure call to software page fault handler
int a[1000];
main ()
{
a[500] = 13;
}
80483b7: c7 05 10 9d 04 08 0d movl $0xd,0x8049d10
User code
Kernel code
Exception: page fault
Execute page fault handler
movl

## Slide 51: Handling Page Fault
Page miss causes page fault (an exception)
null
null
Memory resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 4
Virtual memory
(disk)
Valid
0
1
0
1
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
Virtual address

## Slide 52: Handling Page Fault
Page miss causes page fault (an exception)
Page fault handler selects a victim to be evicted (here VP 4)
null
null
Memory resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 3
Virtual memory
(disk)
Valid
0
1
1
0
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
Virtual address

## Slide 53: Handling Page Fault
Page miss causes page fault (an exception)
Page fault handler selects a victim to be evicted (here VP 4)
Offending instruction is restarted: page hit!
null
null
Memory resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 3
Virtual memory
(disk)
Valid
0
1
1
0
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
Virtual address
Key point: Waiting until the miss to copy the page to DRAM is known as demand paging

## Slide 54: Completing page fault
Page fault handler executes return
  Return to instruction that caused fault
  But, this time there is no page fault
int a[1000];
main ()
{
a[500] = 13;
}
80483b7: c7 05 10 9d 04 08 0d movl $0xd,0x8049d10
User code
Kernel code
Exception: page fault
Copy page from disk to memory
Return and reexecute movl
movl

## Slide 55: Terminology
Pages (= same as blocks)
Swapping or Paging
  The activity of transferring a page between disk and memory
Paging
  The strategy of waiting until the last moment to swap in a page, when a miss occurs
  all modern systems use demand paging.
Other approaches try to predict misses and swap pages in before they are actually referenced

## Slide 56: Allocating Pages
Allocating a new page (VP 5) of virtual memory
  May be as a result of malloc
Subsequent miss will bring it into memory
null
Memory resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 3
Virtual memory
(disk)
Valid
0
1
1
0
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
VP 5

## Slide 57: Locality to the Rescue Again!
Virtual memory works because of locality
At any point in time, programs tend to access a set of active virtual pages called the working set
  Programs with better temporal locality will have smaller working sets
If (working set size < main memory size)
  Good performance for one process (after cold misses)
If (working set size > main memory size )
  Thrashing: Performance meltdown where pages are swapped (copied) in and out continuously
  If multiple processes run at the same time, thrashing occurs if their total working set size > main memory size

## Slide 58: Lecture Summary
Programmer’s view of virtual memory
  Each process has its own private linear address space
  Cannot be corrupted by other processes
System view of virtual memory
  Uses memory efficiently by caching virtual memory pages
    Efficient only because of locality

## Slide 59: Backup

## Slide 60: The Problem
Physical memory is of limited size (cost)
  What if you need more?
  Should the programmer be concerned about the size of code/data blocks fitting physical memory?
  Should the programmer manage data movement from disk to physical memory?
  Should the programmer ensure two processes (different programs) do not use the same physical memory?
Also, ISA can have an address space greater than the physical memory size
  E.g., a 64-bit address space with byte addressability
  What if you do not have enough physical memory?

## Slide 61: Difficulties of Direct Physical Addressing
Programmer needs to manage physical memory space
  Inconvenient and hard
  Harder when you have multiple processes
Difficult to support code and data relocation
  Addresses are directly specified in the program
Difficult to support multiple processes
  Protection and isolation between multiple processes
  Sharing of physical memory space
Difficult to support data/code sharing across processes

## Slide 62: What does a programmer need ?

## Slide 63: Ideal Memory
Zero access time (latency)
Infinite capacity
Zero cost
Infinite bandwidth (to support multiple accesses in parallel)

## Slide 64: Virtual Memory
Idea: Give the programmer the illusion of a large address space while having a small physical memory
  So that the programmer does not worry about managing physical memory
  We will use the term physical memory to refer to main memory
Programmer can assume he/she has “infinite” amount of physical memory
Hardware and software cooperatively and automatically manage the physical memory space to provide the illusion
  Illusion is maintained for each independent process

## Slide 65: Abstraction: Virtual vs. Physical Memory
Programmer sees virtual memory
  Can assume the memory is “infinite”
Reality: Physical memory size is much smaller than what the programmer assumes
The system (system software + hardware, cooperatively) maps virtual memory addresses to physical memory
  The system automatically manages the physical memory space transparently to the programmer
+ Programmer does not need to know the physical size of memory nor manage it  A small physical memory can appear as a huge one to the programmer  Life is easier for the programmer
-- More complex system software and architecture

## Slide 66: Basic Mechanism
Indirection (in addressing)
Address generated by each instruction in a program is a “virtual address”
  i.e., it is not the physical address used to address main memory
  called “linear address” in x86
An “address translation” mechanism maps this address to a “physical address”
  called “real address” in x86
  Address translation mechanism can be implemented in hardware and software together

## Slide 67: Physical Address, Virtual Address Address Space

## Slide 68: A System Using Physical Addressing
Used in “simple” systems like embedded microcontrollers in devices like cars, elevators, and digital picture frames
0:
1:
M-1:
Physical (Main) memory
CPU
2:
3:
4:
5:
6:
7:
Physical address
(PA)
Data word
8:
...
4
Notes: The main memory of a computer system is organized as an array of M contiguous byte-size cells. Each byte has a unique physical address (PA).

## Slide 69: Address Spaces
Linear address space: Ordered set of contiguous non-negative integer addresses: {0, 1, 2, 3 … }
Virtual address space: Set of N = 2n virtual addresses {0, 1, 2, 3, …, N-1}
  N-bit address space: a virtual address space with N = 2n addresses
  Modern systems typically support either 32-bit or 64-bit virtual address spaces.
Physical address space: Set of M = 2m physical addresses {0, 1, 2, 3, …, M-1}

## Slide 70: Address Translation Virtual Memory Organization

## Slide 71: A System with Virtual Memory (Page based)
Address Translation: The hardware converts virtual addresses into physical addresses via an OS-managed lookup table (page table)
CPU
0:
1:
N-1:
Main Memory
0:
1:
P-1:
Page Table
Disk
Virtual
Addresses
Physical
Addresses

## Slide 72: Virtual Pages, Physical Frames
Virtual address space divided into pages
Physical address space divided into frames
A virtual page is mapped to
  A physical frame, if the page is in physical memory
  A location in disk, otherwise
If an accessed virtual page is not in memory, but on disk
  Virtual memory system brings the page into a physical frame and adjusts the mapping  this is called demand paging
Page table is the table that stores the mapping of virtual pages to physical frames

## Slide 73: Physical Memory as a Cache
In other words…
Physical memory is a cache for pages stored on disk
  In fact, it is a fully associative cache in modern systems (a virtual page can potentially be mapped to any physical frame)
  Most accesses hit in the physical memory at the speed of DRAM, yet the program enjoys the capacity of the larger virtual memory
Similar caching issues exist as we have covered earlier:
  Placement: where and how to place/find a page in cache?
  Replacement: what page to remove to make room in cache?
  Granularity of management: large, small, uniform pages?
  Write policy: what do we do about writes? Write back?

## Slide 74: Cache/Virtual Memory Analogues
Cache | Virtual Memory
Block | Page
Block Size | Page Size
Block Offset | Page Offset
Miss | Page Fault
Tag | Virtual Page Number

## Slide 75: Virtual Memory Definitions
Page size: amount of memory transferred from hard disk to DRAM at once
Address translation: determining the physical address from the virtual address
Page table: lookup table used to translate virtual addresses to physical addresses (and find where the associated data is)

## Slide 76: Virtual and Physical Addresses
Most accesses hit in physical memory
But programs see the large capacity of virtual memory

## Slide 77: Virtual Memory Example
System:
  Virtual memory size: 2 GB = 231 bytes
  Physical memory size: 128 MB = 227 bytes
  Page size: 4 KB = 212 bytes

## Slide 78: Virtual Memory Example
System:
  Virtual memory size: 2 GB = 231 bytes
  Physical memory size: 128 MB = 227 bytes
  Page size: 4 KB = 212 bytes
Organization:
  Virtual address: 31 bits
  Physical address: 27 bits
  Page offset: 12 bits
  # Virtual pages = 231/212 = 219 (VPN = 19 bits)
  # Physical pages = 227/212 = 215 (PPN = 15 bits)

## Slide 79: Address Translation

## Slide 80: Virtual Memory Example

## Slide 81: How Do We Translate Addresses?
Page table
  Has entry for each virtual page
Each page table entry has:
  Valid bit: whether the virtual page is located in physical memory (if not, it must be fetched from the hard disk)
  Physical page number: where the page is located
  Dirty bits: Replacement policy

## Slide 82: Page Table Example

## Slide 83: Page Table Example 1
What is the physical address of virtual address 0x5F20?

## Slide 84: Page Table Example 1
What is the physical address of virtual address 0x5F20?
  Note: number of bits in VA: 8
  Virtual Page number: 05
  Entry 5 in page table indicates VPN 5 is in physical page 1
  Physical address is 0x1F20

## Slide 85: Page Table Example 2
What is the physical address of virtual address 0x73E0?

## Slide 86: Page Table Example 2
What is the physical address of virtual address 0x73E0?
  VPN = 7
  Entry 7 in page table is invalid, so the page is not in physical memory
  The virtual page must be swapped into physical memory from disk
86

## Slide 87: Issue: Page Table Size
Suppose 64-bit VA and 40-bit PA, how large is the page table?
  252 entries x ~4 bytes  254 bytes
    that is for just one process!
    the process may not be using the entire VM space!
VPN
Page Offset
page
table
concat
PA
64-bit
12-bit
52-bit
28-bit
40-bit

## Slide 88: Page Table Challenges
Page table is large
  at least part of it needs to be located in physical memory
Each load/store requires at least two memory accesses:
  1. one for translation (page table read)
  2. one to access data with the physical address (after translation)
Two memory accesses to service a load/store greatly degrades load/store execution time

## Slide 89: Translation Lookaside Buffer (TLB)
Page table accesses have great temporal locality
Idea: Cache the page table entries (PTEs) in a hardware structure in the processor
Translation lookaside buffer (TLB)
  Small cache of most recently used translations (Page table entries)
  Significantly reduces number of memory accesses required for most loads/stores to only one

## Slide 90: Translation Lookaside Buffer (TLB)
Page table accesses have a lot of temporal locality
  Data accesses have temporal and spatial locality
  Large page size (say 4KB, 8KB, or even 1-2GB), so consecutive loads/stores likely to access same page
TLB
  Small: accessed in < 1 cycle
  Typically 16 - 512 entries
  High associativity
  > 99 % hit rates typical (depends on workload)
  Reduces # of memory accesses for most loads and stores to only 1

## Slide 91: Example Two-Entry TLB

## Slide 92: Memory Protection

## Slide 93: Memory Protection
Multiple programs (processes) run at once
  Each process has its own page table
  Each process can use entire virtual address space without worrying about where other programs are
A process can only access physical pages mapped in its page table – cannot overwrite memory of another process
  Provides protection and isolation between processes
  Enables access control mechanisms per page

## Slide 94: Virtual Memory Summary
Virtual memory gives the illusion of “infinite” capacity
A subset of virtual pages are located in physical memory
A page table maps virtual pages to physical pages – this is called address translation
A TLB speeds up address translation
Using different page tables for different programs provides memory protection

## Slide 95: Backup

## Slide 96: Supporting Virtual Memory
Virtual memory requires both HW+SW support
  Page Table is in memory
  Can be cached in special hardware structures called Translation Lookaside Buffers (TLBs)
The hardware component is called the MMU (memory management unit)
  Includes Page Table Base Register(s), TLBs, page walkers
It is the job of the software to leverage the MMU to
  Populate page tables, decide what to replace in physical memory
  Change the Page Table Register on context switch (to use the running thread’s page table)
  Handle page faults and ensure correct mapping

## Slide 97: Some System Software Jobs for VM
Keeping track of which physical frames are free
Allocating free physical frames to virtual pages
Page replacement policy
  When no physical frame is free, what should be swapped out?
Sharing pages between processes
Copy-on-write optimization
Page-flip optimization

## Slide 98: Page Fault (“A Miss in Physical Memory”)
If a page is not in physical memory but disk
  Page table entry indicates virtual page not in memory
  Access to such a page triggers a page fault exception
  OS trap handler invoked to move data from disk into memory
    Other processes can continue executing
    OS has full control over placement
CPU
Memory
Page Table
Disk
Virtual
Addresses
Physical
Addresses
CPU
Memory
Page Table
Disk
Virtual
Addresses
Physical
Addresses
Before fault
After fault

## Slide 99: Servicing a Page Fault
Disk
(1) Processor signals controller
  Read block of length P starting at disk address X and store starting at memory address Y
(2) Read occurs
  Direct Memory Access (DMA)
  Under control of I/O controller
(3) Controller signals completion
  Interrupt processor
  OS resumes suspended process
Disk
Memory-I/O bus
Processor
Cache
Memory
I/O
controller
Reg
(2) DMA Transfer
(1) Initiate Block Read
(3) Read Done

## Slide 100: Page Table is Per Process
Each process has its own virtual address space
  Full address space for each program
  Simplifies memory allocation, sharing, linking and loading.
Virtual Address Space for Process 1:
Physical Address
Space (DRAM)
VP 1
VP 2
PP 2
Address Translation
0
0
N-1
0
N-1
M-1
VP 1
VP 2
PP 7
PP 10
(e.g., read/only library code)
...
...
Virtual Address Space for Process 2:

## Slide 101: Address Translation
Parameters
  P = 2p = page size (bytes).
  N = 2n = Virtual-address limit
  M = 2m = Physical-address limit
virtual page number
page offset
virtual address
physical frame number
page offset
physical address
0
p–1
address translation
p
m–1
n–1
0
p–1
p
Page offset bits don’t change as a result of translation

## Slide 102: Address Translation (IV)
virtual page number (VPN)
page offset
virtual address
physical frame number (PFN)
page offset
physical address
0
p–1
p
m–1
n–1
0
p–1
p
page table
base register
(per process)
if valid=0
then page
not in memory (page fault)
valid
physical frame number (PFN)
VPN acts as
table index
Separate (set of) page table(s) per process
VPN forms index into page table (points to a page table entry)
Page Table Entry (PTE) provides information about page
access

## Slide 103: Address Translation: Page Hit

## Slide 104: Address Translation: Page Fault

## Slide 105: Page Replacement Algorithms
If physical memory is full (i.e., list of free physical pages is empty), which physical frame to replace on a page fault?
Is True LRU feasible?
  4GB memory, 4KB pages, how many possibilities of ordering?
Modern systems use approximations of LRU
  E.g., the CLOCK algorithm
And, more sophisticated algorithms to take into account “frequency” of use
  E.g., the ARC algorithm
  Megiddo and Modha, “ARC: A Self-Tuning, Low Overhead Replacement Cache,” FAST 2003.

## Slide 106: A System Using Virtual Addressing
Used in all modern servers, laptops, and smart phones
One of the great ideas in computer science
Keywords: Address Translation, Memory Management Unit
0:
1:
M-1:
Physical (main) memory
MMU
2:
3:
4:
5:
6:
7:
Physical address
(PA)
Data word
8:
...
CPU
Virtual address
(VA)
CPU Chip
4
4100
Notes: MMU provides virtualized view of Physical Memory..It intercepts the request from CPU..
The task of converting a virtual address to a physical one is known as address translation
Dedicated hardware on the CPU chip called the memory management unit (MMU) translates virtual addresses on the fly, using a lookup table stored in main memory whose contents are managed by the operating system