## Slide 1: CS 211 Computer Architecture Lecture 4: Beyond Moore’s Law
Ravi Mittal
ravi.mittal@iitgoa.ac.in
Indian Institute of Technology, Goa

## Slide 2: References
Chapter 1 - Computer Abstractions and Technology - Patterson and Hennessy
High Performance Computer Architecture Challenges – Class presentation, Rajeev Balasubramonian, School of Computing, University of Utah
From Single Core to multi-core: Preparing for new exponential, Paper, by Jeff Parkhurst, John Darringer, Bill Grundmann, IEEE Explore, ICCAD 2006: 67-72
Making Sense of Recent Researchin Temperature-Aware Design, Presentation, Kevin Skadron, Univ. of Virginia

## Slide 3: Last class

## Slide 4: Moore’s Law
The number of transistors on a chip doubles about every 18-24 months
  Gordon Moore, co-founder of Intel, 1965
  True for 50+ years

## Slide 5: Interpretation
Transistor count is increasing per Moore’s law
  Currently Microprocessor chips contain 10 Billion to 60 Billion transistors
    Apple M1 (year 2020): 16 Billion Transistors : 5 nm wide
      about 25 silicon atoms
    Nvidia GA 100 Ampere (year 2020): 54 Billion transistors: 7 nm
    Samsung DRAM eUFS (1 TB) (year 2020): 8Tb; 2048 Billion Transistors
Number of cores is increasing (why?)
The way to utilize increase in transistors –> use multiple cores

## Slide 6: Uniprocessor Performance
Constrained by power, instruction-level parallelism, memory latency
Chart plots performance relative to the VAX 11/780

## Slide 7: Power and Clock Rate - Trend
In CMOS IC technology
Chapter 1 — Computer Abstractions and Technology — Patterson and Hennessy

## Slide 8: Trend in Power
Supply voltage is decreasing over time; 5 V  1 V
  “Voltage scaling” is reaching it’s limit
Clock frequency – not much increase

## Slide 9: In the class we will study
Clock Speed improvements – and Processor design
Power Wall
Moving to Multicore Architecture
Dynamic Power and Thermal Management
Ongoing work (self reading)

## Slide 10: Clock Speed Improvement – Processor Design

## Slide 11: Increase in Clock Speed
Microarchitecture must be able to do meaningful work in each clock cycle
Microarchitecture uses pipeline architecture

## Slide 12
The Basic Pipeline
Consider an automobile assembly line:
Stage 1
Stage 2
Stage 3
Stage 4
1 day
1 day
1 day
1 day
A new car
rolls out
every day
A new car
rolls out every
half day
In each case, it takes 4 days to build a car, but…
More stages  more parallelism and less time
between cars

## Slide 13
What Determines Clock Speed?
Clock speed is a function of work done in each stage – in the earlier examples, the clock speeds were 1 car/day and 2 cars/day
Similarly, it takes plenty of “work” to execute an instruction and this work is broken into stages
Execution of a single instruction
250ps  4GHz clock speed

## Slide 14
Clock Speed Improvements
Why have we seen such dramatic improvements
in clock speed?
  work has been broken up into more stages
  transistors have been becoming faster
    as technology improves, we can draw smaller and smaller transistors/gates on a chip and that improves their speed

## Slide 15
Will these Improvements Continue?
Transistors will continue to shrink and become faster for some more years
Each pipeline stage is already pretty small –improvements from this factor will cease

## Slide 16: Power Wall

## Slide 17: Power Consumption
Power (per unit time) = Dynamic Power + Static Power
Dynamic power ~ capacitance x voltage2 x frequency
Leakage Power ~ Voltage x Leakage Current
Lecture notes: Unit 12 CS 501Computer Architecture – Prof Milo Martin, Univ of Pennsylvania
Notes: Energy = power x time = (dynpower + lkgpower) x time

## Slide 18: Dynamic Power Pdynamic
It is Switching or active power
  Energy to switch a gate (0 to 1, 1 to 0)
  Each gate has capacitance C
  Charge stored is ~ C * V
  Energy to charge/discharge a capacitor is ~ to C * V2
  Time to charge/discharge a capacitor is ~ to V
    Result: frequency ~ to V
Pdynamic ~ a*C*V2 *f ~ a*C*V3
  C: capacitance per transistor (size of transistors)
  V: voltage (supply voltage for gate: Vdd)
  f: frequency (transistor switching freq. is ~ to clock freq.)
  a: activity factor (not all transistors may switch this cycle)

## Slide 19: Static Power
aka idle or leakage power
  Transistors don’t turn off all the way  Transistors “leak”
Pleak ~ V*Ileak
  V: voltage
  Ileak is the current that flows through transistors even when they are off
Pleak increases with the number of transistors on a chip
  It is increasing – as per Moore’s law
Use of materials (other than silicon) and circuit level technology – limit the effect of leakage
Hence, the focus is on reduction of dynamic power – which also reduces leakage power

## Slide 20: Reducing Dynamic Power
Target each component: Pdynamic ~ a*C*V2 *f
Reduce Capacitance
  Smaller size has smaller capacitance
  Integration is reducing value of C: Capacitance of a transistor
Reduce Voltage
  Quadratic reduction in energy consumption
  But also slows transistors (transistor speed is ~ to V)
  V can’t be reduced – as it will increase leakage current
  Currently it is around 0.9 – 1 V

## Slide 21: Reducing Dynamic Power
Reduce frequency (f)
  Slower clock frequency (reduces power but not energy)
  Yes. However it will reduce performance
  Frequency wall: : can’t figure out how to increase clock frequency without unreasonable increase in power
Reduce Activity (a)
  Clock gating disable clock to unused parts of chip
  Don’t switch gates unnecessarily
Power Wall
  Air cooling capped at ~150W (thermal design power - TDP)
  Today: some chips are already thermally limited
Moore’s Law is providing area that a single thread can’t economically use

## Slide 22: What are the limitatons?
Every generation transistor feature size reduces by 0.7
Area reduces by 0.49 = 0.5
Assuming frequency remains flat
Pn  CV2f  0.7 (12) (1) = 0.7 P
  Power reduces by 0.7
Power density = Pn/A = 0.7/0.5 = 1.4
  And this is very optimistic, because C probably scales more like 0.8 or 0.9, and we want frequency to go up, so a more likely number is 1.5-1.75X
So, even if we keep the same frequency and voltage, every generation increase power density by 1.5 times

## Slide 23: Moving to Multicore Architecture

## Slide 24: If power density continues to increase and chip size remains the same..
No “free lunch” for software developers, must consider:
  Parallel systems

## Slide 25: Towards Multicore..
If we keep %-area dedicated to all the cores the same -- total power goes up by same factor
But max TDP for air cooling is expected to stay flat
  Around 200-250 W total and around 1.5 W/mm2
Multicore allows power to scale linearly with # cores
The shift to multicore does not eliminate the wall
  But heat/power can be managed within limits in each core

## Slide 26: Low-Fat Cores???
PClaes Oldenburg, Apple Core – Autumn http://www.greenwicharts.org/pastshows.asp

## Slide 27: Moore’s Law  Multiple cores
https://www.karlrupp.net/2015/06/40-years-of-microprocessor-trend-data/

## Slide 28: An example of Modern Chip Microprocessor
https://www.anandtech.com/show/5091/intel-core-i7-3960x-sandy-bridge-e-review-keeping-the-high-end-alive
Sandy Bridge E die
All on
The same
chip

## Slide 29: Intel’s Tiger Lake (Sept 2020)

## Slide 30: GPU

## Slide 31: Dynamic Power and Thermal Management

## Slide 32: Dynamic Power and Thermal Management
A lot of research happening in this area
Two primary ways
  Increase/Reduce Supply voltage
  Reduce activity
Techniques
  Monitoring
    Monitoring for thermal management
      Take temperature readings – with thermal sensors on chip
    Monitoring for power – not as easy as that of thermal
  Triggering of an action – by comparing with some threshold
  Take actions

## Slide 33: Dynamic Voltage Frequency Scaling (DVFS)
Dynamically trade-off power for performance
  Change the voltage and frequency at runtime under control of OS
  Reduction in voltage will reduce frequency
Note that Pdynamic ~ V3
Reduce V and f linearly
  Cubic decrease in dynamic power
  Linear decrease in performance (due to slower clock)
Linear decrease in static power
  Only modest static energy improvement
Most systems are designed for the peak performance – which is not always needed
Some parts of chip can run at a slower speed without affecting the outcome (without missing deadlines)

## Slide 34: Dynamic Voltage Frequency Scaling
Dynamic voltage/frequency scaling
  Favors parallelism
Example: Intel Xscale
  Can vary he voltage in a continuous fashion
  1 GHz to 200 MHz reduces energy used by 30x
    But around 5x slower
5 x 200 MHz in parallel  uses 1/6th the energy
Power is driving the trend toward multi-core

## Slide 35: DVFS technique (Continued)
Example Mobile device
  No need to apply DVFS – when mobile is plugged in
  When it is on battery, we can apply DVFS
Example Advanced Laptops
  Scaling can be done – task by task basis ( via OS) or within a task
Some microprocessor (eg Pentium 4) stops execution for short period of time – to manage thermal dissipation

## Slide 36: Resource Adaptation
Hibernation mode of Laptops – OS feature
  Dumps the processor state and contents of volatile memory to the hard disk
  Power offs the system
  Restarting (after hibernation state) – restoration of the earlier state
  Faster than a complete restart
Hibernation of some parts of a computer
  Disk or Display
  OS can monitor disk usage and prevent disk rotation ; It powers up the disk when there is a disk request
Selective turning off and on of different parts of computers

## Slide 37: Class Summary
Moore’s law – Number of transistors are doubling every 18-24 months – almost doubling computing power every 2 – 3 years with the same amount of $
No free lunch for programmers in future
  Integration is hitting power wall
Power consumed = Dynamic Power + Static Power
  Pdynamic ~ N*C*V2 *f*A
  Pstatic ~ N*V*e–Vt
Due to heating constraints
  a processor can’t accommodate more transistors  more heat
  Reduce voltage to approx 1 V
  Reduce frequency
Dynamic Voltage and Frequency scaling
Technology is moving towards Multicore architecture

## Slide 38: Backup: Ongoing Work

## Slide 39: Three Big Limits
Design and Manufacturing
  Material limits, design methodology
Speed of Light
  Imposes size/speed trade-off
Power Management
  Inefficiency adds up

## Slide 40: Today's Solutions
Design Changes
  Multiple Processors, active power management, new computer architectures
Interconnection Improvements
  3D interconnections
  Layout optimization, optical transmission
New Materials
  Gallium arsenide, carbon

## Slide 41: 3D Interconnections
Allows for shorter critical paths
Denser circuit layouts
Samsung Technology Development

## Slide 42: Gallium Arsenide Logic
Slowly developing, becoming competitive with silicon
Difficult to work with, but emerging technologies- promising
Combines well with optical interconnects
Compound Semiconductor

## Slide 43: Optical Interconnections
Faster, more efficient than copper
Easier to multiplex
Combines well with GaAs logic
IBM Research

## Slide 44: Power vs Energy
Energy tells us the true “cost” of performing a fixed task
Power (energy/time) poses constraints; can only work fast
enough to max out the power delivery or cooling solution
If processor A consumes 1.2x the power of processor B, but finishes the task in 30% less time, its relative energy is 1.2 X 0.7 = 0.84;
Processor A is better, provided that 1.2x power can be supported by the system

## Slide 45: Problem 1
For a processor running at 100% utilization at 100 W,
20% of the power is attributed to leakage. What is the
total power dissipation when the processor is running at
50% utilization?
Total power = dynamic power + leakage power
= 80W x 50% + 20W
= 60W
Solve for 0% utilization; the system consumes 20W.
This is the basis for “server consolidation” in datacenters
(move processes so you have a few highly utilized servers).

## Slide 46: Problem 2
If processor A consumes 1.4x the power of processor B,
but finishes the task in 20% less time, which processor
would you pick:
(a) if you were constrained by power delivery constraints?
Proc-B
(b) if you were trying to minimize energy per operation?
Proc-A is 1.4x0.8 = 1.12 times the energy of Proc-B
(c) if you were trying to minimize response times?
Proc-A is faster, but we could scale up the frequency
(and power) of Proc-B and match Proc-A’s response
time (while still doing better in terms of power and
energy)

## Slide 47: Problem 2
If processor A consumes 1.4x the power of processor B,
but finishes the task in 20% less time, which processor
would you pick:
(a) if you were constrained by power delivery constraints?
(b) if you were trying to minimize energy per operation?
(c) if you were trying to minimize response times?

## Slide 48: Reducing Power and Energy
Can gate off transistors that are inactive (reduces leakage)
DFS: Dynamic frequency scaling -- only reduces frequency and dynamic power
DVFS: Dynamic voltage and frequency scaling – can reduce voltage and frequency by (say) 10%; can slow a program by (say) 8%, but reduce dynamic power by 27%, reduce total power by (say) 23%, reduce total energy by 17%

## Slide 49: Problem 3
Processor-A at 3 GHz consumes 80 W of dynamic power
and 20 W of static power. It completes a program in 20
seconds.
What is the energy consumption if I scale frequency down
by 20%?
What is the energy consumption if I scale frequency and
voltage down by 20%?

## Slide 50: Moore’s law: Enablement of new era
People carry smart phone in their pocket
  More powerful than the biggest computer made in 1995
Slender laptops, Streaming video, social media, search, the cloud, smart devices, and the Internet, computers in automobiles, WWW, Human Genome project, social engineering, Online entertainment

## Slide 51: Reducing Static Power
Pstatic ~ N*V*e–Vt
Reduce the number of transistors (N)
  Use fewer transistors/gate
Disable transistors
  Power gating disable power to unused parts of chip
  Power down units (or entire core) not being used
    Long latency to power up
Reduce Voltage (V)
  Linear reduction in static energy consumption
  But also slows down transistors (transistor speed is ~ V)
Dual Vt – Use mix of high and low Vt transistors
  Use slow low leak transistors in SRAM
Low-leakage transistors