## Slide 1: CS 211 Computer Architecture Lecture 40: Virtual Memory – 2 Paged Memory
Ravi Mittal
ravi.mittal@iitgoa.ac.in
Indian Institute of Technology, Goa

## Slide 2: We will study today ..
Virtual Memory Concepts (Revision)
Paged Memory
Page Hit, Page Fault, Demand Paging
Page Table Location, Kernel Page Table
Summary

## Slide 3: Acknowledgements
Krste Asanović & Randy H. Katz, CS 61C: Great Ideas in Computer Architecture (Machine Structures), http://inst.eecs.berkeley.edu/~cs61c/
Chapter 6, Memory Hierarchy, Book: Computer Systems: A programmer’s perspective, Randal E. Bryant and David R. O’Hallaron
Prof Onur Mutlu’s Class Presentation, ETH Zürich, Lecture 21b: Memory Hierarchy and Caches, Sprint 2020
Patterson and Hennessy, Book: Computer Organization and Design, Hardware/Software Interface, RISC-V Edition
MIT 6.004 Spring 2020, Class on Caches
Digital Design and Computer Architecture: RISC-V Edition, Harris & Harris Elsevier

## Slide 4: Virtual Memory - Concepts (Last class)

## Slide 5: A System Using Physical Addressing
Used in “simple” systems like embedded microcontrollers in devices like cars, elevators, and digital picture frames
This is not the way most systems work: Desktop, Mobile etc
0:
1:
M-1:
Physical (Main) memory
CPU
2:
3:
4:
5:
6:
7:
Physical address
(PA)
Data word
8:
...
4
Notes: The main memory of a computer system is organized as an array of M contiguous byte-size cells. Each byte has a unique physical address (PA).

## Slide 6: Today’s computers
100’s of processes
  OS multiplexes these over available cores
But what about memory?
  There is only one!
  We cannot just ”save” its contents in a context switch …
100+ Processes, managed by OS
Ref: Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 7: Each process has it’s own (virtual) address space
Process 1
Process 2
Process n

## Slide 8: Virtual vs. Physical Addresses
Each Process uses it’s own address space
Processes use virtual addresses, e.g., 0 … 0xffff,ffff
  Many processes, all using same (conflicting) addresses
Memory uses physical addresses (also, e.g., 0 ... 0xffff,ffff)
Memory manager maps virtual to physical addresses
Processor (& Caches)
Control
Datapath
PC
Registers
(ALU)
Memory (DRAM)
Bytes
?
Virtual Address
Physical Address
Many of these (software & hardware cores)
One main memory
Memory manager

## Slide 9: Review: What is Paged VM?
Divide virtual memory and physical memory into equally sized segments called pages:
Virtual Memory
Physical Memory
0
1
2
3
4
5
6
7
0
1
2
3
Ref: Morgan Rae Reschenberg, Course 61C, Univ of California, Berkeley

## Slide 10: Review: What is Paged VM?
Each process has its own virtual memory, but all processes must share physical memory
Virtual Memory (A)
Physical Memory
0
1
2
3
4
5
6
7
0
1
2
3
Virtual Memory (B)
0
1
2
3
4
5
6
7
Ref: Morgan Rae Reschenberg, Course 61C, Univ of California, Berkeley

## Slide 11: Review: What is Paged VM?
Pages in physical memory correspond to pages in virtual memory
Virtual Memory (A)
Physical Memory
0
1
2
3
4
5
6
7
0
1
2
3
Virtual Memory (B)
0
1
2
3
4
5
6
7
Ref: Morgan Rae Reschenberg, Course 61C, Univ of California, Berkeley

## Slide 12: Review: What is Paged VM?
Each process has a table mapping its physical/virtual pages
Virtual Memory (A)
Physical Memory
0
1
2
3
4
5
6
7
0
1
2
3
VPN | PPN | Valid
0 | X | 0
1 | X | 0
2 | 0 | 1
3 | 2 | 1
4 | X | 0
5 | X | 0
6 | X | 0
7 | 3 | 1
Ref: Morgan Rae Reschenberg, Course 61C, Univ of California, Berkeley

## Slide 13: Review: What is Paged VM?
When a process needs more data, the oldest (LRU) page is removed from PM and replaced with a new page from disk
Virtual Memory (A)
Physical Memory
0
1
2
3
4
5
6
7
0
1
2
3
Virtual Memory (B)
0
1
2
3
4
5
6
7
Ref: Morgan Rae Reschenberg, Course 61C, Univ of California, Berkeley

## Slide 14: Review: What is Paged VM?
When a process needs more data, its oldest (LRU) page is removed from PM and replaced with a new page from disk
Virtual Memory (A)
Physical Memory
0
1
2
3
4
5
6
7
0
1
2
3
Virtual Memory (B)
0
1
2
3
4
5
6
7
Ref: Morgan Rae Reschenberg, Course 61C, Univ of California, Berkeley

## Slide 15: Review: What is Paged VM?
When a process needs more data, its oldest (LRU) page is removed from PM and replaced with a new page from disk
Virtual Memory (A)
Physical Memory
0
1
2
3
4
5
6
7
0
1
2
3
Virtual Memory (B)
0
1
2
3
4
5
6
7
Ref: Morgan Rae Reschenberg, Course 61C, Univ of California, Berkeley

## Slide 16: Paged Memory
Today “paged memory” dominates
We call main memory (incl Caches) as physical memory
Physical memory (DRAM) is broken into fixed size blocks called pages (also called frames)
  Typical page size: 4 KB
Processes use Virtual Address
Virtual address space divided into pages
Interpret each N-bit virtual address as a pair:
  <virtual page number, offset>
Virtual page number (e.g., 20 Bits) | offset (e.g., 12 Bits)
Virtual address (e.g., 32 Bits)

## Slide 17: Modern Virtual Memory Systems Illusion of a large, private, uniform store
Protection
  Several programs, each with their private address space and one or more shared address spaces
Demand Paging
  Provides the ability to run programs larger than the primary memory
  Hides differences in machine configurations
The price is address translation on
each memory reference
OS
progi
Primary
Memory
Swapping
Store
VA
PA
mapping
TLB
Ref: Morgan Rae Reschenberg, Course 61C, Univ of California, Berkeley
Notes: Portability on machines with different memory configurations.

## Slide 18: Paged Memory

## Slide 19: Virtual Pages
A virtual page is mapped to
  A physical page in physical memory, if the virtual page is in physical memory
  A page in disk, otherwise

## Slide 20: Paged Memory for a process

## Slide 21: Page Table
Page table is the table that stores the mapping of virtual pages to physical pages
  Page table contains the physical page number (i.e., starting physical address) for each virtual page number
Note: N=32 in RISC-V system we have seen so far but other values are common
  Must fit within address registers but processor or OS can limit it further (e.g., x86-64 uses 48-bit VA)

## Slide 22: Each Process has a page table
Page N
Page 2
Page 1
Page 0
Memory (DRAM)
Page Table
Page Table
Page Table
Each process has a dedicated page table. Physical memory non-consecutive.

## Slide 23: Each Process has a page table
Page table makes is possible to store the pages of a program non-contiguously

## Slide 24: Paged Memory Address Translation
OS keeps track of which process is active
  Chooses correct page table
Memory manager extracts page number from virtual address
Looks up page address in page table
Computes physical memory address from sum of
  Page address and
  Offset (from virtual address)
Virtual Page Number | offset
Virtual address (e.g. 32 Bits)
Physical Page Number | offset
Physical address
Physical addresses may (but do not have to) have more or fewer bits than virtual addresses

## Slide 25: Virtual to Physical Address
Virtual Address
Virtual Page Number
Offset
Physical Page Number
Offset
Page table lookup!
Physical Address
Ref: Morgan Rae Reschenberg, Course 61C, Univ of California, Berkeley

## Slide 26: Virtual Page not in Physical Memory?
Then it must exist on Disk
Virtual memory system brings the page from disk into a page in physical memory
Updates mapping in the page table

## Slide 27: Virtual Pages on Disk
At any time, the set of virtual pages on disk is partitioned into three disjoint subsets:
  Unallocated: Pages that have not yet been allocated (or created) by the VM system. Unallocated blocks do not have any data associated with them, and thus do not occupy any space on disk
  Cached: Allocated pages that are currently cached in physical memory.
  Uncached: Allocated pages that are not cached in physical memory. They are available in Disk Memory
PP 2m-p-1
Physical memory
Empty
Empty
Uncached
VP 0
VP 1
VP 2n-p-1
Disk memory
Unallocated
Cached
Uncached
Unallocated
Cached
Uncached
PP 0
PP 1
Empty
Cached
0
N-1
M-1
0
Virtual pages (VPs)
stored on disk
Physical pages (PPs)
cached in DRAM
Adapted from Bryant and O’Hallaron, Computer Systems: A Programmer’s Perspective, Third Edition
Notes: Virtual Pages are numbered VP0, VP1, … VP 2n-p - 1

## Slide 28: Page Table on Physical Memory
A page table is an array of page table entries (PTEs) that maps virtual pages to physical pages.
  For every process there is a page table in Main Memory (DRAM)
null
null
Memory resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 4
Disk memory
Valid
0
1
0
1
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
Adapted from Bryant and O’Hallaron, Computer Systems: A Programmer’s Perspective, Third Edition

## Slide 29: Note
Each page in the virtual address space has a PTE at a fixed offset in the page table
Each PTE consists of a valid bit and an n-bit address field
The valid bit indicates whether the virtual page is currently cached in DRAM
If the valid bit is set, the address field indicates the start of the corresponding physical page in DRAM where the virtual page is cached
Valid bit is not set:
  Null address indicates that the virtual page has not been allocated
  Non-null address points to the start of virtual page on disk
Any physical page can contain any virtual page (fully associative)

## Slide 30: Page Hit, Page Fault, Demand Paging

## Slide 31: Page Hit
Page hit: reference to VM word that is in physical memory (DRAM cache hit)
null
null
Memory resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 4
Virtual memory
(disk)
Valid
0
1
0
1
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
VPN Offset
Adapted from Bryant and O’Hallaron, Computer Systems: A Programmer’s Perspective, Third Edition
Page Not hit: PTE refers to location in swap space on disk

## Slide 32: Page Fault
Page fault: reference to VM word that is not in physical memory (DRAM cache miss)
null
null
Memory resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 4
Disk memory
Valid
0
1
0
1
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
Adapted from Bryant and O’Hallaron, Computer Systems: A Programmer’s Perspective, Third Edition
VPN Offset

## Slide 33: Handling Page Fault (1/3)
Page miss causes page fault (an exception)
null
null
page table
Memory resident
(DRAM)
Physical memory
(DRAM)
VP 7
VP 4
Virtual memory
(disk)
Valid
0
1
0
1
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
VPN Offset
Adapted from Bryant and O’Hallaron, Computer Systems: A Programmer’s Perspective, Third Edition
Virtual address

## Slide 34: Handling Page Fault (2/3)
Page fault handler selects a victim to be evicted (here VP4 – see previous page)
  Uses some page replacement policy such as LRU
Brings in VP3 from Disk to Physical Memory
null
null
Memory resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 3
Virtual memory
(disk)
Valid
0
1
1
0
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
VPN Offset
Adapted from Bryant and O’Hallaron, Computer Systems: A Programmer’s Perspective, Third Edition
Virtual address

## Slide 35: Handling Page Fault (3/3)
Offending instruction is restarted: page hit!
null
null
Memory resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 3
Virtual memory
(disk)
Valid
0
1
1
0
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
VPN Offset
Key point: Waiting until the miss to copy the page to DRAM is known as demand paging
Adapted from Bryant and O’Hallaron, Computer Systems: A Programmer’s Perspective, Third Edition
Virtual address

## Slide 36: Triggering a Page Fault
User writes to memory location
That portion (page) of user’s memory is currently on disk
Memory Management Unit (MMU) triggers page fault exception
  Raise privilege level to supervisor mode
  Causes procedure call to software page fault handler
User code
Kernel code
Exception: page fault
Execute page fault handler
sw

## Slide 37: Completing page fault
Page fault handler executes return
  Return to instruction that caused fault
  But, this time there is no page fault
User code
Kernel code
Exception: page fault
Copy page from disk to memory
Return and re-execute sw
sw
Adapted from Bryant and O’Hallaron, Computer Systems: A Programmer’s Perspective, Third Edition

## Slide 38: Swapping and Demand Paging
Swapping or Paging
  The activity of transferring a page between disk and memory
Demand Paging
  The strategy of waiting until the last moment to swap in a page, when a miss occurs
  all modern systems use demand paging.
Other approaches try to predict misses and swap pages in before they are actually referenced
Adapted from Bryant and O’Hallaron, Computer Systems: A Programmer’s Perspective, Third Edition

## Slide 39: Page Table Location Kernel Page Table

## Slide 40: Page Tables
Each program has a page table
Page table contains an entry for each program page
VA1
Prog 1
VA1
Prog 2
VA1
Prog 3
Physical Memory
Page Table
Page Table
Page Table
free
OS
pages
Notes: OS ensures that the page tables are disjoint.

## Slide 41: Where Should Page Tables Reside?
Space required by the page tables (PT) is proportional to the address space, number of users, ...
    ⇒ Too large to keep in registers, or caches….
Idea: Keep PTs in the main memory
  How can we find the page table in memory
    Note that we use page table to learn Physical addresses
  PT Base Register: stores Physical Address of current Page Table

## Slide 42: Page Tables in Physical Memory
PT Base Register
VA1
Proc 1 Virtual Address Space
Proc 2 Virtual Address Space
PT –Proc1
PT-Proc2
VA1
Physical Memory
1) Access page table for address translation
2) Access
correct
physical
address
Requires two
accesses of
physical memory!
Ref: Morgan Rae Reschenberg, Course 61C, Univ of California, Berkeley

## Slide 43: Page Table in Physical Memory
When a process is made active, the OS loads base address of the Page Table in PT Base Register
  OS knows the start address of the page table of each process
Kernel Page table containing entries for all processes also reside in the main memory

## Slide 44: Kernel Page Table for all processes
Kernel Page Table contains entries for each processes
Kernel Page Table is managed by OS
Kernel Page Table also resides in Physical Memory

## Slide 45: Summary
User program view:
  Contiguous memory
  Start from some set VA
  “Infinitely” large
  Is the only running program
Reality:
  Non-contiguous memory
  Start wherever available memory is
  Finite size
  Many programs running simultaneously
Virtual memory provides:
  Illusion of contiguous memory
  All programs starting at same set address
  Illusion of ~ infinite memory (232 or 264 bytes)
  Protection
Implementation:
  Divide memory into chunks (pages)
  OS controls page table that maps virtual into physical addresses
  memory as a cache for disk

## Slide 46: Backup

## Slide 47: Swap Space
Swap-space — Virtual memory uses disk space as an extension of main memory
  Less common now due to memory capacity increases
The OS creates the space on disk for all the pages of a process when it creates the process.
This disk space is called the swap space.
OS also creates a data structure to record where each virtual page is stored on disk

## Slide 48: The Problem
Physical memory is of limited size (cost)
  What if you need more?
  Should the programmer be concerned about the size of code/data blocks fitting physical memory?
  Should the programmer manage data movement from disk to physical memory?
  Should the programmer ensure two processes (different programs) do not use the same physical memory?
Also, ISA can have an address space greater than the physical memory size
  E.g., a 64-bit address space with byte addressability
  What if you do not have enough physical memory?

## Slide 49: Main Memory (DRAM Cache) Organization
Main Memory (DRAM cache) organization driven by the enormous miss penalty
  DRAM is about 10x slower than SRAM
  Disk is about 10,000x slower than DRAM
  Time to load block from disk > 1ms (> 1 million clock cycles)
    CPU can do a lot of computation during that time
Consequences
  Large page (block) size: typically 4 KB
    Linux “huge pages” are 2 MB (default) to 1 GB
  Fully associative
    Any VP can be placed in any PP
    Requires a “large” mapping function – different from cache memories
  Highly sophisticated, expensive replacement algorithms
    Too complicated and open-ended to be implemented in hardware
  Write-back rather than write-through

## Slide 50: Allocating Pages
Allocating a new page (VP 5) of virtual memory (disk)
  May be as a result of malloc
Subsequent miss will bring it into memory
null
Memory resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 3
Virtual memory
(disk)
Valid
0
1
1
0
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
VP 5
Adapted from Bryant and O’Hallaron, Computer Systems: A Programmer’s Perspective, Third Edition

## Slide 51: Locality to the Rescue Again!
Virtual memory works because of locality
At any point in time, programs tend to access a set of active virtual pages called the working set
  Programs with better temporal locality will have smaller working sets
If (working set size < main memory size)
  Good performance for one process (after cold misses)
If (working set size > main memory size )
  Thrashing: Performance meltdown where pages are swapped (copied) in and out continuously
  If multiple processes run at the same time, thrashing occurs if their total working set size > main memory size

## Slide 52: Virtual Memory: Responsibilities
Uses main memory efficiently
  Give illusion of larger memory by storing some content on disk
  Also allows OS to share memory across processes
  Working set of “pages” reside in main memory - others reside on disk
  Disk is usually much larger and slower than DRAM
    Use “clever” caching strategies
Protection:
  Isolates address spaces
  One process can’t interfere with another’s memory
  Protects processes from each other
  User program cannot access privileged kernel information and code
  Errors in one program won’t corrupt memory of other program
Adapted from Bryant and O’Hallaron, Computer Systems: A Programmer’s Perspective, Third Edition

## Slide 53: Difficulties of Direct Physical Addressing
Programmer needs to manage physical memory space
  Inconvenient and hard
  Harder when you have multiple processes
Difficult to support code and data relocation
  Addresses are directly specified in the program
Difficult to support multiple processes
  Protection and isolation between multiple processes
  Sharing of physical memory space
Difficult to support data/code sharing across processes

## Slide 54: Abstraction: Virtual vs. Physical Memory
Programmer sees virtual memory
  Can assume the memory is “infinite”
Reality: Physical memory size is much smaller than what the programmer assumes
The system (system software + hardware, cooperatively) maps virtual memory addresses to physical memory
  The system automatically manages the physical memory space transparently to the programmer
+ Programmer does not need to know the physical size of memory nor manage it  A small physical memory can appear as a huge one to the programmer  Life is easier for the programmer
-- More complex system software and architecture

## Slide 55: Physical Memory as a Cache
In other words…
Physical memory is a cache for pages stored on disk
  In fact, it is a fully associative cache in modern systems (a virtual page can potentially be mapped to any physical frame)
  Most accesses hit in the physical memory at the speed of DRAM, yet the program enjoys the capacity of the larger virtual memory
Similar caching issues exist as we have covered earlier:
  Placement: where and how to place/find a page in cache?
  Replacement: what page to remove to make room in cache?
  Granularity of management: large, small, uniform pages?
  Write policy: what do we do about writes? Write back?

## Slide 56: Cache/Virtual Memory Analogues
Cache | Virtual Memory
Block | Page
Block Size | Page Size
Block Offset | Page Offset
Miss | Page Fault
Tag | Virtual Page Number

## Slide 57: Virtual and Physical Addresses
Most accesses hit in physical memory
But programs see the large capacity of virtual memory

## Slide 58: Supporting Virtual Memory
Virtual memory requires both HW+SW support
  Page Table is in memory
  Can be cached in special hardware structures called Translation Lookaside Buffers (TLBs)
The hardware component is called the MMU (memory management unit)
  Includes Page Table Base Register(s), TLBs, page walkers
It is the job of the software to leverage the MMU to
  Populate page tables, decide what to replace in physical memory
  Change the Page Table Register on context switch (to use the running thread’s page table)
  Handle page faults and ensure correct mapping

## Slide 59: Some System Software Jobs for VM
Keeping track of which physical frames are free
Allocating free physical frames to virtual pages
Page replacement policy
  When no physical frame is free, what should be swapped out?
Sharing pages between processes
Copy-on-write optimization
Page-flip optimization