## Slide 1: CS 211 Computer Architecture Lecture 41: Virtual Memory Part-3 Protection, TLB, Hierarchical Page Table
Ravi Mittal
ravi.mittal@iitgoa.ac.in
Indian Institute of Technology, Goa

## Slide 2: We will study today ..
Virtual Memory Basics (Revision)
Virtual Memory Examples
Protection provided by Virtual Memory
Speeding up – Address Translation using TLB
Page Table Size Issue Solution: Hierarchical Page Table
Intel Core i7 Memory System
TLBs in Datapath
Virtual Memory Summary

## Slide 3: Acknowledgements
Morgan Rae Reschenberg, CS 61C: Great Ideas in Computer Architecture (Machine Structures), http://inst.eecs.berkeley.edu/~cs61c/
Krste Asanović & Randy H. Katz, CS 61C: Great Ideas in Computer Architecture (Machine Structures), http://inst.eecs.berkeley.edu/~cs61c/
Chapter 6, Memory Hierarchy, Book: Computer Systems: A programmer’s perspective, Randal E. Bryant and David R. O’Hallaron
Prof Onur Mutlu’s Class Presentation, ETH Zürich, Lecture 21b: Memory Hierarchy and Caches, Sprint 2020
Patterson and Hennessy, Book: Computer Organization and Design, Hardware/Software Interface, RISC-V Edition
MIT 6.004 Spring 2020, Class on Caches
Digital Design and Computer Architecture: RISC-V Edition, Harris & Harris Elsevier

## Slide 4: Last Class

## Slide 5: Each process has it’s own (virtual) address space
Process 1
Process 2
Process n

## Slide 6: Virtual vs. Physical Addresses
Each Process uses it’s own address space
Processes use virtual addresses, e.g., 0 … 0xffff,ffff
  Many processes, all using same (conflicting) addresses
Memory uses physical addresses (also, e.g., 0 ... 0xffff,ffff)
Memory manager maps virtual to physical addresses
Processor (& Caches)
Control
Datapath
PC
Registers
(ALU)
Memory (DRAM)
Bytes
?
Virtual Address
Physical Address
Many of these (software & hardware cores)
One main memory
Memory manager

## Slide 7: Paged Virtual Memory
Divide virtual memory and physical memory into equally sized segments called pages:
Virtual Memory
Physical Memory
0
1
2
3
4
5
6
7
0
1
2
3
Ref: Morgan Rae Reschenberg, Course 61C, Univ of California, Berkeley

## Slide 8: Each Process has a page table
Page N
Page 2
Page 1
Page 0
Memory (DRAM)
Page Table
Page Table
Page Table
Each process has a dedicated page table. Physical memory non-consecutive.

## Slide 9: Virtual to Physical Address
Virtual Address
Virtual Page Number
Offset
Physical Page Number
Offset
Page table lookup!
Physical Address
Ref: Morgan Rae Reschenberg, Course 61C, Univ of California, Berkeley

## Slide 10: Page Table on Physical Memory
A page table is an array of page table entries (PTEs) that maps virtual pages to physical pages.
  For every process there is a page table in Main Memory (DRAM)
null
null
Memory resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 4
Disk memory
Valid
0
1
0
1
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
Adapted from Bryant and O’Hallaron, Computer Systems: A Programmer’s Perspective, Third Edition

## Slide 11: Page Hit
Page hit: reference to VM word that is in physical memory (DRAM cache hit)
null
null
Memory resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 4
Virtual memory
(disk)
Valid
0
1
0
1
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
VPN Offset
Page Not hit: PTE refers to location in swap space on disk
Adapted from Bryant and O’Hallaron, Computer Systems: A Programmer’s Perspective, Third Edition
Virtual Address

## Slide 12: Address Translation With a Page Table
Virtual page number (VPN)
Virtual page offset (VPO)
Physical page number (PPN)
Physical page offset (PPO)
Virtual address
Physical address
Valid
Physical page number (PPN)
Page table base register (PTBR)
(CR3 in x86)
Page table
Physical page table
address for the current
process
Valid bit = 0:
Page not in memory
(page fault)
0
p-1
p
n-1
0
p-1
p
m-1
Valid bit = 1
Adapted from Bryant and O’Hallaron, Computer Systems: A Programmer’s Perspective, Third Edition

## Slide 13: Virtual Memory Examples

## Slide 14: Virtual Memory Example
System:
  Virtual memory size: 2 GB = 231 bytes
  Physical memory size: 128 MB = 227 bytes
  Page size: 4 KiB = 212 bytes
Organization:
  Virtual address: 31 bits
  Physical address: 27 bits
  Page offset: 12 bits
  # Virtual pages = 231/212 = 219 (VPN = 19 bits)
  # Physical pages = 227/212 = 215 (PPN = 15 bits)
Harris and Harris Book: Digital Design and Computer Architecture

## Slide 15: Virtual Memory Example
Harris and Harris Book: Digital Design and Computer Architecture

## Slide 16: Page Table Example-1
Harris and Harris Book: Digital Design and Computer Architecture

## Slide 17: Virtual Memory: Example - 2
What is the physical address of virtual address 0x5F20?
Harris and Harris Book: Digital Design and Computer Architecture

## Slide 18: Virtual Memory: Example - 2
What is the physical address of virtual address 0x5F20?
  Virtual Page number: 05
  Entry 5 in page table indicates VPN 5 is in physical page 1
  Physical address is 0x1F20
Harris and Harris Book: Digital Design and Computer Architecture

## Slide 19: Protection Provided by Virtual Memory

## Slide 20: VM provides Memory Protection
Extend PTEs with permission bits
MMU checks these bits on each access
Process i:
Address
READ
WRITE
PP 6
Yes
No
PP 4
Yes
Yes
PP 2
Yes
VP 0:
VP 1:
VP 2:
•
•
•
Process j:
Yes
SUP
No
No
Yes
Address
READ
WRITE
PP 9
Yes
No
PP 6
Yes
Yes
PP 11
Yes
Yes
SUP
No
Yes
No
VP 0:
VP 1:
VP 2:
Physical
Address Space
PP 2
PP 4
PP 6
PP 8
PP 9
PP 11
EXEC
Yes
EXEC
Yes
Yes
Yes
Yes
No
SUP: requires kernel mode
Adapted from Bryant and O’Hallaron, Computer Systems: A Programmer’s Perspective, Third Edition

## Slide 21: Speeding up – Address Translation using TLB (Translation Look Aside Buffer)

## Slide 22: Virtual Memory Problem
Two or more physical memory accesses per data access
  SLOW
Since there is locality in pages of data, there must be locality in the translations of those pages
Build a separate cache for the Page Table
  For historical reasons, cache is called a Translation Lookaside Buffer (TLB)
  TLB stores: VPN → PPN mappings

## Slide 23: TLBs and Caches
TLBs usually small, typically 32–128 entries
TLB access time is comparable to that for cache (much faster than accessing main memory)
TLBs usually are fully/highly associativity
Each entry maps a large page, hence less spatial locality across pages
Sometimes larger TLBs (256-512 entries) are 4-8 way set-associative
Data Cache / Instruction Cache
Memory Address
Data at memory address
Access next cache level / main memory
On miss:
TLB
VPN
PPN
Access Page Table in main memory
On miss:
Ref: Morgan Rae Reschenberg, Course 61C, Univ of California, Berkeley

## Slide 24: TLB and Cache
Cache
VA
PA
miss
hit
data
hit
miss
CPU
Main Memory
TLB
Page Table
PPN
VPN
Now the TLB does the translation too, not just the Page Table!
Ref: Morgan Rae Reschenberg, Course 61C, Univ of California, Berkeley

## Slide 25: Fetching Data on a Memory Read
Check TLB (input: VPN, output: PPN)
  TLB Hit: Fetch translation, return PPN
  TLB Miss: Check page table (in memory)
    Page Table Hit: Load page table entry into TLB
    Page Table Miss (Page Fault): Fetch page from disk to memory, update corresponding page table entry, then load entry into TLB
Check cache (input: PPN, output: data)
  Cache Hit: Return data value to processor
  Cache Miss: Fetch data value from memory, store it in cache, return it to processor
Ref: Morgan Rae Reschenberg, Course 61C, Univ of California, Berkeley

## Slide 26: Summary of Address Translation Symbols
Basic Parameters
  N = 2n : Number of addresses in virtual address space
  M = 2m : Number of addresses in physical address space
  P = 2p : Page size (bytes)
Components of the virtual address (VA)
  TLBI: TLB index
  TLBT: TLB tag
  VPO: Virtual page offset
  VPN: Virtual page number
Components of the physical address (PA)
  PPO: Physical page offset (same as VPO)
  PPN: Physical page number
Adapted from Bryant and O’Hallaron, Computer Systems: A Programmer’s Perspective, Third Edition

## Slide 27: TLB Organization (1-way)
TLB Tag
TLB Index
Page Offset
TLB Tag | PPN
(used just like in a cache) | 
. . . | 
TLB
VPN
PPN
Page Offset
Tag
Index
Offset
Virtual Address
Physical Address
 | Tag | Block Data
. . . |  | 
Data Cache
PA split two different ways!
Ref: Morgan Rae Reschenberg, Course 61C, Univ of California, Berkeley

## Slide 28: TLB Organization (2-way)
MMU uses the VPN portion of the virtual address to access the TLB:
TLB tag
TLB index
0
p-1
p
n-1
Page Offset
VPN
p+t-1
p+t
PTE
tag
v
…
PTE
tag
v
Set 0
PTE
tag
v
PTE
tag
v
Set 1
PTE
tag
v
PTE
tag
v
Set T-1
T = 2t sets
TLB Index selects
the set
TLBT matches tag of block within set
Adapted from Bryant and O’Hallaron, Computer Systems: A Programmer’s Perspective, Third Edition

## Slide 29: Typical Values for a TLB
TLB size: 16–512 entries Hit time: 0.5–1 clock cycle Miss penalty: 10–100 clock cycles Miss rate: 0.01%–1%
Associativity: Mostly fully associative
TLB entry replacement: Random (as LRU may be expensive)
Adapted from Bryant and O’Hallaron, Computer Systems: A Programmer’s Perspective, Third Edition

## Slide 30: Data Fetch Scenarios
Are the following scenarios for a single data access possible?
  TLB Miss, Page Fault
  TLB Hit, Page Table Hit
  TLB Miss, Cache Hit
  Page Table Hit, Cache Miss
  Page Fault, Cache Hit
Yes
No
Yes
Yes
No
Cache
VA
PA
miss
hit
data
hit
miss
CPU
Main Memory
TLB
Page Table
Disk
fault
page
PPN
VPN
Ref: Morgan Rae Reschenberg, Course 61C, Univ of California, Berkeley

## Slide 31: Solving Page Table Size Issue with Hierarchical Page Table

## Slide 32: Page Table Size Issue
Given:
  A 32 bit address space (4 GiB)
  4 KiB pages
  A page table entry of 4 bytes
Implication:
  Page table is 4 MiB per process!
  Huge size and context switching costs
Problem is more severe for 48 bit and 64 bit address spaces
  48-bit Address space with 4 KiB page size, 8 byte PTE
    Would need a 512 GiB page table!
Address space usage tends to be sparse
  Most programs don’t use all of 32 bits (or 48 bits)
Adapted from Bryant and O’Hallaron, Computer Systems: A Programmer’s Perspective, Third Edition

## Slide 33: Multilevel Page Table
Break up the logical address space into multiple page tables
A simple technique is a two-level page table
Example: Two level page table
  Level 1 table: each PTE points to a page table (always memory resident)
  Level 2 table: each PTE points to a page (paged in and out like any other data)
Level 1
Table
Level 2
Tables
Memory
Adapted from Bryant and O’Hallaron, Computer Systems: A Programmer’s Perspective, Third Edition

## Slide 34: Two-level page tables
page
frame 0
page
frame 1
page
frame 2
page
frame Y
…
page
frame 3
physical memory
offset
physical address
PPN
Level 1
page table
VPN2
virtual address
VPN1
offset
Level 2
page table
Level 2
page table addr
PPN

## Slide 35: Translating with a k-level Page Table
Page table base register
(PTBR)
VPN 1
0
p-1
n-1
Offset
VPN 2
...
VPN k
PPN
0
p-1
m-1
Offset
PPN
VIRTUAL ADDRESS
PHYSICAL ADDRESS
...
...
Level 1
page table
Level 2
page table
Level k
page table
Adapted from Bryant and O’Hallaron, Computer Systems: A Programmer’s Perspective, Third Edition

## Slide 36: Intel Core i7 Memory System

## Slide 37: Intel Core i7 Memory System
L1 d-cache
32 KB, 8-way
L2 unified cache
256 KB, 8-way
L3 unified cache
8 MB, 16-way
(shared by all cores)
Main memory
Registers
L1 d-TLB
64 entries, 4-way
L1 i-TLB
128 entries, 4-way
L2 unified TLB
512 entries, 4-way
L1 i-cache
32 KB, 8-way
MMU
(addr translation)
Instruction
fetch
Core x4
DDR3 Memory controller
3 x 64 bit @ 10.66 GB/s
32 GB/s total (shared by all cores)
Processor package
QuickPath interconnect
4 links @ 25.6 GB/s each
To other
cores
To I/O
bridge
Adapted from Bryant and O’Hallaron, Computer Systems: A Programmer’s Perspective, Third Edition

## Slide 38: End-to-end Core i7 Address Translation
CPU
VPN
VPO
36
12
TLBTag
TLBIndex
4
32
...
L1 TLB (16 sets, 4 entries/set)
VPN1
VPN2
9
9
PTE
CR3
PPN
PPO
40
12
Page tables
TLB
miss
TLB
hit
Physical
address
(PA)
Result
32/64
...
CT
CO
40
6
CI
6
L2, L3, and
main memory
L1 d-cache
(64 sets, 8 blocks/set)
L1
hit
L1
miss
Virtual address (VA)
VPN3
VPN4
9
9
PTE
PTE
PTE
Adapted from Bryant and O’Hallaron, Computer Systems: A Programmer’s Perspective, Third Edition
CT: Cache Tag
CI: Cache Index
CO: Cache Offset

## Slide 39: TLBs in Datapath

## Slide 40: TLBs in Datapath
Ref: Morgan Rae Reschenberg, Course 61C, Univ of California, Berkeley

## Slide 41: Hardware Page Table Walker
Traditional Approach (without Page Table Walker)
  Processor is expected to context switch to the OS on every TLB miss, interrupting user-level execution, flushing the pipeline, and polluting caches
Hardware page table walkers (PTWs) that are used to handle TLB misses without invoking the OS
Ref: Morgan Rae Reschenberg, Course 61C, Univ of California, Berkeley

## Slide 42: Address Translation
hardware
hardware or software
software
Virtual Address
TLB
Lookup
Page Table
“Walk”
Update
TLB
Page Fault
(OS loads page)
Protection
Check
Physical
Address
TLB Miss
TLB Hit
Page not
in Mem
Access
Denied
Access
Permitted
Protection
Fault
SEGFAULT
Page
in Mem
Check cache
Find in Disk
Find in Mem
Ref: Morgan Rae Reschenberg, Course 61C, Univ of California, Berkeley
Notes: Need to restart instruction.
Soft and hard page faults.

## Slide 43: Virtual Memory: Summary
Programmer’s view of virtual memory
  Each process has its own private linear address space
  Cannot be corrupted by other processes
System view of virtual memory
  Uses memory efficiently by caching virtual memory pages
    Efficient only because of locality
  Simplifies memory management and programming
  Simplifies protection
Virtual Memory system uses
  Cache Memory for storing Page Table
  TLB
  Hierarchical Page Table