## Slide 1: CS 211 Computer Architecture Lecture 6: Computer System: Basics
Ravi Mittal
ravi.mittal@iitgoa.ac.in
Indian Institute of Technology, Goa

## Slide 2: Today’s Thought
Dirty your hands .. If you really want to learn anything..
You can’t learn driving just by reading manuals..
You can’t learn Programming, just by reading books
You can’t even realize God… by reading spiritual Granths
You need to practice … dirty your hands..
Don’t say “my laptop is not working”, “tool is not working”…. Learn to use it .. Fix it .. Make effort..

## Slide 3
"Spoon feeding in the long-run only teaches us the shape of the spoon." E.M. Forster

## Slide 4: Reading
Patt and Patel book, Chapter 4
Lecture slides of Prof Onur Mutlu, Course 18-447, Computer Architecture, Carnegie Mellon University
Computer Systems Book: Bryant and O’Hallaron, Chapter 2

## Slide 5: In today’s class, we will study..
What is in a computer?
Memory
  Addressability – Address Space
  Word-addressable Memory
  Byte-addressable Memory
  Big Endian vs Little Endian
How to interconnect different parts of a computer system?
Trivia – Digital Transformation

## Slide 6: What is in a Computer?

## Slide 7: What is in a computer?

## Slide 8: To get work done by computer
We need
  Computer
  Data
  Program: A set of instructions
    Instruction: The smallest piece of work in computer

## Slide 9: What is in a Computer?
Three key components
Computation
Communication
Storage / memory
From Prof Onur Mutlu’s presentation

## Slide 10: What is in a Computer?
Memory
(program
and data)
I/O
Processing
control
(sequencing)
datapath
From Prof Onur Mutlu’s presentation

## Slide 11: Datapath
The collection of state elements, computation elements, and interconnections that together provide a conduit for the flow and transformation of data in the processor during execution
Element that processes data and addresses
Register file, ALU, Buses, Memories, Buffers, Adders etc

## Slide 12: Memory - basics

## Slide 13: Memory
The memory stores
  Data
  Programs
Memory of two primary types
Volatile Memory
  Memory that looses stored information when there is no electric power; Power is required to retain information
  Example: Random Access Memory (RAM)
    SRAM (Static RAM), DRAM (Dynamic RAM)
Non-volatile Memory
  Memory that retains information when there is no electric power
    Read Only Memory (ROM), Flash Memory, Optance Memory (Phase shift), Hard Disk, Magnetic Tape, Optical Disk, Floppy Disk
Notes: x86-64:
* Memory organization:
- Address space: up to 2^48.
- Addressability: up to 48 bits. The actual length of the address is 64 bits, but bits 48 to 63 are sign extended.

## Slide 14: Memory
Access time: SRAM < DRAM < FLASH < Hard Disk < Magnetic Tape
Storage Capacity: Magnetic Tape > Hard Disk > Flash > DRAM > SRAM
Cost: SRAM > DRAM > Flash > Hard Disk
We use the fastest memory (SRAM) closest to the processor – as it is very fast (less response time)
  Use as Cache memory

## Slide 15: The Memory Hierarchy (will study later)
fast
small
big but slow
move what you use here
backup
everything
here
With good locality of reference, memory appears as fast as
and as large as
faster per byte
cheaper per byte
Processor
From Prof Onur Mutlu’s presentation

## Slide 16: Memory
The memory
  Conceptually, envision it as a very large array of bytes
  Bytes are grouped into words
Machine Words
  Any given computer has a “Word Size”
    Word size" refers to the number of bits processed by a computer's CPU in one go
    Nominal size of integer-valued data and of address (?)
    Typically each register stores one word
  Typical word size: 8, 16, 32, 64 bits
  Intel’s 64-bit processor doesn’t address 264 locations
Until recently, most machines used 32 bits (4 bytes) as word size
    Now it is 64-bit word size in modern machines

## Slide 17: Addressability - Address Space
How the bits are accessed determines the addressability
  Byte- Addressable: 8-bit are addressable at a given address
  Word-addressable
    One word is addressable at a given an address
  RISC-V is byte addressable
The total number of addresses is the address space
  In RISC-V, the address space is 232
    32-bit addresses
  In x86-64, the address space is (up to) 248
    48-bit addresses
Notes: x86-64:
* Memory organization:
- Address space: up to 2^48.
- Addressability: up to 48 bits. The actual length of the address is 64 bits, but bits 48 to 63 are sign extended.

## Slide 18: Word-addressable Memory
Conceptually, memory is envisioned as a very large array of bytes
Each data word has a unique address
  Consider 32-bit data word
One word is read at a time. Most operations are on a word.
For byte operations - one word is read and then byte is extracted by some operation
Most programmer’s want to manipulate single byte
  Word addressable memory is not popular
00•••0
00•••1
Word 0
Word 1
• • •

## Slide 19: Byte-Addressable Memory
Each byte has a unique address
  RISC-V is byte-addressable
We still have notion of word but address uses byte address
  Diagram shows 4-byte word
Close to reality – the way programmers want to manipulate data
  If you are operating on bytes, it’s good to have byte – oriented memory
Within a word – which is byte 0, byte 1, byte 2 and byte 3 ?
00•••0
00•••4
Word 0
Word 1
• • •

## Slide 20: Byte-Addressable Memory – different word sizes
Addresses Specify Byte Locations
  Address of first byte in word
  Addresses of successive words differ by 4 (32-bit) or 8 (64-bit)
For 32-bit words
  Address of the first word: 0000
  Address of the second word: 0004
  And so on
For 64-bit words
  Address of the first word: 0000
  Address of the second word: 0008
  And so on
0000
0001
0002
0003
0004
0005
0006
0007
0008
0009
0010
0011
32-bit
Words
Bytes
Addr.
0012
0013
0014
0015
64-bit
Words
Addr
=
??
Addr
=
??
Addr
=
??
Addr
=
??
Addr
=
??
Addr
=
??
0000
0004
0008
0012
0000
0008

## Slide 21: Big Endian vs Little Endian
Jonathan Swift’s Gulliver’s Travels
  Little Endians broke their eggs on the little end of the egg
  Big Endians broke their eggs on the big end of the egg
From Prof Onur Mutlu’s presentation

## Slide 22: Byte Ordering Example
Big Endian
  Least significant byte has highest address
Little Endian
  Least significant byte has lowest address
Example
  Variable x has 4-byte representation 0x01234567
  Address given by &x is 0x100
0x100
0x101
0x102
0x103
01
23
45
67
0x100
0x101
0x102
0x103
67
45
23
01
Big Endian
Little Endian
01
23
45
67
67
45
23
01
Lower byte Address
Higher byte Address

## Slide 23
Big Endian
Little Endian
Does this really matter?
Answer: No, it is a convention
Qualified answer: No, except when one big-endian system and one little-endian system have to share data
Vs
From Prof Onur Mutlu’s presentation
Notes: It is a convention, same as German is written from left to right, and Persian is written from right to left.

## Slide 24: How to Interconnect different components of a Computer System?

## Slide 25: Interconnecting parts of a computer
We have studied many parts of a computer
  CPU, Memory, Disk, Peripherals, etc
How to connect them to each other ?
Simple Solution: Use a set of shared communication links (wires) to interconnect various subsystems
  Call this arrangement: Bus
Bus
CPU
RAM
Keyboard
Hard
Disk
Display
CD-ROM

## Slide 26: Bus
Bus Lines (Parallel)
  Data lines
    Passes data back and forth
    Number of lines represent width
  Address Lines
    Designates location of source or destination
    Width of address bus specifies maximum memory capacity
  Control Lines
    Carry control signals
      Memory Read or Write, I/O Read or Write, Transfer ACK
      Bus request, Bus grant, Interrupt request etc
data lines
address lines
control lines

## Slide 27: Buses
Main
memory
I/O
bridge
Bus interface
ALU
Register file
CPU chip
System bus
Memory bus
Disk
controller
Graphics
adapter
USB
controller
Mouse
Keyboard
Monitor
Disk
I/O bus
Expansion slots for
other devices such
as network adapters.
PCI Bus
Adapted from Computer Systems Book: Bryant and O’Hallaron

## Slide 28: Trivia

## Slide 29: Big Data, this is just the Beginning
2010
2015
1023
World's Data (Bytes)
You are here
The number of stars in the universe
Sensors & Devices
VoIP
Enterprise Data
Social Media
Notes: “The Internet of [Things] could raise the level of U.S. gross domestic product by 2%-5% by 2025.
This gain… if realized, would boost the annual U.S. GDP growth rate by 0.2%-0.4% points over this period, bringing growth closer to 3% per year.”

## Slide 30: Digital Transformation of Business
Everything is becoming smarter
  Computer with cooling functionality (Fridge), Computer with washing capability (Washing machine)
Digital Technologies (Computer) help devices to become
  Flexible
  User friendly
  Programmable
  Adaptive
  Enhance features
  Interconnected
  …smarter
Businesses that are not adapting digital technologies are dying …

## Slide 31: What is common among these companies
Eastman Kodak Company
  Camera, Photography Equipment, Chemicals
Polaroid Corporation
  Photography
Blockbuster Inc
  Video Rental company
Border’s Group
  Bookstore business

## Slide 32: What is common among these companies
Eastman Kodak Company
  Camera, Photography Equipment, Chemicals
Polaroid Corporation
  Photography
Blockbuster Inc
  Video Rental company
Border’s Group
  Bookstore business
All these companies failed to adopt to digital technologies

## Slide 33: Trivia
Which of the following companies make the largest number of cameras and camera parts
  Nikon
  Cannon
  Fujifilm
  Olympus
  Sony

## Slide 34: Trivia
Which of the following companies make the largest number of cameras and camera parts
  Nikon
  Cannon
  Fujifilm
  Olympus
  Sony
Sony supplies camera parts to almost all smart mobile phone manufacturer
Mobile phone cameras has almost killed traditional camera business

## Slide 35: Next Class: Von Neumann Architecture

## Slide 36: Von Neumann Model
John von Neumann proposed a fundamental model in 1946
It consists of 5 parts
  Memory
  Processing unit
  Input
  Output
  Control unit
  Burks, Goldstein, von Neumann,
  “Preliminary discussion of the logical design
  of an electronic computing instrument,” 1946.
From Prof Onur Mutlu’s presentation

## Slide 37: The Von Neumann Model
CONTROL UNIT
PC or IP
Inst Register
PROCESSING UNIT
ALU
TEMP
MEMORY
Mem Addr Reg
Mem Data Reg
INPUT
Keyboard,
Mouse,
Disk…
OUTPUT
Monitor,
Printer,
Disk…
From Prof Onur Mutlu’s presentation

## Slide 38: The Von Neumann Model
CONTROL UNIT
PC or IP
Inst Register
PROCESSING UNIT
ALU
TEMP
MEMORY
Mem Addr Reg
Mem Data Reg
INPUT
Keyboard,
Mouse,
Disk…
OUTPUT
Monitor,
Printer,
Disk…
From Prof Onur Mutlu’s presentation

## Slide 39: Accessing Memory: MAR and MDR
There are two ways of accessing memory
  Reading or loading
  Writing or storing
Two registers are necessary to access memory
  Memory Address Register (MAR)
  Memory Data Register (MDR)
To read
  Step 1: Load the MAR with the address
  Step 2: Data is placed in MDR
To write
  Step 1: Load the MAR with the address and the MDR with the data
  Step 2: Activate Write Enable signal

## Slide 40: Registers

## Slide 41: Registers
Registers are very important part of Processor
Memory is big but slow
Registers
  Operate at processor speed (a few clock cycles)
  Ensure fast access to operands
  Typically one register contains one word
Register set or file
  A set of registers
    Register size = Word length = 32 bits (in MIPS)

## Slide 42
Register Access time: approx. 0.1 ns
A few processor cycles
Cache Access time: 1-2 ns
DRAM Access time : 50-150 ns
SSD Access time : 40-100 micro second
Hard Disk Access time : 10-15 milli second
Tape Access time : 50-60 seconds

## Slide 43: Register File Interactions
Notes: Memory is slow
Registers are fast – work at processor speed
So, Contents (Instruction and data) are brought from MM to Registers.
Also, contents (data) is stored from Registers to MM
Memory contains both program and data