## Slide 1: CS 211 Computer Architecture Lecture 7: The Von Neumann Architecture- Part 1
Ravi Mittal
ravi.mittal@iitgoa.ac.in
Indian Institute of Technology, Goa

## Slide 2: Reading
Patt and Patel book, Chapter 4, “The von Neumann Model”
Lecture slides of Prof Onur Mutlu, Course 18-447, Computer Architecture, Carnegie Mellon University

## Slide 3: In today’s class, we will study
Von Neumann Model
  Parts
  Model Diagram
  Memory
  Processing Unit
  Input and Output
  Control Unit
  Properties of the model
Von Neumann Machine
  LC3- Learning Computer3

## Slide 4: Introduction: Von Neumann Model

## Slide 5: Von Neumann Model
John von Neumann proposed a fundamental model in 1946
It consists of 5 parts
  Memory
  Processing unit
  Input
  Output
  Control unit
  Burks, Goldstein, von Neumann,
  “Preliminary discussion of the logical design
  of an electronic computing instrument,” 1946.
From Prof Onur Mutlu’s presentation

## Slide 6: The Von Neumann Model
CONTROL UNIT
PC or IP
Inst Register
PROCESSING UNIT
ALU
TEMP
MEMORY
Mem Addr Reg
Mem Data Reg
INPUT
Keyboard,
Mouse,
Disk…
OUTPUT
Monitor,
Printer,
Disk…
From Prof Onur Mutlu’s presentation

## Slide 7: The Von Neumann Model
CONTROL UNIT
PC or IP
Inst Register
PROCESSING UNIT
ALU
TEMP
MEMORY
Mem Addr Reg
Mem Data Reg
INPUT
Keyboard,
Mouse,
Disk…
OUTPUT
Monitor,
Printer,
Disk…
From Prof Onur Mutlu’s presentation

## Slide 8: Accessing Memory: MAR and MDR
There are two ways of accessing memory
  Reading or loading
  Writing or storing
Two registers are necessary to access memory
  Memory Address Register (MAR)
    for addressing individual locations
  Memory Data Register (MDR)
    For holding the contents of a memory location on its way to/from the storage

## Slide 9: Accessing Memory: MAR and MDR
To read
  Step 1: Load the MAR with the address
  Step 2: Data is placed in MDR
To write
  Step 1: Load the MAR with the address and the MDR with the data
  Step 2: Activate Write Enable signal

## Slide 10: The Von Neumann Model
CONTROL UNIT
PC or IP
Inst Register
PROCESSING UNIT
ALU
TEMP
MEMORY
Mem Addr Reg
Mem Data Reg
INPUT
Keyboard,
Mouse,
Disk…
OUTPUT
Monitor,
Printer,
Disk…

## Slide 11: Processing Unit
The processing unit can consist of many functional units
Arithmetic and Logic Unit (ALU), executes computations
  MIPS: add, sub, mult, and, nor, sll, slr, slt…
  RISC-V: add, sub, mult, and, or, sll, ..
The ALU processes quantities that are referred to as words
  Word length
    LC-3: 16 bits
    MIPS: 32 bits
    Intel x86-64: 64 bits
    RISC-V: 32 bits (Extension: 64 bits, 128 bits)
Temporary storage (Scratch pad): Registers
  E.g., to calculate (A+B)*C, the intermediate result of A+B is stored in a register
Notes: 32 bits (Pentium IV) or 64 bits (Itanium, IA-64) in real systems
sll: shift left logical
slr: shift right logical
Slt: set on less than

## Slide 12: Registers (Temp)
Memory is big but slow
Registers
  Operate at processor speed – Clock speed
  Ensure fast access to operands
  Each Register size = Word length = say 32 bits (in RISC-V)
Register set or file
  A set of registers
  Not too many registers
    32 Registers in RISC-V

## Slide 13
Register Access time: approx. 0.1 ns
One clock cycle
SRAM Cache Access time: 1-2 ns
DRAM Access time : 50-150 ns
SSD Access time : 40-100 micro second
Hard Disk Access time : 10-15 milli second
Tape Access time : 50-60 seconds

## Slide 14: Register File Interactions
Three main instructions:
  Arithmetic and Logical
  Load and Store
  Control Transfer
  Load and Store Machine
Notes: Memory is slow
Registers are fast – work at processor speed
So, Contents (Instruction and data) are brought from MM to Registers.
Also, contents (data) is stored from Registers to MM
Memory contains both program and data

## Slide 15: Input and Output
Many devices (Peripherals) can be used for input and output
Input
  Keyboard
  Mouse
  Scanner
  Disks, etc
Output
  Monitor
  Printer
  Disks, etc.

## Slide 16: The Von Neumann Model
CONTROL UNIT
PC or IP
Inst Register
PROCESSING UNIT
ALU
TEMP
MEMORY
Mem Addr Reg
Mem Data Reg
INPUT
Keyboard,
Mouse,
Disk…
OUTPUT
Monitor,
Printer,
Disk…

## Slide 17: Control Unit
The control unit is similar to the conductor of an orchestra
It conducts the step-by-step process of executing (every instruction in) a program
It keeps track of
  where we are within the process of executing the program
    Program Counter (PC): contains the address of the next instruction to be executed. Also, called Instruction Pointer (IP)
    IR (Instruction Register): to keep track of the instruction being executed
  where we are in the process of executing each instruction
    As execution of an instruction involves many activities

## Slide 18: Control Unit
Reads an instruction from memory
  the instruction’s address is in the PC
Interprets the instruction, generating control signals that tell other components what to do
  An instruction may take many machine cycles to complete
  Operation is either executed completely or not at all
    Instruction execution is atomic

## Slide 19: The Von Neumann Model/Architecture: Properties
Also called Stored Program Computer (instructions in memory)
Two key properties:
Stored program
  Instructions stored in a linear memory array
  Memory is unified between instructions and data
    The interpretation of a stored value depends on the control signals
Sequential instruction processing
  One instruction processed (fetched, executed, and completed) at a time
  Program counter (instruction pointer) identifies the current instruction
  Program counter is advanced sequentially except for control transfer instructions (eg. Jump or branch)
When is a value interpreted as an instruction?
From Prof Onur Mutlu’s presentation

## Slide 20: Programmer visible (Architectural) State
M[0]
M[1]
M[2]
M[3]
M[4]
M[N-1]
Memory
array of storage locations
indexed by an address
Program Counter
memory address
of the current instruction
Registers
Given special names in the ISA (as opposed to addresses)
General vs. special purpose
Instructions (and programs) specify how to transform
the values of programmer visible state
From Prof Onur Mutlu’s presentation

## Slide 21: LC-3 Von Neumann Machine

## Slide 22: LC-3: A Von Neumann Machine
MAR contains 16 bits
  Can address 216 locations (address space)
The MDR contains 16 bits
  each memory location contains 16 bits
  Word size = 16 bits
    LC-3 is 16-bit addressable (word addressable)
INPUT/OUTPUT consists of a keyboard and a monitor
  Keyboard: requires two registers: KBDR and KBSR
    KBDR: Keyboard Data Register
      For holding the ASCII codes of key stuck
    KBSR: Keyboard Status Register
      For maintaining status information about the key stuck
  Monitor: Two registers: DDR and DSR
    DDR (Display Data Register): for holding the ASCII code of something to be displayed on the screen
    DSR (Display Status Register): for maintaining associated status info

## Slide 23: LC-3: A Von Neumann Machine
The control Unit
  Finite State Machine - Most important structure
    Directs all activities
    Processing is carried out step by step, clock cycle by clock cycle
    Note that CLK is input to the FSM
  Input to FSM is Instruction Register (IR)
    Instruction being processed – determines what activities must be carried out
  PC (Program Counter) is also part of the control unit – keeps track of the next instruction to be executed after the current instruction finishes
  The output of FSM are control signals – shown with non-filled arrow head
    These outputs control the processing throughout the computer

## Slide 24: LC-3: A Von Neumann Machine
Control signals
(non filled-in Arrow head)
Data
(filled-in Arrow head)
ALU: 2 inputs, 1 output
Memory Data Register
Memory Address
Register
16-bit addressable
Keyboard
KBDR (data), KBSR (status)
Monitor - Display
DDR (data), DSR (status)
8 General Purpose Registers (GPR)
Finite State Machine
(for Generating Control Signals)
Instruction Register
Program Counter
ALU operation
GateALU
From Prof Onur Mutlu’s presentation
Notes: The data path consists of all components that actually process the information during each clock cycle—the functional units that operate on the information, the registers that store information at the end of one cycle so it will be available for further use in subsequent cycles, and the buses and wires that carry information from one point to another in the data path.

## Slide 25: Lecture Summary
In this lecture, we have studied Von Neumann Model
  Parts: Memory, Processing unit, Input, Output, Control unit
Memory Unit contains two registers: MAR and MDR
  Both registers are used for reading and writing to/from memory
Processing Unit contains ALU and Registers
  Registers operate at processor’s speed – very fast – limited in number – Register File
Control Unit
  Conductor of an Orchestra – Generates control signals to execute each instruction
Stored Program Concept
Von Neumann Machine – One simple implementation
  LC3 – Learning Computer 3