## Slide 1: CS 211 Computer Architecture Lecture 8: Von Neumann Architecture – Part 2
Ravi Mittal
ravi.mittal@iitgoa.ac.in
Indian Institute of Technology, Goa

## Slide 2: Acknowledgements
Patt and Patel book, Chapter 4, “The von Neumann Model”
Lecture slides: Prof Onur Mutlu, Course 18-447, Computer Architecture, Carnegie Mellon University
Class presentation slides on The LC-3, University of Texas at Austin CS310H - Computer Organization Spring 2010 Don Fussell

## Slide 3: Last lecture: Von Neumann Model

## Slide 4: The Von Neumann Model
CONTROL UNIT
PC or IP
Inst Register
PROCESSING UNIT
ALU
TEMP
MEMORY
Mem Addr Reg
Mem Data Reg
INPUT
Keyboard,
Mouse,
Disk…
OUTPUT
Monitor,
Printer,
Disk…
From Prof Onur Mutlu’s presentation

## Slide 5: LC-3: A Von Neumann Machine
Control signals
(non filled-in Arrow head)
Data
(filled-in Arrow head)
ALU: 2 inputs, 1 output
Memory Data Register
Memory Address
Register
16-bit addressable
Keyboard
KBDR (data), KBSR (status)
Monitor - Display
DDR (data), DSR (status)
8 General Purpose Registers (GPR)
Finite State Machine
(for Generating Control Signals)
Instruction Register
Program Counter
ALU operation
GateALU
From Prof Onur Mutlu’s presentation
Notes: The data path consists of all components that actually process the information during each clock cycle—the functional units that operate on the information, the registers that store information at the end of one cycle so it will be available for further use in subsequent cycles, and the buses and wires that carry information from one point to another in the data path.

## Slide 6: In today’s class, we will study
Assembly and Machine Instructions
Instruction Processing
  LC-3 Instruction and Microprocessor
  FETCH, DECODE, EVALUATE ADDRESS, FETCH OPERANDS, EXECUTE, STORE RESULT
Instruction steps for
  ADD Instruction
  LDR Instruction
Datapath components and Control signal generation

## Slide 7: LC-3: A Von Neumann Machine
The control Unit
  Two bit output ALUK: which controls the operation of ADD, AND, and NOT
  Output GateALU determines whether or not the output of the ALU is provided to the processor bus during the current clock cycle

## Slide 8: The Von Neumann Model/Architecture: Properties
Also called Stored Program Computer (instructions in memory)
Two key properties:
Stored program
  Instructions stored in a linear memory array
  Memory is unified between instructions and data
    The interpretation of a stored value depends on the control signals
Sequential instruction processing
  One instruction processed (fetched, executed, and completed) at a time
  Program counter (instruction pointer) identifies the current instruction
  Program counter is advanced sequentially except for control transfer instructions (eg. Jump or branch)
When is a value interpreted as an instruction?
From Prof Onur Mutlu’s presentation

## Slide 9: The Von Neumann Model: Instruction Processing
The program and data are stored as a sequence of bits in the computer memory
The program is executed one instruction at a time under the direction of the control unit
Control unit interprets instructions: generates a sequence of control signals to carry out operations
The most basic unit of computer processing: Instruction. It consists of
  Opcode : Operations to be performed
  Operands: Data/Locations to be used for operation
    Example:
    add $s0, $s1, $s2

## Slide 10: LC-3 Instruction set and Microprocessor
Little Computer – 3
For educational purpose
  Simple Instruction Set : 15 Opcodes
  16-bit
  Addressing modes: immediate, register, PC relative, Indirect, base+Offset
We will use LC-3 only for explanation
Later in the course, we will study RISC-V for programming / design

## Slide 11: LC-3: A Von Neumann Machine
Control signals
(non filled-in Arrow head)
Data
(filled-in Arrow head)
ALU: 2 inputs, 1 output
Memory Data Register
Memory Address
Register
16-bit addressable
Keyboard
KBDR (data), KBSR (status)
Monitor - Display
DDR (data), DSR (status)
8 General Purpose Registers (GPR)
Finite State Machine
(for Generating Control Signals)
Instruction Register
Program Counter
ALU operation
GateALU
From Prof Onur Mutlu’s presentation
Notes: The data path consists of all components that actually process the information during each clock cycle—the functional units that operate on the information, the registers that store information at the end of one cycle so it will be available for further use in subsequent cycles, and the buses and wires that carry information from one point to another in the data path.

## Slide 12: About Assembly and Machine Instructions

## Slide 13: Instruction Types
There are three main types of instructions
Operate instructions
  Execute instructions in the ALU
    Ex: ADD
Data movement instructions
  Read from or write to memory
    Ex: Load LD, Store
Control flow instructions
  Change the sequence of execution
    Branch, Jump etc
    Based on decision making

## Slide 14: An Example Operate Instruction
Addition
  add: mnemonic to indicate the operation to perform
  b, c: source operands
  a: destination operand
  a ← b + c
a = b + c;
add a, b, c
High-level code
Assembly
From Prof Onur Mutlu’s presentation

## Slide 15: Registers
We map variables to registers
add R0, R1, R2
b = R1
c = R2
a = R0
Assembly
LC-3 registers

## Slide 16: From Assembly to Machine Code in LC-3
Addition
ADD R0, R1, R2
LC-3 assembly
Machine Code
0x1042
Machine Code, in short (hexadecimal)
0 0 0 1
0 0 0
0 0 1
0
0 0
0 1 0
OP
DR
SR1
SR2
15
14
13
12
11
10
9
8
7
6
2
1
0
5
4
3
From Prof Onur Mutlu’s presentation

## Slide 17: Instruction Format (or Encoding)
LC-3
  OP = opcode (what the instruction does)
    Example: ADD = 0001
      Semantics: DR ← SR1 + SR2
    Example: AND = 0101
      Semantics: DR ← SR1 AND SR2
  SR1, SR2 = source registers
  DR = destination register
OP
DR
SR1
0
00
SR2
4 bits
3 bits
3 bits
3 bits
15
14
13
12
11
10
9
8
7
6
2
1
0
5
4
3
From Prof Onur Mutlu’s presentation

## Slide 18: Instruction Processing

## Slide 19: Instruction Processing
Decode instruction
Evaluate address
Fetch operands from memory
Execute operation
Store result
Fetch instruction from memory

## Slide 20: ADD Instruction
ADD R0, R1, R2
LC-3 assembly

## Slide 21: ADD Instruction

## Slide 22: ADD Instruction: FETCH
Load the instruction (at address stored in PC) from memory into Instruction Register (IR)
  Copy contents of PC into MAR
  Send “read” signal to memory
  Copy contents of MDR into IR
Then increment PC, so that it points to the next instruction in sequence
  PC becomes PC+1
    Note that LC-3 is word addressable
      If it was byte addressable, PC would have been incremented by 2
EA
OP
EX
S
F
D

## Slide 23: ADD Instruction: FETCH
Step 1: Load MAR and increment PC
Step 2: Access memory
Step 3: Load IR with the content of MDR
From Prof Onur Mutlu’s presentation

## Slide 24: ADD Instruction: DECODE
First identify the opcode
  In LC-3, it is 4-to-16 decoder
    The input is the four bits IR[15:12]
Depending on opcode, identify the operands from the remaining bits
EA
OP
EX
S
F
D
0 0 0 1
0 0 0
0 0 1
0
0 0
0 1 0
OP
DR
SR1
SR2

## Slide 25: ADD Instruction: DECODE
DECODE identifies the instruction to be processed
From Prof Onur Mutlu’s presentation

## Slide 26: ADD Instruction: EVALUATE ADDRESS
Computes the address of the memory location that is needed to process the instruction
ADD instruction has operands in registers
This step is not necessary in ADD
EA
OP
EX
S
F
D
ADD R0, R1, R2

## Slide 27: ADD Instruction: FETCH OPERANDS
EA
OP
EX
S
F
D
The FETCH OPERANDS phase obtains the source operands needed to process the instruction
In ADD
  Obtain the source operands from the register file

## Slide 28: ADD Instruction - FETCH Operands
Fetch Registers from Register File
From Prof Onur Mutlu’s presentation

## Slide 29: ADD Instruction: EXECUTE
Perform the operation, using the source operands
For ADD instruction do add contents of two operand Registers – see next slide
EA
OP
EX
S
F
D

## Slide 30: ADD Instruction: EXECUTE
ADD adds SR1 and SR2
ADD Instruction
From Prof Onur Mutlu’s presentation

## Slide 31: ADD Instruction: STORE Result
The STORE RESULT phase writes to the designated destination – Register R0
Once STORE RESULT is completed, a new instruction cycle starts (with the FETCH phase)
EA
OP
EX
S
F
D

## Slide 32: ADD Instruction: STORE Result
From Prof Onur Mutlu’s presentation

## Slide 33: LDR Instruction
LDR R3, R0, #2
LC-3 assembly
R3 ← Memory[R0 + 2]
These instructions use a particular addressing mode
(i.e., the way the address is calculated), called base+offset

## Slide 34: LDR Instruction – All steps

## Slide 35: LDR Instruction: FETCH Instruction
Load the instruction (at address stored in PC) from memory into Instruction Register (IR)
  Copy contents of PC into MAR
  Send “read” signal to memory
  Copy contents of MDR into IR
Then increment PC, so that it points to the next instruction in sequence
  PC becomes PC+1
    Note that LC-3 is word addressable
      If it was byte addressable, PC would have been incremented by 2
EA
OP
EX
S
F
D

## Slide 36: LDR Instruction: FETCH
Step 1: Load MAR and increment PC
Step 2: Access memory
Step 3: Load IR with the content of MDR

## Slide 37: LDR Instruction: DECODE
First identify the opcode
  In LC-3, it is 4-to-16 decoder
    The input is the four bits IR[15:12]
EA
OP
EX
S
F
D

## Slide 38: Instruction Processing: EVALUATE ADDRESS
Computes the address of the memory location that is needed to process the instruction
This phase is necessary in LDR (Load)
It computes the address of the data word that is to be read from memory
By adding an offset to the content of a register
EA
OP
EX
S
F
D

## Slide 39: LDR Instruction: EVALUATE Address
LDR calculates the address by adding a register and an immediate
ADD
LDR Instruction

## Slide 40: LDR Instruction: FETCH Operands
EA
OP
EX
S
F
D
Step 1: Load MAR with the address calculated in EVALUATE ADDRESS
Step 2: Read memory, placing source operand in MDR

## Slide 41: LDR Instruction: FETCH OPERANDS
LDR loads MAR (step 1), and places the results in MDR (step 2)

## Slide 42: LDR Instruction: EXECUTE
Do nothing for LDR
EA
OP
EX
S
F
D

## Slide 43: LDR Instruction: STORE Result
The STORE RESULT phase writes to the designated destination register
EA
OP
EX
S
F
D
LDR R3, R0, #2
Example

## Slide 44: LDR instruction: Store Result
LDR loads MDR into DR

## Slide 45: The Instruction Cycle
  FETCH
  DECODE
  EVALUATE ADDRESS
  FETCH OPERANDS
  EXECUTE
  STORE RESULT

## Slide 46: Changing the Sequence of Instructions
In the FETCH phase, we increment the Program Counter by 1
What if we don’t want to always execute the instruction that follows this one?
  examples: loop, if-then, function call
Need special instructions that change the contents of the PC
These are called control instructions.
  jumps are unconditional - they always change the PC
  branches are conditional - they change the PC only if some condition is true (e.g., the result of an ADD is zero)

## Slide 47: Changing the Sequence of Instructions
Control instructions allow a program to execute out of sequence
  They can change the PC by loading it during the EXECUTE phase
  That wipes out the incremented PC (loaded during the FETCH phase)

## Slide 48: Jump in LC-3
Unconditional branch or jump
LC-3
  BaseR = Base register
  PC ← R2 (Register identified by BaseR)
JMP R2
1100
000
000000
4 bits
BaseR
3 bits
This is register addressing mode
Notes: jr is R-Type

## Slide 49: LC-3 Data Path and Control signals
PC Multiplexer
GatePC
LD.MAR
GateMDR
LD.IR

## Slide 50: Control of the Instruction Cycle
State 1
  The FSM asserts GatePC and LD.MAR
  It selects input (+1) in PCMUX and asserts LD.PC
State 2
  MDR is loaded with the instruction
State 3
  The FSM asserts GateMDR and LD.IR
State 4
  The FSM goes to next state depending on opcode
State 63
  JMP loads register into PC

## Slide 51: Instruction Processing Summary
Instructions look just like data - it’s all interpretation
Three basic kinds of instructions:
  Computational instructions (ADD, AND, …)
  Data movement instructions (LD, ST, …)
  Control instructions (JMP, BRnz, …)
Six basic phases of instruction processing:
F  D  EA  OP  EX  S
  Not all phases are needed by every instruction
  Phases may take variable number of machine cycles

## Slide 52: Class Summary
In this class we have studied
  Step-by-step instruction processing in LC-3
  Data path components

## Slide 53: Backup slides

## Slide 54: LDR instruction
Back

## Slide 55: ADD Instruction in LC-3
Back

## Slide 56: What is Data path?
The data path consists of all components that actually process the information during each clock cycle
  the functional units that operate on the information: ALU
  the registers that store information at the end of one cycle so it will be available for further use in subsequent cycles
  the buses and wires that carry information from one point to another in the data path
  PC, MAR, MUXES, Condition code logic, Control unit etc
  Control signals are associated with each component in the data path
    ALUK (2 control signals) associated with ALU
      These define how ALU will be used in each cycle
    LD.IR 1
    GATE PC 1
n LC-3, there are 42 control signals that control the elements data path in cycle

## Slide 57: The Von Neumann Model - Summary
John von Neumann proposed a fundamental model of a computer for processing computer programs in 1946
It consists of five parts: memory, a processing unit, input, output, and a control unit.
The computer program is contained in the computer’s memory
Data comes from Program’s memory or input devices
It defines Von Neumann Architecture consisting of
  ALU, Control Unit, Memory, Input, Output, Registers etc
Six phases of instruction cycle: Fetch, Decode, Evaluate Address, Fetch Operands, Execute, and store result

## Slide 58: Addressability
How the bits are accessed determines the addressability
  E.g., word-addressable
  E.g., 8-bit addressable (or byte-addressable)
The total number of addresses is the address space
  In MIPS, the address space is 232
    32-bit addresses
  In x86-64, the address space is (up to) 248
    48-bit addresses
  In RISC-V, the address space
    32-bit, 64-bit, and 128-bit (we will consider only 32-bit)

## Slide 59: The Von Neumann Model: Terminology
MAR: Memory Address Register
  Contains the address of memory location where data is to be read/written
MDR: Memory Data Register
  Contains the data/information that is read from a specified memory location or to be written to the memory location
ALU: Arithmetic and Logic Unit
  Capable of performing basic arithmetic functions (ADD and SUBTRACT) and logic operations (bit-wise AND, OR, and NOT)
Word: Data Element
Word length: ALU processes data element of a fixed size called word length; Each ISA has own word length (eg. 32 bits or 64 bits)
Registers: Temporary Storage
  32 registers or 64 registers each of length 32 bits, 64 bits, 128 bits

## Slide 60: Time to Complete One Instruction
It takes fixed number of clock ticks (repetition of rising or falling edge) to execute each instruction
Hence the clock sequences each phase of an instruction by raising the right signals as the right time
So what determines the time between ticks i.e. the length of the clock cycle?