## Slide 1: CS 211 Computer Architecture Lecture 37: Cache Memory – 3 : Writing and Reading Operations; Multilevel Cache Architecture
Ravi Mittal
ravi.mittal@iitgoa.ac.in
Indian Institute of Technology, Goa

## Slide 2: Acknowledgements
Krste Asanović & Randy H. Katz, CS 61C: Great Ideas in Computer Architecture (Machine Structures), http://inst.eecs.berkeley.edu/~cs61c/
Chapter 6, Memory Hierarchy, Book: Computer Systems: A programmer’s perspective, Randal E. Bryant and David R. O’Hallaron
Prof Onur Mutlu’s Class Presentation, ETH Zürich, Lecture 21b: Memory Hierarchy and Caches, Sprint 2020
Patterson and Hennessy, Book: Computer Organization and Design, Hardware/Software Interface, RISC-V Edition
MIT 6.004 Spring 2020, Class on Caches
Digital Design and Computer Architecture: RISC-V Edition, Harris & Harris Elsevier

## Slide 3: Last Class: Direct Mapped – Fully Associative Caches

## Slide 4: Direct-Mapped Cache: 1-way
Block: 00000
Block: 00001
Block: 00010
Block: 00011
Block: 00100
Block: 00101
Block: 00110
Block: 00111
Block: 01000
Block: 01001
Block: 01010
Block: 01011
Block: 01100
Block: 01101
Block: 01110
Block: 01111
Block: 10000
Block: 10001
Block: 10010
Block: 10011
Block: 10100
Block: 10101
Block: 10110
Block: 10111
Block: 11000
Block: 11001
Block: 11010
Block: 11011
Block: 11100
Block: 11101
Block: 11110
Block: 11111
Main Memory
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4

## Slide 5: Set Associative Cache: 2-way
Block: 00000
Block: 00001
Block: 00010
Block: 00011
Block: 00100
Block: 00101
Block: 00110
Block: 00111
Block: 01000
Block: 01001
Block: 01010
Block: 01011
Block: 01100
Block: 01101
Block: 01110
Block: 01111
Block: 10000
Block: 10001
Block: 10010
Block: 10011
Block: 10100
Block: 10101
Block: 10110
Block: 10111
Block: 11000
Block: 11001
Block: 11010
Block: 11011
Block: 11100
Block: 11101
Block: 11110
Block: 11111
Main Memory
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4

## Slide 6: Set Associative Cache: 4-way
Block: 00000
Block: 00001
Block: 00010
Block: 00011
Block: 00100
Block: 00101
Block: 00110
Block: 00111
Block: 01000
Block: 01001
Block: 01010
Block: 01011
Block: 01100
Block: 01101
Block: 01110
Block: 01111
Block: 10000
Block: 10001
Block: 10010
Block: 10011
Block: 10100
Block: 10101
Block: 10110
Block: 10111
Block: 11000
Block: 11001
Block: 11010
Block: 11011
Block: 11100
Block: 11101
Block: 11110
Block: 11111
Main Memory
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
Index : 1 bit
Tag: 4 bits

## Slide 7: Example: Four-Way Set-Associative Cache
28 = 256 sets each with four ways (each with one block)
31 30 . . . 13 12 11 . . . 2 1 0
Byte offset
Data
Tag
V
0
1
2
.
.
.
253
254
255
Data
Tag
V
0
1
2
.
.
.
253
254
255
Data
Tag
V
0
1
2
.
.
.
253
254
255
Index
Data
Tag
V
0
1
2
.
.
.
253
254
255
8
Index
22
Tag
Hit
Data
32
4x1 select
Way 0
Way 1
Way 2
Way 3
Cache size = 256 * 4 * 8 bytes
MM Size = 232 bytes
Notes: This is called a 4-way set associative cache because there are four cache entries for each cache index. Essentially, you have four direct mapped cache working in parallel.
This is how it works: the cache index selects a set from the cache. The four tags in the set are compared in parallel with the upper bits of the memory address.
If no tags match the incoming address tag, we have a cache miss.
Otherwise, we have a cache hit and we will select the data from the way where the tag matches occur.
This is simple enough. What is its disadvantages?
+1 = 36 min. (Y:16)

## Slide 8: Set Associative Cache: 8-way
Block: 00000
Block: 00001
Block: 00010
Block: 00011
Block: 00100
Block: 00101
Block: 00110
Block: 00111
Block: 01000
Block: 01001
Block: 01010
Block: 01011
Block: 01100
Block: 01101
Block: 01110
Block: 01111
Block: 10000
Block: 10001
Block: 10010
Block: 10011
Block: 10100
Block: 10101
Block: 10110
Block: 10111
Block: 11000
Block: 11001
Block: 11010
Block: 11011
Block: 11100
Block: 11101
Block: 11110
Block: 11111
Main Memory
Index : 0 bit
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
Tag: 5 bits : To find out the blocks that are present in
cache
tag
index
byte Offset
3 bits
0 bit
5b

## Slide 9: Fully Associative Cache
Four lines (blocks) per set
Assume: cache block size B=8 bytes
5 bits
0 bit
3 bits
Address
8lines (blocks) per set
1 set
tag
index
Offset
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
Cache size
= S x E x B data bytes
= 64 bytes
S = number of sets (=2)
E = Number of blocks/Set (=4)
B = data bytes per block (= 8)
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
No of comparators = Number of block in a set = 8
Adapted from Bryant and O’Hallaron, Computer Systems: A Programmer’s Perspective, Third Edition

## Slide 10: Costs of Set-Associative Caches
N-way set-associative cache costs
  N comparators (delay and area)
  MUX delay (set selection) before data is available
  Data available after set selection (and Hit/Miss decision).
Ref: Krste Asanović & Randy H. Katz, Univ of California, Berkeley
Notes: First of all, a N-way set associative cache will need N comparators instead of just one comparator (use the right side of the diagram for direct mapped cache).
A N-way set associative cache will also be slower than a direct mapped cache because of this extra multiplexer delay.
Finally, for a N-way set associative cache, the data will be available AFTER the hit/miss signal becomes valid because the hit/mis is needed to control the data MUX.
For a direct mapped cache, that is everything before the MUX on the right or left side, the cache block will be available BEFORE the hit/miss signal (AND gate output) because the data does not have to go through the comparator.
This can be an important consideration because the processor can now go ahead and use the data without knowing if it is a Hit or Miss. Just assume it is a hit.
Since cache hit rate is in the upper 90% range, you will be ahead of the game 90% of the time and for those 10% of the time that you are wrong, just make sure you can recover.
You cannot play this speculation game with a N-way set-associative cache because as I said earlier, the data will not be available to you until the hit/miss signal is valid.
+2 = 38 min. (Y:18)

## Slide 11: General Cache Organization (S, E, B)
E = 2e lines per set
S = 2s sets
set
line
0
1
2
B-1
tag
v
B = 2b bytes per cache block (the data)
Cache size
= S x E x B data bytes
valid bit
E-way Set Associative
Adapted from Bryant and O’Hallaron, Computer Systems: A Programmer’s Perspective, Third Edition

## Slide 12: Cache Terminology (Self Reading)
Capacity (C):
  number of data bytes in cache
Block size (b):
  bytes of data brought into cache at once
Number of blocks (B = C/b):
  number of blocks in cache: B = C/b
Degree of associativity (N):
  number of blocks in a set
Number of sets (S = B/N):
  each memory address maps to exactly one cache set

## Slide 13: In this class we will study
Reading from Memory
Writing into Memory
Cache block replacement policies
Multilevel Caches

## Slide 14: Reading from Memory

## Slide 15: Reading from Memory
When reading memory, there are two possibilities: Cache hit or Cache miss
Cache hit: Cache holds a valid copy of the block, so it returns the desired data
Cache miss: Cache does not have desired block, so fetch from memory and put in empty (invalid) slot. Returns the desired data
  If cache is full you must discard one valid block and replace it with desired data

## Slide 16: Writing into Cache

## Slide 17: Writing into Cache
Situation with Writing to cache is complicated
Multiple copies of data exist:
  L1, L2, L3, Main Memory, Disk
Write hit - Suppose we write a word w that is already cached (earlier)
  First update the cache location with w
  What is the approach to update the next level of hierarchy?
  Two approaches: Write-Though, and Write-back
Write miss - Suppose we write a word that is not cached
  Two approaches: Write-Allocate, and Write No-Allocate

## Slide 18: Write-Hit case: Write-Through
First update the cash location
Immediately write w’s block to lower levels
  + Simple. All levels are up to date.
  + Consistency: Simpler cache coherence
  Causes more traffic with every write
Every write gets to (main) memory
Writing to memory is slow – may take many cycles
  include Write Buffer to allow processor to continue once data in Buffer
Buffer updates memory in parallel to processor
Advantages of Buffer:
  Write buffer stops CPU from stalling if memory cannot keep up
  Write buffer may have multiple entries to absorb bursts of writes

## Slide 19: Use of Write buffer (ARM)

## Slide 20: Example: Write-Hit case: Write-Through
  Data is updated simultaneously to cache and memory
  Process is simple and reliable
https://www.geeksforgeeks.org/write-through-and-write-back-in-cache/

## Slide 21: Write-Hit case: Write-Back
Defers the update as long as possible by writing the updated block to the next lower level only when it is evicted from the cache by the replacement algorithm
  + Can combine multiple writes to the same block before eviction
    Potentially saves bandwidth between cache levels + saves energy
  - Need a bit in the tag store indicating the block is “dirty/modified”
Memory and Cache are inconsistent

## Slide 22: Write-Hit case: Write-Back
https://www.geeksforgeeks.org/write-through-and-write-back-in-cache/

## Slide 23: Write-Miss cases
Write-Allocate
  Load the corresponding block from the next lower level into the cache and then update the cache block
  Can combine writes instead of writing each of them individually to next level
  Write allocate almost always paired with write-back
    Accessing same address many times -> cache it
  Simpler because write misses can be treated the same way as read misses
  Tries to exploit the spatial locality of writes
  Requires transfer of the whole cache block
Write No-Allocate
  Bypass the cache and write the word directly to the next lower level
  Conserves cache space if locality of writes is low
  Typically paired with write-through

## Slide 24: Write Allocation - Example
https://www.geeksforgeeks.org/write-through-and-write-back-in-cache/

## Slide 25: Write No-Allocate Example
https://www.geeksforgeeks.org/write-through-and-write-back-in-cache/

## Slide 26: Write-Through vs. Write-Back (Self Reading)
Write-Through:
  Simpler control logic
  More predictable timing simplifies processor control logic
  Easier to make reliable, since memory always has copy of data (big idea: Redundancy!)
Write-Back
  More complex control logic
  More variable timing (0,1,2 memory accesses per cache access)
  Usually reduces write traffic
  Harder to make reliable, sometimes cache has only copy of data
Ref: Krste Asanović & Randy H. Katz, Univ of California, Berkeley

## Slide 27: Cache Replacement Policies

## Slide 28: Cache Replacement Policies
Random Replacement
  Hardware randomly selects a cache evict
First In First Out (FIFO)
Least-Recently Used
  Hardware keeps track of access history
  Replace the entry that has not been used for the longest time
  For 2-way set-associative cache, need one bit for LRU replacement
Example of a Simple “Pseudo” LRU Implementation
  Assume 64 Fully Associative entries
  Hardware replacement pointer points to one cache entry
  Whenever access is made to the entry the pointer points to:
    the next entry
  Otherwise: do not move the pointer
  Approximates “not-most-recently used” replacement policy
:
Entry 0
Entry 1
Entry 63
Replacement
Pointer

## Slide 29: Multilevel Cache Architectures

## Slide 30: ARM Cortex A8 Architecture

## Slide 31: ARMv8 8-core processor

## Slide 32: Intel Core i7 Cache Hierarchy
Regs
L1
d-cache
L1
i-cache
L2 unified cache
Core 0
Regs
L1
d-cache
L1
i-cache
L2 unified cache
Core 3
…
L3 unified cache
(shared by all cores)
Main memory
Processor package
L1 i-cache and d-cache:
  32 KB, 8-way,
  Access: 4 cycles
L2 unified cache:
  256 KB, 8-way,
  Access: 10 cycles
L3 unified cache:
  8 MB, 16-way,
  Access: 40-75 cycles
Block size: 64 bytes for all caches.
Bryant and O’Hallaron, Computer Systems: A Programmer’s Perspective, Third Edition

## Slide 33: Intel Nehalem Architecture

## Slide 34: Cache Architecture – A few points
Instruction and Data are accessed in different places in the pipeline
For pipeline reasons, the first level caches are always split
  I-Cache
  D-Cache
Higher level caches are almost always unified

## Slide 35: Multi-level Caching in a Pipelined Design
First-level caches (instruction and data)
  Decisions very much affected by cycle time
  Small, lower associativity; latency is critical
  Tag store and data store accessed in parallel
Second-level caches
  Decisions need to balance hit rate and access latency
  Usually large and highly associative; latency not as important
  Tag store and data store accessed serially
Serial access of levels
  Second level cache accessed only if first-level misses
  Second level does not see the same accesses as the first
    First level acts as a filter (filters some temporal and spatial locality)
    Management policies are therefore different
Ref: Prof Onur Mutlu’s Presentation

## Slide 36: Cache Memory: Performance

## Slide 37: Cache Performance Metrics
Hit Rate
  Percentage of memory accesses in a program or set of instructions that result in a cache hit
  In cache, which is almost million times smaller than MM, the hit rate is 90%-95% (eg 4KiB cache vs 4 GiB Main Memory)
  Hit Rate = No of hits / No of memory accesses
  = 1 – Miss Rate
Miss Rate
  Fraction of memory references that are not found in cache (misses / accesses) = 1 – hit rate
  Typical numbers (in percentages):
    3-10% for L1
    can be quite small (e.g., < 1%) for L2, depending on size, etc.
Miss Penalty
  Time it takes to service a miss
  Additional time required because of a miss (to replace a block in the cache from lower level)
    typically 1000 cycles for main memory

## Slide 38: Cache Performance Metrics
Hit Time
  Time to deliver a line (block) in the cache to the processor
    includes time to determine whether the line is in the cache (tag comparison)
Note that cache is a circuit structure that sits inside core of the processor. It’s critical path component for the processor
Cache has to be properly chosen so that it doesn’t impact the cycle time of the processor
Hit time of the cash is in nano seconds – usually one fourth of a cycle

## Slide 39: Lecture Summary
Reading from Cache
  Cache Hit – Good
  Cache Miss
    Empty block available: Bring the block from MM and put it into an empty block
    Cache is full: Use replacement policy to replace one block and put the block from MM
Writing to Cache
  Write Hit
    Write-Through, Write-back
  Write Miss
    Write-Allocate
    Write No-allocate
L1, L2, and L3 levels of Caches
Cache Memory Performance: Hit Rate, Miss Rate, Miss Penalty, Hit time

## Slide 40: Backup Slides

## Slide 41: Cache Organization Recap
Capacity: C
Block size: b
Number of blocks in cache: B = C/b
Number of blocks in a set: N
Number of sets: S = B/N
Organization | Number of Ways (N) | Number of Sets (S = B/N)
Direct Mapped | 1 | B
N-Way Set Associative | 1 < N < B | B / N
Fully Associative | B | 1

## Slide 42: Multilevel Cache – Advanced design?
Return
L1$
L2$
Main Memory
.
.
.
CPU
Memory
Access
Path of data back to CPU
Miss
Miss
Hit
Hit
Legend:
Request for data
Return of data
Store
Store
If Write Allocate
Write Miss
Write Miss
Notes: The stores back in higher-level caches depends on your write-miss policy (write allocate or no-write allocate).

## Slide 43: Costs of Set-Associative Caches
N-way set-associative cache costs
  N comparators (delay and area)
  MUX delay (set selection) before data is available
  Data available after set selection (and Hit/Miss decision).
Ref: Krste Asanović & Randy H. Katz, Univ of California, Berkeley
Notes: First of all, a N-way set associative cache will need N comparators instead of just one comparator (use the right side of the diagram for direct mapped cache).
A N-way set associative cache will also be slower than a direct mapped cache because of this extra multiplexer delay.
Finally, for a N-way set associative cache, the data will be available AFTER the hit/miss signal becomes valid because the hit/mis is needed to control the data MUX.
For a direct mapped cache, that is everything before the MUX on the right or left side, the cache block will be available BEFORE the hit/miss signal (AND gate output) because the data does not have to go through the comparator.
This can be an important consideration because the processor can now go ahead and use the data without knowing if it is a Hit or Miss. Just assume it is a hit.
Since cache hit rate is in the upper 90% range, you will be ahead of the game 90% of the time and for those 10% of the time that you are wrong, just make sure you can recover.
You cannot play this speculation game with a N-way set-associative cache because as I said earlier, the data will not be available to you until the hit/miss signal is valid.
+2 = 38 min. (Y:18)