## Slide 1: CS 211 Computer Architecture Lecture 42: Input Output Systems – Part 1 Introduction, Polling, Interrupt driven I/O
Ravi Mittal
ravi.mittal@iitgoa.ac.in
Indian Institute of Technology, Goa

## Slide 2: Acknowledgements
Contents of this presentation has been taken from various sources. Would like to thank original contributors
Course 61c, Great Ideas in Computer Architecture, University of California, Berkeley, lecture Input/Output, Instructor Branden Ghena, 2019
Morgan Rae Reschenberg, CS 61C: Great Ideas in Computer Architecture (Machine Structures), http://inst.eecs.berkeley.edu/~cs61c/
Lecture Slides on I/O, course CS 3410, Prof Hakim Weatherspoon, Cornell University
Chapter 7, Input/Output, Computer Organization, William Stallings
Book: Computer Systems: A programmer’s perspective, Randal E. Bryant and David R. O’Hallaron

## Slide 3: We will study today ..
I/O Devices: An Introduction
I/O Devices: Architectures
Memory Mapped I/O: Polling
Memory Mapped I/O: Interrupt

## Slide 4: Input Output Devices: An Introduction

## Slide 5: Five Components of a Computer
Components a computer needs to work
  Control
  Datapath
  Memory
  Input
  Output
Processor
Computer
Control
Datapath
Memory
Devices
Input
Output
Ref: Morgan Rae Reschenberg, Course 61C, Univ of California, Berkeley

## Slide 6: Big Picture: Input/Output (I/O)
How does a processor interact with its environment?
Ref: I/O lecture, Prof Hakim Weatherspoon, Cornell Univ

## Slide 7: Big Picture: Input/Output (I/O)
How does a processor interact with its environment?
Computer System =
Memory + Datapath + Control
Display
Keyboard
Network
Disk
+ Input + Output
Ref: I/O lecture, Prof Hakim Weatherspoon, Cornell Univ

## Slide 8: The importance of I/O
I/O handles persistent storage
  Disks, SSD memory, etc
I/O handles user interfaces
  Keyboard, mouse, display
I/O handles network

## Slide 9: Mouse
I got the idea for the mouse while attending a talk at a computer conference. The speaker was so boring that I started daydreaming and hit upon the idea.
Doug Englebart

## Slide 10: Input Output Devices for Daily use
Laptop
  Keyboard, Mouse, touch pad, Screen, USB ports, Ethernet, WiFi, Bluetooth, Speakers, GPS sensors, heat sensors etc
Ipad
  Touch Screen, WiFi, Bluetooth, USB port, Various sensors
Mobile
WiFi Router
TV
Digital Camera
Mouse

## Slide 11: Inputs have many forms
Keyboard and mouse (USB)
Touch screen
Audio input
Camera
Motion
Fingerprint sensor

## Slide 12: Inputs have many forms
Tiny Radar (Pixel 4)
Ref: CS 61C, Lecture on Input/Output, Branden Ghena, Univ of California, Berkeley
Notes: Google introduced the revolutionary “Motion Sense” technology on the Google Pixel 4 devices.

## Slide 13: Outputs have many forms too
Displays
Audio output
Printers
LEDs
RFID Reader
Ref: CS 61C, Lecture on Input/Output, Branden Ghena, Univ of California, Berkeley

## Slide 14: General-Purpose Computer
Input Output
Computer
Mouse
Keyboard
Ethernet
Bluetooth
Monitor
Headphones
Ethernet
Bluetooth
Ref: CS 61C, Lecture on Input/Output, Branden Ghena, Univ of California, Berkeley

## Slide 15: Cyber-Physical System
Input Output
Computer
Lidar
Inertial Measurement Unit
Camera
CAN
Throttle Control
Brake Control
Wheel Rotation
CAN
CAN: Controller Area Network
Ref: CS 61C, Lecture on Input/Output, Branden Ghena, Univ of California, Berkeley
Notes: Lidar: Light Detection and Ranging: It uses lasers to ping off objects and return to the source of the laser, measuring distance by timing the travel, or flight, of the light pulse.
An inertial measurement unit (IMU) is an electronic device that measures and reports a body's specific force, angular rate, and sometimes the orientation of the body, using a combination of accelerometers, gyroscopes, and sometimes magnetometers.
CAN: Controller Area Network (CAN) is a serial network technology that was originally designed for the automotive industry, especially for European cars, but has also become a popular bus in industrial automation as well as other applications.

## Slide 16: Computers without Input or Output?
Imagine a laptop
  Without a screen
  Without a keyboard or touchpad
  Without WiFi or Ethernet
  Without USB ports
What is it good for?
A computer without I/O is like a car without wheels
  Interesting technology, but gets you nowhere
Ref: CS 61C, Lecture on Input/Output, Branden Ghena, Univ of California, Berkeley

## Slide 17: I/O Device Examples and Speeds
Device | Behavior | Partner | Data Rate (Kb/s)
Keyboard | Input | Human | 0.2
Mouse | Input | Human | 0.4
Microphone | Input | Human | 700.0
Bluetooth | Input or Output | Machine | 20,000.0
Hard disk drive | Storage | Machine | 100,000.0
Wireless network | Input or Output | Machine | 300,000.0
Solid state drive | Storage | Machine | 500,000.0
Wired LAN network | Input or Output | Machine | 1,000,000.0
Graphics display | Output | Human | 3,000,000.0
I/O speeds: 8 orders of magnitude between keyboard and graphics
 System should efficiently handle varying speed I/O devices
Ref: CS 61C, Lecture on Input/Output, Branden Ghena, Univ of California, Berkeley
Notes: keyboard - 1~30*8 byte per secondhttps://www.quora.com/What-amount-of-data-is-transferred-between-a-mouse-and-a-laptop-when-they%E2%80%99re-connected-via-USB
mouse - ~400 byte per second https://www.howtogeek.com/193866/are-there-any-benefits-from-plugging-your-mouse-into-a-usb-3.0-port/ microphone - 44.1 kHz * 16 bit audio
disks - https://www.storagereview.com/ssd_vs_hdd

## Slide 18: Disk Storage and SSD (Self Reading)

## Slide 19: Great Idea: Principle of Locality/ Memory Hierarchy
Primary
Memory
Registers
Hard Disk Drives

## Slide 20: Disk: I/O or Memory?
What qualities might make them one or the other?
A | B | C | D | E
Disks are I/O | Disks are Memory | I don’t know |  | 
Ref: CS 61C, Lecture on Input/Output, Branden Ghena, Univ of California, Berkeley

## Slide 21: Disks are I/O
CPU
RAM
Process A
Process B
Process A
Process B
Process C
Process C
DISK
Disk is never accessed as memory
  Pages are loaded from disk into RAM
Ref: CS 61C, Lecture on Input/Output, Branden Ghena, Univ of California, Berkeley

## Slide 22: Disks (self reading)
Nonvolatile storage
  Retains its value without power
  Long-term, inexpensive storage for files
Two Types:
  Magnetic Drives (Mechanical Drive and Floppy Disk)
    Information stored by magnetizing ferrite material on surface of rotating disk
  Flash Drives (Solid State Drives and Thumb Drives)
    Information stored by trapping charge in a semiconductor and MOSFET based dual-gate transistor
Ref: CS 61C, Lecture on Input/Output, Branden Ghena, Univ of California, Berkeley

## Slide 23: Hard Drive in Action (self reading)
Ref: CS 61C, Lecture on Input/Output, Branden Ghena, Univ of California, Berkeley

## Slide 24: Video of a HDD (self reading)
Video of hard disk in action

## Slide 25
Several platters with information recorded magnetically on both surfaces (usually)
  Bits recorded in tracks, which in turn are divided into sectors (usually 4 kB)
Sector 0
Sector 1
Sector 2
Track 3
Track 3
Ref: CS 61C, Lecture on Input/Output, Branden Ghena, Univ of California, Berkeley
Notes:   Average Rotation Time = time for 1/2 a rotation
  Transfer Time = size of data request / transfer rate

## Slide 26
Reading and writing from the disk:
  Actuator moves head (end of arm) over track (“seek”), wait for sector to rotate under head, then read or write
Disk Access Time =
Seek Time + Rotation Time + Transfer Time + Controller Overhead
Seek Time - time to position head to correct track
Rotation Time - time for disk to rotate to proper sector
Transfer Time - time for data to rotate under the head
Notes:   Average Rotation Time = time for 1/2 a rotation
  Transfer Time = size of data request / transfer rate

## Slide 27: Disk Device Performance (self reading)
To find performance, we can estimate some values
Rotation Time: Average distance of sector from head?
  Average rotation time = 1/2 time of a rotation
    7200 Revolutions Per Minute ⇒ 120 Rev/sec
    1 revolution = 1/120 sec ⇒ 8.33 milliseconds
    1/2 rotation (revolution) ⇒ 4.17 ms ~16,000,000 instructions...
Seek time: Average number of tracks to move arm?
  Number of tracks/3 (see CS186 for the math)
  Average seek time = average number of tracks moved × time to move across one track
Ref: CS 61C, Lecture on Input/Output, Branden Ghena, Univ of California, Berkeley

## Slide 28: Faster Hard Drives (self reading)
Many disks have on-disk caches (totally hidden from the rest of the computer)
L1 cache -> L2 cache -> L3 cache -> RAM -> Disk Cache -> Disk
Ref: CS 61C, Lecture on Input/Output, Branden Ghena, Univ of California, Berkeley

## Slide 29: HDD Difficulties
Fast-spinning disk with moving armatures. What could go wrong?
Head Crash
Literally the head hitting into the disk surface
Ref: CS 61C, Lecture on Input/Output, Branden Ghena, Univ of California, Berkeley

## Slide 30: Fragmentation
To spend less seek and rotation time, we want data to be contiguous whenever possible
Fragmentation occurs when files are not stored contiguously on the disk
Ref: CS 61C, Lecture on Input/Output, Branden Ghena, Univ of California, Berkeley

## Slide 31: What about Solid State Drives?
~10 years ago: Microdrives and Flash memory (e.g., CompactFlash) went head-to-head
Both non-volatile (retains contents without power supply)
  Flash benefits: lower power, no crashes (no moving parts, need to spin µdrives up/down)
  Disk cost = fixed cost of motor + arm mechanics, but actual magnetic media cost very low
  Flash cost = most cost/bit of flash chips
Cost/bit of flash came down, became cost competitive for dense storage
Ref: CS 61C, Lecture on Input/Output, Branden Ghena, Univ of California, Berkeley

## Slide 32: Flash Memory / SSD Technology
NMOS transistor with an additional conductor between gate and source/drain which “traps” electrons. The presence/absence is a 1 or 0

## Slide 33: Flash Memory Problems
Flash has a limited number of program-erase cycles
  10,000 - 100,000 writes total…
Solutions:
  Apply wear leveling to distribute writes evenly
    Move frequently written data around
    Create a map from addresses to real locations
  Lie about how much space you have
    Sell a 100 GB SSD that secretly has 120 GB
    Slowly move memory over as sections die
Ref: CS 61C, Lecture on Input/Output, Branden Ghena, Univ of California, Berkeley

## Slide 34: Original iPods
Ref: CS 61C, Lecture on Input/Output, Branden Ghena, Univ of California, Berkeley

## Slide 35: Smartphones Use Flash Memory
Ref: CS 61C, Lecture on Input/Output, Branden Ghena, Univ of California, Berkeley

## Slide 36
DRAM
Flash
Disk
Notes: DIMM: Dual in-line Memory Module (which has replaced Single in-line Memory Module SIMM)
Flash stick is better known as a USB drive

## Slide 37: Comparing Drive Types
 | HDD | Flash-based SSD
Durability and Noise | Loud and susceptible to shock | No moving parts!
Access Time | ~ 12 ms ≈ 30M clock cycles | ~ 0.1 ms ≈ 250K clock cycles
Relative Power | 1 | 1/3
Cost | ~ $0.017 / GB | ~ $0.099 / GB
Capacity | 500GB - 4TB | 128GB - 500GB
Other Problems | Fragmentation | Limited Writes
Lifespan | 5-10 years | 3-5 years
Ref: CS 61C, Lecture on Input/Output, Branden Ghena, Univ of California, Berkeley

## Slide 38: Methods for I/O

## Slide 39: What do we need for I/O to work?
A way to connect many types of devices
A way to control these devices, respond to them, and transfer data
A way to present them to user programs so they are useful
Proc
Mem
Computer
Ref: CS 61C, Lecture on Input/Output, Branden Ghena, Univ of California, Berkeley

## Slide 40: Methods for I/O
What must the processor do for I/O?
  Input: read a sequence of bytes
  Output: write a sequence of bytes
Interface options
  Input/output instructions: Some processors have special instructions (example: CISC processors) – We will not study it further
  Memory mapped I/O
    Portion of address space dedicated to communication paths to input and output devices
    Use of normal load/store instructions, e.g. lw/sw
    Very common, used by RISC-V
    I/O device use registers there (no memory)
Ref: CS 61C, Lecture on Input/Output, Branden Ghena, Univ of California, Berkeley

## Slide 41: Memory Mapped I/O
Certain addresses are not regular memory addresses
Instead, they correspond to registers in I/O devices
Loads and stores read/write to the device
Ref: CS 61C, Lecture on Input/Output, Branden Ghena, Univ of California, Berkeley
control reg.
data reg.
0x00000000
0xFFFFFFFF
0xFFFF0000
Address

## Slide 42: Memory Maps
Example from EE149
(nRF52832 microcontroller)
Flash from 0x0 - 0x800000
RAM at 0x20000000
Memory-mapped peripherals start at 0x40000000
Ref: CS 61C, Lecture on Input/Output, Branden Ghena, Univ of California, Berkeley

## Slide 43: Memory Mapped Input Output: Polling

## Slide 44: Processor-I/O Speed Mismatch
1 GHz microprocessor can execute 1 billion load or store instructions/sec (32,000,000 Kb/s data rate)
  Recall: I/O devices data rates range from less than 1 Kb/s to more than 1,000,000 Kb/s
Input: Device may not be ready to send data as fast as the processor loads it
  Also, might be waiting for human to act
Output: Device may not be ready to accept data as fast as processor stores it
Ref: CS 61C, Lecture on Input/Output, Branden Ghena, Univ of California, Berkeley

## Slide 45: Processor Checks Status before Acting
Device registers generally serve two functions:
  Control Register, says it’s OK to read/write (I/O ready) - Flag
  Data Register, contains data
Processor reads from Control Register in loop
  Waiting for device to set Ready bit in Control register (0  1)
  Indicates “data available” or “ready to accept data”
Processor then loads from (input) or writes to (output) data register
  I/O device resets control register bit (1  0)
Procedure called “Polling”
Ref: CS 61C, Lecture on Input/Output, Branden Ghena, Univ of California, Berkeley

## Slide 46: I/O Example (Polling)
Input: Read from keyboard into a0
lui t0,0x7ffff #7ffff000 (io addr) Waitloop: lw t1,0(t0) #read control andi t1,t1,0x1 #ready bit beq t1,zero,Waitloop lw a0,4(t0) #data
Output: Write to display from a1
lui t0,0x7ffff #7ffff0000 Waitloop: lw t1,8(t0) #write control andi t1,t1,0x1 #ready bit beq t1,zero,Waitloop sw a1,12(t0) #data
“Ready” bit is from processor’s point of view!
Ref: CS 61C, Lecture on Input/Output, Branden Ghena, Univ of California, Berkeley

## Slide 47: Cost of Polling a Mouse?
Assume for a processor with a 1GHz clock it takes 400 clock cycles for a polling operation (call polling routine, accessing the device, and returning). Determine % of processor time for polling
Mouse: polled 30 times/sec so as not to miss user movement
Mouse Polling [clocks/sec]
  = 30 [polls/s] * 400 [clocks/poll] = 12K [clocks/s]
% Processor for polling:
  12*103 [clocks/s] / 1*109 [clocks/s] = 0.0012%
   Polling mouse little impact on processor’s performance
Ref: CS 61C, Lecture on Input/Output, Branden Ghena, Univ of California, Berkeley

## Slide 48: Cost of Polling a Hard Disk?
Hard disk: transfers data in 16-Byte chunks and can transfer at 16 MB/second. No transfer can be missed
Frequency of Polling Disk
  = 16 [MB/s] / 16 [B/poll] = 1M [polls/s]
Disk Polling, Clocks/sec = 1M [polls/s] * 400 [clocks/poll] = 400M [clocks/s]
% Processor for polling:
  400*106 [clocks/s] / 1*109 [clocks/s] = 40%
   Unacceptable
  (Polling is only part of the problem – main problem is that accessing in small chunks is inefficient)
Ref: CS 61C, Lecture on Input/Output, Branden Ghena, Univ of California, Berkeley

## Slide 49: Memory Mapped Input Output: Interrupt

## Slide 50: What is the Alternative to Polling?
Polling wastes processor resources
Akin to waiting at the door for guests to show up
  What about a bell?
Computer lingo for bell: Interrupt
Solution: Use exception mechanism to help trigger I/O, then interrupt program when I/O is done with data transfer
Ref: CS 61C, Lecture on Input/Output, Branden Ghena, Univ of California, Berkeley

## Slide 51: Exceptions and Interrupts
“Unexpected” events requiring change in flow of control
  Different ISAs use the terms differently
Exception
  Arises within the CPU (e.g. undefined opcode, overflow, syscall, TLB Miss)
  Segmentation fault – core dumped
Interrupt
  From an external I/O controller
  Caused by an event external to current running program
  Example: Key Press, Disk I/O
Dealing with these without sacrificing performance is difficult!
Ref: CS 61C, Lecture on Input/Output, Branden Ghena, Univ of California, Berkeley

## Slide 52: Interrupting the Processor
Ref: CS 61C, Lecture on Input/Output, Branden Ghena, Univ of California, Berkeley

## Slide 53: Exception/Interrupt Steps
External event occurs
Save the PC and registers!
Change PC to exception/interrupt handler
Execute handler code
Restore registers and PC

## Slide 54: Exceptions in a Pipeline
Another kind of control hazard
Consider overflow on fadd.s in EX stage
  fadd.s x1, x2, x1
  Prevent x1 from being clobbered
  Complete previous instructions
  Flush fadd and subsequent instructions
  Save PC and registers
  Transfer control to handler
Similar to mis-predicted branch
  Use much of the same hardware

## Slide 55: I/O Interrupt
An I/O interrupt is like an exception except:
  An I/O interrupt is “asynchronous”
  More information needs to be conveyed
“Asynchronous” with respect to instruction execution:
  I/O interrupt is not associated with any instruction, but it can happen in the middle of any given instruction
  I/O interrupt does not prevent any instruction from running to completion
Ref: Krste Asanović & Randy H. Katz, Univ of California, Berkeley
Notes: How does an I/O interrupt different from the exception you already learned?
Well, an I/O interrupt is asynchronous with respect to the instruction execution while exception such as overflow or page fault are always associated with a certain instruction.
Also for exception, the only information needs to be conveyed is the fact that an exceptional condition has occurred but for interrupt, there is more information to be conveyed.
Let me elaborate on each of these two points.
Unlike exception, which is always associated with an instruction, interrupt is not associated with any instruction. The user program is just doing its things when an I/O interrupt occurs.
So I/O interrupt does not prevent any instruction from completing so you can pick your own convenient point to take the interrupt.
As far as conveying more information is concerned, the interrupt detection hardware must somehow let the OS know who is causing the interrupt.
Furthermore, interrupt requests needs to be prioritized. The hardware that can do all these looks like this.

## Slide 56: Interrupt-Driven Data Transfer
(1) I/O
interrupt
(2) save PC
Memory
add
sub
and
or
user
program
read
store
...
jr
interrupt
service
routine
(3) jump to interrupt
service routine
(4) perform transfer
(5)
Ref: CS 61C, Lecture on Input/Output, Branden Ghena, Univ of California, Berkeley
Notes: That is, whenever an I/O device needs attention from the processor, it interrupts the processor from what it is currently doing.
This is how an I/O interrupt looks in the overall scheme of things. The processor is minding its business when one of the I/O device wants its attention and causes an I/O interrupt.
The processor then save the current PC, branch to the address where the interrupt service routine resides, and start executing the interrupt service routine.
When it finishes executing the interrupt service routine, it branches back to the point of the original program where we stop and continue.
The advantage of this approach is efficiency. The user program’s progress is halted only during actual transfer.
The disadvantage is that it require special hardware in the I/O device to generate the interrupt. And on the processor side, we need special hardware to detect the interrupt and then to save the proper states so we can resume after the interrupt.
+2 = 62 min. (Y:42)

## Slide 57: Interrupt-Driven I/O Example (1/2)
Assume the following system properties:
  500 clock cycle overhead for each transfer, including interrupt
  Disk throughput of 16 MB/s
  Disk interrupts after transferring 16 B
  Processor running at 1 GHz
If disk is active 5% of program, what % of processor is consumed by the disk?
  5% × 16 [MB/s] / 16 [B/inter] = 50,000 [inter/s]
  50,000 [inter/s] × 500 [clocks/inter] = 2.5×107 [clocks/s]
  2.5×107 [clocks/s] / 109 [clock/s] = 2.5% busy
Ref: CS 61C, Lecture on Input/Output, Branden Ghena, Univ of California, Berkeley

## Slide 58: Interrupt-Driven I/O Example (2/2)
2.5% busy (interrupts) much better than 40% (polling) but still not good enough…
Especially if I have multiple devices
Ref: CS 61C, Lecture on Input/Output, Branden Ghena, Univ of California, Berkeley

## Slide 59: Lecture Summary
I/O devices are very important part of any consumer system/Computing platform
I/O devices operate
  at varying degree of bandwidth
  At different timing requirements (non real-time or real-time)
ISA may provide instructions for I/O with external devices
  Not much in use
Memory Mapped I/O (commonly used). Approaches include
  Polling
  Interrupt
  DMA (In the next class)