## Slide 1: CS212 Lecture: Link Layer Technology - Introduction
Ravi Mittal
ravi.mittal@iitgoa.ac.in
Indian Institute of Technology, Goa

## Slide 2: Contents
What is the role of DLL when you connect to a website?
Link Layer Protocols
  CSMA/CD
Ethernet - Introduction

## Slide 3: References
Class Presentation, CS 161, Computer Security, Connection: TLS, Prof Racula Ada Popa, Univ of California, Berkeley
Computer Networking: A Top-down Approach, Book, Jim Kurose and Ross, 8th Edition
Lecture slides: Prof Scott Shenker – Univ of Berkeley at California

## Slide 4: What is the role of Data Link Layer when you connect to a website?

## Slide 5: Connecting to a www server !
Server
Connection to ISP

## Slide 6: What devices you use to connect to Internet?
WiFi Router
Connected to service
Providers eg Airtel
Over Fiber/Ethernet
ADSL Modem connected
to service provider over
Telephone line

## Slide 7: What devices you use to connect to Internet?
Use 3G/4G data-connection
Mobile Network

## Slide 9
Your laptop shouts:
HEY, DOES WIRELESS NETWORK X EXIST?
1. Join the wireless network

## Slide 10
1. Join the wireless network
Wireless access point(s) continually shout: HEY, I’M WIRELESS NETWORK Y, JOIN ME!

## Slide 11
1. Join the wireless network
If either match up, your laptop joins the network. Optionally performs a cryptographic exchange.

## Slide 12
2. Configure your connection
Your laptop shouts:
HEY, ANYBODY, WHAT BASIC CONFIG DO I NEED TO USE?
I need IP address and
other parameters

## Slide 13
2. Configure your connection
Some system on the local network replies: Here’s your config, enjoy
DHCP server

## Slide 14
2. Configure your connection
The configuration includes:
An Internet address (IP address) your laptop should use; typ. 32 bits (IPv4). May also include 64b of the 128b IPv6 address
The address of a “gateway” system to use to access hosts beyond the local network
The address of a DNS server (“resolver”) to map names like google.com to IP addresses
192.168.1.14

## Slide 15
3. Find the address of google.com
Your laptop sends a DNS request asking: “address for google.com?”
It’s transmitted using the UDP protocol (lightweight, unreliable).
The DNS resolver might not be on the local network.
192.168.1.14

## Slide 16
gateway
3. Find the address of google.com
192.168.1.14

## Slide 17
gateway
resolver
router
172.217.6.78
The Rest of
the Internet
3. Find the address of google.com
192.168.1.14

## Slide 18
gateway
resolver
router
172.217.6.78
The Rest of
the Internet
google.com?
3. Find the address of google.com
192.168.1.14

## Slide 19
gateway
resolver
router
172.217.6.78
The Rest of
the Internet
google.com?
(The resolver now itself uses DNS queries to other DNS servers to figure out the address associated with google.com.)
3. Find the address of google.com
192.168.1.14

## Slide 20
gateway
resolver
router
172.217.6.78
The Rest of
the Internet
google.com’s address is 172.217.6.78
3. Find the address of google.com
192.168.1.14

## Slide 21
gateway
resolver
router
172.217.6.78
The Rest of
the Internet
4. Connect to google.com server
192.168.1.14

## Slide 22: Integrated view of the Internet
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Ethernet
HTTP
Skype
IP
WiFi
4G
TCP
Streaming
video
Source: Kurose and Ross Book: 8th Edition

## Slide 23: We know.. IP layer does Routing It interconnects different networks

## Slide 24: The Internet – to glue different type of Networks

## Slide 25
Core Network
Metro Ethernet
Access Network
Mobile Backhaul
Mobile Network
Fixed Network
Enterprise Network
Data Center Network
Broadband
GPON, EPON, DSL,
DSLAMs, CABLE
IP Routers and Switches
Servers
Top of Rack
Agg. Switches
Workgroup switches
edge routers, connectivity
Mobile Backhaul ,
Base Station
The Internet – to glue different type of Networks
The Internet

## Slide 26: Distributed mechanism of Internet
end-system
switch
link
packet
path
Source: Prof Scott Shenker – Univ of Berkeley at California

## Slide 27: Where are links?
Source: Book: Peterson and Davie

## Slide 28: With a path links can be of different types
Source: Book: Peterson and Davie
ADSL –
UTP
Ethernet-
Fiber
WiFi
Cellular
Ethernet-
Cable
Satellite
Ethernet-
Fiber
SONET- Fiber
Ethernet-
Fiber

## Slide 29: Links for home connection
Ethernet
WiFi
Cellular (3G, 4G, 5G)

## Slide 30: Link Layer Protocols

## Slide 31: Link Layer Protocol: Functions
Main functionality: Responsibility of transferring datagram from one node to adjacent node over a link. It achieves it using:
  Framing, physical addressing:
    Encapsulates datagram into frame, adding header, trailer
    Channel access if shared medium
    “MAC” addresses used in frame headers to identify source, dest
  Reliable delivery between adjacent nodes
    Seldom used on low bit-error link (fiber, some twisted pair)
    wireless links: high error rates
  Flow control
    pacing between adjacent sending and receiving nodes
  Error control
    Use of Error correcting codes
  Access Control
Layer-2 packet is a frame, encapsulates datagram

## Slide 32: Data Link Layer

## Slide 33: Data Link Layer
two physically connected devices:
  host-router, router-router, host-host
unit of data: frame
application
transport
network
link
physical
network
link
physical
M
M
M
M
H
t
H
t
H
n
H
t
H
n
H
l
M
H
t
H
n
H
l
frame
phys. link
data link
protocol
adapter card

## Slide 34: Various Link layers within a route
HTTP
TCP
IP
Ethernet
interface
HTTP
TCP
IP
Ethernet
interface
IP
IP
Ethernet
interface
Ethernet
interface
SONET
interface
SONET
interface
host
host
router
router
HTTP message
TCP segment
IP packet
IP packet
IP packet

## Slide 35: Digital adaptors Communicating
Link layer implemented in adaptor (network interface card)
  Ethernet card, 802.11 card
Sending side:
  Encapsulates datagram in a frame
  Adds error checking bits, flow control, etc.
Receiving side
  Looks for errors, flow control, etc.
  Extracts datagram and passes to receiving node
sending
node
frame
receiving
node
datagram
frame
adapter
adapter
link layer protocol

## Slide 36: Multiple Access Protocols

## Slide 37: MAC protocols: taxonomy
Three broad classes:
Channel partitioning
  divide channel into smaller “pieces” (time slots, frequency, code)
  allocate piece to node for exclusive use
  TDMA, FDMA, CDMA
“taking turns”
  nodes take turns, but nodes with more to send can take longer turns
Random access (our interest)
  channel not divided, allow collisions
  “recover” from collisions

## Slide 38: Multiple access links, protocols
Two types of “links”:
Point-to-point
  Point-to-point link between Ethernet switch and host
  PPP for dial-up access
Broadcast (shared wire or medium)
  Old-fashioned Ethernet
  Upstream HFC in cable-based access network
  802.11 wireless LAN, 4G/4G. satellite
shared wire (e.g.,
cabled Ethernet)
shared radio: WiFi
shared radio: satellite
humans at a cocktail party
(shared air, acoustical)
shared radio: 4G/5G

## Slide 39: Multiple access protocols
Single shared broadcast channel
Two or more simultaneous transmissions by nodes: interference
  Collision if node receives two or more signals at the same time
Distributed algorithm that determines how nodes share channel, i.e., determine when node can transmit
Communication about channel sharing must use channel itself!
  No out-of-band channel for coordination
Multiple access protocol

## Slide 40: CSMA (carrier sense multiple access)
Simple CSMA: listen before transmit:
  if channel sensed idle: transmit entire frame
  if channel sensed busy: defer transmission
  human analogy: don’t interrupt others!
CSMA/CD: CSMA with collision detection
  collisions detected within short time
  colliding transmissions aborted, reducing channel wastage
  collision detection easy in wired, difficult with wireless

## Slide 41: CSMA: collisions
Collisions can still occur with carrier sensing:
  Propagation delay means two nodes may not hear each other’s just-started transmission
Collision: entire packet transmission time wasted
  Distance & propagation delay play role in in determining collision probability
spatial layout of nodes

## Slide 42: CSMA/CD:
CSMA/CD reduces the amount of time wasted in collisions
  transmission aborted on collision detection
spatial layout of nodes

## Slide 43: Ethernet CSMA/CD algorithm
NIC receives datagram from network layer, creates frame
If NIC senses channel:
    if idle: start frame transmission.
    if busy: wait until channel idle, then transmit
If NIC transmits entire frame without collision, NIC is done with frame !
If NIC detects another transmission while sending: abort, send jam signal
After aborting, NIC enters binary (exponential) backoff:
  after mth collision, NIC chooses K at random from {0,1,2, …, 2m-1}. NIC waits K·512 bit times, returns to Step 2
  more collisions: longer backoff interval

## Slide 44: Local Area Network (LAN): Ethernet

## Slide 45: Ethernet Generations
Original Ethernet:
  Coaxial cable (10Base5)
  Thicknet.
Next Generation:
  Thin coax cable (10Base2)
  Thinnet.
Modern Ethernet:
  Twisted pair ethernet (10BaseT)
  Uses hub: physical star but logical bus.

## Slide 46: Physical Media for Ethernet
Fiber
Wireless

## Slide 47: Ethernet Switches
Initially, hubs (passive) were used in Ethernet
  Just a signal repeater
Now, active switch in center
Each “spoke” runs a (separate) Ethernet protocol
  No collision
switch
bus: coaxial cable
star

## Slide 49: Lecture Summary
Link Layer is responsible for transferring datagram/frame from one end of the link to the other end of the link
  Error detection, correction
  Sharing a broadcast channel: multiple access
  Link layer addressing
Ethernet is the most important LAN technology
  It uses CSMA/CD protocol
    Simple Algorithm
    In modern switch based Ethernet  No collisions
  Evolved from 10 Mbps link speed to 400 Gbps link speed
  Ethernet + IP  Great combination
  Inexpensive implementation

## Slide 50: Backup Slides

## Slide 51: Corporate Network

## Slide 52: In-Vehicle Network (VAN)
Ref: In-Vehicle Networking Solutions, Renesas
:

## Slide 53: Industrial Ethernet
Image credit: AutomationDirect.com :

## Slide 54: Many flavors of LANs
Ethernet IP
Powerlink
Ethercat
Wireless Sensor Network