## Slide 1: CS 211 Computer Architecture Lecture 5: Inside a Modern Computer System
Ravi Mittal
ravi.mittal@iitgoa.ac.in
Indian Institute of Technology, Goa

## Slide 2: We will study today
What are the components inside a modern desktop?
GPU – Specification
  Why do we need GPUs?

## Slide 3: Today’s Thought
Do you listen?

## Slide 4: Today’s Thought …. By J Krishamurti
“To be able to really listen, one should abandon or put aside all prejudices.
When you are in a receptive state of mind, things can be easily understood
But, unfortunately most of us listen through a screen of resistance.
We are screened with prejudices, whether religious or spiritual, psychological or scientific, or with daily worries, desires or fears.
And with these fears for a screen, we listen.
Therefore, we listen really to our own noise, our own sound, not to what is being said”

## Slide 5: What is inside a modern Desktop?
Processors:
10th Gen Intel® Core™ i9-10900K processor(10-Core, 20M Cache, 3.7GHz to 5.3GHz) – 20 threads
  Integrated GPU: Intel UHD Graphics 630
Discrete GPU: NVIDIA® GeForce® RTX 2070 SUPER™ 8GB GDDR6
Memory:
256GB M.2 PCIe NVMe Solid State Drive
2TB 7200 rpm 3.5" SATA Hard Drive
Intel Optane Memory - 32 GB, Storage Accelerator
DRAM: 128 GB, 4 x 32 GB, DDR4, 2666 MHz/2933 MHz, UDIMM, dual-channel
Chipset
DRAM Bus Width: 64-bits
Flash EPROM 32 MB
Computer Architecture

## Slide 6: What is inside a modern Desktop?
Bus
Peripheral Component Interconnect Express (PCIe or PCI-E) – Gen 3.0
Network
Ethernet: 10/100/1000 Mbps
WLAN
  WLAN: WiFi 802.11a/b/g
  Wi-Fi 4 (WiFi 802.11n)
  Wi-Fi 5 (WiFi 802.11ac)
  Wi-Fi 6 (WiFi 802.11ax)
    2.40 GHz/5 GHz
    64-bit/128-bit WEP, AES-CCMP, TKIP
Bluetooth 5.1

## Slide 7: What is inside a modern Desktop?
Ports: Seven USB 3.1 Gen 1 ports, Two USB 2.0 ports, One USB 3.1 Gen 1 (Type C), Headset port, RJ-45 port (Network), One audio line-out port, other sound ports
Sensors:
Air temperature sensor, Battery Sensor, Finger print sensor

## Slide 8: What is inside a modern Desktop (Dell PC)?
Processors:
10th Gen Intel® Core™ i9-10900K processor(10-Core, 20M Cache, 3.7GHz to 5.3GHz) – 20 threads
  Integrated GPU: Intel UHD Graphics 630
Discrete GPU: NVIDIA® GeForce® RTX 2070 SUPER™ 8GB GDDR6
Memory:
2TB 7200 rpm 3.5" SATA Hard Drive
256GB M.2 PCIe NVMe Solid State Drive
Intel Optane Memory - 32 GB, Storage Accelerator
128 GB, 4 x 32 GB, DDR4, 2666 MHz/2933 MHz, UDIMM, dual-channel
Chipset
DRAM Bus Width: 64-bits
Flash EPROM 32 MB

## Slide 9: Intel’s 10 Core Core i9-10900K

## Slide 10: Main Processor (1)
10th Gen Intel® Core™ i9-10900K processor(10-Core, 20M Cache, 3.7GHz to 5.3GHz) – 20 threads
  Integrated GPU: Intel UHD Graphics 630
Number of cores: 10 ; Number of threads: 20
  Homogeneous Cores ?
  How does a programmer usesthese cores?
  What is the role of OS in using cores?
  How are the cores interconnected? Using bus ?
20 MB built-in cache
  What is Cache Memory? How is it organized?
  How many levels of Cache Memory? Why many levels of Cache?
    L1 instruction cache, L1 data cache, L2 Cache, L3 Cache
Did you notice variable clock speed: 3.7GHz to 5.3GHz
  Why do we need to change clock speed?

## Slide 11: A quad-core Homogeneous Processor Architecture
See backup slides for Advantages and Disadvantages of Multicore processing

## Slide 12: Main Processor (2)
Thermal Design Power (TDP) : 125 W
  The average power, in watts, the processor dissipates when operating at Base Frequency with all cores active under an Intel-defined, high-complexity workload
Processor’s Base Frequency: 3.7 GHz
  The processor base frequency is the operating point where TDP is defined
Max Turbo Frequency: 5.30 GHz
  Max turbo frequency is the maximum single core frequency at which the processor is capable of operating
  How to increase frequency of a processor ?
    Use of Thermal Velocity Boost Feature - automatically increases clock frequency based on how much the processor is operating below its maximum temperature and whether turbo power budget is available
    Depends on the workload, capabilities of the processor and the processor cooling solution
Can we increase frequency selectively on specific core ? Yes.

## Slide 13: What is inside a modern Desktop?
Processors:
10th Gen Intel® Core™ i9-10900K processor(10-Core, 20M Cache, 3.7GHz to 5.3GHz) – 20 threads
  Integrated GPU: Intel UHD Graphics 630
Discrete GPU: NVIDIA® GeForce® RTX 2070 SUPER™ 8GB GDDR6
Memory:
2TB 7200 rpm 3.5" SATA Hard Drive
256GB M.2 PCIe NVMe Solid State Drive
Intel Optane Memory - 32 GB, Storage Accelerator
128 GB, 4 x 32 GB, DDR4, 2666 MHz/2933 MHz, UDIMM, dual-channel
Chipset
DRAM Bus Width: 64-bits
Flash EPROM 32 MB

## Slide 14
CPUs consist of a few cores optimized for serial processing and general purpose calculations.
GPUs consist of hundreds or thousands of smaller, efficient cores designed for parallel performance. The hardware is designed for specific calculations.
CPU
GPU
Notes: Modern CPU's nowadays typically have 2 to 12 cores and are highly optimized for serial processing.
GPUs consist of hundreds or even thousands of smaller efficient cores designed for parallel processing

## Slide 15
Intel Xeon E5-2680v4 :
64 cores
Memory size: 256 GB
Bandwidth: 76.8 GB/sec
NVIDIA Tesla P100:
3840 single precision cores
Memory size: 12GB total
Bandwidth: 549 GB/sec
SCC CPU
SCC GPU
SCC: Single Chip Cloud : Chip designed specially for parallel processing: based
on cloud datacenter architecture
Notes: There is a significant difference in memory size and bandwidth that should be taken into account while deciding where to perform the calculations.

## Slide 16
Minimum Change, Big Speed-up
Application Code
GPU
CPU
Use GPU to Parallelize
Compute-Intensive Functions
Rest of Sequential
CPU Code
+

## Slide 17: GPU: NVIDIA® GeForce® RTX 2070 SUPER™ 8GB GDDR6
Specification:
Number of cores: 2560
Giga Rays/Second: 7
Base Clock: 1770
Boost Clock: 1605
Memory Speed: 14 Gbps
Standard Memory Config: 8 GB GDDR6
  Graphics double data rate type six - synchronous dynamic random-access memory
  It is a type of synchronous graphics random-access memory (SGRAM) with a high bandwidth ("double data rate") interface designed for use in graphics cards, game consoles, and high-performance computing
Notes: In 3D computer graphics, ray tracing is a rendering technique for generating an image by tracing the path of light as pixels in an image plane and simulating the effects of its encounters with virtual objects.
A giga ray is a billion rays cast per second.

## Slide 18: GPU: NVIDIA® GeForce® RTX 2070 SUPER™ 8GB GDDR6
RT Cores
  Dedicated ray tracing hardware enables fast real-time ray tracing with physically accurate shadows, reflections, refractions, and global illumination
Tensor Cores
  For AI processing
Next-Gen Shading
Concurrent Processing
  Simultaneous floating point and integer processing

## Slide 19: What is inside a modern Desktop
Processors:
10th Gen Intel® Core™ i9-10900K processor(10-Core, 20M Cache, 3.7GHz to 5.3GHz) – 20 threads
  Integrated GPU: Intel UHD Graphics 630
Discrete GPU: NVIDIA® GeForce® RTX 2070 SUPER™ 8GB GDDR6
Memory:
2TB 7200 rpm 3.5" SATA Hard Drive
256GB M.2 PCIe NVMe Solid State Drive
Intel Optane Memory - 32 GB, Storage Accelerator
128 GB, 4 x 32 GB, DDR4, 2666 MHz/2933 MHz, UDIMM, dual-channel
Chipset
DRAM Bus Width: 64-bits
Flash EPROM 32 MB
CS 211: Computer Architecture

## Slide 20: A Hard Disk
Common Disk Interfaces
ST-506  ATA  IDE  SATA
For bulk data storage
Suitable for workloads that are largely sequential and not performance sensitive
Lowest $/GB cost
Sizes are decreasing and capacities are increasing
  Up to 14 TB for desktops
Built-in cache: 256MB
  Read and Write caching
Rotational Speed: 7200 rpm
Access times: 6 to 15 ms
  200 times slower than average DRAM

## Slide 21: What is inside a modern Desktop
Processors:
10th Gen Intel® Core™ i9-10900K processor(10-Core, 20M Cache, 3.7GHz to 5.3GHz) – 20 threads
  Integrated GPU: Intel UHD Graphics 630
Discrete GPU: NVIDIA® GeForce® RTX 2070 SUPER™ 8GB GDDR6
Memory:
2TB 7200 rpm 3.5" SATA Hard Drive
256GB M.2 PCIe NVMe Solid State Drive
Intel Optane Memory - 32 GB, Storage Accelerator
128 GB, 4 x 32 GB, DDR4, 2666 MHz/2933 MHz, UDIMM, dual-channel
Chipset
DRAM Bus Width: 64-bits
Flash EPROM 32 MB
CS 211: Computer Architecture

## Slide 22: Beyond Spinning Disks
Hard drives have been around since 1956
  The cheapest way to store large amounts of data
  Sizes are still increasing rapidly
However, hard drives are typically the slowest component in most computers
  CPU and RAM operate at GHz
  PCI-X Bus and Ethernet are GB/s
    Hard disk access time: 6-15 milli-second
    Hard disk bandwidth: 100 – 200 MB/sec
Hard drives are not suitable for mobile devices
  Fragile mechanical components can break
  The disk motor is extremely power hungry

## Slide 23: Solid State Drives
Non-volatile memory
NAND flash memory-based drives
  High voltage is able to change the configuration of a floating-gate transistor
  State of the transistor interpreted as binary data
Flash memory chip
Data is striped across all chips

## Slide 24: Solid State Drives (SSD)
A typical SSD has access speeds of 20 to 100 microseconds, which is nearly 100 times faster than a HDD
Cost: 16 TB SSD: USD 4000
  VS 16 TB HDD: USD 400
Higher reliability as no moving parts
  SDD failure rate: 1-3% per year
  HDD failure rate: 2-9% per year
SDD limitation: Finite number of writes
  3000 write cycles
Significantly low power consumption
Useful for
  graphics or processing video processing
  streaming videos in real-time - no-lag video streaming
In all modern computing machines
https://www.liquidweb.com/blog/ssd-vs-hdd/

## Slide 25: What is inside a modern Desktop
Processors:
10th Gen Intel® Core™ i9-10900K processor(10-Core, 20M Cache, 3.7GHz to 5.3GHz) – 20 threads
  Integrated GPU: Intel UHD Graphics 630
Discrete GPU: NVIDIA® GeForce® RTX 2070 SUPER™ 8GB GDDR6
Memory:
2TB 7200 rpm 3.5" SATA Hard Drive
256GB M.2 PCIe NVMe Solid State Drive
Intel Optane Memory - 32 GB, Storage Accelerator
128 GB, 4 x 32 GB, DDR4, 2666 MHz/2933 MHz, UDIMM, dual-channel
Chipset
DRAM Bus Width: 64-bits
Flash EPROM 32 MB
CS 305: Computer Architecture

## Slide 26: Intel Optane Persistent Memory (2019)
Non-volatile memory – that sits between MM and storage (HDD); Faster than SSD
https://www.storagereview.com/intel_optane_dc_persistent_memory_module_pmm

## Slide 27: Intel Optane Persistent Memory (2019)
Based on 3D-XPoint Technology
  Phase-Change Technology
    What is this technology? How does it work?
Because it is significantly less expensive than DRAM and can have 15X – 20X the memory capacity per die
  8GB vs. 128GB
Speeds at least 10X that of NAND (SSD Drive)
  However, slower than DRAM (Main Memory)
An ideal ‘intermediary’ memory element

## Slide 28: What is inside a modern Desktop
Processors:
10th Gen Intel® Core™ i9-10900K processor(10-Core, 20M Cache, 3.7GHz to 5.3GHz) – 20 threads
  Integrated GPU: Intel UHD Graphics 630
Discrete GPU: NVIDIA® GeForce® RTX 2070 SUPER™ 8GB GDDR6
Memory:
2TB 7200 rpm 3.5" SATA Hard Drive
256GB M.2 PCIe NVMe Solid State Drive
Intel Optane Memory - 32 GB, Storage Accelerator
SDRAM (Synchronous DRAM): 128 GB, 4 x 32 GB, DDR4, 2666 MHz/2933 MHz, UDIMM, dual-channel (Main Memory)
Chipset
DRAM Bus Width: 64-bits
Flash EPROM 32 MB
CS 211: Computer Architecture
Notes: Synchronous random access memory (SDRAM) is the same as DRAM except that regular DRAM is asynchronous. Synchronous random access memory stays synchronized with the computer's clock which allows greater efficiency in storing and retrieving data compared to asynchronous DRAM
DDR4 : double data rate 4

## Slide 29: Main Memory (Volatile + Non-volatile)
Processors
and caches
Main Memory
Storage (SSD/HDD)
GPUs
Most computers use Volatile Memory: DRAM (mainly Synchronous DRAM)
SDRAM Speed: 60-100 ns
Advantages of DRAM: Simplicity (only one Transistor and one capacitor); High density
Notes: SRAM - four or six transistors per bit
SRAM – Used primarily in cache

## Slide 30: Main Memory: DRAM in the System
CORE 1
L2 CACHE 0
SHARED L3 CACHE
DRAM INTERFACE
CORE 0
CORE 2
CORE 3
L2 CACHE 1
L2 CACHE 2
L2 CACHE 3
DRAM BANKS
Multi-Core
Chip
*Die photo credit: AMD Barcelona
DRAM MEMORY CONTROLLER

## Slide 31: What is inside a modern Desktop
Bus
Peripheral Component Interconnect Express (PCIe or PCI-E) – Gen 3.0
Network
Ethernet: 10/100/1000 Mbps
WLAN
  WLAN: WiFi 802.11a/b/g
  Wi-Fi 4 (WiFi 802.11n)
  Wi-Fi 5 (WiFi 802.11ac)
  Wi-Fi 6 (WiFi 802.11ax)
    2.40 GHz/5 GHz
    64-bit/128-bit WEP, AES-CCMP, TKIP
Bluetooth 5.1

## Slide 32: Buses
Main
memory
I/O
bridge
Bus interface
ALU
Register file
CPU chip
System bus
Memory bus
Disk
controller
Graphics
adapter
USB
controller
Mouse
Keyboard
Monitor
Disk
I/O bus
Expansion slots for
other devices such
as network adapters.
PCI Bus

## Slide 33: Ethernet, WiFi, Bluetooth
Ethernet – IEEE 802.5 standard
  De facto LAN technology
  Port speed: 10/100/1000 Mbps ; 48 bit MAC address; CSMA/CD protocol
  Over cable and fiber
  Inexpensive and mature technology
  Easy to understand, implement, manage, and maintain
Wireless LAN – IEEE 802.11b
  Extremely popular
  CSMA based MAC
  Data Rates up to 3.5 Gbps (for 802.11ax)
Bluetooth
  Limited range, Limited speed up to 5 Mbps
  Low power ; Popular in mobile and Laptop

## Slide 34: Computer Architecture Today – Lecture Summary
General Purpose GPUs
Heterogeneous
Processors and
Accelerators
Hybrid Main Memory
Persistent Memory/Storage
High Speed Network

## Slide 35: References
Dell Desktops: www.dell.com
Lecture presentation, Lecture 21a, Memory Organization and Memory Technology, Prof Onur Mutlu, ETH Zürich, Spring 2020
Blog, Donald Firesmith, Multicore processing, https://insights.sei.cmu.edu/sei_blog/2017/08/multicore-processing.html
https://software.intel.com/content/www/us/en/develop/articles/software-techniques-for-shared-cache-multi-core-systems.html?wapkw=smart+cache
https://www.liquidweb.com/blog/ssd-vs-hdd/

## Slide 36: Advantages of Multicore Processing
Energy Efficiency
  Overcome heat generation – Refer Moore’s law
  When low load, some processors can run at low frequency or may be switched off
True Parallelism
Higher Performance
Isolation may improve
  Spatial Isolation
  Temporal Isolation
    Software running on one core may not affect the software on the other core
Reliability and Robustness

## Slide 37: Issues with Multicore Processing
Shared Resources
  Cache, Buses, Memory controller, I/O devices, Network
    May cause interference
    Security Issues
Non-determinism
Analysis Difficulty
If not properly fine tuned, it can have adverse effect on
  Performance
  Real-time guarantees
https://insights.sei.cmu.edu/sei_blog/2017/08/multicore-processing.html

## Slide 38: PCI: Peripheral Component Interconnect Bus