## Slide 1: CS 211 Computer Architecture Lecture 9: ISA - Introduction
Ravi Mittal
ravi.mittal@iitgoa.ac.in
Indian Institute of Technology, Goa

## Slide 2: In this class, we will study
Instruction Set Architecture (ISA) - Basics
ISA vs Microarchitecture
ISA – Specification
Microarchitecture
Trivia

## Slide 3: Acknowledgements
The contents of the presentation has been taken from many sources. Thanks are due to all original contributors – who made my work simple – by sharing their class/book presentations.
Prof Onur Mutulu, ETH Zurich, Lecture 11 Microarchitecture, Digital Design and Architecture Course
Pratt and Patel, Book, Introduction to Computing Systems: From Bits & Gates to C & Beyond (Computer Engineering)

## Slide 4: Instruction Set Architecture (ISA) - Basics

## Slide 5: We will learn that is in-between..
How does an assembly program end up executing as digital logic?
What happens in-between?
How is a computer designed using logic gates and wires to satisfy specific goals?
Systems Prog.
Digital Design
“C” as a model of computation
Digital logic as a
model of computation
Programmer’s view of how
a computer system works
HW designer’s view of how
a computer system works
Architect/microarchitect’s view:
How to design a computer that
meets system design goals.
Choices critically affect both
the SW programmer and
the HW designer
From Prof Onur Mutlu’s presentation
Notes: How is the HW/SW interface designed

## Slide 6: Instruction
An instruction is the fundamental unit of work
An instruction is encoded as a sequence of bits. (Just like data!)
  Often, but not always, instructions have a fixed length, such as 16, 32, or 64 bits
  Control unit interprets instruction: generates sequence of control signals to carry out operation
  Operation is either executed completely, or not at all (atomic)
From Book by Patt and Patel

## Slide 7: Instruction Set
Instruction Set: A set of instructions for a computer
Different computers have different instruction sets
  However, many aspects are common
  Example: x86 Instruction set, ARM instruction set, RISC-V Instruction set, MIPS instruction set, SPARC, PowerPC
Early computers had a very simple instruction sets
  Led to simplified implementation
The ISA is the interface between what the software commands and what the hardware carries out

## Slide 8: Levels of Transformation
Microarchitecture
ISA (Architecture)
Program/Language
Algorithm
Problem
Logic
Devices
Runtime System
(VM, OS, MM)
Electrons
Algorithm
Step-by-step procedure that is guaranteed to terminate where each step is precisely stated and can be carried out by a computer
Finiteness
Definiteness
Effective computability
Many algorithms for the same
problem
ISA
(Instruction Set Architecture)
Interface/contract between SW and HW.
What the programmer assumes hardware will satisfy.
Microarchitecture
An implementation of the ISA
Digital logic circuits
Building blocks of micro-arch (e.g., gates)
From Prof Onur Mutlu’s presentation
Notes: ISA is the interface between hardware and software… It is a contract that the hardware promises to satisfy.
Algorithm: step by step procedure where each step is effectively computable (by a computer), is definite (precisely defined) – “do until fast” is not definite, and terminates

## Slide 9: ISA vs Microarchitecture

## Slide 10: ISA vs. Microarchitecture
ISA: Agreed upon interface between software and hardware
  Specifies how the programmer sees instructions to be executed
  What the software writer needs to know to write and debug system/user programs
Microarchitecture: Specific implementation of an ISA
  How the underlying implementation actually executes instructions
  Microarchitecture can execute instructions in any order as long as it obeys the semantics specified by the ISA when making the instruction results visible to software
    Programmer should see the order specified by the ISA
Microprocessor
  ISA + Microarchitecture + circuits
Microarchitecture
ISA
Program
Algorithm
Problem
Circuits
Electrons
From Prof Onur Mutlu’s presentation

## Slide 11: ISA vs. Microarchitecture
What is part of ISA vs. Microarchitecture?
  Gas pedal of a car: interface for “acceleration”
  Internals of the engine: implement “acceleration”
    An average driver doesn’t care what is under the hood
Implementation (Microarchitecture) can be various as long as it satisfies the specification (ISA)
  Adder implementation
    Bit serial, ripple carry, carry lookahead adders are all part of microarchitecture
  x86 ISA has many implementations: 286, 386, 486, Pentium, Pentium Pro, Pentium 4, Core, …
Microarchitecture usually changes faster than ISA
  Few ISAs (x86, ARM, SPARC, MIPS, Alpha) but many microarchitecture
  Why?
From Prof Onur Mutlu’s presentation

## Slide 12: The Von-Neumann Model and ISA
All major instruction set architectures today use this model
  x86, ARM, RISC, MIPS, SPARC, Alpha, POWER
Underneath (at the microarchitecture level), the execution model of almost all implementations (or, microarchitectures) is very different
  Pipelined instruction execution: Intel 80486 microarchitecture
  Multiple instructions at a time: Intel Pentium microarchitecture
  Out-of-order execution: Intel Pentium Pro microarchitecture
  Separate instruction and data caches
What happens underneath that is not consistent with the von Neumann model is not exposed to software

## Slide 13: Instruction Set Architecture (ISA) –Specification

## Slide 14: ISA Specifies..
The memory organization
  Address space (LC-3: 216, RISC-V: 232 )
  Addressability (LC-3: 16 bits, RISC-V: 32 bits)
  Word- or Byte-addressable (LC-3 is word addressable, RISC-V is byte addressable
  Big endian vs. little endian?
  Support for virtual memory
The register set
  LC-3: R0 to R7
  32 registers in RISC-V
The instruction set
  Opcodes
  Data types
  Addressing modes
From Prof Onur Mutlu’s presentation

## Slide 15: Opcodes in LC-3

## Slide 16: Opcodes in RISC-V (RV32I)

## Slide 17: Opcodes in x-86 (64 bits)
Opcode size: 1, 2, or 3 byte
Instruction format changes - based on Instruction prefix

## Slide 18: Data Types
Definition: Representation of information for which there are instructions that operate on the representation
  Integer, floating point, two’s complement integer, character, binary, decimal, BCD
  Doubly linked list, queue, string, bit vector, stack (Not in RISC)
    VAX: INSQUEUE and REMQUEUE instructions on a doubly linked list or queue; FINDFIRST
    X86: SCAN opcode operates on character strings; PUSH/POP
    Even Hash table is a high level data type defined in an ISA
Advantages and disadvantages of high level data types
  Too many high level data types make ISA/Microarch complex

## Slide 19: Data Types
An ISA supports one or several data types
LC-3 only supports 2’s complement integers
MIPS supports
  2’s complement integers
  Unsigned integers
  Floating point
Tradeoffs
  What data types should be supported and what should not be?

## Slide 20
An addressing mode is a mechanism for specifying where an operand is located
RISC-V Addressing Modes
  Register Only (all operands are in registers)
  Immediate or literal (constant)
  Base Addressing
  PC-Relative
  Pseudo Direct (for J and jal)
Other addressing Modes (Not in RISC-V)
  Direct
  Indirect
  Index
  Register Indirect
Addressing Modes

## Slide 21: Number of operands
Number of operands
  0, 1, 2, 3 address machines
    0-address: stack machine (push A, pop A, op)
    1-address: accumulator machine (ld A, st A, op A)
    2-address: 2-operand machine (one is both source and dest)
    3-address: 3-operand machine (source and dest are separate)
  Tradeoffs
    Larger operate instructions – code size
    Commonly executed instructions
Number of operands may vary in a processor
  Intel x86 instruction can have 0 to 3 operands

## Slide 22: Microarchitecture

## Slide 23: Microarchitecture
Implementation of the ISA design constraints and goals
Anything done in hardware without exposure to software
  Pipelining
  In-order versus out-of-order instruction execution
  Memory access scheduling policy
  Speculative execution
  Superscalar processing
  Clock gating
  Caching: Levels, size, associativity, replacement policy
  Prefetching
  Voltage/frequency scaling?
    Is this feature exposed to programmers? If this is done automatically, then it is a part of Microarchitecture
From Prof Onur Mutlu’s presentation
Notes: Clock gating is a popular technique used in many synchronous circuits for reducing dynamic power dissipation, by removing the clock signal when the circuit is not in use. Clock gating saves power by pruning the clock tree, at the cost of adding more logic to a circuit.

## Slide 24: Quiz: Property of ISA or Microarchitecture?
ADD instruction’s opcode
  ISA
Number of general purpose registers
  ISA
Number of ports to the register file
  Microarchitecture
Number of cycles to execute the MUL instruction
  Microarchitecture
Whether or not the machine employs pipelined instruction execution
  Microarchitecture
Remember
  Microarchitecture: Implementation of the ISA under specific design constraints and goals
From Prof Onur Mutlu’s presentation

## Slide 25: Factors to consider when designing ISA
Cost
Performance
Maximum power consumption
Energy consumption (battery life)
Availability
Reliability and Correctness
Time to Market
Application space – drive design considerations
  General Purpose Computer
  Special Purpose computer
Microarchitecture
ISA
Program
Algorithm
Problem
Circuits
Electrons
From Prof Onur Mutlu’s presentation

## Slide 26: Levels of Transformation – A user centric view
Microarchitecture
ISA
Program/Language
Algorithm
Problem
Runtime System
(VM, OS, MM)
User
Logic
Circuits
Electrons
The entire stack should be optimized for user
From Prof Onur Mutlu’s presentation
Notes: ISA is the interface between hardware and software… It is a contract that the hardware promises to satisfy.

## Slide 27: Demands of Applications
Application have varied set of characteristics
  Scientific applications
  Transaction based applications such as ATM transfers
  Data processing applications
  Network Applications
  Graphics based applications
  Embedded Applications
  Media applications
This leads to different set of demands and tradeoffs
  ISA level tradeoffs
  Micro-architecture level tradeoffs
  System and Task level tradeoffs (how to divide labor between hardware and software

## Slide 28: Different ISAs Over Decades
x86
PDP-x: Programmed Data Processor (PDP-11)
VAX
IBM 360
CDC 6600
SIMD ISAs: CRAY-1, Connection Machine
VLIW ISAs: Multiflow, Cydrome, IA-64 (EPIC)
PowerPC, POWER
RISC ISAs: Alpha, MIPS, SPARC, ARM, RISC - V
What are the fundamental differences?
  How instructions are specified and what they do?
  How complex are the instructions?

## Slide 29: Trivia

## Slide 30: Optical Fiber
In today’s class we are using Zoom Session
Bandwidth requirement: 1 Mbps – 2 Mbps (approximately)
How many Zoom Session a single Fiber can carry ?
100 sessions
1000 sessions
10000 sessions
1 Million Sessions
10 Million Sessions
100 Million Sessions

## Slide 31: Optical Fiber
In today’s class we are using Zoom Session
Bandwidth requirement: 1 Mbps – 2 Mbps (approximately)
How many Zoom Session a single Fiber can carry ?
100 sessions
1000 sessions
10000 sessions
1 Million Sessions
10 Million Sessions
100 Million Sessions
https://spectrum.ieee.org/tech-talk/telecom/internet/single-optical-fibers-100-million-zoom

## Slide 32: Nielsen's Law of Internet Bandwidth
Users' bandwidth grows by 50% per year
  10% less than Moore's Law for computer speed
  The new law fits data from 1983 to 2019

## Slide 33: Backup

## Slide 34: ARM

## Slide 35: LC-3b ISA
LC-3b ISA
  http://users.ece.utexas.edu/~patt/17s.460N/handouts/new_byte.pdf
Concept of “bit steering”
  A bit in the instruction determines the interpretation of other bits

## Slide 36: X86-64 ISA
Just too many instructions and details to fit into this page..
Too complex

## Slide 37: X86-64 ISA
x86-64 ISA manual has over 3,800 pages
This makes compiler very complex
And many other issues..
Complex Instruction Set Architecture
Yet. Intel is very successful

## Slide 38
The instruction format determines the behavior and complexity of the instruction fetch (IF) and decode (ID) pipeline stages
Fixed-size makes fetching instructions easy: just get the next n bytes.
Fixed-size enables a decoding optimization known as direct encoding, in which the bits of the opcode’s value are mapped directly to various CPU control flags. E.g., one bit in the opcode might specify whether the Ex pipeline stage is enabled. Four bits might specify an index into the register file for the source register. This implies that the Decode pipeline stage is a no-op: once we have loaded the instruction, it is already decoded.

## Slide 39
Instruction fetch and decode are inextricably mixed with variable-width instruction formats. We cannot know how long the instruction is until we have decoded at least part of it. Ideally, the low byte of the instruction contains enough information to know the full instruction size, so that the process is: Fetch 1 byte, Decode, Fetch remaining bytes, Decode. Often, however, this is not the case, and the IF and ID proceed in a loop-like fashion: fetch the beginning of the instruction, decode it to determine how much more to fetch, then fetch more, decode, and so forth, until the entire instruction has been fetched and decoded.
Decoding variable-size instructions, even if the entire instruction is available (it isn’t!) is more complex. Direct encoding is almost impossible. The relevant parts of the instruction may be in different places for different instructions. As we’ll see below, MIPS has only three different instruction formats, and the operation is always in the same place in all three. x86, in contrast, has
Extending a variable-size instruction format with new instructions is relatively easy.

## Slide 40: Types of Instructions
Operate instructions
  Process data: arithmetic and logical operations
Data movement instructions
  Move data between memory, registers, I/O devices
Control flow instructions
  Change the sequence of instructions that are executed

## Slide 41: Addressing Modes
Addressing modes specify how to obtain the operands
  Absolute or immediate: LW rt, 10000
  use immediate value as address
  Register Indirect: LW rt, (rbase)
  use GPR[rbase] as address
  Displaced or base+Offset: LW rt, offset(rbase)
  use offset+GPR[rbase] as address
  Indexed: LW rt, (rbase, rindex)
  use GPR[rbase]+GPR[rindex] as address
  Memory Indirect LW rt ((rbase))
  use value at M[ GPR[ rbase ] ] as address
  Auto inc/decrement LW Rt, (rbase)
  use GRP[rbase] as address, but inc. or dec. GPR[rbase] each time
Notes: Indexed mode for gather scatter.

## Slide 42: Evolution of Register Architecture
Accumulator
  a legacy from the “adding” machine days
Accumulator + address registers
  need register indirection
  initially address registers were special-purpose, i.e., can only be loaded with an address for indirection
  eventually arithmetic on addresses became supported
General purpose registers (GPR)
  all registers good for all purposes
  grew from a few registers to 32 (common for RISC) to 128 in Intel IA-64

## Slide 43: Elements of ISA –Register (Repeat)
Registers
  How many?
  Size of each register
Why - having registers a good idea?
  Because programs exhibit a characteristic called data locality
  A recently produced/accessed value is likely to be used more than once (temporal locality)
    Storing that value in a register eliminates the need to go to memory each time that value is needed
  Registers are built directly in hardware – so they are very fast – faster than 1 ns i.e. 5-10 times faster than cache memory
  In Load-store (register –register) architecture, data never goes to ALU from memory. Data is first brought to registers.